## Slide 1
D.C. circuits
Loops, Junctions and Real Cells
ΣI in = ΣI out
PREDICT · TEST · EXPLAIN
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
01 / 20
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
A minimal dark cover with one large topic title, one lesson title and one governing equation.
[Teacher cue]
Do not explain yet. Give students five seconds to identify one symbol they already know.
[Activity]
Opening
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 1 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 2
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
02 / 20
Start with a prediction
A 12 V battery reads only 10.8 V while delivering current. Where did the missing 1.2 V go?
THINK 20 s → PAIR → COMMIT
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
One large diagnostic question fills the slide; no answer or hint is visible.
[Teacher cue]
Students write an answer before speaking. Collect two contrasting predictions and revisit them on slide 15.
[Activity]
Diagnostic hook
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 2 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 3
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
03 / 20
Two quick checks before we build
Q1
First law at junction conserves?
A energy
B charge
C resistance
D power
Q2
V–I graph intercept for a cell?
A r
B E
C 1/r
D power
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Two multiple-choice retrieval questions share a clean split canvas; answers are absent.
[Teacher cue]
Use mini-whiteboards. Ask for one reason, not a show of hands.
[Activity]
Retrieval vote
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 3 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Teacher detail]
Q1: charge. Steady current cannot accumulate charge at a junction. Q2: E. At I = 0 there is no lost volts.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 4
04 / 20
See the idea
ONE SENTENCE
Kirchhoff’s first law is charge conservation at a junction.
E, r
R₂
R₁
junction: I = I₁ + I₂
I
loop: ΣE = ΣIR
I₂
I₁
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
The original editable native diagram is preserved, paired with one concise governing statement and larger labels.
[Teacher cue]
Ask students to point to the part of the figure that makes the sentence true. Invite one student to relabel a shape.
[Activity]
Concept figure
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 4 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 5
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
05 / 20
Build the model: what happens?
01
Kirchhoff’s first law is charge conservation at a junction.
02
Kirchhoff’s second law is energy conservation around a loop.
Connect them in one spoken sentence.
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Two large numbered physical ideas appear with no formula list.
[Teacher cue]
Reveal one idea at a time verbally. Ask a student to connect cause and effect.
[Activity]
Model stage one
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 5 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 6
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
06 / 20
Build the model: what controls it?
A real source has e.m.f. and internal resistance: terminal p.d. falls with current.
Potential dividers and potentiometers compare or control potential differences.
EQUATIONS TO EXPLAIN
ΣI in = ΣI out
ΣE = ΣIR
V = E − Ir
EXAM EDGE · E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Two controlling ideas sit beside a large equation stack. Vocabulary is moved to notes.
[Teacher cue]
Students name every symbol and unit. Ask which equation can be rejected by dimensions before calculation.
[Activity]
Model stage two
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 6 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Teacher detail]
Key vocabulary: e.m.f., terminal p.d., internal resistance, junction, loop, potential divider.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 7
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
07 / 20
Predict the graph before the data appear
Terminal p.d. (V)
Current (A)
SKETCH → LABEL → DEFEND
linear?
curved?
constant?
changes sign?
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
A large blank pair of labelled axes occupies most of the slide; four relationship prompts sit at the right.
[Teacher cue]
Students sketch individually, then compare gradients, intercepts and curvature before the next slide reveals data.
[Activity]
Graph prediction
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 7 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 8
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
08 / 20
Terminal p.d. falls linearly with current
Chart: Terminal p.d. (V)
| 0 | 2 | 4 | 6 | 8
D.C. circuits | 12 | 11 | 10 | 9 | 8
EDIT THE CHART · Change internal resistance from 0.50 Ω to 0.80 Ω while keeping E = 12.0 V.
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
A large editable native chart fills the canvas. The only additional copy is one data-edit challenge.
[Teacher cue]
Compare the class sketches with the data, then use Edit Data in PowerPoint. Require a physical explanation for every changed point.
[Activity]
Graph reveal and edit
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 8 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Teacher detail]
Intercept gives e.m.f.; negative gradient magnitude gives internal resistance. Data: (0, 12), (2, 11), (4, 10), (6, 9), (8, 8).
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 9
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
09 / 20
Worked problem: commit before the reveal
A cell of e.m.f. 1.50 V and internal resistance 0.20 Ω is connected to a 2.8 Ω resistor. Find current and terminal p.d.
ESTIMATE · CHOOSE THE MODEL · STATE THE SIGN
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Only the problem and three decision verbs are visible; no working or answer appears.
[Teacher cue]
Ask for an estimate and the governing model before touching a calculator.
[Activity]
Worked problem prompt
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 9 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 10
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
10 / 20
Worked reveal: make the first two decisions
01
Total resistance = 2.8 + 0.20 = 3.0 Ω.
02
I = E/(R + r) = 1.50/3.0 = 0.50 A.
Your turn: write the next line before clicking.
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
The first two calculation decisions appear as large numbered lines; the final result is absent.
[Teacher cue]
Pause before each line. Students predict the operation, then justify it with units or a sign convention.
[Activity]
Worked method reveal
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 10 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 11
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
11 / 20
Worked reveal: finish and sense-check
V = IR = 0.50 × 2.8 = 1.40 V.
I = 0.50 A; terminal p.d. = 1.40 V.
Does the sign, unit and size make physical sense?
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
The final calculation step and answer appear at large scale on a dark high-contrast slide.
[Teacher cue]
Ask students to challenge the sign, unit and order of magnitude before accepting the answer.
[Activity]
Worked answer reveal
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 11 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 12
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
12 / 20
Guided problem: solver and sceptic
A 6.0 V supply feeds 2.0 kΩ and 4.0 kΩ in series. Find the p.d. across the 4.0 kΩ resistor and explain one sensor use.
01 · FIRST HINT · Use the potential-divider ratio.
SOLVER proposes · SCEPTIC checks units and assumptions
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
A single problem and one first hint are visible. Pair roles make the discussion active.
[Teacher cue]
Give ninety seconds. The solver proposes a line; the sceptic must approve the physics before it is written.
[Activity]
Guided pair attempt
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 12 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 13
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
13 / 20
Guided reveal: test the route
01 Use the potential-divider ratio.
02 The larger resistor gets the larger share.
03 A sensor’s resistance can replace one resistor.
V = 4.0 V; a thermistor or LDR can make the output depend on temperature or light.
CHANGE ONE VALUE · predict what must change before recalculating
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Two remaining hints, one answer and a change-one-value extension are separated clearly.
[Teacher cue]
Students compare routes, not just answers. Change one given value orally and ask for a proportional prediction.
[Activity]
Guided route reveal
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 13 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 14
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
14 / 20
Spot the physics trap
“Kirchhoff’s second law says every component gets the same voltage.”
A TRUE · B PARTLY TRUE · C FALSE
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Only the misconception claim and three voting choices are visible; the repair is absent.
[Teacher cue]
Everyone commits. Ask one student from each choice to identify the exact word that creates the problem.
[Activity]
Misconception vote
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 14 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 15
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
15 / 20
Repair the idea
The algebraic sum of potential changes around a complete loop is zero; individual drops depend on resistance and current.
Voltage is shared by the loop, not handed out as identical party bags.
Rewrite the claim in 12 words or fewer.
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
The correction and one memorable humorous line appear only after the class vote.
[Teacher cue]
Return to the opening hook. Students rewrite the misconception precisely in twelve words or fewer.
[Activity]
Misconception repair
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 15 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 16
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
16 / 20
Original exam-style challenge
5 MARKS · ORIGINAL GIOPHYSICS QUESTION
A 9.0 V source with internal resistance 1.0 Ω supplies two 6.0 Ω resistors in parallel. Calculate the source current and terminal p.d.
MODEL → WORKING → UNITS → SENSE-CHECK
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
The original exam-style question stands alone with four method words and no mark scheme.
[Teacher cue]
Allow silent first work. Students underline the command word and box the data before comparing methods.
[Activity]
Independent exam attempt
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 16 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 17
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
17 / 20
Mark it, improve it, explain it
1
Parallel external resistance = 3.0 Ω.
2
Total resistance = 4.0 Ω.
3
I = 9.0/4.0 = 2.25 A.
4
V = E − Ir = 9.0 − 2.25 = 6.75 V.
5
Equivalent check V = IRext = 6.75 V.
Recover one mark: add the missing physics, not extra prose.
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Up to five concise mark points form one spacious vertical reveal.
[Teacher cue]
Reveal one point at a time. Students annotate where each mark was earned and improve one line.
[Activity]
Peer mark and improve
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 17 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 18
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
18 / 20
Exit quiz · questions 1–2
Q1
First law at junction conserves?
A energy
B charge
C resistance
D power
Q2
V–I graph intercept for a cell?
A r
B E
C 1/r
D power
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Two multiple-choice questions share the slide at large type; answers are withheld.
[Teacher cue]
Use mini-whiteboards or finger voting. Require a written reason for the less confident item.
[Activity]
Exit quiz pair
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 18 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Teacher detail]
Q1: charge. Steady current cannot accumulate charge at a junction. Q2: E. At I = 0 there is no lost volts.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 19
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
19 / 20
Exit quiz · questions 3–4
Q3
Gradient magnitude of terminal V vs I?
A E
B r
C R+r
D 1/E
Q4
Two equal parallel resistors have?
A different p.d.
B same branch p.d.
C zero current
D series current
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Two multiple-choice questions share the slide at large type; answers are withheld.
[Teacher cue]
Use mini-whiteboards or finger voting. Require a written reason for the less confident item.
[Activity]
Exit quiz pair
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 19 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Teacher detail]
Q3: r. V = E − Ir. Q4: same branch p.d.. Parallel branches share the same endpoints.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.

## Slide 20
AS · CAMBRIDGE PHYSICS 9702 · TOPIC 10 · D.C. CIRCUITS
20 / 20
Answers, then one minute of thinking
Q1 charge
Q2 E
Q3 r
Q4 same branch p.d.
ONE-MINUTE PAPER · Which idea changed your answer?
Notes: [Sources]
Cambridge International AS & A Level Physics 9702 syllabus (2025–2027, Version 1), https://www.cambridgeinternational.org/Images/664565-2025-2027-syllabus.pdf
Cambridge International qualification page, https://www.cambridgeinternational.org/programmes-and-qualifications/view/cambridge-international-as-and-a-level-physics-9702/
All worked examples, class questions, charts and quiz items are original GioPhysics material; none is copied from a Cambridge paper.
No external visual assets are used; visible content remains editable PowerPoint text, shapes and charts.
[Visual description]
Four short answers precede one large one-minute-paper prompt. Explanations stay in the notes.
[Teacher cue]
Students correct in a different colour, then answer the reflection before leaving.
[Activity]
Answers and reflection
[Curriculum alignment]
AS Level; Topic 10 D.C. circuits; slide 20 of 20.
[Syllabus edge]
E.m.f. is the energy the source gives each coulomb round the whole circuit; p.d. is what each coulomb delivers to a component.
[Teacher detail]
Q1: charge. Steady current cannot accumulate charge at a junction. Q2: E. At I = 0 there is no lost volts. Q3: r. V = E − Ir. Q4: same branch p.d.. Parallel branches share the same endpoints.
[Safety]
Use low-voltage current-limited supplies; check polarity and component ratings before energising.
Independent GioPhysics resource; not endorsed by Cambridge International.