## Slide 1
CAMBRIDGE IGCSE PHYSICS 0625 · SYLLABUS 4.2
Electrical quantities
Electrical Quantity Control Room
A lamp has 3 V across it and 0.020 A through it. Which number describes flow and which describes energy per charge?
EDITABLE · 45-MINUTE CLASSROOM LESSON · CORE + SUPPLEMENT
GROUP 4 · ELECTRICITY AND MAGNETISM
01 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A dark-green opening slide with the exact topic title “Electrical quantities”, an accent ring for group 4, and a single hook question.
[Teacher cue]
Ask the hook question before revealing any explanation. Listen for the vocabulary students already use, then connect their answers to syllabus section 4.2.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.

## Slide 2
GROUP 4 · ELECTRICITY AND MAGNETISM
02 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Three ideas to wake up
Think alone → compare with a partner → vote with one reason.
1
Where is an ammeter connected?
2
Where is a voltmeter connected?
3
State the unit of resistance.
Mini-whiteboard challenge: sketch or calculate one idea you expect to use today.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Three large numbered retrieval questions run down the slide, followed by a mini-whiteboard challenge. No answers are visible on this slide.
[Teacher cue]
Allow silent think time first. Ask for answers without confirming immediately; invite a partner to explain or challenge each response before the reveal later in the lesson.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.

## Slide 3
GROUP 4 · ELECTRICITY AND MAGNETISM
03 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Four electrical quantities answer four different questions
01
Core: E.m.f. is energy supplied per charge; p.d. is energy transferred per charge in a component.
02
Core: Resistance R = V/I; d.c. is one-way, while a.c. repeatedly reverses.
03
Core: Power P = IV and energy E = IVt; wire R rises with length and falls with area; cost = kWh × tariff.
04
Supplement: Current I = Q/t and e.m.f./p.d. = W/Q; conventional current opposes electron drift in metals.
05
Supplement: Electric field is force per positive charge, from + to −. Wire R is directly proportional to length and inversely proportional to area.
EQUATIONS TO OWN
CORE · R = V/I
Units: R in Ω, V in V, I in A
CORE · P = IV; E = IVt
Units: P in W, E in J or kWh with consistent units
SAY IT PRECISELY
charge · current · e.m.f. · potential difference · resistance · power
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Five concise syllabus ideas form a vertical sequence on the left. An editable dark equation panel and vocabulary rail sit on the right.
[Teacher cue]
Explain one core idea at a time. Ask students to restate each idea using one vocabulary word, then reveal the relevant equation only after its variables are named.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.

## Slide 4
GROUP 4 · ELECTRICITY AND MAGNETISM
04 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
In one sentence: electrical quantities
SIMPLE DEFINITION
This topic names what flows and what pushes it: charge is what moves, current is the charge passing a point each second, potential difference is the energy every coulomb delivers to a component, and resistance is how strongly that component opposes the flow.
R = 200 Ω
6.0 V cell
A
V
I = 0.030 A, the same all round the loop
p.d. 6.0 V: the energy each coulomb gives up in R
Q = It and R = V/I
The ammeter sits in the path to count the flow; the voltmeter sits across the component to count what each coulomb loses there.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
The simple definition is stated in one sentence across the top of the slide. Below it a drawn diagram is labelled R = 200 Ω, 6.0 V cell, A, V, I = 0.030 A, the same all round the loop, Q = It and R = V/I. A caption reads: The ammeter sits in the path to count the flow; the voltmeter sits across the component to count what each coulomb loses there.
[Teacher cue]
Explain one core idea at a time. Ask students to restate each idea using one vocabulary word, then reveal the relevant equation only after its variables are named.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.

## Slide 5
GROUP 4 · ELECTRICITY AND MAGNETISM
05 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
For a fixed resistor, V is proportional to I
INTERACTIVE GRAPH · PREDICT → EDIT → EXPLAIN
Predict the shape first. Then click the native chart in PowerPoint, change one value and explain what physics changed.
Data: 100 Ω resistor: (0, 0), (0.01, 1), …, (0.03, 3), (0.04, 4).
Scale: chart 0–4 V; source 0–4 V. Source: Current / A; Potential difference / V. Chart: Current / mA; Potential difference / V.
Chart: Potential difference / V
| 0 | 10 | 20 | 30 | 40
100 Ω resistor | 0 | 1 | 2 | 3 | 4
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
An editable line chart plots Potential difference in V against Current in A; Current is converted from amperes to milliamperes; Potential difference remains in V. The left rail states the original data and scale so the graph remains accessible without colour.
[Teacher cue]
Ask for a silent prediction before showing the plotted relationship. Then select the native chart, edit one data value and ask which physical quantity and conclusion must change. Exact ohmic model at constant temperature; if plotting I against V, the gradient would be 1/R instead.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Quantitative visual] Values: 100 Ω resistor: (0, 0), (0.01, 1), (0.02, 2), (0.03, 3), (0.04, 4). Data: illustrative lesson data. Scale: 0 to 4 V.
Units: x uses amps; y uses volts.

## Slide 6
GROUP 4 · ELECTRICITY AND MAGNETISM
06 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Worked example: charge and energy
CORE + SUPPLEMENT · FULLY WORKED PROBLEM · SHOW THE METHOD
A current of 0.50 A flows for 3.0 min through a 12 V device. Find charge transferred and electrical energy.
Step 1
3.0 min = 180 s.
Step 2
Q = It = 0.50×180 = 90 C.
Step 3
E = IVt = 0.50×12×180.
Answer: Q = 90 C; E = 1080 J.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A large problem statement is followed by three editable Step 1–3 reasoning lines and a high-contrast answer band.
[Teacher cue]
Model the reasoning aloud, then ask students to explain why each operation is valid. Pause before the answer and listen for unit or substitution errors.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Worked problem] Steps: 1) 3.0 min = 180 s. 2) Q = It = 0.50×180 = 90 C. 3) E = IVt = 0.50×12×180. Answer: Q = 90 C; E = 1080 J.

## Slide 7
GROUP 4 · ELECTRICITY AND MAGNETISM
07 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Your turn: resistance and power
CORE · GUIDED WORKED PROBLEM · TRY EACH STEP BEFORE READING ON
A component has 6.0 V across it and current 0.030 A. Find resistance and power.
Step 1
R = 6.0/0.030.
Step 2
P = 0.030×6.0.
Step 3
Check the direction, significant figures and physical meaning of the result.
Answer: R = 200 Ω; P = 0.18 W.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A large problem statement is followed by three editable Step 1–3 reasoning lines and a high-contrast answer band.
[Teacher cue]
Ask students to solve each line on mini-whiteboards before you explain and reveal the next step. Compare units and methods, not only final numbers.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Worked problem] Steps: 1) R = 6.0/0.030. 2) P = 0.030×6.0. 3) Check the direction, significant figures and physical meaning of the result. Answer: R = 200 Ω; P = 0.18 W.

## Slide 8
GROUP 4 · ELECTRICITY AND MAGNETISM
08 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Meter placement triage
CLASS ACTIVITY · CIRCUIT-CARD-AUDIT
YOU NEED
• four circuit cards • ammeter/voltmeter symbols
1
Identify unsafe/incorrect meter placements.
2
Move ammeter into series and voltmeter into parallel.
3
Predict which reading each meter reports.
Success check: No ammeter is placed directly across a source.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A dark activity slide shows required materials on the left, three large numbered instructions on the right and a success criterion at the bottom.
[Teacher cue]
Explain the success check before starting. Circulate, listen for misconceptions and ask pairs to compare evidence. Stop the activity with enough time for one group to model a strong answer.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Safety] Use low-voltage supplies only; no mains electricity is used in class.

## Slide 9
GROUP 4 · ELECTRICITY AND MAGNETISM
09 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
MISCONCEPTION SHOWDOWN · SPOT THE MISTAKE
“Voltage flows through a circuit.”
Charge flows; potential difference is energy transferred per unit charge between points.
Voltage is not commuting around the circuit with a tiny briefcase.
Mini-whiteboard: Which quantity is measured at one point in a branch, and which between two points?
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A full accent-colour slide contrasts one large misconception with a dark correction band, a classroom-safe joke and a mini-whiteboard check.
[Teacher cue]
Ask students to vote true or false before reading the correction. Invite one pair to explain the trap, then use the humorous line as a memory cue rather than as the scientific explanation.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Humor] Voltage is not commuting around the circuit with a tiny briefcase.

## Slide 10
GROUP 4 · ELECTRICITY AND MAGNETISM
10 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Original exam-style: sensor resistor
Core + Supplement · 7 MARKS · CALCULATE · EXPLAIN
A 240 Ω sensor carries 0.025 A for 80 s. Calculate p.d., charge and energy transferred. Explain what the V–I graph gradient represents when V is vertical.
SOLVE PAIR COMPARE JUSTIFY
Original GioPhysics exam-style question · not a Cambridge past-paper question.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
An original 7-mark exam-style question occupies the main page, with a dark solve–pair–compare–justify sequence beside it.
[Teacher cue]
Give independent thinking time, then ask pairs to compare methods before answers. Listen for each command word: calculate, explain. Do not reveal the mark scheme until slide 11.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.

## Slide 11
GROUP 4 · ELECTRICITY AND MAGNETISM
11 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Mark it like an examiner
Compare evidence, award one idea at a time, then improve one line.
1
V = IR = 0.025×240 = 6.0 V.
2
Q = It = 0.025×80 = 2.0 C.
3
E = IVt = 0.025×6.0×80 = 12 J.
4
Gradient = ΔV/ΔI.
5
For an ohmic resistor this equals resistance.
6
Correct units.
Add one missing physics term and one unit to your response, then explain the hardest mark to a partner.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Six numbered mark-scheme ideas are arranged in two readable columns, followed by a dark pair-improvement challenge.
[Teacher cue]
Reveal one numbered marking point at a time. Ask students to locate matching evidence in their own answer, explain missing reasoning and improve one line before counting marks.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.

## Slide 12
GROUP 4 · ELECTRICITY AND MAGNETISM
12 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Final quiz: four questions, one calm brain
Answer all four. Add one reason to the question you found hardest.
Q1
Current unit?
A C · B A · C V · D Ω
Q2
Voltmeter connection?
A series · B parallel · C source short · D earth only
Q3
3 V, 0.02 A: R?
A 0.006 Ω · B 0.15 Ω · C 60 Ω · D 150 Ω
Q4
Electrical power?
A IV · B I/V · C V/I · D It only
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A four-question final quiz is presented in two columns. Each question has four editable answer choices and space for independent reasoning.
[Teacher cue]
Run the quiz independently first. Ask students to commit to all four answers, then compare only the question they found hardest. Do not reveal solutions until slide 13.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Final quiz] Four original retrieval and application questions. Require at least one spoken or written justification before the answer reveal.

## Slide 13
GROUP 4 · ELECTRICITY AND MAGNETISM
13 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.2
Quiz answers: correct, explain, improve
1.
Answer: A
Ampere is coulomb per second.
2.
Answer: parallel
It compares two points.
3.
Answer: 150 Ω
3/0.02.
4.
Answer: IV
P = IV.
Next move: Correct one response, name the governing physics idea, and write one question you can now answer that you could not answer at the start.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-22/electric-current-charge
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Four numbered quiz answers appear as horizontal rows on a dark background, each pairing the correct answer with a concise reason and ending with an exit ticket.
[Teacher cue]
Reveal answers one at a time. Ask for the reason before reading it, then invite students to correct in a different colour and complete the one-sentence exit ticket.
[Syllabus coverage]
Describe positive/negative charge, charging by friction, attraction/repulsion and conductor/insulator behaviour.; Define current as charge flow and distinguish conventional current from electron drift; use I = Q/t (Supplement).; Distinguish e.m.f. and p.d. as work/energy per charge and use E or V = W/Q (Supplement).; Define/use resistance R = V/I and interpret V–I characteristics for ohmic and non-ohmic components.; Use P = IV and E = IVt, including kWh/cost contexts where data are supplied.; Connect ammeters in series and voltmeters in parallel safely.
[Safety]
Use low-voltage supplies only; no mains electricity is used in class.
[Quiz answers] 1. A — Ampere is coulomb per second. 2. parallel — It compares two points. 3. 150 Ω — 3/0.02. 4. IV — P = IV.