## Slide 1
CAMBRIDGE IGCSE PHYSICS 0625 · SYLLABUS 4.4
Electrical safety
Mains Safety Casebook
A metal-cased appliance develops a live-wire fault. Which wire and device prevent the case remaining live?
EDITABLE · 45-MINUTE CLASSROOM LESSON · CORE
GROUP 4 · ELECTRICITY AND MAGNETISM
01 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A dark-green opening slide with the exact topic title “Electrical safety”, an accent ring for group 4, and a single hook question.
[Teacher cue]
Ask the hook question before revealing any explanation. Listen for the vocabulary students already use, then connect their answers to syllabus section 4.4.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 2
GROUP 4 · ELECTRICITY AND MAGNETISM
02 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Three ideas to wake up
Think alone → compare with a partner → vote with one reason.
1
Which conductor is dangerous relative to earth?
2
What is the purpose of a fuse?
3
What does double insulation remove the need for?
Mini-whiteboard challenge: sketch or calculate one idea you expect to use today.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Three large numbered retrieval questions run down the slide, followed by a mini-whiteboard challenge. No answers are visible on this slide.
[Teacher cue]
Allow silent think time first. Ask for answers without confirming immediately; invite a partner to explain or challenge each response before the reveal later in the lesson.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 3
GROUP 4 · ELECTRICITY AND MAGNETISM
03 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Safety devices reduce fault duration and accessible voltage
01
Core: Switches and fuses belong in the live conductor.
02
Core: An earth wire provides a low-resistance fault path from a metal case.
03
Core: A fuse/trip rating should be just above normal operating current.
04
Core: Double-insulated appliances use non-conducting outer cases or two insulation barriers.
EQUATIONS TO OWN
CORE · P = IV, so I = P/V
Units: P in W, I in A, V in V
SAY IT PRECISELY
live · neutral · earth · fuse · trip switch · double insulation
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Four concise syllabus ideas form a vertical sequence on the left. An editable dark equation panel and vocabulary rail sit on the right.
[Teacher cue]
Explain one core idea at a time. Ask students to restate each idea using one vocabulary word, then reveal the relevant equation only after its variables are named.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 4
GROUP 4 · ELECTRICITY AND MAGNETISM
04 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
In one sentence: electrical safety
SIMPLE DEFINITION
Electrical safety is the set of arrangements that keeps mains electricity from passing through a person: live, neutral and earth each have a job, and fuses, trip switches, earthing and double insulation cut the supply or stop exposed metal becoming live.
live wire touches the metal case: what happens next
metal case
fuse
live
neutral
earth
fault current
the surge melts the fuse and disconnects the live supply
The earth wire offers the fault an easy route, and the surge that follows is exactly what blows the fuse in the live wire.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
The simple definition is stated in one sentence across the top of the slide. Below it a drawn diagram is labelled metal case, fuse, live, neutral, earth, fault current. A caption reads: The earth wire offers the fault an easy route, and the surge that follows is exactly what blows the fuse in the live wire.
[Teacher cue]
Explain one core idea at a time. Ask students to restate each idea using one vocabulary word, then reveal the relevant equation only after its variables are named.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 5
GROUP 4 · ELECTRICITY AND MAGNETISM
05 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Operating current guides fuse selection
INTERACTIVE GRAPH · PREDICT → EDIT → EXPLAIN
Predict the shape first. Then click the native chart in PowerPoint, change one value and explain what physics changed.
Data: I = P/V: (60 W lamp, 0.26), (1150 W heater, 5), (2300 W kettle, 10).
Scale: chart 0.26–10 A; source 0.26–10 A. Source: Appliance at 230 V / category; Operating current / A. Chart: Appliance at 230 V / category; Operating current / A.
Chart: Appliance at 230 V / category
| 60 W lamp | 1150 W heater | 2300 W kettle
I = P/V | 0.26 | 5 | 10
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
An editable bar chart plots Operating current in A against Appliance at 230 V in category; Appliance at 230 V remains in category; Operating current remains in A. The left rail states the original data and scale so the graph remains accessible without colour.
[Teacher cue]
Ask for a silent prediction before showing the plotted relationship. Then select the native chart, edit one data value and ask which physical quantity and conclusion must change. Theoretical mains calculation only. Actual plug systems/ratings vary by country; use the ratings provided in the question and local standards.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Quantitative visual] Values: I = P/V: (60 W lamp, 0.26), (1150 W heater, 5), (2300 W kettle, 10). Data: illustrative lesson data. Scale: 0.26 to 10 A.
Units: x uses category; y uses amps.

## Slide 6
GROUP 4 · ELECTRICITY AND MAGNETISM
06 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Worked example: fuse choice
CORE · FULLY WORKED PROBLEM · SHOW THE METHOD
A 2300 W kettle operates at 230 V. Find current and choose from 3 A, 5 A or 13 A fuses.
Step 1
I = P/V.
Step 2
I = 2300/230 = 10 A.
Step 3
Choose the smallest listed rating safely above 10 A.
Answer: Operating current = 10 A; choose 13 A.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A large problem statement is followed by three editable Step 1–3 reasoning lines and a high-contrast answer band.
[Teacher cue]
Model the reasoning aloud, then ask students to explain why each operation is valid. Pause before the answer and listen for unit or substitution errors.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Worked problem] Steps: 1) I = P/V. 2) I = 2300/230 = 10 A. 3) Choose the smallest listed rating safely above 10 A. Answer: Operating current = 10 A; choose 13 A.

## Slide 7
GROUP 4 · ELECTRICITY AND MAGNETISM
07 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Your turn: fault sequence
CORE · GUIDED WORKED PROBLEM · TRY EACH STEP BEFORE READING ON
Order these events: live wire touches metal case; fuse melts; earth current becomes large; supply disconnects.
Step 1
Live touches case.
Step 2
Large current flows through earth.
Step 3
Fuse/trip operates.
Answer: Fault → large earth current → protection operates → supply disconnects.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A large problem statement is followed by three editable Step 1–3 reasoning lines and a high-contrast answer band.
[Teacher cue]
Ask students to solve each line on mini-whiteboards before you explain and reveal the next step. Compare units and methods, not only final numbers.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Worked problem] Steps: 1) Live touches case. 2) Large current flows through earth. 3) Fuse/trip operates. Answer: Fault → large earth current → protection operates → supply disconnects.

## Slide 8
GROUP 4 · ELECTRICITY AND MAGNETISM
08 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Safety inspector: approve, reject, explain
CLASS ACTIVITY · CASE-CARD-AUDIT
YOU NEED
• damaged cable • wet hands • overloaded extension • double-insulated case cards
1
Identify the hazard or protection.
2
Name the dangerous consequence.
3
State the corrective action without touching real mains equipment.
Success check: Every rejection names both fault and protection/action.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A dark activity slide shows required materials on the left, three large numbered instructions on the right and a success criterion at the bottom.
[Teacher cue]
Explain the success check before starting. Circulate, listen for misconceptions and ask pairs to compare evidence. Stop the activity with enough time for one group to model a strong answer.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Safety] Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 9
GROUP 4 · ELECTRICITY AND MAGNETISM
09 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
MISCONCEPTION SHOWDOWN · SPOT THE MISTAKE
“The earth wire carries current all the time in normal operation.”
It normally carries negligible current; it provides a fault path when needed.
Earth is the emergency exit, not the daily commute.
Mini-whiteboard: Why must the earth path have low resistance?
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A full accent-colour slide contrasts one large misconception with a dark correction band, a classroom-safe joke and a mini-whiteboard check.
[Teacher cue]
Ask students to vote true or false before reading the correction. Invite one pair to explain the trap, then use the humorous line as a memory cue rather than as the scientific explanation.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Humor] Earth is the emergency exit, not the daily commute.

## Slide 10
GROUP 4 · ELECTRICITY AND MAGNETISM
10 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Original exam-style: metal toaster
Core · 7 MARKS · CALCULATE · EXPLAIN · STATE
A 0.92 kW metal-cased toaster operates at 230 V. Calculate current and select 3 A, 5 A or 13 A protection. Explain how earth and fuse protect a user after a live-case fault. State one reason a plastic-cased double-insulated device may not need earth.
SOLVE PAIR COMPARE JUSTIFY
Original GioPhysics exam-style question · not a Cambridge past-paper question.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
An original 7-mark exam-style question occupies the main page, with a dark solve–pair–compare–justify sequence beside it.
[Teacher cue]
Give independent thinking time, then ask pairs to compare methods before answers. Listen for each command word: calculate, explain, state. Do not reveal the mark scheme until slide 11.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 11
GROUP 4 · ELECTRICITY AND MAGNETISM
11 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Mark it like an examiner
Compare evidence, award one idea at a time, then improve one line.
1
920 W used.
2
I = 920/230 = 4.0 A.
3
Select 5 A as the smallest listed rating above normal current.
4
Earth gives low-resistance path.
5
Large fault current operates fuse/trip.
6
Live supply disconnects.
Add one missing physics term and one unit to your response, then explain the hardest mark to a partner.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Six numbered mark-scheme ideas are arranged in two readable columns, followed by a dark pair-improvement challenge.
[Teacher cue]
Reveal one numbered marking point at a time. Ask students to locate matching evidence in their own answer, explain missing reasoning and improve one line before counting marks.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.

## Slide 12
GROUP 4 · ELECTRICITY AND MAGNETISM
12 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Final quiz: four questions, one calm brain
Answer all four. Add one reason to the question you found hardest.
Q1
Fuse belongs in?
A live · B neutral only · C earth · D case
Q2
Earth purpose?
A normal load · B fault path · C raise voltage · D store charge
Q3
2.3 kW at 230 V draws?
A 0.01 A · B 1 A · C 10 A · D 529 A
Q4
Double-insulated case is?
A conducting · B non-conducting/protected by two barriers · C always earthed metal · D fuse-free mains
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A four-question final quiz is presented in two columns. Each question has four editable answer choices and space for independent reasoning.
[Teacher cue]
Run the quiz independently first. Ask students to commit to all four answers, then compare only the question they found hardest. Do not reveal solutions until slide 13.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Final quiz] Four original retrieval and application questions. Require at least one spoken or written justification before the answer reveal.

## Slide 13
GROUP 4 · ELECTRICITY AND MAGNETISM
13 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.4
Quiz answers: correct, explain, improve
1.
Answer: live
Breaking live isolates the appliance from dangerous potential.
2.
Answer: fault path
It carries fault current safely.
3.
Answer: 10 A
2300/230.
4.
Answer: non-conducting/protected by two barriers
Accessible parts cannot become live under a single insulation fault.
Next move: Correct one response, name the governing physics idea, and write one question you can now answer that you could not answer at the start.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-39/electrical-safety
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Four numbered quiz answers appear as horizontal rows on a dark background, each pairing the correct answer with a concise reason and ending with an exit ticket.
[Teacher cue]
Reveal answers one at a time. Ask for the reason before reading it, then invite students to correct in a different colour and complete the one-sentence exit ticket.
[Syllabus coverage]
Identify live, neutral and earth conductors and place switches/fuses in live.; Recognise hazards from damaged insulation, damp conditions, overheated/overloaded cables and incorrect connections.; Explain fuse and trip-switch operation and select a rating just above normal operating current.; Explain earthing of metal cases and why double-insulated appliances need no earth connection.; Use P = IV to calculate appliance current while treating real mains work as diagram/data only.
[Safety]
Use a simulation or de-energised model only; no mains electricity is used in class.
[Quiz answers] 1. live — Breaking live isolates the appliance from dangerous potential. 2. fault path — It carries fault current safely. 3. 10 A — 2300/230. 4. non-conducting/protected by two barriers — Accessible parts cannot become live under a single insulation fault.