## Slide 1
CAMBRIDGE IGCSE PHYSICS 0625 · SYLLABUS 4.5
Electromagnetic effects
Motor, Generator, Transformer
A motor and generator contain similar ingredients. Why does one take electricity in while the other sends it out?
EDITABLE · 45-MINUTE CLASSROOM LESSON · CORE + SUPPLEMENT
GROUP 4 · ELECTRICITY AND MAGNETISM
01 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A dark-green opening slide with the exact topic title “Electromagnetic effects”, an accent ring for group 4, and a single hook question.
[Teacher cue]
Ask the hook question before revealing any explanation. Listen for the vocabulary students already use, then connect their answers to syllabus section 4.5.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 2
GROUP 4 · ELECTRICITY AND MAGNETISM
02 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Three ideas to wake up
Think alone → compare with a partner → vote with one reason.
1
What field forms around a current-carrying wire?
2
What change is needed to induce an e.m.f.?
3
Does a transformer require a.c. or steady d.c.?
Mini-whiteboard challenge: sketch or calculate one idea you expect to use today.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Three large numbered retrieval questions run down the slide, followed by a mini-whiteboard challenge. No answers are visible on this slide.
[Teacher cue]
Allow silent think time first. Ask for answers without confirming immediately; invite a partner to explain or challenge each response before the reveal later in the lesson.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 3
GROUP 4 · ELECTRICITY AND MAGNETISM
03 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Three devices rearrange the same field relationships
01
Core: Current creates magnetic fields; solenoids strengthen them and operate relays.
02
Core: A current-carrying conductor feels force; a loudspeaker uses this motor effect.
03
Core: Changing flux induces e.m.f.; transformers transfer changing flux between coils.
04
Supplement: A split-ring sustains motor rotation; a.c. generators reverse output. Moving charged particles also feel magnetic force.
05
Supplement: Direction follows field/current/force rules and Lenz's law; high voltage lowers current and I²R cable loss.
EQUATIONS TO OWN
CORE · Vp/Vs = Np/Ns
Units: voltage ratio equals turns ratio
SUPPLEMENT · IpVp = IsVs (ideal)
Units: power in W
SAY IT PRECISELY
solenoid · motor effect · electromagnetic induction · generator · transformer · Lenz's law
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Five concise syllabus ideas form a vertical sequence on the left. An editable dark equation panel and vocabulary rail sit on the right.
[Teacher cue]
Explain one core idea at a time. Ask students to restate each idea using one vocabulary word, then reveal the relevant equation only after its variables are named.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 4
GROUP 4 · ELECTRICITY AND MAGNETISM
04 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
In one sentence: electromagnetic effects
SIMPLE DEFINITION
Electricity and magnetism are two faces of one thing: a current creates a magnetic field, a current sitting in a field feels a force that can turn a motor, and a changing field induces a voltage, which is what generators and transformers exploit.
Vp/Vs = Np/Ns
Np = 1200
Ns = 200
240 V a.c. in
40 V a.c. out
changing flux
iron core
steady d.c. would give no output at all
Nothing crosses the gap but a changing magnetic field — and it must be changing, which is why transformers refuse steady d.c.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
The simple definition is stated in one sentence across the top of the slide. Below it a drawn diagram is labelled Vp/Vs = Np/Ns, Np = 1200, Ns = 200, 240 V a.c. in, 40 V a.c. out, changing flux, iron core, steady d.c. would give no output at all. A caption reads: Nothing crosses the gap but a changing magnetic field — and it must be changing, which is why transformers refuse steady d.c.
[Teacher cue]
Explain one core idea at a time. Ask students to restate each idea using one vocabulary word, then reveal the relevant equation only after its variables are named.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 5
GROUP 4 · ELECTRICITY AND MAGNETISM
05 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Rotating generator produces alternating e.m.f.
INTERACTIVE GRAPH · PREDICT → EDIT → EXPLAIN
Predict the shape first. Then click the native chart in PowerPoint, change one value and explain what physics changed.
Data: One cycle: (0, 0), (0.25, 2), …, (0.75, -2), (1, 0).
Scale: chart -2–2 V; source -2–2 V. Axes: source Time / s; Induced e.m.f. / V; chart Time / ms; Induced e.m.f. / V.
Chart: Induced e.m.f. / V
| 0 | 250 | 500 | 750 | 1000
One cycle | 0 | 2 | 0 | -2 | 0
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
An editable line chart plots Induced e.m.f. in V against Time in s; Time is converted from seconds to milliseconds; Induced e.m.f. remains in V. The left rail states the original data and scale so the graph remains accessible without colour.
[Teacher cue]
Ask for a silent prediction before showing the plotted relationship. Then select the native chart, edit one data value and ask which physical quantity and conclusion must change. Ideal illustrative sinusoidal output; use editable points and a zero axis.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Quantitative visual] Values: One cycle: (0, 0), (0.25, 2), (0.5, 0), (0.75, -2), (1, 0). Data: illustrative lesson data. Scale: -2 to 2 V.
Units: x uses s; y uses volts.

## Slide 6
GROUP 4 · ELECTRICITY AND MAGNETISM
06 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Worked example: step-down transformer
CORE · FULLY WORKED PROBLEM · SHOW THE METHOD
A transformer has 1200 primary turns and 200 secondary turns. Primary p.d. is 240 V. Find secondary p.d.
Step 1
Vp/Vs = Np/Ns.
Step 2
240/Vs = 1200/200 = 6.
Step 3
Vs = 240/6.
Answer: Vs = 40 V; it is step-down.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A large problem statement is followed by three editable Step 1–3 reasoning lines and a high-contrast answer band.
[Teacher cue]
Model the reasoning aloud, then ask students to explain why each operation is valid. Pause before the answer and listen for unit or substitution errors.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Worked problem] Steps: 1) Vp/Vs = Np/Ns. 2) 240/Vs = 1200/200 = 6. 3) Vs = 240/6. Answer: Vs = 40 V; it is step-down.

## Slide 7
GROUP 4 · ELECTRICITY AND MAGNETISM
07 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Your turn: transmission loss
SUPPLEMENT / EXTENDED · GUIDED WORKED PROBLEM · TRY EACH STEP BEFORE READING ON
A cable has resistance 4.0 Ω. Compare loss at 20 A and 2.0 A.
Step 1
At 20 A: 20²×4.0 = 1600 W.
Step 2
At 2.0 A: 2.0²×4.0 = 16 W.
Step 3
Check the direction, significant figures and physical meaning of the result.
Answer: Loss falls from 1600 W to 16 W—a factor of 100.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A large problem statement is followed by three editable Step 1–3 reasoning lines and a high-contrast answer band.
[Teacher cue]
Ask students to solve each line on mini-whiteboards before you explain and reveal the next step. Compare units and methods, not only final numbers.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Worked problem] Steps: 1) At 20 A: 20²×4.0 = 1600 W. 2) At 2.0 A: 2.0²×4.0 = 16 W. 3) Check the direction, significant figures and physical meaning of the result. Answer: Loss falls from 1600 W to 16 W—a factor of 100.

## Slide 8
GROUP 4 · ELECTRICITY AND MAGNETISM
08 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Device sequence sort
CLASS ACTIVITY · SUPPLEMENT · CAUSE-EFFECT-CHAIN
YOU NEED
• motor, generator, transformer process cards
1
Build each cause-effect chain.
2
Label input and output energy pathways.
3
Reverse one condition and predict direction/output change.
Success check: Motor and generator chains are not swapped; transformer includes changing flux.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A dark activity slide shows required materials on the left, three large numbered instructions on the right and a success criterion at the bottom.
[Teacher cue]
Explain the success check before starting. Circulate, listen for misconceptions and ask pairs to compare evidence. Stop the activity with enough time for one group to model a strong answer.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Safety] Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 9
GROUP 4 · ELECTRICITY AND MAGNETISM
09 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
MISCONCEPTION SHOWDOWN · SPOT THE MISTAKE
“A magnet near a coil always produces current.”
An e.m.f. requires changing flux; a stationary unchanging arrangement induces none.
The coil needs change, not just a magnet standing nearby looking important.
Mini-whiteboard: Name three ways to increase induced e.m.f.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A full accent-colour slide contrasts one large misconception with a dark correction band, a classroom-safe joke and a mini-whiteboard check.
[Teacher cue]
Ask students to vote true or false before reading the correction. Invite one pair to explain the trap, then use the humorous line as a memory cue rather than as the scientific explanation.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Humor] The coil needs change, not just a magnet standing nearby looking important.

## Slide 10
GROUP 4 · ELECTRICITY AND MAGNETISM
10 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Original exam-style: grid transformer
Core + Supplement · 8 MARKS · CALCULATE · EXPLAIN · STATE
A transformer raises 10 kV to 250 kV. Its primary has 800 turns. Calculate secondary turns. Explain why a.c. is required and why high voltage reduces cable loss for fixed transmitted power. State how to reverse motor force.
SOLVE PAIR COMPARE JUSTIFY
Original GioPhysics exam-style question · not a Cambridge past-paper question.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
An original 8-mark exam-style question occupies the main page, with a dark solve–pair–compare–justify sequence beside it.
[Teacher cue]
Give independent thinking time, then ask pairs to compare methods before answers. Listen for each command word: calculate, explain, state. Do not reveal the mark scheme until slide 11.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 11
GROUP 4 · ELECTRICITY AND MAGNETISM
11 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Mark it like an examiner
Compare evidence, award one idea at a time, then improve one line.
1
Vs/Vp = Ns/Np.
2
Ns = 800×250/10 = 20 000 turns.
3
A.c. produces changing current/field/flux.
4
For fixed power, higher V means lower I.
5
Cable loss is I²R, so lower I greatly reduces loss.
6
Reverse current or magnetic field to reverse force.
Add one missing physics term and one unit to your response, then explain the hardest mark to a partner.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Six numbered mark-scheme ideas are arranged in two readable columns, followed by a dark pair-improvement challenge.
[Teacher cue]
Reveal one numbered marking point at a time. Ask students to locate matching evidence in their own answer, explain missing reasoning and improve one line before counting marks.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.

## Slide 12
GROUP 4 · ELECTRICITY AND MAGNETISM
12 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Final quiz: four questions, one calm brain
Answer all four. Add one reason to the question you found hardest.
Q1
Motor converts electrical mainly to?
A kinetic · B nuclear · C chemical · D gravitational only
Q2
Induction needs?
A constant flux · B changing flux · C no field · D d.c. only
Q3
Step-up transformer has Ns?
A less than Np · B greater than Np · C always equal · D zero
Q4 · SUPPLEMENT
Halve current: I²R loss becomes?
A half · B quarter · C double · D four times
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
A four-question final quiz is presented in two columns. Each question has four editable answer choices and space for independent reasoning.
[Teacher cue]
Run the quiz independently first. Ask students to commit to all four answers, then compare only the question they found hardest. Do not reveal solutions until slide 13.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Final quiz] Four original retrieval and application questions. Require at least one spoken or written justification before the answer reveal.

## Slide 13
GROUP 4 · ELECTRICITY AND MAGNETISM
13 / 13
GIOPHYSICS · CAMBRIDGE IGCSE PHYSICS 0625 · 4.5
Quiz answers: correct, explain, improve
1.
Answer: kinetic
Motor effect creates motion.
2.
Answer: changing flux
Flux linkage must change.
3.
Answer: greater than Np
Vs/Vp = Ns/Np.
4.
SUPPLEMENT · Answer: quarter
Loss depends on current squared.
Next move: Correct one response, name the governing physics idea, and write one question you can now answer that you could not answer at the start.
Notes: [Sources]
Cambridge IGCSE Physics 0625 syllabus (2026–2028), https://www.cambridgeinternational.org/Images/697209-2026-2028-syllabus.pdf
GioPhysics lesson route, https://giophysics.com/chapter-28
This deck uses original GioPhysics worked examples and questions; it is not a Cambridge past paper.
[Visual description]
Four numbered quiz answers appear as horizontal rows on a dark background, each pairing the correct answer with a concise reason and ending with an exit ticket.
[Teacher cue]
Reveal answers one at a time. Ask for the reason before reading it, then invite students to correct in a different colour and complete the one-sentence exit ticket.
[Syllabus coverage]
Describe magnetic fields around current-carrying wires and solenoids and how current/turns/core affect electromagnet strength.; Describe force on a current-carrying conductor, determine direction where required, and explain a simple d.c. motor including split-ring action.; Describe electromagnetic induction and factors increasing induced e.m.f.; apply Lenz's-law direction reasoning (Supplement).; Explain an a.c. generator's construction/output and connect rotation to alternating e.m.f.; Explain transformer operation with changing flux and use Vp/Vs = Np/Ns; use ideal power relation (Supplement).; Explain high-voltage transmission through lower current and reduced I²R cable loss (Supplement calculation).
[Safety]
Use low-voltage teacher demonstrations only; no mains electricity is used in class.
[Quiz answers] 1. kinetic — Motor effect creates motion. 2. changing flux — Flux linkage must change. 3. greater than Np — Vs/Vp = Ns/Np. 4. quarter — Loss depends on current squared.