## Slide 1
08 · Solid Deformation
Slopes and areas of the curve
Deformation Calculus
Differentiate a force–extension curve to read stiffness, and integrate it to find stored energy — in springs, stressed material, and a rod hanging under its own weight.
POSITION
Lesson 7 of 7 in Solid Deformation
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-14/deformation-calculus/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 33
Notes: [Lesson] Solid Deformation — Deformation Calculus. Lesson 7 of 7.
[Intro] Differentiate a force–extension curve to read stiffness, and integrate it to find stored energy — in springs, stressed material, and a rod hanging under its own weight.
[Source] https://giophysics.com/chapter-14/deformation-calculus/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
THINK FIRST
A bungee cord stiffens the further it stretches. Can you still find its stored energy from ½kx²?
Take answers before you click — the point is the commitment
Its force–extension graph is a curve that gets steeper all the way to the end.
THE ANSWER
No. ½kx² is nothing more than the area of the triangle under a straight line F = kx; the moment the graph bends, the shape underneath it is not a triangle and the formula has no claim on it. What survives is the idea behind it — the energy is the area, ∫F dx — and that has to be integrated for the curve you actually have.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A bungee cord stiffens the further it stretches. Can you still find its stored energy from ½kx²? Its force–extension graph is a curve that gets steeper all the way to the end.
[Answer] No. ½kx² is nothing more than the area of the triangle under a straight line F = kx; the moment the graph bends, the shape underneath it is not a triangle and the formula has no claim on it. What survives is the idea behind it — the energy is the area, ∫F dx — and that has to be integrated for the curve you actually have.

## Slide 3
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Deformation calculus treats stiffness as the derivative dF/dx of a force–extension curve and stored elastic energy as the integral ∫F dx beneath it.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Deformation calculus treats stiffness as the derivative dF/dx of a force–extension curve and stored elastic energy as the integral ∫F dx beneath it.

## Slide 4
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
For F = kx + bx³ the tangent stiffness k + 3bx² rises as the spring stretches, and the stored energy ½kx² + ¼bx⁴ is the exact area under the curve.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] For F = kx + bx³ the tangent stiffness k + 3bx² rises as the spring stretches, and the stored energy ½kx² + ¼bx⁴ is the exact area under the curve.

## Slide 5
THE BIG IDEA
Slopes and areas of the curve
Introduce the idea — The big idea and the definition
Stored elastic energy is the integral ∫F dx for any elastic force curve, not only the Hookean triangle. The local gradient dF/dx is the effective stiffness at that extension, so a hardening spring F = kx + bx³ grows stiffer as it stretches. Per unit volume the same idea reads u = ∫σ dε, and when tension varies along a sample — a rod loaded by its own weight — the total extension comes from integrating the strain slice by slice.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] Stored elastic energy is the integral ∫F dx for any elastic force curve, not only the Hookean triangle. The local gradient dF/dx is the effective stiffness at that extension, so a hardening spring F = kx + bx³ grows stiffer as it stretches. Per unit volume the same idea reads u = ∫σ dε, and when tension varies along a sample — a rod loaded by its own weight — the total extension comes from integrating the strain slice by slice.

## Slide 6
THE PHYSICS · 1 OF 3
Slope is stiffness
Build the model — The formulae, one at a time, in plain English
At any point on a force–extension curve the gradient dF/dx is the effective stiffness. Only a Hookean spring has the same slope everywhere.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] At any point on a force–extension curve the gradient dF/dx is the effective stiffness. Only a Hookean spring has the same slope everywhere.

## Slide 7
THE PHYSICS · 2 OF 3
Area is energy
Build the model — The formulae, one at a time, in plain English
½kx² is just the triangle area under F = kx. Once the curve bends, integrate F(x) instead of forcing the triangle formula onto it.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] ½kx² is just the triangle area under F = kx. Once the curve bends, integrate F(x) instead of forcing the triangle formula onto it.

## Slide 8
THE PHYSICS · 3 OF 3
Integrate along the sample
Build the model — The formulae, one at a time, in plain English
When tension varies with position, treat each slice dz separately: find its local strain, then integrate the strains to get the total extension.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] When tension varies with position, treat each slice dz separately: find its local strain, then integrate the strains to get the total extension.

## Slide 9
FORMULA 1 OF 5
Stored energy
Build the model — The formulae, one at a time, in plain English
U = ∫₀ˣ F dx′
Exact for any elastic force curve
IN PLAIN ENGLISH
Add up force times each tiny slice of stretch — the area under the force–extension curve is the energy stored.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Stored energy: U = ∫₀ˣ F dx′
[In plain English] Add up force times each tiny slice of stretch — the area under the force–extension curve is the energy stored.
[Note] Exact for any elastic force curve

## Slide 10
FORMULA 2 OF 5
Cubic spring
Build the model — The formulae, one at a time, in plain English
U = ½kx² + ¼bx⁴
From integrating F = kx + bx³
IN PLAIN ENGLISH
Integrating a hardening spring term by term: the familiar ½kx² plus a quarter-of-bx⁴ correction from the cubic part.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Cubic spring: U = ½kx² + ¼bx⁴
[In plain English] Integrating a hardening spring term by term: the familiar ½kx² plus a quarter-of-bx⁴ correction from the cubic part.
[Note] From integrating F = kx + bx³

## Slide 11
FORMULA 3 OF 5
Tangent stiffness
Build the model — The formulae, one at a time, in plain English
dF/dx = k + 3bx²
Gradient of the F–x curve at extension x
IN PLAIN ENGLISH
The local slope of the force–extension curve is the stiffness right now — a hardening spring gets steeper the further you stretch it.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Tangent stiffness: dF/dx = k + 3bx²
[In plain English] The local slope of the force–extension curve is the stiffness right now — a hardening spring gets steeper the further you stretch it.
[Note] Gradient of the F–x curve at extension x

## Slide 12
FORMULA 4 OF 5
Strain-energy density
Build the model — The formulae, one at a time, in plain English
u = ∫σ dε = ½σε
½σε only in the linear region
IN PLAIN ENGLISH
Energy stored per cubic metre of material — the area under the stress–strain curve, a triangle while the graph is straight.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Strain-energy density: u = ∫σ dε = ½σε
[In plain English] Energy stored per cubic metre of material — the area under the stress–strain curve, a triangle while the graph is straight.
[Note] ½σε only in the linear region

## Slide 13
FORMULA 5 OF 5
Rod under own weight
Build the model — The formulae, one at a time, in plain English
x = ρgL²/(2E)
Uniform rod hanging from its top end
IN PLAIN ENGLISH
Each slice stretches differently because it carries only the weight below it; integrating the varying strain gives half the answer you would get by hanging the whole weight on the end.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Rod under own weight: x = ρgL²/(2E)
[In plain English] Each slice stretches differently because it carries only the weight below it; integrating the varying strain gives half the answer you would get by hanging the whole weight on the end.
[Note] Uniform rod hanging from its top end

## Slide 14
THE PICTURE
A spring that stiffens as it stretches
Drawn for this lesson
Force–extension axes running to 0.10 m and 15 N, carrying the curve F = kx + bx³, which starts shallow and steepens all the way. A dashed straight chord runs from the origin to the curve's end point, and dashed lines drop from that point to both axes.
The live version of this figure — click here
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] Force–extension axes running to 0.10 m and 15 N, carrying the curve F = kx + bx³, which starts shallow and steepens all the way. A dashed straight chord runs from the origin to the curve's end point, and dashed lines drop from that point to both axes.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
U = ½kx² is not a universal energy law — it is the result of integrating F = kx. For a hardening spring F = kx + bx³ the exact energy is ½kx² + ¼bx⁴, and the triangle estimate ½Fx overstates it because the curve lies below its straight chord.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] U = ½kx² is not a universal energy law — it is the result of integrating F = kx. For a hardening spring F = kx + bx³ the exact energy is ½kx² + ¼bx⁴, and the triangle estimate ½Fx overstates it because the curve lies below its straight chord.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A Hookean spring has k = 200 N/m. Use U = ∫₀ˣ F dx′ to find the energy stored at x = 0.30 m.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A Hookean spring has k = 200 N/m. Use U = ∫₀ˣ F dx′ to find the energy stored at x = 0.30 m.
[Answer] U = 9.0 J

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A Hookean spring has k = 200 N/m. Use U = ∫₀ˣ F dx′ to find the energy stored at x = 0.30 m.
1.
U = ∫₀ˣ kx′ dx′ = ½kx².
2.
U = ½ × 200 × 0.30² = ½ × 200 × 0.090.
3.
U = 9.0 J.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] U = ∫₀ˣ kx′ dx′ = ½kx².
[Step 2] U = ½ × 200 × 0.30² = ½ × 200 × 0.090.
[Step 3] U = 9.0 J.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
U = 9.0 J
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] U = 9.0 J

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A hardening spring follows F = 50x + 8000x³ (F in newtons, x in metres). Find the stored energy and the tangent stiffness at x = 0.10 m.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A hardening spring follows F = 50x + 8000x³ (F in newtons, x in metres). Find the stored energy and the tangent stiffness at x = 0.10 m.
[Answer] U = 0.45 J; dF/dx = 290 N m⁻¹

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A hardening spring follows F = 50x + 8000x³ (F in newtons, x in metres). Find the stored energy and the tangent stiffness at x = 0.10 m.
1.
U = ½kx² + ¼bx⁴ = ½(50)(0.10)² + ¼(8000)(0.10)⁴.
2.
U = 0.25 + 0.20 = 0.45 J.
3.
Stiffness: dF/dx = 50 + 3(8000)(0.10)² = 50 + 240 = 290 N m⁻¹.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] U = ½kx² + ¼bx⁴ = ½(50)(0.10)² + ¼(8000)(0.10)⁴.
[Step 2] U = 0.25 + 0.20 = 0.45 J.
[Step 3] Stiffness: dF/dx = 50 + 3(8000)(0.10)² = 50 + 240 = 290 N m⁻¹.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
U = 0.45 J; dF/dx = 290 N m⁻¹
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] U = 0.45 J; dF/dx = 290 N m⁻¹

## Slide 22
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
The spring obeys F = 50x + 8000x³, so U = ∫₀ˣ (50x′ + 8000x′³) dx′.
2.
Integrating term by term: U = ½(50)x² + ⅓(8000)x⁴.
3.
At x = 0.10 m: U = 0.25 + ⅓(8000)(1.0 × 10⁻⁴) = 0.25 + 0.267.
4.
U = 0.52 J.
LINE 2 IS WRONG
The cubic term was integrated as though it were a square: ∫x³ dx is x⁴/4, not x⁴/3. Raising the power by one is the half of the rule everyone remembers; dividing by the NEW power is the half that slips.
IT SHOULD SAY
Integrating term by term: U = ½(50)x² + ¼(8000)x⁴.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 2 is wrong] The cubic term was integrated as though it were a square: ∫x³ dx is x⁴/4, not x⁴/3. Raising the power by one is the half of the rule everyone remembers; dividing by the NEW power is the half that slips.
[It should say] Integrating term by term: U = ½(50)x² + ¼(8000)x⁴.

## Slide 23
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The rod hangs and stretches under nothing but its own weight. How far does it extend altogether?
A MgL/(EA) — the same as hanging the rod's whole weight on its end
B Half of that
C Not at all: it is only supporting itself
A long uniform rod hanging from a fixed support, with a thin horizontal slice marked part of the way down at a depth z, an arrow at that cut showing the tension in the rod there, and the total length L dimensioned alongside.
The live version of this figure — click here
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The rod hangs and stretches under nothing but its own weight. How far does it extend altogether?
[Options] A MgL/(EA) — the same as hanging the rod's whole weight on its end B Half of that C Not at all: it is only supporting itself
[Figure] A long uniform rod hanging from a fixed support, with a thin horizontal slice marked part of the way down at a depth z, an arrow at that cut showing the tension in the rod there, and the total length L dimensioned alongside.

## Slide 24
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B Half of that
WHY
Look at where the tension arrow is drawn. At the very top the rod carries all of itself; at the bottom it carries nothing; every slice in between carries only what hangs below it. Integrating that varying strain averages out at half, which is why the answer is ρgL²/2E and not the full MgL/(EA).
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — Half of that. Look at where the tension arrow is drawn. At the very top the rod carries all of itself; at the bottom it carries nothing; every slice in between carries only what hangs below it. Integrating that varying strain averages out at half, which is why the answer is ρgL²/2E and not the full MgL/(EA).

## Slide 25
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A hardening spring obeys F = kx + bx³ with b > 0. Compared with the triangle estimate ½Fx, the true stored energy ∫F dx is…
A
Smaller, because the curve lies below the straight chord to the endpoint
B
Larger, because the curve is steeper at the endpoint
C
Identical — ½Fx applies to every elastic curve
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A hardening spring obeys F = kx + bx³ with b > 0. Compared with the triangle estimate ½Fx, the true stored energy ∫F dx is…
[Options] A Smaller, because the curve lies below the straight chord to the endpoint B Larger, because the curve is steeper at the endpoint C Identical — ½Fx applies to every elastic curve

## Slide 26
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
A Smaller, because the curve lies below the straight chord to the endpoint
HOW TO GET THERE
The exact integral is ½kx² + ¼bx⁴, while ½Fx = ½kx² + ½bx⁴. The convex hardening curve stays below its chord, so the triangle overestimates the area.
WHY THE OTHERS TEMPT
A Right. The exact integral is ½kx² + ¼bx⁴ while ½Fx works out as ½kx² + ½bx⁴. The hardening curve is convex, so it lies under its own chord and encloses the smaller area.
B It is steeper at the end point — that is what hardening means — but the energy is the whole area from zero, and over most of that range the curve sits below the straight chord rather than above it.
C ½Fx is the area of a triangle, and a triangle is only the right shape when the graph is straight. Every curved F–x graph has to be integrated.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A hardening spring obeys F = kx + bx³ with b > 0. Compared with the triangle estimate ½Fx, the true stored energy ∫F dx is…
[Option by option] A: Right. The exact integral is ½kx² + ¼bx⁴ while ½Fx works out as ½kx² + ½bx⁴. The hardening curve is convex, so it lies under its own chord and encloses the smaller area. B: It is steeper at the end point — that is what hardening means — but the energy is the whole area from zero, and over most of that range the curve sits below the straight chord rather than above it. C: ½Fx is the area of a triangle, and a triangle is only the right shape when the graph is straight. Every curved F–x graph has to be integrated.
[Answer] A — Smaller, because the curve lies below the straight chord to the endpoint
[Why] The exact integral is ½kx² + ¼bx⁴, while ½Fx = ½kx² + ½bx⁴. The convex hardening curve stays below its chord, so the triangle overestimates the area.
[Reveal] One click for the answer, then one for the reason.

## Slide 27
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A steel wire (E = 200 GPa) is stressed to 250 MPa within its linear region. Find the strain, the strain-energy density, and the energy stored in 2.0 × 10⁻⁶ m³ of wire.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A steel wire (E = 200 GPa) is stressed to 250 MPa within its linear region. Find the strain, the strain-energy density, and the energy stored in 2.0 × 10⁻⁶ m³ of wire.
[Answer] ε = 1.25 × 10⁻³; u ≈ 1.6 × 10⁵ J m⁻³; ≈ 0.31 J stored

## Slide 28
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A steel wire (E = 200 GPa) is stressed to 250 MPa within its linear region. Find the strain, the strain-energy density, and the energy stored in 2.0 × 10⁻⁶ m³ of wire.
1.
ε = σ/E = (250 × 10⁶)/(200 × 10⁹) = 1.25 × 10⁻³.
2.
u = ½σε = ½ × 250 × 10⁶ × 1.25 × 10⁻³ ≈ 1.56 × 10⁵ J m⁻³.
3.
Energy = uV = 1.56 × 10⁵ × 2.0 × 10⁻⁶ ≈ 0.31 J.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] ε = σ/E = (250 × 10⁶)/(200 × 10⁹) = 1.25 × 10⁻³.
[Step 2] u = ½σε = ½ × 250 × 10⁶ × 1.25 × 10⁻³ ≈ 1.56 × 10⁵ J m⁻³.
[Step 3] Energy = uV = 1.56 × 10⁵ × 2.0 × 10⁻⁶ ≈ 0.31 J.

## Slide 29
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
ε = 1.25 × 10⁻³; u ≈ 1.6 × 10⁵ J m⁻³; ≈ 0.31 J stored
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ε = 1.25 × 10⁻³; u ≈ 1.6 × 10⁵ J m⁻³; ≈ 0.31 J stored

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A uniform steel rod (ρ = 7850 kg/m³, E = 200 GPa) of length 120 m hangs from its top end. Show that its self-weight extension is x = ρgL²/(2E) and evaluate it with g = 9.81 m/s².
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A uniform steel rod (ρ = 7850 kg/m³, E = 200 GPa) of length 120 m hangs from its top end. Show that its self-weight extension is x = ρgL²/(2E) and evaluate it with g = 9.81 m/s².
[Answer] x = ρgL²/(2E) ≈ 2.8 mm — half the naive MgL/(EA) value

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A uniform steel rod (ρ = 7850 kg/m³, E = 200 GPa) of length 120 m hangs from its top end. Show that its self-weight extension is x = ρgL²/(2E) and evaluate it with g = 9.81 m/s².
1.
Tension a distance z below the support carries only the rod beneath it: T(z) = ρgA(L − z).
2.
Local strain = T/(EA) = ρg(L − z)/E, so x = ∫₀ᴸ ρg(L − z)/E dz = ρgL²/(2E).
3.
x = (7850 × 9.81 × 120²)/(2 × 200 × 10⁹) ≈ 2.8 × 10⁻³ m.
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Tension a distance z below the support carries only the rod beneath it: T(z) = ρgA(L − z).
[Step 2] Local strain = T/(EA) = ρg(L − z)/E, so x = ∫₀ᴸ ρg(L − z)/E dz = ρgL²/(2E).
[Step 3] x = (7850 × 9.81 × 120²)/(2 × 200 × 10⁹) ≈ 2.8 × 10⁻³ m.

## Slide 32
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
x = ρgL²/(2E) ≈ 2.8 mm — half the naive MgL/(EA) value
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] x = ρgL²/(2E) ≈ 2.8 mm — half the naive MgL/(EA) value

## Slide 33
SOLID DEFORMATION
Where to go next
Plenary — What to take away, what to practise next
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-14/deformation-calculus/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-14/presentation/?lesson=calculus
Chapter
All Solid Deformation lessons
https://giophysics.com/chapter-14/
PDF
Download the lesson PDF
https://giophysics.com/downloads/14-7-deformation-calculus.pdf
SOLID DEFORMATION · DEFORMATION CALCULUS
GIOPHYSICS LESSON
Solid Deformation — Deformation Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
33 / 33
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-14/presentation/?lesson=calculus moves them.