## Slide 1
08 · Solid Deformation
Turn a design brief into checks
Material Selection & Deformation Modelling
Choose geometry and material together, then test stiffness, stress, deformation, and the limits of the model.
POSITION
Lesson 6 of 7 in Solid Deformation
PLAN
16 slides in the 45-minute core run, about 44 minutes of it
LESSON PAGE
https://giophysics.com/chapter-14/material-selection-deformation-modelling/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 31
Notes: [Lesson] Solid Deformation — Material Selection & Deformation Modelling. Lesson 6 of 7.
[Intro] Choose geometry and material together, then test stiffness, stress, deformation, and the limits of the model.
[Source] https://giophysics.com/chapter-14/material-selection-deformation-modelling/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
THINK FIRST
Diamond is the stiffest material we know of. Why is nothing structural made from it?
Take answers before you click — the point is the commitment
Every table of Young modulus puts diamond about five times above steel.
THE ANSWER
Because stiffness is only one of the requirements. Diamond is brittle: it takes almost no plastic strain, absorbs almost no energy and gives no warning whatever before it goes. A structure wants a material that visibly deforms first — and that is before anyone raises the cost or how you would machine it.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 31
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Diamond is the stiffest material we know of. Why is nothing structural made from it? Every table of Young modulus puts diamond about five times above steel.
[Answer] Because stiffness is only one of the requirements. Diamond is brittle: it takes almost no plastic strain, absorbs almost no energy and gives no warning whatever before it goes. A structure wants a material that visibly deforms first — and that is before anyone raises the cost or how you would machine it.

## Slide 3
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Material selection is choosing a material and shape whose stiffness, strength, toughness, mass, and working conditions fit a design safely.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Material selection is choosing a material and shape whose stiffness, strength, toughness, mass, and working conditions fit a design safely.

## Slide 4
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A bridge cable needs high tensile strength, limited extension, and ductile warning before failure, so both material and cable diameter matter.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A bridge cable needs high tensile strength, limited extension, and ductile warning before failure, so both material and cable diameter matter.

## Slide 5
THE BIG IDEA
Turn a design brief into checks
Introduce the idea — The big idea and the definition
A safe design is not selected from Young modulus alone. Use E to predict elastic extension, an independently specified allowable stress to check loading, and the required behaviour—ductile warning, brittle rigidity, or recoverable polymer deformation—to choose a material. Then state where the linear model stops being trustworthy.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A safe design is not selected from Young modulus alone. Use E to predict elastic extension, an independently specified allowable stress to check loading, and the required behaviour—ductile warning, brittle rigidity, or recoverable polymer deformation—to choose a material. Then state where the linear model stops being trustworthy.

## Slide 6
THE PHYSICS · 1 OF 3
Start from requirements
Build the model — The formulae, one at a time, in plain English
A bridge tie, phone screen, spring, and seal need different combinations of stiffness, strength, toughness, and recoverability.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A bridge tie, phone screen, spring, and seal need different combinations of stiffness, strength, toughness, and recoverability.

## Slide 7
THE PHYSICS · 2 OF 3
Change geometry
Build the model — The formulae, one at a time, in plain English
Increasing diameter strongly reduces stress and extension because area varies with d².
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Increasing diameter strongly reduces stress and extension because area varies with d².

## Slide 8
THE PHYSICS · 3 OF 3
Audit assumptions
Build the model — The formulae, one at a time, in plain English
The simple model assumes axial loading, uniform area, small strain, constant E, and no stress concentration.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The simple model assumes axial loading, uniform area, small strain, constant E, and no stress concentration.

## Slide 9
FORMULA 1 OF 3
Circular area
Build the model — The formulae, one at a time, in plain English
A = πd²/4
Convert diameter to metres
IN PLAIN ENGLISH
The cross-section of a round wire from its diameter — needed before any stress calculation.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Circular area: A = πd²/4
[In plain English] The cross-section of a round wire from its diameter — needed before any stress calculation.
[Note] Convert diameter to metres

## Slide 10
FORMULA 2 OF 3
Elastic extension
Build the model — The formulae, one at a time, in plain English
x = FL/(EA)
Linear, uniform, axial model
IN PLAIN ENGLISH
How much a wire stretches: more force or length stretches it more; a stiffer material or fatter wire stretches less.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Elastic extension: x = FL/(EA)
[In plain English] How much a wire stretches: more force or length stretches it more; a stiffer material or fatter wire stretches less.
[Note] Linear, uniform, axial model

## Slide 11
FORMULA 3 OF 3
Allowable-force check
Build the model — The formulae, one at a time, in plain English
F ≤ σₐₗₗₒw A
Use a design value supplied for the task
IN PLAIN ENGLISH
A design rule: keep the force below the material's safe stress times the cross-section, with room to spare.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Allowable-force check: F ≤ σₐₗₗₒw A
[In plain English] A design rule: keep the force below the material's safe stress times the cross-section, with room to spare.
[Note] Use a design value supplied for the task

## Slide 12
THE PICTURE
A tie, and the circle that carries it
Drawn for this lesson
A steel tie rod 1.5 m long hanging from a fixed support with a 1.0 kN load on its lower end and its 4.0 mm diameter marked by a leader line. Its circular cross-section is drawn separately at a much larger scale with the diameter dimensioned across it.
The live version of this figure — click here
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A steel tie rod 1.5 m long hanging from a fixed support with a 1.0 kN load on its lower end and its 4.0 mm diameter marked by a leader line. Its circular cross-section is drawn separately at a much larger scale with the diameter dimensioned across it.

## Slide 13
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A material with the largest Young modulus is not automatically the best or safest. Strength, toughness, density, environment, cost, and geometry may control the choice.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A material with the largest Young modulus is not automatically the best or safest. Strength, toughness, density, environment, cost, and geometry may control the choice.

## Slide 14
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A design requires stress below 80 MPa. What minimum cross-section must a rod have to carry 16 kN?
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A design requires stress below 80 MPa. What minimum cross-section must a rod have to carry 16 kN?
[Answer] A ≥ 200 mm²

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A design requires stress below 80 MPa. What minimum cross-section must a rod have to carry 16 kN?
1.
A = F/σ = 16 000 ÷ 80 × 10⁶.
2.
A = 2.0 × 10⁻⁴ m² = 200 mm².
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] A = F/σ = 16 000 ÷ 80 × 10⁶.
[Step 2] A = 2.0 × 10⁻⁴ m² = 200 mm².

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
A ≥ 200 mm²
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] A ≥ 200 mm²

## Slide 17
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A 1.5 m steel tie has diameter 4.0 mm, E = 210 GPa, and carries 1.0 kN. Find stress and elastic extension.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 1.5 m steel tie has diameter 4.0 mm, E = 210 GPa, and carries 1.0 kN. Find stress and elastic extension.
[Answer] σ = 79.6 MPa and x = 0.568 mm

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A 1.5 m steel tie has diameter 4.0 mm, E = 210 GPa, and carries 1.0 kN. Find stress and elastic extension.
1.
A = π(0.0040)²/4 = 1.257 × 10⁻⁵ m².
2.
σ = 1000/A = 7.96 × 10⁷ Pa = 79.6 MPa.
3.
x = FL/(EA) = (1000)(1.5)/[(210 × 10⁹)A].
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] A = π(0.0040)²/4 = 1.257 × 10⁻⁵ m².
[Step 2] σ = 1000/A = 7.96 × 10⁷ Pa = 79.6 MPa.
[Step 3] x = FL/(EA) = (1000)(1.5)/[(210 × 10⁹)A].

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
σ = 79.6 MPa and x = 0.568 mm
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] σ = 79.6 MPa and x = 0.568 mm

## Slide 20
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
Area: A = πd²/4 = π(4.0 × 10⁻³)² ÷ 4 = 1.257 × 10⁻⁵ m².
2.
Stress: σ = F/A = 1000 ÷ (1.257 × 10⁻⁵) = 79.6 MPa.
3.
Extension: x = FL/(EA) = (1000 × 1.5) ÷ (210 × 1.257 × 10⁻⁵).
4.
x = 5.7 × 10⁵ m.
LINE 3 IS WRONG
E was copied off the data sheet as 210 and never turned into 210 × 10⁹ Pa. The giveaway is the answer — a 1.5 m steel tie stretching several hundred kilometres — but by the time a page of working ends in a number, nobody is asking whether it is physically possible.
IT SHOULD SAY
x = FL/(EA) = (1000 × 1.5) ÷ (210 × 10⁹ × 1.257 × 10⁻⁵) = 5.68 × 10⁻⁴ m.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] E was copied off the data sheet as 210 and never turned into 210 × 10⁹ Pa. The giveaway is the answer — a 1.5 m steel tie stretching several hundred kilometres — but by the time a page of working ends in a number, nobody is asking whether it is physically possible.
[It should say] x = FL/(EA) = (1000 × 1.5) ÷ (210 × 10⁹ × 1.257 × 10⁻⁵) = 5.68 × 10⁻⁴ m.

## Slide 21
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The rod is swapped for one of the same material and length but twice the diameter, under the same 1.0 kN. What happens to the stress in it?
A It halves — twice the diameter, half the stress
B It falls to a quarter
C It is unchanged: the load has not changed
A steel tie rod 1.5 m long hanging from a fixed support with a 1.0 kN load on its lower end and its 4.0 mm diameter marked by a leader line. Its circular cross-section is drawn separately at a much larger scale with the diameter dimensioned across it.
The live version of this figure — click here
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The rod is swapped for one of the same material and length but twice the diameter, under the same 1.0 kN. What happens to the stress in it?
[Options] A It halves — twice the diameter, half the stress B It falls to a quarter C It is unchanged: the load has not changed
[Figure] A steel tie rod 1.5 m long hanging from a fixed support with a 1.0 kN load on its lower end and its 4.0 mm diameter marked by a leader line. Its circular cross-section is drawn separately at a much larger scale with the diameter dimensioned across it.

## Slide 22
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B It falls to a quarter
WHY
The load is carried by the circle drawn beside the rod, and that circle's area is πd²/4. Doubling d multiplies the area by four, so σ = F/A drops to a quarter. It is the d² that catches people: geometry rewards thickness far more generously than intuition expects.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — It falls to a quarter. The load is carried by the circle drawn beside the rod, and that circle's area is πd²/4. Doubling d multiplies the area by four, so σ = F/A drops to a quarter. It is the d² that catches people: geometry rewards thickness far more generously than intuition expects.

## Slide 23
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Which change most directly reduces both stress and elastic extension in the same wire under the same load?
A
Increase its diameter
B
Increase its length
C
Choose a lower Young modulus
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Which change most directly reduces both stress and elastic extension in the same wire under the same load?
[Options] A Increase its diameter B Increase its length C Choose a lower Young modulus

## Slide 24
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
A Increase its diameter
HOW TO GET THERE
A larger diameter increases area, reducing σ = F/A and x = FL/(EA).
WHY THE OTHERS TEMPT
A Right. A larger diameter means a larger area, and the area sits underneath in both σ = F/A and x = FL₀/(EA).
B A longer wire has exactly the same cross-section, so exactly the same stress — and x = FL₀/(EA) is proportional to L₀, so it stretches more, not less.
C A lower E makes the material less stiff: the same stress now produces more strain. It is the one change that leaves the stress untouched while making the extension worse.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Which change most directly reduces both stress and elastic extension in the same wire under the same load?
[Option by option] A: Right. A larger diameter means a larger area, and the area sits underneath in both σ = F/A and x = FL₀/(EA). B: A longer wire has exactly the same cross-section, so exactly the same stress — and x = FL₀/(EA) is proportional to L₀, so it stretches more, not less. C: A lower E makes the material less stiff: the same stress now produces more strain. It is the one change that leaves the stress untouched while making the extension worse.
[Answer] A — Increase its diameter
[Why] A larger diameter increases area, reducing σ = F/A and x = FL/(EA).
[Reveal] One click for the answer, then one for the reason.

## Slide 25
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
An aluminium strut (E = 70 GPa) 2.5 m long with A = 5.0 cm² must not compress more than 1.0 mm. Find the maximum allowable load.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] An aluminium strut (E = 70 GPa) 2.5 m long with A = 5.0 cm² must not compress more than 1.0 mm. Find the maximum allowable load.
[Answer] F(max) = 14 kN

## Slide 26
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
An aluminium strut (E = 70 GPa) 2.5 m long with A = 5.0 cm² must not compress more than 1.0 mm. Find the maximum allowable load.
1.
F = EAx/L = 70 × 10⁹ × 5.0 × 10⁻⁴ × 1.0 × 10⁻³ ÷ 2.5.
2.
F = 70 × 10⁹ × 2.0 × 10⁻⁷.
3.
F = 14 kN.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] F = EAx/L = 70 × 10⁹ × 5.0 × 10⁻⁴ × 1.0 × 10⁻³ ÷ 2.5.
[Step 2] F = 70 × 10⁹ × 2.0 × 10⁻⁷.
[Step 3] F = 14 kN.

## Slide 27
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
F(max) = 14 kN
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] F(max) = 14 kN

## Slide 28
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A climbing rope must arrest an 80 kg fall generating a peak 8 kN with stress ≤ 200 MPa and store 3 kJ elastically. Specify the minimum cross-section and check whether a 60 m rope of that section with E = 2.0 GPa meets the energy budget.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A climbing rope must arrest an 80 kg fall generating a peak 8 kN with stress ≤ 200 MPa and store 3 kJ elastically. Specify the minimum cross-section and check whether a 60 m rope of that section with E = 2.0 GPa meets the energy budget.
[Answer] A ≥ 40 mm²; the 60 m rope stores ~24 kJ — comfortably enough

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A climbing rope must arrest an 80 kg fall generating a peak 8 kN with stress ≤ 200 MPa and store 3 kJ elastically. Specify the minimum cross-section and check whether a 60 m rope of that section with E = 2.0 GPa meets the energy budget.
1.
Stress limit: A ≥ F/σ = 8000 ÷ 2.0 × 10⁸ = 4.0 × 10⁻⁵ m² (40 mm² — about 7 mm diameter).
2.
At 8 kN: strain = σ/E = 0.10, extension = 6.0 m; energy = ½Fx = ½ × 8000 × 6.0 = 24 kJ ≥ 3 kJ ✓.
3.
The rope's low modulus is a feature: big stretch spreads the impulse and absorbs the fall energy.
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Stress limit: A ≥ F/σ = 8000 ÷ 2.0 × 10⁸ = 4.0 × 10⁻⁵ m² (40 mm² — about 7 mm diameter).
[Step 2] At 8 kN: strain = σ/E = 0.10, extension = 6.0 m; energy = ½Fx = ½ × 8000 × 6.0 = 24 kJ ≥ 3 kJ ✓.
[Step 3] The rope's low modulus is a feature: big stretch spreads the impulse and absorbs the fall energy.

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
A ≥ 40 mm²; the 60 m rope stores ~24 kJ — comfortably enough
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] A ≥ 40 mm²; the 60 m rope stores ~24 kJ — comfortably enough

## Slide 31
SOLID DEFORMATION
Where to go next
Plenary — What to take away, what to practise next
Next
8.7 Deformation Calculus
https://giophysics.com/chapter-14/deformation-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-14/material-selection-deformation-modelling/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-14/presentation/?lesson=selection
Chapter
All Solid Deformation lessons
https://giophysics.com/chapter-14/
PDF
Download the lesson PDF
https://giophysics.com/downloads/14-6-material-selection-deformation-modelling.pdf
SOLID DEFORMATION · MATERIAL SELECTION & DEFORMATION MODELLING
GIOPHYSICS LESSON
Solid Deformation — Material Selection & Deformation Modelling. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 31
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-14/presentation/?lesson=selection moves them.