## Slide 1
09 · Statics
Translate constraints into forces
Beams, Supports & Reactions
Support reactions are not guessed values: their possible directions come from the motion each support prevents.
POSITION
Lesson 5 of 7 in Statics
PLAN
16 slides in the 45-minute core run, about 44 minutes of it
LESSON PAGE
https://giophysics.com/chapter-15/beams-supports-reactions/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 31
Notes: [Lesson] Statics — Beams, Supports & Reactions. Lesson 5 of 7.
[Intro] Support reactions are not guessed values: their possible directions come from the motion each support prevents.
[Source] https://giophysics.com/chapter-15/beams-supports-reactions/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
THINK FIRST
Two people carry a long plank, one at each end, with a heavy toolbox a quarter of the way from the front. Do they share it equally?
Take answers before you click — the point is the commitment
The plank itself is light enough to ignore. The toolbox is not.
THE ANSWER
No — the one nearest the box takes three quarters of it. Take moments about the far carrier and each person's share turns out to be fixed by how far the box sits from the OTHER one. Slide it right over one person's shoulder and the other feels nothing at all.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 31
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Two people carry a long plank, one at each end, with a heavy toolbox a quarter of the way from the front. Do they share it equally? The plank itself is light enough to ignore. The toolbox is not.
[Answer] No — the one nearest the box takes three quarters of it. Take moments about the far carrier and each person's share turns out to be fixed by how far the box sits from the OTHER one. Slide it right over one person's shoulder and the other feels nothing at all.

## Slide 3
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A support reaction is the force or moment a support exerts because it prevents particular motions of a structure.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A support reaction is the force or moment a support exerts because it prevents particular motions of a structure.

## Slide 4
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A pin at one end of a beam can provide horizontal and vertical reactions, while a roller at the other end provides one normal reaction.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A pin at one end of a beam can provide horizontal and vertical reactions, while a roller at the other end provides one normal reaction.

## Slide 5
THE BIG IDEA
Translate constraints into forces
Introduce the idea — The big idea and the definition
In a planar idealisation, a roller supplies one reaction normal to its surface, a pin supplies two force components, and a fixed support can also supply a reaction moment. Choose moments to solve the reactions with the fewest simultaneous equations.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] In a planar idealisation, a roller supplies one reaction normal to its surface, a pin supplies two force components, and a fixed support can also supply a reaction moment. Choose moments to solve the reactions with the fewest simultaneous equations.

## Slide 6
THE PHYSICS · 1 OF 3
Roller
Build the model — The formulae, one at a time, in plain English
A frictionless roller prevents motion normal to its surface and therefore supplies one reaction in that direction.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A frictionless roller prevents motion normal to its surface and therefore supplies one reaction in that direction.

## Slide 7
THE PHYSICS · 2 OF 3
Pin or hinge
Build the model — The formulae, one at a time, in plain English
A pin prevents horizontal and vertical translation but permits rotation, so it has two force components and no ideal reaction couple.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A pin prevents horizontal and vertical translation but permits rotation, so it has two force components and no ideal reaction couple.

## Slide 8
THE PHYSICS · 3 OF 3
Fixed support
Build the model — The formulae, one at a time, in plain English
A fixed end prevents translation and rotation, so it can supply two force components and a moment in a planar model.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A fixed end prevents translation and rotation, so it can supply two force components and a moment in a planar model.

## Slide 9
FORMULA 1 OF 3
Vertical balance
Build the model — The formulae, one at a time, in plain English
RA + RB = total downward load
For vertical loading
IN PLAIN ENGLISH
The two supports together must hold up everything pressing down on the beam.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Vertical balance: RA + RB = total downward load
[In plain English] The two supports together must hold up everything pressing down on the beam.
[Note] For vertical loading

## Slide 10
FORMULA 2 OF 3
Point load P
Build the model — The formulae, one at a time, in plain English
RB = Pa/L
a measured from A
IN PLAIN ENGLISH
The farther a load sits from a support, the more of it the other support carries — a see-saw rule.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Point load P: RB = Pa/L
[In plain English] The farther a load sits from a support, the more of it the other support carries — a see-saw rule.
[Note] a measured from A

## Slide 11
FORMULA 3 OF 3
Other reaction
Build the model — The formulae, one at a time, in plain English
RA = P(L − a)/L
Both are upward for 0 < a < L
IN PLAIN ENGLISH
The nearer support carries the rest; the two shares always total the full load.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Other reaction: RA = P(L − a)/L
[In plain English] The nearer support carries the rest; the two shares always total the full load.
[Note] Both are upward for 0 < a < L

## Slide 12
THE PICTURE
Three supports, three constraints
Drawn for this lesson
The three ideal planar supports drawn side by side under short lengths of beam: a roller as a wheel between the beam and hatched ground, a pin as a triangle with an axle at its apex, and a fixed end with the beam running into a hatched wall. No reaction arrows are drawn on any of the three.
The live version of this figure — click here
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] The three ideal planar supports drawn side by side under short lengths of beam: a roller as a wheel between the beam and hatched ground, a pin as a triangle with an axle at its apex, and a fixed end with the beam running into a hatched wall. No reaction arrows are drawn on any of the three.

## Slide 13
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A support symbol does not automatically mean an upward force. The reaction direction follows the constrained motion and the solved sign.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A support symbol does not automatically mean an upward force. The reaction direction follows the constrained motion and the solved sign.

## Slide 14
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A 6.0 m beam on end supports carries a 10 kN load at its centre. Find each reaction.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 6.0 m beam on end supports carries a 10 kN load at its centre. Find each reaction.
[Answer] 5.0 kN each

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A 6.0 m beam on end supports carries a 10 kN load at its centre. Find each reaction.
1.
Symmetry: each support carries half.
2.
RA = RB = 5.0 kN.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Symmetry: each support carries half.
[Step 2] RA = RB = 5.0 kN.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
5.0 kN each
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 5.0 kN each

## Slide 17
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A simply supported 8.0 m beam carries a 20 kN point load 2.0 m from A. Find RA and RB.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A simply supported 8.0 m beam carries a 20 kN point load 2.0 m from A. Find RA and RB.
[Answer] RA = 15 kN upward; RB = 5.0 kN upward

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A simply supported 8.0 m beam carries a 20 kN point load 2.0 m from A. Find RA and RB.
1.
Take moments about A: RB(8.0) − 20(2.0) = 0.
2.
RB = 5.0 kN.
3.
Use vertical balance: RA + RB = 20 kN.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Take moments about A: RB(8.0) − 20(2.0) = 0.
[Step 2] RB = 5.0 kN.
[Step 3] Use vertical balance: RA + RB = 20 kN.

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
RA = 15 kN upward; RB = 5.0 kN upward
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] RA = 15 kN upward; RB = 5.0 kN upward

## Slide 20
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A 10 m beam on supports A and B carries 8.0 kN at 3.0 m from A and 4.0 kN at 8.0 m from A.
2.
Take moments about A, so that RA drops out of the equation.
3.
10RB = 8.0 × 3.0 + 4.0 × 2.0 = 32, giving RB = 3.2 kN.
4.
Vertical balance then gives RA = 12 − RB.
LINE 3 IS WRONG
The second load's distance was measured from B instead of from A. Once a point has been chosen to take moments about, every distance in that equation has to be measured from THAT point — mixing the two ends is the commonest way a correct-looking moment equation goes wrong.
IT SHOULD SAY
10RB = 8.0 × 3.0 + 4.0 × 8.0 = 56, giving RB = 5.6 kN.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The second load's distance was measured from B instead of from A. Once a point has been chosen to take moments about, every distance in that equation has to be measured from THAT point — mixing the two ends is the commonest way a correct-looking moment equation goes wrong.
[It should say] 10RB = 8.0 × 3.0 + 4.0 × 8.0 = 56, giving RB = 5.6 kN.

## Slide 21
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The 20 kN load sits 2.0 m from A on the 8.0 m span. What does each support carry?
A A takes 15 kN and B takes 5.0 kN
B B takes 15 kN and A takes 5.0 kN — the far support does the work
C 10 kN each: they are holding one beam between them
An 8.0 m beam resting on a pin at A and a roller at B, carrying a single 20 kN load 2.0 m from A. Both distances are dimensioned beneath the beam with dashed lines dropped from the load and the supports; no reaction arrows are drawn at either end.
The live version of this figure — click here
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The 20 kN load sits 2.0 m from A on the 8.0 m span. What does each support carry?
[Options] A A takes 15 kN and B takes 5.0 kN B B takes 15 kN and A takes 5.0 kN — the far support does the work C 10 kN each: they are holding one beam between them
[Figure] An 8.0 m beam resting on a pin at A and a roller at B, carrying a single 20 kN load 2.0 m from A. Both distances are dimensioned beneath the beam with dashed lines dropped from the load and the supports; no reaction arrows are drawn at either end.

## Slide 22
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
A A takes 15 kN and B takes 5.0 kN
WHY
Take moments about A: RB × 8.0 = 20 × 2.0, so B carries only 5.0 kN and vertical balance leaves 15 kN for A. The nearer support takes the bigger share, and the split is the see-saw rule — each support's share is set by the distance from the load to the OTHER support.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] A — A takes 15 kN and B takes 5.0 kN. Take moments about A: RB × 8.0 = 20 × 2.0, so B carries only 5.0 kN and vertical balance leaves 15 kN for A. The nearer support takes the bigger share, and the split is the see-saw rule — each support's share is set by the distance from the load to the OTHER support.

## Slide 23
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Which planar ideal support can provide a reaction moment?
A
Roller
B
Pin
C
Fixed support
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Which planar ideal support can provide a reaction moment?
[Options] A Roller B Pin C Fixed support

## Slide 24
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
C Fixed support
HOW TO GET THERE
A fixed support prevents rotation; a pin and roller permit it and therefore do not provide an ideal reaction couple.
WHY THE OTHERS TEMPT
A A roller cannot even stop the beam sliding along its surface, let alone stop it rotating. It supplies one force, normal to that surface.
B A pin stops the beam's end going anywhere, which is two force components — but it turns freely in its hole, so it supplies no couple.
C Right. A built-in end prevents rotation as well as translation, so in a planar model it can supply two force components and a reaction moment.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Which planar ideal support can provide a reaction moment?
[Option by option] A: A roller cannot even stop the beam sliding along its surface, let alone stop it rotating. It supplies one force, normal to that surface. B: A pin stops the beam's end going anywhere, which is two force components — but it turns freely in its hole, so it supplies no couple. C: Right. A built-in end prevents rotation as well as translation, so in a planar model it can supply two force components and a reaction moment.
[Answer] C — Fixed support
[Why] A fixed support prevents rotation; a pin and roller permit it and therefore do not provide an ideal reaction couple.
[Reveal] One click for the answer, then one for the reason.

## Slide 25
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A 10 m beam on supports A and B carries 8.0 kN at 3.0 m from A and 4.0 kN at 8.0 m from A. Find both reactions.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 10 m beam on supports A and B carries 8.0 kN at 3.0 m from A and 4.0 kN at 8.0 m from A. Find both reactions.
[Answer] RA = 6.4 kN, RB = 5.6 kN

## Slide 26
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A 10 m beam on supports A and B carries 8.0 kN at 3.0 m from A and 4.0 kN at 8.0 m from A. Find both reactions.
1.
Moments about A: 10RB = 8.0 × 3.0 + 4.0 × 8.0 = 56 → RB = 5.6 kN.
2.
Vertical balance: RA = 12 − 5.6.
3.
RA = 6.4 kN.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Moments about A: 10RB = 8.0 × 3.0 + 4.0 × 8.0 = 56 → RB = 5.6 kN.
[Step 2] Vertical balance: RA = 12 − 5.6.
[Step 3] RA = 6.4 kN.

## Slide 27
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
RA = 6.4 kN, RB = 5.6 kN
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] RA = 6.4 kN, RB = 5.6 kN

## Slide 28
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A uniform 4.0 kN beam of length 8.0 m rests on supports at 1.0 m and 6.0 m from the left end. A person of 0.80 kN walks toward the right tip. How far past the right support can they go before tipping?
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A uniform 4.0 kN beam of length 8.0 m rests on supports at 1.0 m and 6.0 m from the left end. A person of 0.80 kN walks toward the right tip. How far past the right support can they go before tipping?
[Answer] Tipping would need 10 m of overhang; the tip is only 2.0 m out — safe to the end

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A uniform 4.0 kN beam of length 8.0 m rests on supports at 1.0 m and 6.0 m from the left end. A person of 0.80 kN walks toward the right tip. How far past the right support can they go before tipping?
1.
Tipping is imminent when the left reaction reaches zero — take moments about the right support (at 6.0 m).
2.
Beam weight acts at 4.0 m, i.e. 2.0 m left of that support: restoring moment = 4.0 × 2.0 = 8.0 kN·m.
3.
Person at distance d beyond: 0.80d = 8.0 → d = 10 m — beyond the beam's 2.0 m overhang, so they can safely reach the tip.
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Tipping is imminent when the left reaction reaches zero — take moments about the right support (at 6.0 m).
[Step 2] Beam weight acts at 4.0 m, i.e. 2.0 m left of that support: restoring moment = 4.0 × 2.0 = 8.0 kN·m.
[Step 3] Person at distance d beyond: 0.80d = 8.0 → d = 10 m — beyond the beam's 2.0 m overhang, so they can safely reach the tip.

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
Tipping would need 10 m of overhang; the tip is only 2.0 m out — safe to the end
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Tipping would need 10 m of overhang; the tip is only 2.0 m out — safe to the end

## Slide 31
STATICS
Where to go next
Plenary — What to take away, what to practise next
Next
9.6 Ladders, Hinges & Friction
https://giophysics.com/chapter-15/ladders-hinges-friction/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-15/beams-supports-reactions/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-15/presentation/?lesson=beams
Chapter
All Statics lessons
https://giophysics.com/chapter-15/
PDF
Download the lesson PDF
https://giophysics.com/downloads/15-5-beams-supports-reactions.pdf
STATICS · BEAMS, SUPPORTS & REACTIONS
GIOPHYSICS LESSON
Statics — Beams, Supports & Reactions. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 31
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-15/presentation/?lesson=beams moves them.