## Slide 1
09 · Statics
Turn a load shape into one force
Distributed Loads & Resultants
A continuously distributed load can be replaced by an equivalent resultant whose magnitude is graph area and whose location follows from first moments.
POSITION
Lesson 4 of 7 in Statics
PLAN
16 slides in the 45-minute core run, about 44 minutes of it
LESSON PAGE
https://giophysics.com/chapter-15/distributed-loads-resultants/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 31
Notes: [Lesson] Statics — Distributed Loads & Resultants. Lesson 4 of 7.
[Intro] A continuously distributed load can be replaced by an equivalent resultant whose magnitude is graph area and whose location follows from first moments.
[Source] https://giophysics.com/chapter-15/distributed-loads-resultants/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
THINK FIRST
Snow drifts across a flat roof, deep at one end and nothing at the other. Does its whole weight press down at the middle?
Take answers before you click — the point is the commitment
You want one number and one place to put it, so that the roof beam can be checked.
THE ANSWER
No — it presses at the balance point of the SNOW, not of the roof. Replace a spread-out load with a single force and that force has to act through the centroid of the load shape, which for a wedge of snow is a third of the way in from the deep end. Put it at the middle and every moment calculated afterwards is wrong.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 31
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Snow drifts across a flat roof, deep at one end and nothing at the other. Does its whole weight press down at the middle? You want one number and one place to put it, so that the roof beam can be checked.
[Answer] No — it presses at the balance point of the SNOW, not of the roof. Replace a spread-out load with a single force and that force has to act through the centroid of the load shape, which for a wedge of snow is a third of the way in from the deep end. Put it at the middle and every moment calculated afterwards is wrong.

## Slide 3
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A distributed load is a force spread continuously along a length; its equivalent resultant is the area under the load graph and acts at the graph's centroid.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A distributed load is a force spread continuously along a length; its equivalent resultant is the area under the load graph and acts at the graph's centroid.

## Slide 4
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
Snow spread evenly over a 4 m roof beam is replaced by one total downward force acting at the middle of the loaded length.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] Snow spread evenly over a 4 m roof beam is replaced by one total downward force acting at the middle of the loaded length.

## Slide 5
THE BIG IDEA
Turn a load shape into one force
Introduce the idea — The big idea and the definition
For load intensity w(x), a narrow strip carries dW = w(x)dx. Integrating the strips gives total load. Matching moments fixes the resultant's line of action at the centroid of the load diagram.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] For load intensity w(x), a narrow strip carries dW = w(x)dx. Integrating the strips gives total load. Matching moments fixes the resultant's line of action at the centroid of the load diagram.

## Slide 6
THE PHYSICS · 1 OF 3
Area gives force
Build the model — The formulae, one at a time, in plain English
The area under a load-intensity graph has units of force, not force per length.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The area under a load-intensity graph has units of force, not force per length.

## Slide 7
THE PHYSICS · 2 OF 3
Centroid gives position
Build the model — The formulae, one at a time, in plain English
A uniform load acts at midspan; a triangular load acts one-third of its length from the larger end.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A uniform load acts at midspan; a triangular load acts one-third of its length from the larger end.

## Slide 8
THE PHYSICS · 3 OF 3
Equivalent is contextual
Build the model — The formulae, one at a time, in plain English
The single resultant preserves external force and moment balance, but not the internal stress at every point.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The single resultant preserves external force and moment balance, but not the internal stress at every point.

## Slide 9
FORMULA 1 OF 3
Resultant load
Build the model — The formulae, one at a time, in plain English
W = ∫₀ᴸw(x) dx
(kN/m)·m = kN
IN PLAIN ENGLISH
A spread-out load (like a beam's own weight) adds up to one total force — the area under the loading diagram.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Resultant load: W = ∫₀ᴸw(x) dx
[In plain English] A spread-out load (like a beam's own weight) adds up to one total force — the area under the loading diagram.
[Note] (kN/m)·m = kN

## Slide 10
FORMULA 2 OF 3
Line of action
Build the model — The formulae, one at a time, in plain English
x̄ = [∫₀ᴸxw(x) dx]/W
First moment divided by area
IN PLAIN ENGLISH
That total force acts at the loading diagram's balance point (its centroid).
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Line of action: x̄ = [∫₀ᴸxw(x) dx]/W
[In plain English] That total force acts at the loading diagram's balance point (its centroid).
[Note] First moment divided by area

## Slide 11
FORMULA 3 OF 3
Linear load
Build the model — The formulae, one at a time, in plain English
W = ½(wA + wB)L
Trapezoid area
IN PLAIN ENGLISH
For a load that varies steadily along the beam, the total is the average intensity times the length.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Linear load: W = ½(wA + wB)L
[In plain English] For a load that varies steadily along the beam, the total is the average intensity times the length.
[Note] Trapezoid area

## Slide 12
THE PICTURE
Two load shapes
Drawn for this lesson
Two loading diagrams. The upper beam carries arrows of equal length all along its 4.0 m, topped by a level line marked 3.0 kN/m. The lower beam carries arrows that grow steadily from nothing at end A to their longest at end B, topped by a line sloping from zero up to w₀. Neither beam has a resultant marked on it.
The live version of this figure — click here
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] Two loading diagrams. The upper beam carries arrows of equal length all along its 4.0 m, topped by a level line marked 3.0 kN/m. The lower beam carries arrows that grow steadily from nothing at end A to their longest at end B, topped by a line sloping from zero up to w₀. Neither beam has a resultant marked on it.

## Slide 13
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Do not place every triangular-load resultant at its geometric midpoint. Its line of action is one-third from the high-intensity end.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Do not place every triangular-load resultant at its geometric midpoint. Its line of action is one-third from the high-intensity end.

## Slide 14
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A beam carries a uniform load of 3.0 kN/m along its 4.0 m length. Find the total load and where it effectively acts.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A beam carries a uniform load of 3.0 kN/m along its 4.0 m length. Find the total load and where it effectively acts.
[Answer] 12 kN at midspan

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A beam carries a uniform load of 3.0 kN/m along its 4.0 m length. Find the total load and where it effectively acts.
1.
W = wL = 3.0 × 4.0 = 12 kN.
2.
It acts at the middle: 2.0 m from either end.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] W = wL = 3.0 × 4.0 = 12 kN.
[Step 2] It acts at the middle: 2.0 m from either end.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
12 kN at midspan
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 12 kN at midspan

## Slide 17
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A triangular load rises from 0 to 12 kN/m over 6.0 m. Find its resultant and location from the zero end.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A triangular load rises from 0 to 12 kN/m over 6.0 m. Find its resultant and location from the zero end.
[Answer] W = 36 kN at x̄ = 4.0 m from the zero end

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A triangular load rises from 0 to 12 kN/m over 6.0 m. Find its resultant and location from the zero end.
1.
The load diagram is a triangle: W = ½×6.0×12.
2.
Its centroid is two-thirds of the span from the zero-intensity end.
3.
x̄ = (2/3)×6.0.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] The load diagram is a triangle: W = ½×6.0×12.
[Step 2] Its centroid is two-thirds of the span from the zero-intensity end.
[Step 3] x̄ = (2/3)×6.0.

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
W = 36 kN at x̄ = 4.0 m from the zero end
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] W = 36 kN at x̄ = 4.0 m from the zero end

## Slide 20
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
w(x) = 2 + 0.6x kN/m over 5.0 m, so W = ∫₀⁵ (2 + 0.6x) dx = [2x + 0.3x²]₀⁵ = 17.5 kN.
2.
First moment about the left end: ∫₀⁵ x(2 + 0.6x) dx = [x² + 0.2x³]₀⁵ = 50.
3.
So the resultant acts at x̄ = 50 m from the left end.
4.
The whole distributed load can now be replaced by W acting at x̄.
LINE 3 IS WRONG
The first moment was worked out correctly and then read as if it were a position. It is 50 kN·m, not 50 m; a position only appears once you divide it by the total load. The units catch it immediately — and so does the beam, which is 5.0 m long.
IT SHOULD SAY
x̄ = (first moment) ÷ (total load) = 50 ÷ 17.5 = 2.86 m from the left end.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The first moment was worked out correctly and then read as if it were a position. It is 50 kN·m, not 50 m; a position only appears once you divide it by the total load. The units catch it immediately — and so does the beam, which is 5.0 m long.
[It should say] x̄ = (first moment) ÷ (total load) = 50 ÷ 17.5 = 2.86 m from the left end.

## Slide 21
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The lower beam's load reaches 12 kN/m at B over a span of 6.0 m. What is the total load on it?
A 72 kN — the biggest intensity times the length
B 36 kN
C 12 kN — the intensity is already a load
Two loading diagrams. The upper beam carries arrows of equal length all along its 4.0 m, topped by a level line marked 3.0 kN/m. The lower beam carries arrows that grow steadily from nothing at end A to their longest at end B, topped by a line sloping from zero up to w₀. Neither beam has a resultant marked on it.
The live version of this figure — click here
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The lower beam's load reaches 12 kN/m at B over a span of 6.0 m. What is the total load on it?
[Options] A 72 kN — the biggest intensity times the length B 36 kN C 12 kN — the intensity is already a load
[Figure] Two loading diagrams. The upper beam carries arrows of equal length all along its 4.0 m, topped by a level line marked 3.0 kN/m. The lower beam carries arrows that grow steadily from nothing at end A to their longest at end B, topped by a line sloping from zero up to w₀. Neither beam has a resultant marked on it.

## Slide 22
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B 36 kN
WHY
The total is the AREA of the load shape, and that shape is a triangle: ½ × 6.0 m × 12 kN/m = 36 kN. Multiplying by the peak intensity treats the load as though it were that deep all the way along, which the drawing plainly shows it is not.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — 36 kN. The total is the AREA of the load shape, and that shape is a triangle: ½ × 6.0 m × 12 kN/m = 36 kN. Multiplying by the peak intensity treats the load as though it were that deep all the way along, which the drawing plainly shows it is not.

## Slide 23
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A triangular load rises from zero at A to w₀ at B. Where does its resultant act?
A
L/2 from A
B
2L/3 from A
C
L/3 from A
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A triangular load rises from zero at A to w₀ at B. Where does its resultant act?
[Options] A L/2 from A B 2L/3 from A C L/3 from A

## Slide 24
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 2L/3 from A
HOW TO GET THERE
The centroid lies one-third from the larger end B, which is 2L/3 from the zero end A.
WHY THE OTHERS TEMPT
A L/2 is where a uniform load acts. This one is not uniform — most of it sits near B — so its balance point has to be past the middle.
B Right. The centroid of a triangle lies one third of the way from its wide end, and that end is B, which puts it 2L/3 from A.
C One third of the way along is right, but measured from the wrong end. It is one third from the high-intensity end, which is B, not A.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A triangular load rises from zero at A to w₀ at B. Where does its resultant act?
[Option by option] A: L/2 is where a uniform load acts. This one is not uniform — most of it sits near B — so its balance point has to be past the middle. B: Right. The centroid of a triangle lies one third of the way from its wide end, and that end is B, which puts it 2L/3 from A. C: One third of the way along is right, but measured from the wrong end. It is one third from the high-intensity end, which is B, not A.
[Answer] B — 2L/3 from A
[Why] The centroid lies one-third from the larger end B, which is 2L/3 from the zero end A.
[Reveal] One click for the answer, then one for the reason.

## Slide 25
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A load rises linearly from zero at A to 9.0 kN/m at B along a 6.0 m beam. Find the resultant and its position from A.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A load rises linearly from zero at A to 9.0 kN/m at B along a 6.0 m beam. Find the resultant and its position from A.
[Answer] 27 kN acting 4.0 m from A

## Slide 26
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A load rises linearly from zero at A to 9.0 kN/m at B along a 6.0 m beam. Find the resultant and its position from A.
1.
Triangle: W = ½ × 9.0 × 6.0 = 27 kN.
2.
A triangle's centroid sits at two-thirds from the zero end.
3.
x̄ = (2/3) × 6.0 = 4.0 m from A.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Triangle: W = ½ × 9.0 × 6.0 = 27 kN.
[Step 2] A triangle's centroid sits at two-thirds from the zero end.
[Step 3] x̄ = (2/3) × 6.0 = 4.0 m from A.

## Slide 27
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
27 kN acting 4.0 m from A
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 27 kN acting 4.0 m from A

## Slide 28
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A 5.0 m beam carries w(x) = 2 + 0.6x kN/m from x = 0. Use integrals to find the resultant and its line of action.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 5.0 m beam carries w(x) = 2 + 0.6x kN/m from x = 0. Use integrals to find the resultant and its line of action.
[Answer] 17.5 kN at x̄ ≈ 2.86 m

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A 5.0 m beam carries w(x) = 2 + 0.6x kN/m from x = 0. Use integrals to find the resultant and its line of action.
1.
W = ∫₀⁵ (2 + 0.6x)dx = [2x + 0.3x²]₀⁵ = 10 + 7.5 = 17.5 kN.
2.
First moment: ∫₀⁵ x(2 + 0.6x)dx = [x² + 0.2x³]₀⁵ = 25 + 25 = 50 kN·m.
3.
x̄ = 50 ÷ 17.5 ≈ 2.86 m.
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] W = ∫₀⁵ (2 + 0.6x)dx = [2x + 0.3x²]₀⁵ = 10 + 7.5 = 17.5 kN.
[Step 2] First moment: ∫₀⁵ x(2 + 0.6x)dx = [x² + 0.2x³]₀⁵ = 25 + 25 = 50 kN·m.
[Step 3] x̄ = 50 ÷ 17.5 ≈ 2.86 m.

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
17.5 kN at x̄ ≈ 2.86 m
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 17.5 kN at x̄ ≈ 2.86 m

## Slide 31
STATICS
Where to go next
Plenary — What to take away, what to practise next
Next
9.5 Beams, Supports & Reactions
https://giophysics.com/chapter-15/beams-supports-reactions/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-15/distributed-loads-resultants/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-15/presentation/?lesson=distributed
Chapter
All Statics lessons
https://giophysics.com/chapter-15/
PDF
Download the lesson PDF
https://giophysics.com/downloads/15-4-distributed-loads-resultants.pdf
STATICS · DISTRIBUTED LOADS & RESULTANTS
GIOPHYSICS LESSON
Statics — Distributed Loads & Resultants. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 31
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-15/presentation/?lesson=distributed moves them.