## Slide 1
09 · Statics
Balance several contacts
Ladders, Hinges & Friction
Ladder and hinged-beam problems become manageable when every contact is modelled correctly and moments are taken through the busiest support.
POSITION
Lesson 6 of 7 in Statics
PLAN
16 slides in the 45-minute core run, about 44 minutes of it
LESSON PAGE
https://giophysics.com/chapter-15/ladders-hinges-friction/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 31
Notes: [Lesson] Statics — Ladders, Hinges & Friction. Lesson 6 of 7.
[Intro] Ladder and hinged-beam problems become manageable when every contact is modelled correctly and moments are taken through the busiest support.
[Source] https://giophysics.com/chapter-15/ladders-hinges-friction/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
THINK FIRST
Why does a ladder slip out at the bottom and never slide down at the top?
Take answers before you click — the point is the commitment
You have seen it happen, or seen the poster warning you about it.
THE ANSWER
Because a smooth wall can only push horizontally — it has nothing to grip the ladder with. That horizontal push has to be balanced by something horizontal at the other end, and the only candidate in the whole problem is friction at the foot. When the floor cannot supply enough of it, the foot is what moves.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 31
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Why does a ladder slip out at the bottom and never slide down at the top? You have seen it happen, or seen the poster warning you about it.
[Answer] Because a smooth wall can only push horizontally — it has nothing to grip the ladder with. That horizontal push has to be balanced by something horizontal at the other end, and the only candidate in the whole problem is friction at the foot. When the floor cannot supply enough of it, the foot is what moves.

## Slide 3
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A ladder equilibrium model replaces each contact by its allowed reactions, then balances all forces and moments while checking available friction.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A ladder equilibrium model replaces each contact by its allowed reactions, then balances all forces and moments while checking available friction.

## Slide 4
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
For a ladder against a smooth wall, the wall pushes horizontally and floor friction acts toward the wall to stop the foot sliding away.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] For a ladder against a smooth wall, the wall pushes horizontally and floor friction acts toward the wall to stop the foot sliding away.

## Slide 5
THE BIG IDEA
Balance several contacts
Introduce the idea — The big idea and the definition
For a uniform ladder against a smooth wall, the wall pushes horizontally while the rough floor supplies vertical normal force and horizontal friction. Taking moments about the foot removes both floor forces from the moment equation.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] For a uniform ladder against a smooth wall, the wall pushes horizontally while the rough floor supplies vertical normal force and horizontal friction. Taking moments about the foot removes both floor forces from the moment equation.

## Slide 6
THE PHYSICS · 1 OF 3
Smooth means no friction
Build the model — The formulae, one at a time, in plain English
A smooth wall supplies only a normal reaction perpendicular to the wall.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A smooth wall supplies only a normal reaction perpendicular to the wall.

## Slide 7
THE PHYSICS · 2 OF 3
A hinge has components
Build the model — The formulae, one at a time, in plain English
An ideal planar hinge can supply horizontal and vertical reactions but no reaction couple.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] An ideal planar hinge can supply horizontal and vertical reactions but no reaction couple.

## Slide 8
THE PHYSICS · 3 OF 3
Three-force shortcut
Build the model — The formulae, one at a time, in plain English
A rigid body in equilibrium under exactly three non-parallel forces has concurrent lines of action. Do not use this shortcut after adding another load.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A rigid body in equilibrium under exactly three non-parallel forces has concurrent lines of action. Do not use this shortcut after adding another load.

## Slide 9
FORMULA 1 OF 3
Friction condition
Build the model — The formulae, one at a time, in plain English
|fₛ| ≤ μₛNfloor
Impending slip uses equality
IN PLAIN ENGLISH
The floor's grip has a ceiling; a ladder slips the moment it demands more than that.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Friction condition: |fₛ| ≤ μₛNfloor
[In plain English] The floor's grip has a ceiling; a ladder slips the moment it demands more than that.
[Note] Impending slip uses equality

## Slide 10
FORMULA 2 OF 3
Uniform ladder
Build the model — The formulae, one at a time, in plain English
Nwall = mg/(2 tan θ)
Smooth wall, rough level floor
IN PLAIN ENGLISH
The flatter a ladder leans, the harder it presses on the wall — and the more grip its base needs.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Uniform ladder: Nwall = mg/(2 tan θ)
[In plain English] The flatter a ladder leans, the harder it presses on the wall — and the more grip its base needs.
[Note] Smooth wall, rough level floor

## Slide 11
FORMULA 3 OF 3
Required grip
Build the model — The formulae, one at a time, in plain English
μrequired = 1/(2 tan θ)
For the same ideal ladder
IN PLAIN ENGLISH
The minimum friction the floor must offer to keep the ladder from slipping at that angle.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Required grip: μrequired = 1/(2 tan θ)
[In plain English] The minimum friction the floor must offer to keep the ladder from slipping at that angle.
[Note] For the same ideal ladder

## Slide 12
THE PICTURE
Everything acting on the ladder
Drawn for this lesson
A uniform ladder with its foot on a rough level floor and its top against a smooth vertical wall, at about fifty degrees to the floor with the angle marked. The wall's push is drawn horizontally away from the wall at the top contact, the floor's normal force vertically upwards at the foot, and the ladder's weight downwards from its midpoint. No friction arrow is drawn.
The live version of this figure — click here
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A uniform ladder with its foot on a rough level floor and its top against a smooth vertical wall, at about fifty degrees to the floor with the angle marked. The wall's push is drawn horizontally away from the wall at the top contact, the floor's normal force vertically upwards at the foot, and the ladder's weight downwards from its midpoint. No friction arrow is drawn.

## Slide 13
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Static friction is not always μₛN. It adjusts to the value required for equilibrium and reaches μₛN only at impending motion.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Static friction is not always μₛN. It adjusts to the value required for equilibrium and reaches μₛN only at impending motion.

## Slide 14
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A ladder leans against a smooth wall at 60° to the ground. What supplies the horizontal force balancing the wall's push?
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A ladder leans against a smooth wall at 60° to the ground. What supplies the horizontal force balancing the wall's push?
[Answer] Floor friction

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A ladder leans against a smooth wall at 60° to the ground. What supplies the horizontal force balancing the wall's push?
1.
The smooth wall pushes horizontally only.
2.
Friction at the floor supplies the equal and opposite horizontal force.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] The smooth wall pushes horizontally only.
[Step 2] Friction at the floor supplies the equal and opposite horizontal force.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
Floor friction
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Floor friction

## Slide 17
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A uniform ladder rests at 45° against a smooth wall. Find the minimum static-friction coefficient at the floor.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A uniform ladder rests at 45° against a smooth wall. Find the minimum static-friction coefficient at the floor.
[Answer] μₛ,min = 0.50

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A uniform ladder rests at 45° against a smooth wall. Find the minimum static-friction coefficient at the floor.
1.
For this ideal model, μrequired = 1/(2 tan θ).
2.
At 45°, tan θ = 1.
3.
The minimum coefficient equals the impending-slip value.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] For this ideal model, μrequired = 1/(2 tan θ).
[Step 2] At 45°, tan θ = 1.
[Step 3] The minimum coefficient equals the impending-slip value.

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
μₛ,min = 0.50
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] μₛ,min = 0.50

## Slide 20
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A uniform 20 kg, 5.0 m ladder leans at 55° against a smooth wall. Take moments about the foot.
2.
The wall's push is horizontal and the weight is vertical, so each needs its own perpendicular arm.
3.
N(wall) × 5.0 cos55° = 196 × 2.5 sin55°.
4.
N(wall) = 196 × 2.5 × 0.819 ÷ (5.0 × 0.574) ≈ 140 N.
LINE 3 IS WRONG
The two arms have been swapped. The wall's push is horizontal, so its perpendicular arm about the foot is the ladder's vertical height, 5.0 sin 55°; the weight is vertical, so its arm is the horizontal distance out, 2.5 cos 55°. A perpendicular arm is always measured across the force, never along the ladder.
IT SHOULD SAY
N(wall) × 5.0 sin55° = 196 × 2.5 cos55°.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The two arms have been swapped. The wall's push is horizontal, so its perpendicular arm about the foot is the ladder's vertical height, 5.0 sin 55°; the weight is vertical, so its arm is the horizontal distance out, 2.5 cos 55°. A perpendicular arm is always measured across the force, never along the ladder.
[It should say] N(wall) × 5.0 sin55° = 196 × 2.5 cos55°.

## Slide 21
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The same ladder is moved so that it leans at a shallower angle to the floor. What happens to the friction the floor must supply?
A It falls — the ladder is lying more nearly flat, so it is closer to simply resting there
B It rises
C It does not change: the ladder's weight is the same either way
A uniform ladder with its foot on a rough level floor and its top against a smooth vertical wall, at about fifty degrees to the floor with the angle marked. The wall's push is drawn horizontally away from the wall at the top contact, the floor's normal force vertically upwards at the foot, and the ladder's weight downwards from its midpoint. No friction arrow is drawn.
The live version of this figure — click here
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The same ladder is moved so that it leans at a shallower angle to the floor. What happens to the friction the floor must supply?
[Options] A It falls — the ladder is lying more nearly flat, so it is closer to simply resting there B It rises C It does not change: the ladder's weight is the same either way
[Figure] A uniform ladder with its foot on a rough level floor and its top against a smooth vertical wall, at about fifty degrees to the floor with the angle marked. The wall's push is drawn horizontally away from the wall at the top contact, the floor's normal force vertically upwards at the foot, and the ladder's weight downwards from its midpoint. No friction arrow is drawn.

## Slide 22
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B It rises
WHY
Take moments about the foot and the wall's push comes out as mg/(2 tan θ), so as θ falls, tan θ falls and that push climbs steeply. Horizontal balance means the floor's friction has to match it exactly — which is why the safe-working advice is one metre out for every four up.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — It rises. Take moments about the foot and the wall's push comes out as mg/(2 tan θ), so as θ falls, tan θ falls and that push climbs steeply. Horizontal balance means the floor's friction has to match it exactly — which is why the safe-working advice is one metre out for every four up.

## Slide 23
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
For a uniform ladder against a smooth vertical wall and rough floor, which way does floor friction act?
A
Toward the wall
B
Away from the wall
C
Vertically upward
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] For a uniform ladder against a smooth vertical wall and rough floor, which way does floor friction act?
[Options] A Toward the wall B Away from the wall C Vertically upward

## Slide 24
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
A Toward the wall
HOW TO GET THERE
The wall pushes the top away from itself; floor friction acts toward the wall to balance that horizontal force.
WHY THE OTHERS TEMPT
A Right. The smooth wall can only push horizontally, away from itself, and the one other horizontal force in the problem is the friction at the foot — so it must point back toward the wall.
B This is the direction the foot would slide if it went, and friction always opposes the sliding rather than joining in with it.
C Friction acts along the surface, so on a level floor it is horizontal. The vertical push from the floor is the normal force, which is a separate thing.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] For a uniform ladder against a smooth vertical wall and rough floor, which way does floor friction act?
[Option by option] A: Right. The smooth wall can only push horizontally, away from itself, and the one other horizontal force in the problem is the friction at the foot — so it must point back toward the wall. B: This is the direction the foot would slide if it went, and friction always opposes the sliding rather than joining in with it. C: Friction acts along the surface, so on a level floor it is horizontal. The vertical push from the floor is the normal force, which is a separate thing.
[Answer] A — Toward the wall
[Why] The wall pushes the top away from itself; floor friction acts toward the wall to balance that horizontal force.
[Reveal] One click for the answer, then one for the reason.

## Slide 25
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A uniform 20 kg, 5.0 m ladder leans at 55° against a smooth wall. Find the wall force and the friction needed at the base.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A uniform 20 kg, 5.0 m ladder leans at 55° against a smooth wall. Find the wall force and the friction needed at the base.
[Answer] Wall pushes ≈ 69 N; base friction ≈ 69 N

## Slide 26
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A uniform 20 kg, 5.0 m ladder leans at 55° against a smooth wall. Find the wall force and the friction needed at the base.
1.
Moments about the base: N(wall) × 5.0 sin55° = 196 × 2.5 cos55°.
2.
N(wall) = 196 × 2.5 × 0.574 ÷ (5.0 × 0.819) ≈ 68.6 N.
3.
Friction at base = N(wall) ≈ 69 N (horizontal balance).
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Moments about the base: N(wall) × 5.0 sin55° = 196 × 2.5 cos55°.
[Step 2] N(wall) = 196 × 2.5 × 0.574 ÷ (5.0 × 0.819) ≈ 68.6 N.
[Step 3] Friction at base = N(wall) ≈ 69 N (horizontal balance).

## Slide 27
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
Wall pushes ≈ 69 N; base friction ≈ 69 N
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Wall pushes ≈ 69 N; base friction ≈ 69 N

## Slide 28
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
For the same ladder (μs = 0.35 at the floor, smooth wall), how far up can a 75 kg painter climb before it slips?
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] For the same ladder (μs = 0.35 at the floor, smooth wall), how far up can a 75 kg painter climb before it slips?
[Answer] ≈ 2.5 m along the ladder (about halfway)

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
For the same ladder (μs = 0.35 at the floor, smooth wall), how far up can a 75 kg painter climb before it slips?
1.
Max friction = μN(floor) = 0.35 × (20 + 75) × 9.81 ≈ 326 N = max wall force.
2.
Moments about the base with painter a distance d up the ladder: N(wall) × 5 sin55° = 196 × 2.5 cos55° + 736 × d cos55°.
3.
326 × 4.10 = 281 + 422d → d = (1336 − 281) ÷ 422 ≈ 2.5 m — halfway up.
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Max friction = μN(floor) = 0.35 × (20 + 75) × 9.81 ≈ 326 N = max wall force.
[Step 2] Moments about the base with painter a distance d up the ladder: N(wall) × 5 sin55° = 196 × 2.5 cos55° + 736 × d cos55°.
[Step 3] 326 × 4.10 = 281 + 422d → d = (1336 − 281) ÷ 422 ≈ 2.5 m — halfway up.

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
≈ 2.5 m along the ladder (about halfway)
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 2.5 m along the ladder (about halfway)

## Slide 31
STATICS
Where to go next
Plenary — What to take away, what to practise next
Next
9.7 Advanced Statics & Calculus
https://giophysics.com/chapter-15/advanced-statics-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-15/ladders-hinges-friction/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-15/presentation/?lesson=ladders
Chapter
All Statics lessons
https://giophysics.com/chapter-15/
PDF
Download the lesson PDF
https://giophysics.com/downloads/15-6-ladders-hinges-friction.pdf
STATICS · LADDERS, HINGES & FRICTION
GIOPHYSICS LESSON
Statics — Ladders, Hinges & Friction. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 31
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-15/presentation/?lesson=ladders moves them.