## Slide 1
13 · Circuits
How fast circuits transfer energy
Electric Power
Every component transfers the energy its charge carries. Power measures how fast: volts times amperes gives joules per second, and the resistor forms let you use whichever pair of quantities you know.
POSITION
Lesson 7 of 8 in Circuits
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-22/electric-power/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Circuits — Electric Power. Lesson 7 of 8.
[Intro] Every component transfers the energy its charge carries. Power measures how fast: volts times amperes gives joules per second, and the resistor forms let you use whichever pair of quantities you know.
[Source] https://giophysics.com/chapter-22/electric-power/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Voltage & energy
https://giophysics.com/chapter-22/voltage-potential-difference/
Recall
Power & efficiency
https://giophysics.com/chapter-5/power-efficiency/
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Voltage & energy; Power & efficiency

## Slide 3
THINK FIRST
Cables waste energy as heat. To halve that waste, would you rather halve the current in them or halve their resistance?
Take answers before you click — the point is the commitment
Halving the resistance means twice as much copper strung between every pylon in the country. Halving the current costs a transformer at each end.
THE ANSWER
Halve the current — and you get far more than you asked for. The waste is I²R, so halving R halves the loss, but halving I quarters it. That single squared term is why the grid runs at hundreds of kilovolts: high voltage is how you buy a small current.
One power station feeding one town twice over: in the upper circuit 100 kW is sent at 10 kV so the cables carry 10 A, and in the lower one the same 100 kW goes at 100 kV so the same 5.0 Ω of cable carries 1.0 A; neither power loss is printed.
The live version of this figure — click here
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Cables waste energy as heat. To halve that waste, would you rather halve the current in them or halve their resistance? Halving the resistance means twice as much copper strung between every pylon in the country. Halving the current costs a transformer at each end.
[Answer] Halve the current — and you get far more than you asked for. The waste is I²R, so halving R halves the loss, but halving I quarters it. That single squared term is why the grid runs at hundreds of kilovolts: high voltage is how you buy a small current.
[Figure] One power station feeding one town twice over: in the upper circuit 100 kW is sent at 10 kV so the cables carry 10 A, and in the lower one the same 100 kW goes at 100 kV so the same 5.0 Ω of cable carries 1.0 A; neither power loss is printed.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Electric power is the energy a component transfers each second.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Electric power is the energy a component transfers each second.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A lamp on 230 V drawing 0.26 A transfers about 60 J every second — a 60 W lamp.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A lamp on 230 V drawing 0.26 A transfers about 60 J every second — a 60 W lamp.

## Slide 6
THE BIG IDEA
How fast circuits transfer energy
Introduce the idea — The big idea and the definition
P = VI comes straight from the definitions: energy per charge times charge per second is energy per second. Substituting V = IR gives P = I²R and P = V²/R for resistive components, and multiplying power by time gives the energy bill.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] P = VI comes straight from the definitions: energy per charge times charge per second is energy per second. Substituting V = IR gives P = I²R and P = V²/R for resistive components, and multiplying power by time gives the energy bill.

## Slide 7
THE PHYSICS · 1 OF 3
Follow the units
Build the model — The formulae, one at a time, in plain English
V is J/C and I is C/s, so VI is J/s. Every power formula is that one idea rearranged.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] V is J/C and I is C/s, so VI is J/s. Every power formula is that one idea rearranged.

## Slide 8
THE PHYSICS · 2 OF 3
Rating a device
Build the model — The formulae, one at a time, in plain English
A '60 W, 230 V' rating states the design operating point; from it you can recover the working current and resistance.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A '60 W, 230 V' rating states the design operating point; from it you can recover the working current and resistance.

## Slide 9
THE PHYSICS · 3 OF 3
Heating in wires
Build the model — The formulae, one at a time, in plain English
P = I²R explains transmission losses: halving the current (by raising voltage) quarters the power wasted in the cable.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] P = I²R explains transmission losses: halving the current (by raising voltage) quarters the power wasted in the cable.

## Slide 10
FORMULA 1 OF 3
Electrical power
Build the model — The formulae, one at a time, in plain English
P = VI
1 W = 1 J/s = 1 V·A
IN PLAIN ENGLISH
Energy per charge (volts) times charge per second (amps) equals energy per second — power.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Electrical power: P = VI
[In plain English] Energy per charge (volts) times charge per second (amps) equals energy per second — power.
[Note] 1 W = 1 J/s = 1 V·A

## Slide 11
FORMULA 2 OF 3
Resistor forms
Build the model — The formulae, one at a time, in plain English
P = I²R = V²/R
Substitute V = IR into P = VI
IN PLAIN ENGLISH
Two rearrangements for resistors: use I²R when you know the current, V²/R when you know the voltage.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Resistor forms: P = I²R = V²/R
[In plain English] Two rearrangements for resistors: use I²R when you know the current, V²/R when you know the voltage.
[Note] Substitute V = IR into P = VI

## Slide 12
FORMULA 3 OF 3
Energy transferred
Build the model — The formulae, one at a time, in plain English
W = Pt = VIt
Joules; utilities bill the kWh = 3.6 MJ
IN PLAIN ENGLISH
Power times how long it runs gives the total energy — what an electricity meter actually counts.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Energy transferred: W = Pt = VIt
[In plain English] Power times how long it runs gives the total energy — what an electricity meter actually counts.
[Note] Joules; utilities bill the kWh = 3.6 MJ

## Slide 13
CIRCUIT MODEL
Read the topology before the values
Build the model — nodes are where connections meet, branches are what lies between them
parallel network — components are branches between nodes.
Switch topology and hide the values on the live version — click here
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Topology] Nodes are the points where connections meet; branches are the components between them. The live version switches between series, parallel and bridge and can hide the values.

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
P = V²/R does not mean more resistance always means more power. At fixed voltage, more resistance means less power; at fixed current (P = I²R), it means more. Identify what is held constant first.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] P = V²/R does not mean more resistance always means more power. At fixed voltage, more resistance means less power; at fixed current (P = I²R), it means more. Identify what is held constant first.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A lamp draws 0.26 A from a 230 V supply. Find its power.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A lamp draws 0.26 A from a 230 V supply. Find its power.
[Answer] ≈ 60 W

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A lamp draws 0.26 A from a 230 V supply. Find its power.
1.
P = VI = 230 × 0.26.
2.
P ≈ 60 W.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] P = VI = 230 × 0.26.
[Step 2] P ≈ 60 W.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
≈ 60 W
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 60 W

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A 2.0 kW kettle runs on 230 V. Find its current, its element's resistance, and the energy used in 3.0 minutes.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 2.0 kW kettle runs on 230 V. Find its current, its element's resistance, and the energy used in 3.0 minutes.
[Answer] I ≈ 8.7 A, R ≈ 26 Ω, W = 3.6 × 10⁵ J

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A 2.0 kW kettle runs on 230 V. Find its current, its element's resistance, and the energy used in 3.0 minutes.
1.
I = P/V = 2000 ÷ 230 ≈ 8.7 A.
2.
R = V²/P = 230² ÷ 2000 ≈ 26 Ω.
3.
W = Pt = 2000 × 180 = 3.6 × 10⁵ J (= 0.10 kWh).
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] I = P/V = 2000 ÷ 230 ≈ 8.7 A.
[Step 2] R = V²/P = 230² ÷ 2000 ≈ 26 Ω.
[Step 3] W = Pt = 2000 × 180 = 3.6 × 10⁵ J (= 0.10 kWh).

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
I ≈ 8.7 A, R ≈ 26 Ω, W = 3.6 × 10⁵ J
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] I ≈ 8.7 A, R ≈ 26 Ω, W = 3.6 × 10⁵ J

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A 2.0 kW kettle runs on 230 V. Find the energy it transfers in 3.0 minutes.
2.
W = Pt
3.
W = 2.0 × 3.0 = 6.0
4.
W = 6.0 kJ
5.
So the kettle transfers 6.0 kJ.
LINE 3 IS WRONG
The kilowatts have been left as kilowatts and the minutes as minutes, and the two mistakes hide each other — the answer even carries a plausible-looking unit. A joule is a watt second, so both quantities have to come to base units first: 2000 W and 180 s. The 60-fold error is the size of the slip, and 6 kJ is roughly what a kettle uses in three seconds, not three minutes.
IT SHOULD SAY
W = Pt = 2000 × 180 = 3.6 × 10⁵ J = 360 kJ
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The kilowatts have been left as kilowatts and the minutes as minutes, and the two mistakes hide each other — the answer even carries a plausible-looking unit. A joule is a watt second, so both quantities have to come to base units first: 2000 W and 180 s. The 60-fold error is the size of the slip, and 6 kJ is roughly what a kettle uses in three seconds, not three minutes.
[It should say] W = Pt = 2000 × 180 = 3.6 × 10⁵ J = 360 kJ

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The same 100 kW goes down the same 5.0 Ω of cable, once at 10 kV and once at 100 kV. How much less power is wasted in the cable at the higher voltage?
A Ten times less
B A hundred times less
C No less — the same 100 kW is being sent either way
One power station feeding one town twice over: in the upper circuit 100 kW is sent at 10 kV so the cables carry 10 A, and in the lower one the same 100 kW goes at 100 kV so the same 5.0 Ω of cable carries 1.0 A; neither power loss is printed.
The live version of this figure — click here
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The same 100 kW goes down the same 5.0 Ω of cable, once at 10 kV and once at 100 kV. How much less power is wasted in the cable at the higher voltage?
[Options] A Ten times less B A hundred times less C No less — the same 100 kW is being sent either way
[Figure] One power station feeding one town twice over: in the upper circuit 100 kW is sent at 10 kV so the cables carry 10 A, and in the lower one the same 100 kW goes at 100 kV so the same 5.0 Ω of cable carries 1.0 A; neither power loss is printed.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B A hundred times less
WHY
The two figures already give the currents, and P = VI is where they came from: ten times the voltage carries the same 100 kW with one tenth of the current, so 10 A becomes 1.0 A. What the cable wastes is not that 100 kW but I²R, and the square is what does the work — 10² × 5.0 = 500 W in the upper drawing against 1.0² × 5.0 = 5 W in the lower one. Ten times the voltage, a hundredth of the loss.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — A hundred times less. The two figures already give the currents, and P = VI is where they came from: ten times the voltage carries the same 100 kW with one tenth of the current, so 10 A becomes 1.0 A. What the cable wastes is not that 100 kW but I²R, and the square is what does the work — 10² × 5.0 = 500 W in the upper drawing against 1.0² × 5.0 = 5 W in the lower one. Ten times the voltage, a hundredth of the loss.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Doubling the current through a fixed resistor changes the power dissipated by a factor of…
A
2
B
4
C
½
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Doubling the current through a fixed resistor changes the power dissipated by a factor of…
[Options] A 2 B 4 C ½

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 4
HOW TO GET THERE
P = I²R — power grows with the square of the current, so doubling I quadruples P.
WHY THE OTHERS TEMPT
A 2 comes from P = VI read as though only one of the two factors changed. Through a fixed resistor, doubling the current also doubles the p.d. across it — both factors double, so the power goes up four times.
B Correct. P = I²R with R fixed, so doubling I multiplies the power by 2² = 4.
C ½ is what P = V²/R gives when R is the quantity being doubled. That is the right formula for a different question. Here the resistor is fixed and the current is what changes, so P = I²R is the form that applies — which is exactly why it pays to identify what is being held constant before choosing between the three.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Doubling the current through a fixed resistor changes the power dissipated by a factor of…
[Option by option] A: 2 comes from P = VI read as though only one of the two factors changed. Through a fixed resistor, doubling the current also doubles the p.d. across it — both factors double, so the power goes up four times. B: Correct. P = I²R with R fixed, so doubling I multiplies the power by 2² = 4. C: ½ is what P = V²/R gives when R is the quantity being doubled. That is the right formula for a different question. Here the resistor is fixed and the current is what changes, so P = I²R is the form that applies — which is exactly why it pays to identify what is being held constant before choosing between the three.
[Answer] B — 4
[Why] P = I²R — power grows with the square of the current, so doubling I quadruples P.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
An 1800 W heater runs 3.0 hours daily. At $0.15 per kWh, find the energy per day and the 30-day cost.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] An 1800 W heater runs 3.0 hours daily. At $0.15 per kWh, find the energy per day and the 30-day cost.
[Answer] 5.4 kWh/day; ≈ $24 per month

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
An 1800 W heater runs 3.0 hours daily. At $0.15 per kWh, find the energy per day and the 30-day cost.
1.
E = Pt = 1.8 kW × 3.0 h = 5.4 kWh/day.
2.
Month: 5.4 × 30 = 162 kWh.
3.
Cost = 162 × 0.15 ≈ $24.30.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E = Pt = 1.8 kW × 3.0 h = 5.4 kWh/day.
[Step 2] Month: 5.4 × 30 = 162 kWh.
[Step 3] Cost = 162 × 0.15 ≈ $24.30.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
5.4 kWh/day; ≈ $24 per month
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 5.4 kWh/day; ≈ $24 per month

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A power station sends 100 kW through cables of total resistance 5.0 Ω. Compare the cable losses at 10 kV and at 100 kV transmission, and state the loss fractions.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A power station sends 100 kW through cables of total resistance 5.0 Ω. Compare the cable losses at 10 kV and at 100 kV transmission, and state the loss fractions.
[Answer] 500 W vs 5 W — 100× less loss at 10× the voltage

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A power station sends 100 kW through cables of total resistance 5.0 Ω. Compare the cable losses at 10 kV and at 100 kV transmission, and state the loss fractions.
1.
At 10 kV: I = P/V = 10 A → loss = I²R = 500 W (0.5%).
2.
At 100 kV: I = 1.0 A → loss = 5.0 W (0.005%).
3.
Raising the voltage tenfold cuts the loss a hundredfold — the entire rationale for the high-voltage grid.
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] At 10 kV: I = P/V = 10 A → loss = I²R = 500 W (0.5%).
[Step 2] At 100 kV: I = 1.0 A → loss = 5.0 W (0.005%).
[Step 3] Raising the voltage tenfold cuts the loss a hundredfold — the entire rationale for the high-voltage grid.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
500 W vs 5 W — 100× less loss at 10× the voltage
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 500 W vs 5 W — 100× less loss at 10× the voltage

## Slide 32
CIRCUITS
Where to go next
Plenary — What to take away, what to practise next
Next
13.8 Current Calculus
https://giophysics.com/chapter-22/current-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-22/electric-power/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-22/presentation/?lesson=power
Chapter
All Circuits lessons
https://giophysics.com/chapter-22/
PDF
Download the lesson PDF
https://giophysics.com/downloads/22-7-electric-power.pdf
CIRCUITS · ELECTRIC POWER
GIOPHYSICS LESSON
Circuits — Electric Power. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-22/presentation/?lesson=power moves them.