## Slide 1
14 · Advanced Circuits
When the I–V line bends
Non-Ohmic Components
A filament lamp heats as current grows, so its resistance climbs. A diode conducts in only one direction, and only past a threshold. Their curved I–V characteristics tell the story.
POSITION
Lesson 2 of 7 in Advanced Circuits
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-23/non-ohmic-components/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Advanced Circuits — Non-Ohmic Components. Lesson 2 of 7.
[Intro] A filament lamp heats as current grows, so its resistance climbs. A diode conducts in only one direction, and only past a threshold. Their curved I–V characteristics tell the story.
[Source] https://giophysics.com/chapter-23/non-ohmic-components/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Resistance & Ohm's law
https://giophysics.com/chapter-22/resistance-ohms-law/
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Resistance & Ohm's law

## Slide 3
THINK FIRST
A headlamp bulb measures 2.0 Ω on a multimeter. Connected to 12 V it should draw 6.0 A — and the fuse is rated at 5 A. Does the fuse blow?
Take answers before you click — the point is the commitment
The meter was clipped across the bulb cold, on the bench. The fuse is the one in the car's lighting circuit.
THE ANSWER
No. The 2.0 Ω is the resistance of a cold filament, and it survives for a fraction of a second: as soon as current flows the wire climbs towards 2500 °C, its resistance rises several-fold and the current settles well under 5 A. The only moment a filament lamp comes anywhere near its cold-resistance current is the instant of switch-on — which is exactly when bulbs blow.
Current plotted against the p.d. across the component, carrying a single straight line through the origin labelled as a metal wire held at constant temperature; the rest of the grid is empty, with no curve drawn for the filament lamp.
The live version of this figure — click here
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A headlamp bulb measures 2.0 Ω on a multimeter. Connected to 12 V it should draw 6.0 A — and the fuse is rated at 5 A. Does the fuse blow? The meter was clipped across the bulb cold, on the bench. The fuse is the one in the car's lighting circuit.
[Answer] No. The 2.0 Ω is the resistance of a cold filament, and it survives for a fraction of a second: as soon as current flows the wire climbs towards 2500 °C, its resistance rises several-fold and the current settles well under 5 A. The only moment a filament lamp comes anywhere near its cold-resistance current is the instant of switch-on — which is exactly when bulbs blow.
[Figure] Current plotted against the p.d. across the component, carrying a single straight line through the origin labelled as a metal wire held at constant temperature; the rest of the grid is empty, with no curve drawn for the filament lamp.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A non-ohmic component's current is not proportional to the voltage across it, so its I–V graph is not a straight line through the origin.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A non-ohmic component's current is not proportional to the voltage across it, so its I–V graph is not a straight line through the origin.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A filament lamp draws proportionally less extra current at high voltage because its hot filament resists more.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A filament lamp draws proportionally less extra current at high voltage because its hot filament resists more.

## Slide 6
THE BIG IDEA
When the I–V line bends
Introduce the idea — The big idea and the definition
R = V/I still gives the resistance at any operating point, but for non-ohmic components that ratio changes along the curve. The filament lamp's graph flattens as its temperature—and resistance—rise; the diode's leaps up after its threshold voltage, and stays near zero in reverse.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] R = V/I still gives the resistance at any operating point, but for non-ohmic components that ratio changes along the curve. The filament lamp's graph flattens as its temperature—and resistance—rise; the diode's leaps up after its threshold voltage, and stays near zero in reverse.

## Slide 7
THE PHYSICS · 1 OF 3
Metal at constant temperature
Build the model — The formulae, one at a time, in plain English
The reference case: a straight line through the origin — constant R, Ohm's law obeyed.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The reference case: a straight line through the origin — constant R, Ohm's law obeyed.

## Slide 8
THE PHYSICS · 2 OF 3
Filament lamp
Build the model — The formulae, one at a time, in plain English
Current heats the filament to ~2500 °C. Rising temperature raises resistance, so the I–V curve bends over symmetrically for ±V.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Current heats the filament to ~2500 °C. Rising temperature raises resistance, so the I–V curve bends over symmetrically for ±V.

## Slide 9
THE PHYSICS · 3 OF 3
Semiconductor diode
Build the model — The formulae, one at a time, in plain English
Forward biased past the threshold it conducts readily; reverse biased it blocks. LEDs also emit light at their higher thresholds.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Forward biased past the threshold it conducts readily; reverse biased it blocks. LEDs also emit light at their higher thresholds.

## Slide 10
FORMULA 1 OF 3
Always true
Build the model — The formulae, one at a time, in plain English
R = V/I at each point
A definition, not Ohm's law
IN PLAIN ENGLISH
You can still compute resistance anywhere on the curve — it just changes from point to point.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Always true: R = V/I at each point
[In plain English] You can still compute resistance anywhere on the curve — it just changes from point to point.
[Note] A definition, not Ohm's law

## Slide 11
FORMULA 2 OF 3
Filament lamp
Build the model — The formulae, one at a time, in plain English
R rises with temperature
The I–V curve flattens at high V
IN PLAIN ENGLISH
More current heats the filament; hotter metal scatters electrons more, so each extra volt buys less extra current.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Filament lamp: R rises with temperature
[In plain English] More current heats the filament; hotter metal scatters electrons more, so each extra volt buys less extra current.
[Note] The I–V curve flattens at high V

## Slide 12
FORMULA 3 OF 3
Diode
Build the model — The formulae, one at a time, in plain English
conducts for V > V_threshold
≈0.6 V silicon, ≈2 V typical LED; reverse ≈ no current
IN PLAIN ENGLISH
A diode is a one-way valve: almost infinite resistance in reverse, and very low resistance once forward voltage passes the threshold.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Diode: conducts for V > V_threshold
[In plain English] A diode is a one-way valve: almost infinite resistance in reverse, and very low resistance once forward voltage passes the threshold.
[Note] ≈0.6 V silicon, ≈2 V typical LED; reverse ≈ no current

## Slide 13
CIRCUIT MODEL
Read the topology before the values
Build the model — nodes are where connections meet, branches are what lies between them
series network — components are branches between nodes.
Switch topology and hide the values on the live version — click here
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Topology] Nodes are the points where connections meet; branches are the components between them. The live version switches between series, parallel and bridge and can hide the values.

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A curved I–V graph does not mean R = V/I fails — it means the ratio differs at each point. Compute it point by point; do not use the gradient of a curved graph.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A curved I–V graph does not mean R = V/I fails — it means the ratio differs at each point. Compute it point by point; do not use the gradient of a curved graph.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A filament lamp's resistance is 2.0 Ω cold. Would you expect more or less than 6.0 A when 12 V is applied? Why?
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A filament lamp's resistance is 2.0 Ω cold. Would you expect more or less than 6.0 A when 12 V is applied? Why?
[Answer] Less — resistance rises as it heats

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A filament lamp's resistance is 2.0 Ω cold. Would you expect more or less than 6.0 A when 12 V is applied? Why?
1.
Naively 12/2 = 6.0 A, but current heats the filament.
2.
Hot resistance is higher, so the actual current is less than 6.0 A.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Naively 12/2 = 6.0 A, but current heats the filament.
[Step 2] Hot resistance is higher, so the actual current is less than 6.0 A.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
Less — resistance rises as it heats
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Less — resistance rises as it heats

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
From a lamp's I–V data: 2.0 V → 1.0 A and 8.0 V → 2.0 A. Show the lamp is non-ohmic.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] From a lamp's I–V data: 2.0 V → 1.0 A and 8.0 V → 2.0 A. Show the lamp is non-ohmic.
[Answer] R grows from 2.0 Ω to 4.0 Ω — non-ohmic behaviour

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
From a lamp's I–V data: 2.0 V → 1.0 A and 8.0 V → 2.0 A. Show the lamp is non-ohmic.
1.
At 2.0 V: R = 2.0 ÷ 1.0 = 2.0 Ω.
2.
At 8.0 V: R = 8.0 ÷ 2.0 = 4.0 Ω.
3.
Resistance changed with operating point, so I is not proportional to V.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] At 2.0 V: R = 2.0 ÷ 1.0 = 2.0 Ω.
[Step 2] At 8.0 V: R = 8.0 ÷ 2.0 = 4.0 Ω.
[Step 3] Resistance changed with operating point, so I is not proportional to V.

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
R grows from 2.0 Ω to 4.0 Ω — non-ohmic behaviour
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] R grows from 2.0 Ω to 4.0 Ω — non-ohmic behaviour

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A diode (threshold 0.60 V, negligible resistance beyond it) is in series with a 100 Ω resistor across 6.0 V, forward biased. Find the current.
2.
The diode drops 0.60 V, so the resistor takes 6.0 − 0.60 = 5.4 V
3.
The diode's resistance is 0.60 / I, which must be added to the 100 Ω
4.
I = 6.0 / (100 + 0.60/I)
5.
This cannot be solved without knowing I first.
LINE 3 IS WRONG
The first line had already finished the job. Trying to turn the diode's 0.60 V into a resistance and add it in series double-counts the same volt and leads straight into a circle. A conducting diode is not a resistor: it holds a roughly fixed p.d. whatever the current, so it is handled by subtracting its drop from the supply and letting the resistor take the rest.
IT SHOULD SAY
I = 5.4 / 100 = 54 mA, with 0.60 V across the diode and 5.4 V across the resistor
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The first line had already finished the job. Trying to turn the diode's 0.60 V into a resistance and add it in series double-counts the same volt and leads straight into a circle. A conducting diode is not a resistor: it holds a roughly fixed p.d. whatever the current, so it is handled by subtracting its drop from the supply and letting the resistor take the rest.
[It should say] I = 5.4 / 100 = 54 mA, with 0.60 V across the diode and 5.4 V across the resistor

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The straight line is a metal wire at constant temperature. Where does a filament lamp's curve go — which way does it bend?
A It bends upward, getting steeper as the p.d. rises
B It bends over, getting shallower as the p.d. rises
C It stays straight, just with a smaller gradient
Current plotted against the p.d. across the component, carrying a single straight line through the origin labelled as a metal wire held at constant temperature; the rest of the grid is empty, with no curve drawn for the filament lamp.
The live version of this figure — click here
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The straight line is a metal wire at constant temperature. Where does a filament lamp's curve go — which way does it bend?
[Options] A It bends upward, getting steeper as the p.d. rises B It bends over, getting shallower as the p.d. rises C It stays straight, just with a smaller gradient
[Figure] Current plotted against the p.d. across the component, carrying a single straight line through the origin labelled as a metal wire held at constant temperature; the rest of the grid is empty, with no curve drawn for the filament lamp.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B It bends over, getting shallower as the p.d. rises
WHY
Every extra volt pushes more current, more current means more heating, and a hotter filament resists more — so each extra volt buys less extra current than the one before it. On these axes, with current up the page, "less extra current per volt" is a line flattening off. And flattening is the same statement as R = V/I growing, because the p.d. is running ahead of the current it produces.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — It bends over, getting shallower as the p.d. rises. Every extra volt pushes more current, more current means more heating, and a hotter filament resists more — so each extra volt buys less extra current than the one before it. On these axes, with current up the page, "less extra current per volt" is a line flattening off. And flattening is the same statement as R = V/I growing, because the p.d. is running ahead of the current it produces.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A diode passes 20 mA at +1.0 V but 0.25 μA at −1.0 V. What is its reverse-bias resistance?
A
50 Ω
B
4.0 MΩ
C
0.05 Ω
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A diode passes 20 mA at +1.0 V but 0.25 μA at −1.0 V. What is its reverse-bias resistance?
[Options] A 50 Ω B 4.0 MΩ C 0.05 Ω

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 4.0 MΩ
HOW TO GET THERE
R = V/I = 1.0 ÷ 0.25 × 10⁻⁶ = 4.0 × 10⁶ Ω — effectively blocking. Forward: only 50 Ω.
WHY THE OTHERS TEMPT
A 50 Ω is the right calculation on the wrong pair of readings: 1.0 V ÷ 0.020 A is the diode's forward resistance. Reverse biased it passes 0.25 μA, eighty thousand times less current for the same volt.
B Correct. R = V/I = 1.0 ÷ (0.25 × 10⁻⁶) = 4.0 × 10⁶ Ω — effectively an open circuit.
C 0.05 Ω is 1.0 ÷ 20, using the forward reading and treating its 20 mA as 20 A. Either slip alone still leaves an answer far too small; together they land a hundred million times below the truth.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A diode passes 20 mA at +1.0 V but 0.25 μA at −1.0 V. What is its reverse-bias resistance?
[Option by option] A: 50 Ω is the right calculation on the wrong pair of readings: 1.0 V ÷ 0.020 A is the diode's forward resistance. Reverse biased it passes 0.25 μA, eighty thousand times less current for the same volt. B: Correct. R = V/I = 1.0 ÷ (0.25 × 10⁻⁶) = 4.0 × 10⁶ Ω — effectively an open circuit. C: 0.05 Ω is 1.0 ÷ 20, using the forward reading and treating its 20 mA as 20 A. Either slip alone still leaves an answer far too small; together they land a hundred million times below the truth.
[Answer] B — 4.0 MΩ
[Why] R = V/I = 1.0 ÷ 0.25 × 10⁻⁶ = 4.0 × 10⁶ Ω — effectively blocking. Forward: only 50 Ω.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A diode (threshold 0.60 V, negligible resistance beyond it) is in series with a 100 Ω resistor across 6.0 V, forward biased. Find the current and each p.d.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A diode (threshold 0.60 V, negligible resistance beyond it) is in series with a 100 Ω resistor across 6.0 V, forward biased. Find the current and each p.d.
[Answer] 54 mA; 0.60 V on the diode, 5.4 V on the resistor

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A diode (threshold 0.60 V, negligible resistance beyond it) is in series with a 100 Ω resistor across 6.0 V, forward biased. Find the current and each p.d.
1.
The diode takes its threshold 0.60 V; the resistor gets the rest: 5.4 V.
2.
I = 5.4 ÷ 100 = 54 mA.
3.
Reverse the supply and the diode blocks: I ≈ 0, diode holds all 6.0 V.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] The diode takes its threshold 0.60 V; the resistor gets the rest: 5.4 V.
[Step 2] I = 5.4 ÷ 100 = 54 mA.
[Step 3] Reverse the supply and the diode blocks: I ≈ 0, diode holds all 6.0 V.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
54 mA; 0.60 V on the diode, 5.4 V on the resistor
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 54 mA; 0.60 V on the diode, 5.4 V on the resistor

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
An LED (threshold 2.0 V) must run at 20 mA from a 9.0 V supply. Specify the series protection resistor, its power rating, and what happens with no resistor.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] An LED (threshold 2.0 V) must run at 20 mA from a 9.0 V supply. Specify the series protection resistor, its power rating, and what happens with no resistor.
[Answer] 350 Ω (¼ W); omitting it destroys the LED

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
An LED (threshold 2.0 V) must run at 20 mA from a 9.0 V supply. Specify the series protection resistor, its power rating, and what happens with no resistor.
1.
Resistor drops 9.0 − 2.0 = 7.0 V at 20 mA: R = 7.0 ÷ 0.020 = 350 Ω.
2.
P = VI = 7.0 × 0.020 = 0.14 W → use a 0.25 W resistor.
3.
Without it, the near-vertical diode characteristic lets current run away — the LED burns out almost instantly.
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Resistor drops 9.0 − 2.0 = 7.0 V at 20 mA: R = 7.0 ÷ 0.020 = 350 Ω.
[Step 2] P = VI = 7.0 × 0.020 = 0.14 W → use a 0.25 W resistor.
[Step 3] Without it, the near-vertical diode characteristic lets current run away — the LED burns out almost instantly.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
350 Ω (¼ W); omitting it destroys the LED
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 350 Ω (¼ W); omitting it destroys the LED

## Slide 32
ADVANCED CIRCUITS
Where to go next
Plenary — What to take away, what to practise next
Next
14.3 Thermistors & LDRs
https://giophysics.com/chapter-23/thermistors-ldrs/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-23/non-ohmic-components/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-23/presentation/?lesson=nonOhmic
Chapter
All Advanced Circuits lessons
https://giophysics.com/chapter-23/
PDF
Download the lesson PDF
https://giophysics.com/downloads/23-2-non-ohmic-components.pdf
ADVANCED CIRCUITS · NON-OHMIC COMPONENTS
GIOPHYSICS LESSON
Advanced Circuits — Non-Ohmic Components. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-23/presentation/?lesson=nonOhmic moves them.