## Slide 1
14 · Advanced Circuits
Measure e.m.f. by balancing it
Potentiometer Circuits
A potentiometer slides a contact along a uniform resistance wire, tapping any fraction of the driver voltage. At the balance point it reads an unknown e.m.f. while drawing no current from it.
POSITION
Lesson 6 of 7 in Advanced Circuits
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-23/potentiometer-circuits/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Advanced Circuits — Potentiometer Circuits. Lesson 6 of 7.
[Intro] A potentiometer slides a contact along a uniform resistance wire, tapping any fraction of the driver voltage. At the balance point it reads an unknown e.m.f. while drawing no current from it.
[Source] https://giophysics.com/chapter-23/potentiometer-circuits/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Potential dividers
https://giophysics.com/chapter-23/potential-dividers/
Recall
E.m.f. & internal resistance
https://giophysics.com/chapter-23/emf-internal-resistance/
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Potential dividers; E.m.f. & internal resistance

## Slide 3
THINK FIRST
A voltmeter across a fresh 1.5 V cell reads 1.49 V. Is the meter faulty?
Take answers before you click — the point is the commitment
It is a good digital meter, freshly calibrated, and the cell is new out of the packet.
THE ANSWER
No — the meter is right and so is the cell. The instant the meter is connected it draws a current, tiny but not zero, and that current drops Ir inside the cell. So the meter is reading the terminal p.d., which is always a little under the e.m.f. To see the e.m.f. itself you need a measurement that draws no current at all, which is exactly what a potentiometer is for.
A 2.0 V driver cell across a uniform resistance wire running from A to B, with a sliding contact tapping a length ℓ from A; the unknown cell and a galvanometer form a second branch from A to that contact, and the galvanometer face carries no needle.
The live version of this figure — click here
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A voltmeter across a fresh 1.5 V cell reads 1.49 V. Is the meter faulty? It is a good digital meter, freshly calibrated, and the cell is new out of the packet.
[Answer] No — the meter is right and so is the cell. The instant the meter is connected it draws a current, tiny but not zero, and that current drops Ir inside the cell. So the meter is reading the terminal p.d., which is always a little under the e.m.f. To see the e.m.f. itself you need a measurement that draws no current at all, which is exactly what a potentiometer is for.
[Figure] A 2.0 V driver cell across a uniform resistance wire running from A to B, with a sliding contact tapping a length ℓ from A; the unknown cell and a galvanometer form a second branch from A to that contact, and the galvanometer face carries no needle.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A potentiometer compares voltages by finding the point on a uniform wire where the tapped potential balances an unknown e.m.f., signalled by zero galvanometer current.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A potentiometer compares voltages by finding the point on a uniform wire where the tapped potential balances an unknown e.m.f., signalled by zero galvanometer current.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
If balance occurs at 65 cm of a 100 cm wire driven by 2.0 V, the unknown e.m.f. is 0.65 × 2.0 = 1.3 V.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] If balance occurs at 65 cm of a 100 cm wire driven by 2.0 V, the unknown e.m.f. is 0.65 × 2.0 = 1.3 V.

## Slide 6
THE BIG IDEA
Measure e.m.f. by balancing it
Introduce the idea — The big idea and the definition
The tapped voltage is proportional to the tapped length of uniform wire. Slide the jockey until a galvanometer in the unknown-cell branch reads zero: no current flows through the unknown cell, so the tapped voltage equals its full e.m.f. — unaffected by internal resistance.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] The tapped voltage is proportional to the tapped length of uniform wire. Slide the jockey until a galvanometer in the unknown-cell branch reads zero: no current flows through the unknown cell, so the tapped voltage equals its full e.m.f. — unaffected by internal resistance.

## Slide 7
THE PHYSICS · 1 OF 3
Why zero current matters
Build the model — The formulae, one at a time, in plain English
At balance no current flows through the unknown cell, so no volts are lost across its internal resistance: the potentiometer reads the true e.m.f., not the terminal p.d.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] At balance no current flows through the unknown cell, so no volts are lost across its internal resistance: the potentiometer reads the true e.m.f., not the terminal p.d.

## Slide 8
THE PHYSICS · 2 OF 3
Finding balance
Build the model — The formulae, one at a time, in plain English
Touch the jockey at the wire's ends first: the galvanometer should deflect opposite ways. Home in until the deflection is zero.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Touch the jockey at the wire's ends first: the galvanometer should deflect opposite ways. Home in until the deflection is zero.

## Slide 9
THE PHYSICS · 3 OF 3
Sensitivity
Build the model — The formulae, one at a time, in plain English
A longer wire or a smaller driver current spreads the volts over more length, making the balance point sharper to locate.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A longer wire or a smaller driver current spreads the volts over more length, making the balance point sharper to locate.

## Slide 10
FORMULA 1 OF 3
Uniform wire
Build the model — The formulae, one at a time, in plain English
V ∝ ℓ
Equal lengths tap equal voltages
IN PLAIN ENGLISH
A uniform wire drops voltage evenly along its length, so the tapped length measures the tapped voltage.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Uniform wire: V ∝ ℓ
[In plain English] A uniform wire drops voltage evenly along its length, so the tapped length measures the tapped voltage.
[Note] Equal lengths tap equal voltages

## Slide 11
FORMULA 2 OF 3
Balance condition
Build the model — The formulae, one at a time, in plain English
E_unknown = V_driver·ℓ/L
Galvanometer reads zero
IN PLAIN ENGLISH
At balance, the fraction of wire tapped gives the exact fraction of the driver voltage equal to the unknown e.m.f.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Balance condition: E_unknown = V_driver·ℓ/L
[In plain English] At balance, the fraction of wire tapped gives the exact fraction of the driver voltage equal to the unknown e.m.f.
[Note] Galvanometer reads zero

## Slide 12
FORMULA 3 OF 3
Comparing two cells
Build the model — The formulae, one at a time, in plain English
E₁/E₂ = ℓ₁/ℓ₂
Balance lengths for each cell in turn
IN PLAIN ENGLISH
Balance each cell on the same wire and the ratio of balance lengths is the ratio of their e.m.f.s — no meter calibration needed.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Comparing two cells: E₁/E₂ = ℓ₁/ℓ₂
[In plain English] Balance each cell on the same wire and the ratio of balance lengths is the ratio of their e.m.f.s — no meter calibration needed.
[Note] Balance lengths for each cell in turn

## Slide 13
CIRCUIT MODEL
Read the topology before the values
Build the model — nodes are where connections meet, branches are what lies between them
bridge network — components are branches between nodes.
Switch topology and hide the values on the live version — click here
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Topology] Nodes are the points where connections meet; branches are the components between them. The live version switches between series, parallel and bridge and can hide the values.

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A voltmeter always draws some current, so it reads slightly less than the e.m.f. of a real cell. The potentiometer at balance draws none — that is exactly why the method is used.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A voltmeter always draws some current, so it reads slightly less than the e.m.f. of a real cell. The potentiometer at balance draws none — that is exactly why the method is used.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A potentiometer wire is driven by 2.0 V. A cell balances at 40 cm of the 100 cm wire. Find its e.m.f.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A potentiometer wire is driven by 2.0 V. A cell balances at 40 cm of the 100 cm wire. Find its e.m.f.
[Answer] 0.80 V

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A potentiometer wire is driven by 2.0 V. A cell balances at 40 cm of the 100 cm wire. Find its e.m.f.
1.
E = V × ℓ/L = 2.0 × 0.40.
2.
E = 0.80 V.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E = V × ℓ/L = 2.0 × 0.40.
[Step 2] E = 0.80 V.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
0.80 V
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 0.80 V

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
Cell A balances at 40.0 cm and cell B at 62.5 cm on the same potentiometer wire. Cell A's e.m.f. is 1.02 V. Find cell B's.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Cell A balances at 40.0 cm and cell B at 62.5 cm on the same potentiometer wire. Cell A's e.m.f. is 1.02 V. Find cell B's.
[Answer] E_B ≈ 1.6 V

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
Cell A balances at 40.0 cm and cell B at 62.5 cm on the same potentiometer wire. Cell A's e.m.f. is 1.02 V. Find cell B's.
1.
E_B/E_A = ℓ_B/ℓ_A = 62.5 ÷ 40.0 = 1.5625.
2.
E_B = 1.02 × 1.5625.
3.
E_B ≈ 1.59 V.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E_B/E_A = ℓ_B/ℓ_A = 62.5 ÷ 40.0 = 1.5625.
[Step 2] E_B = 1.02 × 1.5625.
[Step 3] E_B ≈ 1.59 V.

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
E_B ≈ 1.6 V
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] E_B ≈ 1.6 V

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
Cell A of e.m.f. 1.02 V balances at 40.0 cm. Cell B balances at 62.5 cm on the same wire. Find cell B's e.m.f.
2.
E ∝ ℓ, so E(A)/E(B) = ℓ(A)/ℓ(B)
3.
1.02 / E(B) = 62.5 / 40.0
4.
E(B) = 1.02 × 40.0 / 62.5
5.
E(B) = 0.65 V
LINE 3 IS WRONG
The proportion has been written with the lengths crossed over. The first line is stated correctly and the third follows the second faithfully, which is why the slip survives to the answer. The picture is the guard: cell B balances further along the wire, so it is balancing a larger tapped voltage and must have the larger e.m.f. Any answer below 1.02 V contradicts the apparatus.
IT SHOULD SAY
1.02 / E(B) = 40.0 / 62.5, so E(B) = 1.02 × 62.5/40.0 = 1.6 V
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The proportion has been written with the lengths crossed over. The first line is stated correctly and the third follows the second faithfully, which is why the slip survives to the answer. The picture is the guard: cell B balances further along the wire, so it is balancing a larger tapped voltage and must have the larger e.m.f. Any answer below 1.02 V contradicts the apparatus.
[It should say] 1.02 / E(B) = 40.0 / 62.5, so E(B) = 1.02 × 62.5/40.0 = 1.6 V

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The contact is slid until the galvanometer reads zero. What current then flows through the unknown cell?
A The same current as flows along the wire
B Zero
C A small current, set by the cell's internal resistance
A 2.0 V driver cell across a uniform resistance wire running from A to B, with a sliding contact tapping a length ℓ from A; the unknown cell and a galvanometer form a second branch from A to that contact, and the galvanometer face carries no needle.
The live version of this figure — click here
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The contact is slid until the galvanometer reads zero. What current then flows through the unknown cell?
[Options] A The same current as flows along the wire B Zero C A small current, set by the cell's internal resistance
[Figure] A 2.0 V driver cell across a uniform resistance wire running from A to B, with a sliding contact tapping a length ℓ from A; the unknown cell and a galvanometer form a second branch from A to that contact, and the galvanometer face carries no needle.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B Zero
WHY
A galvanometer reading zero is a statement about its own branch — and in the drawing the unknown cell is in that branch, in series with it. So no charge is moving through the cell at all. No current through the cell means no volts lost across its internal resistance, which means the length ℓ tapped off the wire is balancing the cell's full e.m.f. and not its terminal p.d. Everything else about the method exists to reach this one condition.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — Zero. A galvanometer reading zero is a statement about its own branch — and in the drawing the unknown cell is in that branch, in series with it. So no charge is moving through the cell at all. No current through the cell means no volts lost across its internal resistance, which means the length ℓ tapped off the wire is balancing the cell's full e.m.f. and not its terminal p.d. Everything else about the method exists to reach this one condition.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
With a 2.0 V driver across a 1.0 m uniform wire, a cell balances at 75 cm. What is its e.m.f.?
A
0.75 V
B
1.5 V
C
2.7 V
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] With a 2.0 V driver across a 1.0 m uniform wire, a cell balances at 75 cm. What is its e.m.f.?
[Options] A 0.75 V B 1.5 V C 2.7 V

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 1.5 V
HOW TO GET THERE
E = 2.0 × 0.75/1.00 = 1.5 V — the tapped fraction of the driver voltage.
WHY THE OTHERS TEMPT
A 0.75 is the balance length as a fraction of the wire, read off as though it were a voltage. The fraction still has to be applied to the driver: 0.75 of 2.0 V.
B Correct. E = 2.0 × 0.75/1.00 = 1.5 V — the tapped fraction of the driver's voltage.
C 2.7 V is 2.0 ÷ 0.75, the fraction divided in rather than multiplied by. It is also impossible on this apparatus: the driver puts only 2.0 V across the entire wire, so no length of it could ever balance a larger e.m.f. — the galvanometer would deflect the same way at both ends and never null.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] With a 2.0 V driver across a 1.0 m uniform wire, a cell balances at 75 cm. What is its e.m.f.?
[Option by option] A: 0.75 is the balance length as a fraction of the wire, read off as though it were a voltage. The fraction still has to be applied to the driver: 0.75 of 2.0 V. B: Correct. E = 2.0 × 0.75/1.00 = 1.5 V — the tapped fraction of the driver's voltage. C: 2.7 V is 2.0 ÷ 0.75, the fraction divided in rather than multiplied by. It is also impossible on this apparatus: the driver puts only 2.0 V across the entire wire, so no length of it could ever balance a larger e.m.f. — the galvanometer would deflect the same way at both ends and never null.
[Answer] B — 1.5 V
[Why] E = 2.0 × 0.75/1.00 = 1.5 V — the tapped fraction of the driver voltage.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
With a standard cell of 1.018 V balancing at 50.9 cm, an unknown cell balances at 63.5 cm on the same wire. Find the unknown e.m.f. and explain why no wire calibration is needed.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] With a standard cell of 1.018 V balancing at 50.9 cm, an unknown cell balances at 63.5 cm on the same wire. Find the unknown e.m.f. and explain why no wire calibration is needed.
[Answer] ≈ 1.27 V — ratios eliminate every wire property

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
With a standard cell of 1.018 V balancing at 50.9 cm, an unknown cell balances at 63.5 cm on the same wire. Find the unknown e.m.f. and explain why no wire calibration is needed.
1.
E₁/E₂ = ℓ₁/ℓ₂ (same driver, same wire).
2.
E₂ = 1.018 × 63.5 ÷ 50.9 ≈ 1.27 V.
3.
The driver voltage and wire resistivity cancel in the ratio — only the two lengths matter.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E₁/E₂ = ℓ₁/ℓ₂ (same driver, same wire).
[Step 2] E₂ = 1.018 × 63.5 ÷ 50.9 ≈ 1.27 V.
[Step 3] The driver voltage and wire resistivity cancel in the ratio — only the two lengths matter.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
≈ 1.27 V — ratios eliminate every wire property
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 1.27 V — ratios eliminate every wire property

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A cell balances at 55.0 cm on open circuit and at 49.5 cm while it drives a current through a 9.0 Ω resistor. Find the cell's internal resistance.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A cell balances at 55.0 cm on open circuit and at 49.5 cm while it drives a current through a 9.0 Ω resistor. Find the cell's internal resistance.
[Answer] r = 1.0 Ω

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A cell balances at 55.0 cm on open circuit and at 49.5 cm while it drives a current through a 9.0 Ω resistor. Find the cell's internal resistance.
1.
Open circuit reads e.m.f. E ∝ 55.0; on load it reads terminal V ∝ 49.5.
2.
V/E = 49.5/55.0 = 0.90, and V = ER/(R + r) → R/(R + r) = 0.90.
3.
9.0/(9.0 + r) = 0.90 → r = 1.0 Ω.
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Open circuit reads e.m.f. E ∝ 55.0; on load it reads terminal V ∝ 49.5.
[Step 2] V/E = 49.5/55.0 = 0.90, and V = ER/(R + r) → R/(R + r) = 0.90.
[Step 3] 9.0/(9.0 + r) = 0.90 → r = 1.0 Ω.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
r = 1.0 Ω
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] r = 1.0 Ω

## Slide 32
ADVANCED CIRCUITS
Where to go next
Plenary — What to take away, what to practise next
Next
14.7 Circuit Calculus
https://giophysics.com/chapter-23/circuit-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-23/potentiometer-circuits/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-23/presentation/?lesson=potentiometer
Chapter
All Advanced Circuits lessons
https://giophysics.com/chapter-23/
PDF
Download the lesson PDF
https://giophysics.com/downloads/23-6-potentiometer-circuits.pdf
ADVANCED CIRCUITS · POTENTIOMETER CIRCUITS
GIOPHYSICS LESSON
Advanced Circuits — Potentiometer Circuits. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-23/presentation/?lesson=potentiometer moves them.