## Slide 1
14 · Advanced Circuits
Resistance that senses the world
Thermistors & LDRs
Thermistors and light-dependent resistors are semiconductor components whose resistance responds sharply to temperature and light — the sensing elements of electronic circuits.
POSITION
Lesson 3 of 7 in Advanced Circuits
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-23/thermistors-ldrs/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Advanced Circuits — Thermistors & LDRs. Lesson 3 of 7.
[Intro] Thermistors and light-dependent resistors are semiconductor components whose resistance responds sharply to temperature and light — the sensing elements of electronic circuits.
[Source] https://giophysics.com/chapter-23/thermistors-ldrs/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Non-ohmic components
https://giophysics.com/chapter-23/non-ohmic-components/
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Non-ohmic components

## Slide 3
THINK FIRST
Warm a metal wire and its resistance goes up. Warm a thermistor and its resistance goes down. One of them must be wrong — which?
Take answers before you click — the point is the commitment
Both are solid lumps of material with two wires coming out of them, sitting in the same beaker of water on the same hotplate.
THE ANSWER
Neither. In a metal the number of charge carriers is fixed, so heating only makes the lattice vibrate harder and scatter them more: resistance rises. In a semiconductor, heat frees extra carriers that were not conducting at all, and that gain beats the extra scattering many times over: resistance falls, and falls steeply. The two behaviours look contradictory because the same word, resistance, is hiding two different mechanisms.
Resistance in kilohms against temperature in degrees Celsius: a metal wire's line rises almost imperceptibly across the whole range, and a single cross marks the NTC thermistor's one measured reading at 20 °C with no line drawn through it.
The live version of this figure — click here
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Warm a metal wire and its resistance goes up. Warm a thermistor and its resistance goes down. One of them must be wrong — which? Both are solid lumps of material with two wires coming out of them, sitting in the same beaker of water on the same hotplate.
[Answer] Neither. In a metal the number of charge carriers is fixed, so heating only makes the lattice vibrate harder and scatter them more: resistance rises. In a semiconductor, heat frees extra carriers that were not conducting at all, and that gain beats the extra scattering many times over: resistance falls, and falls steeply. The two behaviours look contradictory because the same word, resistance, is hiding two different mechanisms.
[Figure] Resistance in kilohms against temperature in degrees Celsius: a metal wire's line rises almost imperceptibly across the whole range, and a single cross marks the NTC thermistor's one measured reading at 20 °C with no line drawn through it.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A thermistor's resistance changes rapidly with temperature; an LDR's resistance changes with light intensity — both are semiconductor sensors.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A thermistor's resistance changes rapidly with temperature; an LDR's resistance changes with light intensity — both are semiconductor sensors.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
An NTC thermistor might read 10 kΩ in a cold room but only a few hundred ohms in hot water.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] An NTC thermistor might read 10 kΩ in a cold room but only a few hundred ohms in hot water.

## Slide 6
THE BIG IDEA
Resistance that senses the world
Introduce the idea — The big idea and the definition
In semiconductors, energy frees extra charge carriers. Warm an NTC thermistor and its resistance falls steeply; brighten the light on an LDR and its resistance falls too. Put either into a potential divider and the changing resistance becomes a changing voltage a circuit can act on.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] In semiconductors, energy frees extra charge carriers. Warm an NTC thermistor and its resistance falls steeply; brighten the light on an LDR and its resistance falls too. Put either into a potential divider and the changing resistance becomes a changing voltage a circuit can act on.

## Slide 7
THE PHYSICS · 1 OF 3
Why opposite to metals
Build the model — The formulae, one at a time, in plain English
Metals have fixed carriers that scatter more when hot. Semiconductors gain carriers with energy — the freed-carrier effect dominates, so resistance falls.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Metals have fixed carriers that scatter more when hot. Semiconductors gain carriers with energy — the freed-carrier effect dominates, so resistance falls.

## Slide 8
THE PHYSICS · 2 OF 3
Thermistor uses
Build the model — The formulae, one at a time, in plain English
Digital thermometers, fridge and engine sensors, over-temperature protection: circuits that must respond to warmth.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Digital thermometers, fridge and engine sensors, over-temperature protection: circuits that must respond to warmth.

## Slide 9
THE PHYSICS · 3 OF 3
LDR uses
Build the model — The formulae, one at a time, in plain English
Automatic streetlights, camera exposure control, night lights: circuits that must respond to brightness.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Automatic streetlights, camera exposure control, night lights: circuits that must respond to brightness.

## Slide 10
FORMULA 1 OF 3
NTC thermistor
Build the model — The formulae, one at a time, in plain English
T ↑ ⇒ R ↓
Negative temperature coefficient
IN PLAIN ENGLISH
Heating a semiconductor frees more charge carriers, so — opposite to a metal — its resistance drops as it warms.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] NTC thermistor: T ↑ ⇒ R ↓
[In plain English] Heating a semiconductor frees more charge carriers, so — opposite to a metal — its resistance drops as it warms.
[Note] Negative temperature coefficient

## Slide 11
FORMULA 2 OF 3
LDR
Build the model — The formulae, one at a time, in plain English
light intensity ↑ ⇒ R ↓
Dark: MΩ; bright: a few hundred Ω
IN PLAIN ENGLISH
Light energy frees charge carriers in the semiconductor, so brighter light means lower resistance.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] LDR: light intensity ↑ ⇒ R ↓
[In plain English] Light energy frees charge carriers in the semiconductor, so brighter light means lower resistance.
[Note] Dark: MΩ; bright: a few hundred Ω

## Slide 12
FORMULA 3 OF 3
Sensor in a divider
Build the model — The formulae, one at a time, in plain English
Vout tracks the sensed quantity
See 23.5 Potential Dividers
IN PLAIN ENGLISH
The sensor's changing resistance re-shares the divider's voltage, turning temperature or light into an electrical signal.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Sensor in a divider: Vout tracks the sensed quantity
[In plain English] The sensor's changing resistance re-shares the divider's voltage, turning temperature or light into an electrical signal.
[Note] See 23.5 Potential Dividers

## Slide 13
CIRCUIT MODEL
Read the topology before the values
Build the model — nodes are where connections meet, branches are what lies between them
bridge network — components are branches between nodes.
Switch topology and hide the values on the live version — click here
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Topology] Nodes are the points where connections meet; branches are the components between them. The live version switches between series, parallel and bridge and can hide the values.

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
An NTC thermistor is not a metal resistor that happens to be sensitive. Metals' resistance rises with temperature; NTC semiconductors' falls — the microscopic mechanism is different.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] An NTC thermistor is not a metal resistor that happens to be sensitive. Metals' resistance rises with temperature; NTC semiconductors' falls — the microscopic mechanism is different.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
An NTC thermistor reads 8.0 kΩ at 20 °C. Roughly what happens to its resistance at 60 °C?
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] An NTC thermistor reads 8.0 kΩ at 20 °C. Roughly what happens to its resistance at 60 °C?
[Answer] It falls sharply (to roughly a tenth)

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
An NTC thermistor reads 8.0 kΩ at 20 °C. Roughly what happens to its resistance at 60 °C?
1.
NTC: resistance falls steeply as temperature rises.
2.
It drops to a small fraction — typically a few hundred ohms to ~1 kΩ.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] NTC: resistance falls steeply as temperature rises.
[Step 2] It drops to a small fraction — typically a few hundred ohms to ~1 kΩ.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
It falls sharply (to roughly a tenth)
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] It falls sharply (to roughly a tenth)

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A thermistor reads 4.0 kΩ at 20 °C and 250 Ω at 80 °C, carrying 2.0 mA at 20 °C from a fixed p.d. Describe the current change as it heats to 80 °C at the same p.d.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A thermistor reads 4.0 kΩ at 20 °C and 250 Ω at 80 °C, carrying 2.0 mA at 20 °C from a fixed p.d. Describe the current change as it heats to 80 °C at the same p.d.
[Answer] Current rises from 2.0 mA to 32 mA

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A thermistor reads 4.0 kΩ at 20 °C and 250 Ω at 80 °C, carrying 2.0 mA at 20 °C from a fixed p.d. Describe the current change as it heats to 80 °C at the same p.d.
1.
At 20 °C: V = IR = 2.0 × 10⁻³ × 4000 = 8.0 V.
2.
At 80 °C with the same 8.0 V: I = V/R = 8.0 ÷ 250.
3.
I = 32 mA — a sixteen-fold rise as resistance fell sixteen-fold.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] At 20 °C: V = IR = 2.0 × 10⁻³ × 4000 = 8.0 V.
[Step 2] At 80 °C with the same 8.0 V: I = V/R = 8.0 ÷ 250.
[Step 3] I = 32 mA — a sixteen-fold rise as resistance fell sixteen-fold.

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
Current rises from 2.0 mA to 32 mA
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Current rises from 2.0 mA to 32 mA

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A thermistor carries 1.5 mA at 6.0 V in iced water and 24 mA at the same p.d. in hot water. Find both resistances.
2.
In ice: R = V/I = 6.0 / 1.5 = 4.0 Ω
3.
In hot water: R = 6.0 / 24 = 0.25 Ω
4.
So the resistance falls from 4.0 Ω to 0.25 Ω, a sixteen-fold fall.
LINE 2 IS WRONG
The milliamps have been used as amps. The factor of sixteen at the end survives untouched, which is what makes this so hard to spot — the answer to the interesting part of the question is right, and both resistances are out by exactly the same thousand. A thermistor of 4.0 Ω would be a piece of wire; the sensible-magnitude check is that anything worth putting in a divider is kilohms.
IT SHOULD SAY
In ice: R = 6.0 / (1.5 × 10⁻³) = 4.0 kΩ, and in hot water 6.0 / (24 × 10⁻³) = 250 Ω
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 2 is wrong] The milliamps have been used as amps. The factor of sixteen at the end survives untouched, which is what makes this so hard to spot — the answer to the interesting part of the question is right, and both resistances are out by exactly the same thousand. A thermistor of 4.0 Ω would be a piece of wire; the sensible-magnitude check is that anything worth putting in a divider is kilohms.
[It should say] In ice: R = 6.0 / (1.5 × 10⁻³) = 4.0 kΩ, and in hot water 6.0 / (24 × 10⁻³) = 250 Ω

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The cross is the thermistor's 8 kΩ at 20 °C. Which way does its line leave that point as the temperature rises?
A Upward, more steeply than the metal wire's line
B Downward, and steeply — to roughly a tenth by 60 °C
C Flat — a semiconductor's resistance does not depend on temperature
Resistance in kilohms against temperature in degrees Celsius: a metal wire's line rises almost imperceptibly across the whole range, and a single cross marks the NTC thermistor's one measured reading at 20 °C with no line drawn through it.
The live version of this figure — click here
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The cross is the thermistor's 8 kΩ at 20 °C. Which way does its line leave that point as the temperature rises?
[Options] A Upward, more steeply than the metal wire's line B Downward, and steeply — to roughly a tenth by 60 °C C Flat — a semiconductor's resistance does not depend on temperature
[Figure] Resistance in kilohms against temperature in degrees Celsius: a metal wire's line rises almost imperceptibly across the whole range, and a single cross marks the NTC thermistor's one measured reading at 20 °C with no line drawn through it.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B Downward, and steeply — to roughly a tenth by 60 °C
WHY
The metal's line in the drawing is nearly flat because a few tenths of a percent per degree barely shows on a kilohm axis. An NTC thermistor is not a small version of that line, nor a steep version of it — it is the opposite sign. Heating frees more carriers, so it falls, and it falls fast enough that 8 kΩ at 20 °C is down near 800 Ω by 60 °C. That steepness is exactly why thermistors are used to sense temperature and metals are not.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — Downward, and steeply — to roughly a tenth by 60 °C. The metal's line in the drawing is nearly flat because a few tenths of a percent per degree barely shows on a kilohm axis. An NTC thermistor is not a small version of that line, nor a steep version of it — it is the opposite sign. Heating frees more carriers, so it falls, and it falls fast enough that 8 kΩ at 20 °C is down near 800 Ω by 60 °C. That steepness is exactly why thermistors are used to sense temperature and metals are not.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Darkness falls on an LDR. What happens to its resistance?
A
It falls
B
It rises
C
It is unchanged
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Darkness falls on an LDR. What happens to its resistance?
[Options] A It falls B It rises C It is unchanged

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B It rises
HOW TO GET THERE
Less light frees fewer charge carriers, so the LDR's resistance climbs — toward megohms in true darkness.
WHY THE OTHERS TEMPT
A This is the right sentence with the direction reversed: it is brighter light that lowers an LDR's resistance, because more photons free more charge carriers in the semiconductor. Darkness takes that supply of carriers away.
B Correct. Fewer photons means fewer free carriers, so the resistance climbs — towards megohms in real darkness.
C That would make an LDR useless, since its entire job is to have a resistance that reports the light level. It runs from a few hundred ohms in bright sunlight to a megohm or more in the dark, which is a change of thousands of times.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Darkness falls on an LDR. What happens to its resistance?
[Option by option] A: This is the right sentence with the direction reversed: it is brighter light that lowers an LDR's resistance, because more photons free more charge carriers in the semiconductor. Darkness takes that supply of carriers away. B: Correct. Fewer photons means fewer free carriers, so the resistance climbs — towards megohms in real darkness. C: That would make an LDR useless, since its entire job is to have a resistance that reports the light level. It runs from a few hundred ohms in bright sunlight to a megohm or more in the dark, which is a change of thousands of times.
[Answer] B — It rises
[Why] Less light frees fewer charge carriers, so the LDR's resistance climbs — toward megohms in true darkness.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A thermistor carries 1.5 mA at 6.0 V in iced water and 24 mA at the same p.d. in hot water. Find both resistances and the factor of change.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A thermistor carries 1.5 mA at 6.0 V in iced water and 24 mA at the same p.d. in hot water. Find both resistances and the factor of change.
[Answer] 4.0 kΩ → 250 Ω, a 16-fold fall

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A thermistor carries 1.5 mA at 6.0 V in iced water and 24 mA at the same p.d. in hot water. Find both resistances and the factor of change.
1.
Cold: R = 6.0 ÷ 0.0015 = 4.0 kΩ.
2.
Hot: R = 6.0 ÷ 0.024 = 250 Ω.
3.
Factor = 16× decrease — the steep response that makes thermistors useful sensors.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Cold: R = 6.0 ÷ 0.0015 = 4.0 kΩ.
[Step 2] Hot: R = 6.0 ÷ 0.024 = 250 Ω.
[Step 3] Factor = 16× decrease — the steep response that makes thermistors useful sensors.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
4.0 kΩ → 250 Ω, a 16-fold fall
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 4.0 kΩ → 250 Ω, a 16-fold fall

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
Design a dark-activated switch: an LDR (1 MΩ dark, 400 Ω bright) and fixed resistor divide 6.0 V, and the lamp circuit triggers when the output exceeds 4.0 V. Where must the output be taken, and what fixed R makes it trigger at dusk (LDR ≈ 10 kΩ)?
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Design a dark-activated switch: an LDR (1 MΩ dark, 400 Ω bright) and fixed resistor divide 6.0 V, and the lamp circuit triggers when the output exceeds 4.0 V. Where must the output be taken, and what fixed R makes it trigger at dusk (LDR ≈ 10 kΩ)?
[Answer] Output across the LDR with R = 5.0 kΩ on top

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
Design a dark-activated switch: an LDR (1 MΩ dark, 400 Ω bright) and fixed resistor divide 6.0 V, and the lamp circuit triggers when the output exceeds 4.0 V. Where must the output be taken, and what fixed R makes it trigger at dusk (LDR ≈ 10 kΩ)?
1.
Take the output across the LDR: dark → LDR resistance dominates → output high. (Across the fixed resistor it would be light-activated.)
2.
Trigger condition: 6.0 × R(LDR)/(R + R(LDR)) = 4.0 at R(LDR) = 10 kΩ.
3.
10k/(R + 10k) = 2/3 → R = 5.0 kΩ. Check dark: 6.0 × 1M/1.005M ≈ 6.0 V ✓ on; bright: 6.0 × 400/5400 ≈ 0.44 V ✓ off.
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Take the output across the LDR: dark → LDR resistance dominates → output high. (Across the fixed resistor it would be light-activated.)
[Step 2] Trigger condition: 6.0 × R(LDR)/(R + R(LDR)) = 4.0 at R(LDR) = 10 kΩ.
[Step 3] 10k/(R + 10k) = 2/3 → R = 5.0 kΩ. Check dark: 6.0 × 1M/1.005M ≈ 6.0 V ✓ on; bright: 6.0 × 400/5400 ≈ 0.44 V ✓ off.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
Output across the LDR with R = 5.0 kΩ on top
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Output across the LDR with R = 5.0 kΩ on top

## Slide 32
ADVANCED CIRCUITS
Where to go next
Plenary — What to take away, what to practise next
Next
14.4 E.m.f. & Internal Resistance
https://giophysics.com/chapter-23/emf-internal-resistance/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-23/thermistors-ldrs/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-23/presentation/?lesson=sensors
Chapter
All Advanced Circuits lessons
https://giophysics.com/chapter-23/
PDF
Download the lesson PDF
https://giophysics.com/downloads/23-3-thermistors-ldrs.pdf
ADVANCED CIRCUITS · THERMISTORS & LDRS
GIOPHYSICS LESSON
Advanced Circuits — Thermistors & LDRs. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-23/presentation/?lesson=sensors moves them.