## Slide 1
19 · Electromagnetism
Taming the sine wave
A.C., R.M.S. & Rectification
Mains electricity arrives as a sine wave. R.m.s. values give it an honest d.c. equivalent — 230 V mains actually peaks near 325 V — and diodes plus a smoothing capacitor turn the wave back into the steady d.c. electronics need.
POSITION
Lesson 7 of 7 in Electromagnetism
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-28/ac-rms-rectification/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 33
Notes: [Lesson] Electromagnetism — A.C., R.M.S. & Rectification. Lesson 7 of 7.
[Intro] Mains electricity arrives as a sine wave. R.m.s. values give it an honest d.c. equivalent — 230 V mains actually peaks near 325 V — and diodes plus a smoothing capacitor turn the wave back into the steady d.c. electronics need.
[Source] https://giophysics.com/chapter-28/ac-rms-rectification/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Generators & transformers
https://giophysics.com/chapter-28/generators-transformers/
Recall
Electric power
https://giophysics.com/chapter-22/electric-power/
Recall
Diodes
https://giophysics.com/chapter-23/non-ohmic-components/
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Generators & transformers; Electric power; Diodes

## Slide 3
THINK FIRST
UK mains is 230 volts. What is the largest voltage that ever appears between the two pins of a socket?
Take answers before you click — the point is the commitment
It says 230 V on every appliance in the house, and the number is not a rounding of anything.
THE ANSWER
About 325 V — and it gets there twice in every cycle, a hundred times a second. 230 V is the r.m.s. value, the steady d.c. voltage that would heat a kettle at the same rate; the peak is √2 times it, and the full swing between the extremes is 650 V. Insulation and component ratings have to survive the peak, not the label.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] UK mains is 230 volts. What is the largest voltage that ever appears between the two pins of a socket? It says 230 V on every appliance in the house, and the number is not a rounding of anything.
[Answer] About 325 V — and it gets there twice in every cycle, a hundred times a second. 230 V is the r.m.s. value, the steady d.c. voltage that would heat a kettle at the same rate; the peak is √2 times it, and the full swing between the extremes is 650 V. Insulation and component ratings have to survive the peak, not the label.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
The r.m.s. value of an alternating current or voltage is the steady d.c. value that would deliver the same average heating: I_rms = I₀/√2 and V_rms = V₀/√2 for sine waves.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] The r.m.s. value of an alternating current or voltage is the steady d.c. value that would deliver the same average heating: I_rms = I₀/√2 and V_rms = V₀/√2 for sine waves.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A lamp on 230 V r.m.s. mains glows exactly as brightly as on a 230 V battery — even though the mains wave is peaking at about 325 V a hundred times each second.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A lamp on 230 V r.m.s. mains glows exactly as brightly as on a 230 V battery — even though the mains wave is peaking at about 325 V a hundred times each second.

## Slide 6
THE BIG IDEA
Taming the sine wave
Introduce the idea — The big idea and the definition
Alternating current I = I₀ sin ωt averages to zero, yet it plainly heats. The honest average is the mean of I², and its square root — I_rms = I₀/√2 for a sine — is the steady d.c. current with the same heating effect.
Average power is P = I_rms·V_rms, exactly half the peak power. A single diode passes only half the wave; a four-diode bridge steers both half-cycles through the load the same way; and a reservoir capacitor smooths the bumps into near-d.c., with ripple set by how RC compares to the period.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] Alternating current I = I₀ sin ωt averages to zero, yet it plainly heats. The honest average is the mean of I², and its square root — I_rms = I₀/√2 for a sine — is the steady d.c. current with the same heating effect. Average power is P = I_rms·V_rms, exactly half the peak power. A single diode passes only half the wave; a four-diode bridge steers both half-cycles through the load the same way; and a reservoir capacitor smooths the bumps into near-d.c., with ripple set by how RC compares to the period.

## Slide 7
THE PHYSICS · 1 OF 3
Why root-mean-square
Build the model — The formulae, one at a time, in plain English
Squaring makes both half-cycles heat positively, and the mean of sin² over a cycle is exactly ½. Root it back and the effective value is peak/√2 — the d.c. value with identical heating, which is why meters and ratings quote r.m.s.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Squaring makes both half-cycles heat positively, and the mean of sin² over a cycle is exactly ½. Root it back and the effective value is peak/√2 — the d.c. value with identical heating, which is why meters and ratings quote r.m.s.

## Slide 8
THE PHYSICS · 2 OF 3
Diodes make d.c.
Build the model — The formulae, one at a time, in plain English
One diode gives half-wave rectification: positive half-cycles pass, negative ones are blocked, leaving gaps. A four-diode bridge fixes it — each half-cycle, the pair of diodes that happens to be forward-biased conducts, and both routes send current through the load in the same direction.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] One diode gives half-wave rectification: positive half-cycles pass, negative ones are blocked, leaving gaps. A four-diode bridge fixes it — each half-cycle, the pair of diodes that happens to be forward-biased conducts, and both routes send current through the load in the same direction.

## Slide 9
THE PHYSICS · 3 OF 3
Smoothing and the grid
Build the model — The formulae, one at a time, in plain English
A reservoir capacitor across the load rides over the dips: charge at the peaks, discharge slowly between them, with ripple shrinking as RC grows beyond the period. And the grid stays a.c. for one reason — only a.c. works transformers, and stepping up to hundreds of kilovolts slashes the I²R lost in the cables.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A reservoir capacitor across the load rides over the dips: charge at the peaks, discharge slowly between them, with ripple shrinking as RC grows beyond the period. And the grid stays a.c. for one reason — only a.c. works transformers, and stepping up to hundreds of kilovolts slashes the I²R lost in the cables.

## Slide 10
FORMULA 1 OF 4
Sinusoidal a.c.
Build the model — The formulae, one at a time, in plain English
I = I₀ sin ωt
ω = 2πf; mains f = 50 Hz
IN PLAIN ENGLISH
Current swings between +I₀ and −I₀, so its plain average is zero — averaging anything useful means squaring first.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Sinusoidal a.c.: I = I₀ sin ωt
[In plain English] Current swings between +I₀ and −I₀, so its plain average is zero — averaging anything useful means squaring first.
[Note] ω = 2πf; mains f = 50 Hz

## Slide 11
FORMULA 2 OF 4
R.m.s. values
Build the model — The formulae, one at a time, in plain English
I_rms = I₀/√2, V_rms = V₀/√2
Sine waves only
IN PLAIN ENGLISH
Square, average, square-root: the d.c. equivalent for heating. Mains 230 V is r.m.s. — the peak is √2 higher, about 325 V.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] R.m.s. values: I_rms = I₀/√2, V_rms = V₀/√2
[In plain English] Square, average, square-root: the d.c. equivalent for heating. Mains 230 V is r.m.s. — the peak is √2 higher, about 325 V.
[Note] Sine waves only

## Slide 12
FORMULA 3 OF 4
A.c. power
Build the model — The formulae, one at a time, in plain English
P̄ = I_rms V_rms = ½ I₀V₀
Peak power is twice the mean
IN PLAIN ENGLISH
Using r.m.s. values, the d.c. power formulas work unchanged — and the instantaneous power at the crests is exactly double the average.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] A.c. power: P̄ = I_rms V_rms = ½ I₀V₀
[In plain English] Using r.m.s. values, the d.c. power formulas work unchanged — and the instantaneous power at the crests is exactly double the average.
[Note] Peak power is twice the mean

## Slide 13
FORMULA 4 OF 4
Smoothing ripple
Build the model — The formulae, one at a time, in plain English
ΔV ≈ I(T/2)/C
Full-wave; want RC ≫ T
IN PLAIN ENGLISH
The reservoir capacitor tops up at each peak and the load drains it between peaks — a bigger capacitor or a lighter load means shallower ripple.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Smoothing ripple: ΔV ≈ I(T/2)/C
[In plain English] The reservoir capacitor tops up at each peak and the load drains it between peaks — a bigger capacitor or a lighter load means shallower ripple.
[Note] Full-wave; want RC ≫ T

## Slide 14
THE PICTURE
Both half-cycles, one way up
Drawn for this lesson
A four-diode bridge drawn as a diamond fed from an a.c. supply at the left, all four diodes pointing the same way round the loop towards the positive rail, with the two output corners taken off to a load resistor at the right and a reservoir capacitor connected across it.
The live version of this figure — click here
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A four-diode bridge drawn as a diamond fed from an a.c. supply at the left, all four diodes pointing the same way round the loop towards the positive rail, with the two output corners taken off to a load resistor at the right and a reservoir capacitor connected across it.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Mains '230 V' is not the peak — it is the r.m.s. value. The wave really swings to ±325 V, and insulation and component ratings must survive the peak, not the label.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Mains '230 V' is not the peak — it is the r.m.s. value. The wave really swings to ±325 V, and insulation and component ratings must survive the peak, not the label.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
UK mains is 230 V r.m.s. Find the peak voltage and the peak-to-peak swing.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] UK mains is 230 V r.m.s. Find the peak voltage and the peak-to-peak swing.
[Answer] Peak ≈ 325 V; peak-to-peak ≈ 650 V

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
UK mains is 230 V r.m.s. Find the peak voltage and the peak-to-peak swing.
1.
V₀ = V_rms × √2 = 230 × 1.414 ≈ 325 V.
2.
Peak-to-peak = 2V₀ ≈ 650 V — the full swing insulation must survive.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] V₀ = V_rms × √2 = 230 × 1.414 ≈ 325 V.
[Step 2] Peak-to-peak = 2V₀ ≈ 650 V — the full swing insulation must survive.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
Peak ≈ 325 V; peak-to-peak ≈ 650 V
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Peak ≈ 325 V; peak-to-peak ≈ 650 V

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A heater of resistance 23 Ω runs from 230 V r.m.s. mains. Find the mean power and the peak instantaneous power.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A heater of resistance 23 Ω runs from 230 V r.m.s. mains. Find the mean power and the peak instantaneous power.
[Answer] 2.3 kW mean; 4.6 kW peak

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A heater of resistance 23 Ω runs from 230 V r.m.s. mains. Find the mean power and the peak instantaneous power.
1.
Mean power uses r.m.s. directly: P̄ = V_rms²/R = 230² ÷ 23 = 2300 W.
2.
Peak power = V₀²/R = (325)² ÷ 23 ≈ 4600 W.
3.
Peak is exactly twice the mean — the factor of 2 that r.m.s. quietly absorbs.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Mean power uses r.m.s. directly: P̄ = V_rms²/R = 230² ÷ 23 = 2300 W.
[Step 2] Peak power = V₀²/R = (325)² ÷ 23 ≈ 4600 W.
[Step 3] Peak is exactly twice the mean — the factor of 2 that r.m.s. quietly absorbs.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
2.3 kW mean; 4.6 kW peak
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 2.3 kW mean; 4.6 kW peak

## Slide 22
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A heater of resistance 23 Ω runs from 230 V r.m.s. mains. Find the mean power it delivers.
2.
V₀ = 230 × √2 = 325 V
3.
P = V²/R
4.
P = 325² / 23 = 4.6 kW
5.
So the heater delivers a mean power of 4.6 kW.
LINE 4 IS WRONG
325 V is the peak, and a peak voltage in P = V²/R gives a peak power, not a mean one. The r.m.s. value exists precisely so that the d.c. power formulae can be used unchanged — that is what it is for — so the conversion on the first line was not only unnecessary, it was the thing that broke the calculation. Note that 4.6 kW is not junk: it is exactly twice the right answer, because mean power is always half the peak for a sine.
IT SHOULD SAY
P = 230² / 23 = 2.3 kW — and 4.6 kW is the peak instantaneous power, exactly twice it
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 4 is wrong] 325 V is the peak, and a peak voltage in P = V²/R gives a peak power, not a mean one. The r.m.s. value exists precisely so that the d.c. power formulae can be used unchanged — that is what it is for — so the conversion on the first line was not only unnecessary, it was the thing that broke the calculation. Note that 4.6 kW is not junk: it is exactly twice the right answer, because mean power is always half the peak for a sine.
[It should say] P = 230² / 23 = 2.3 kW — and 4.6 kW is the peak instantaneous power, exactly twice it

## Slide 23
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The wave on the screen peaks at 17 V. What is its average value over one whole cycle?
A 17 V
B About 11 V
C Zero
Two cycles of a sine wave plotted against time on plain axes, with dashed horizontal lines ruled the full width of the trace at +17 V and −17 V so the wave just touches each of them twice. One cycle is dimensioned along the bottom, and no level in between is marked at all.
The live version of this figure — click here
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The wave on the screen peaks at 17 V. What is its average value over one whole cycle?
[Options] A 17 V B About 11 V C Zero
[Figure] Two cycles of a sine wave plotted against time on plain axes, with dashed horizontal lines ruled the full width of the trace at +17 V and −17 V so the wave just touches each of them twice. One cycle is dimensioned along the bottom, and no level in between is marked at all.

## Slide 24
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
C Zero
WHY
The wave spends exactly as long below the axis as above it and the two halves are the same shape, so they cancel to nothing: the mean over a full cycle is exactly zero. Yet a resistor across it plainly gets hot, and gets hot in BOTH halves of the cycle, because heating goes as I² and a square is positive whichever way the current happens to be running. That is the whole reason r.m.s. exists — the honest average of an alternating quantity is the mean of its square, and the root of that mean is the number worth quoting. About 11 V is the mean of the wave with its sign stripped off, 2/π × 17; a real number, but the wrong average for heating.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] C — Zero. The wave spends exactly as long below the axis as above it and the two halves are the same shape, so they cancel to nothing: the mean over a full cycle is exactly zero. Yet a resistor across it plainly gets hot, and gets hot in BOTH halves of the cycle, because heating goes as I² and a square is positive whichever way the current happens to be running. That is the whole reason r.m.s. exists — the honest average of an alternating quantity is the mean of its square, and the root of that mean is the number worth quoting. About 11 V is the mean of the wave with its sign stripped off, 2/π × 17; a real number, but the wrong average for heating.

## Slide 25
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A signal generator outputs a sine wave of peak value 17 V. Its r.m.s. value is…
A
24 V
B
12 V
C
8.5 V
Two cycles of a sine wave plotted against time on plain axes, with dashed horizontal lines ruled the full width of the trace at +17 V and −17 V so the wave just touches each of them twice. One cycle is dimensioned along the bottom, and no level in between is marked at all.
The live version of this figure — click here
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A signal generator outputs a sine wave of peak value 17 V. Its r.m.s. value is…
[Figure] Two cycles of a sine wave plotted against time on plain axes, with dashed horizontal lines ruled the full width of the trace at +17 V and −17 V so the wave just touches each of them twice. One cycle is dimensioned along the bottom, and no level in between is marked at all.
[Options] A 24 V B 12 V C 8.5 V

## Slide 26
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 12 V
HOW TO GET THERE
V_rms = V₀/√2 = 17 ÷ 1.414 ≈ 12 V — the d.c. voltage with the same heating effect.
WHY THE OTHERS TEMPT
A 24 V is 17 × √2 — the conversion run backwards. Multiplying by √2 takes you from r.m.s. up to peak, and the peak is what was given. It is also impossible on its face: an r.m.s. value is an average of numbers none of which exceeds 17, so it cannot come out above 17.
B Correct. V_rms = V₀/√2 = 17 ÷ 1.414 ≈ 12 V — the d.c. voltage with the same heating effect.
C 8.5 V is 17/2, the natural guess if you picture the wave spending half its time up and half its time down. The factor is not a half: the mean of sin² over a cycle is a half, and it is the square root of that, 1/√2 ≈ 0.707, that scales the voltage.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A signal generator outputs a sine wave of peak value 17 V. Its r.m.s. value is…
[Option by option] A: 24 V is 17 × √2 — the conversion run backwards. Multiplying by √2 takes you from r.m.s. up to peak, and the peak is what was given. It is also impossible on its face: an r.m.s. value is an average of numbers none of which exceeds 17, so it cannot come out above 17. B: Correct. V_rms = V₀/√2 = 17 ÷ 1.414 ≈ 12 V — the d.c. voltage with the same heating effect. C: 8.5 V is 17/2, the natural guess if you picture the wave spending half its time up and half its time down. The factor is not a half: the mean of sin² over a cycle is a half, and it is the square root of that, 1/√2 ≈ 0.707, that scales the voltage.
[Answer] B — 12 V
[Why] V_rms = V₀/√2 = 17 ÷ 1.414 ≈ 12 V — the d.c. voltage with the same heating effect.
[Reveal] One click for the answer, then one for the reason.

## Slide 27
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A full-wave rectified 50 Hz supply of about 12 V feeds a 100 Ω load with a 470 µF reservoir capacitor. Estimate the ripple voltage.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A full-wave rectified 50 Hz supply of about 12 V feeds a 100 Ω load with a 470 µF reservoir capacitor. Estimate the ripple voltage.
[Answer] ΔV ≈ 2.6 V — swap in a bigger capacitor to shrink it

## Slide 28
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A full-wave rectified 50 Hz supply of about 12 V feeds a 100 Ω load with a 470 µF reservoir capacitor. Estimate the ripple voltage.
1.
Full-wave ripple repeats every half period: T/2 = 10 ms.
2.
Load current I ≈ V/R = 12 ÷ 100 = 0.12 A drains the capacitor between peaks.
3.
ΔV ≈ I(T/2)/C = 0.12 × 0.010 ÷ (470 × 10⁻⁶) ≈ 2.6 V.
4.
Too bumpy? Increase C (or lighten the load) so RC ≫ T and the ripple shrinks in proportion.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Full-wave ripple repeats every half period: T/2 = 10 ms.
[Step 2] Load current I ≈ V/R = 12 ÷ 100 = 0.12 A drains the capacitor between peaks.
[Step 3] ΔV ≈ I(T/2)/C = 0.12 × 0.010 ÷ (470 × 10⁻⁶) ≈ 2.6 V.
[Step 4] Too bumpy? Increase C (or lighten the load) so RC ≫ T and the ripple shrinks in proportion.

## Slide 29
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
ΔV ≈ 2.6 V — swap in a bigger capacitor to shrink it
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ΔV ≈ 2.6 V — swap in a bigger capacitor to shrink it

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A bridge rectifier is fed 12 V r.m.s. Two of its four diodes conduct at any instant, each dropping 0.7 V. Find the peak output voltage and the fraction of the peak lost in the diodes.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A bridge rectifier is fed 12 V r.m.s. Two of its four diodes conduct at any instant, each dropping 0.7 V. Find the peak output voltage and the fraction of the peak lost in the diodes.
[Answer] ≈ 15.6 V peak; about 8% lost across the two conducting diodes

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A bridge rectifier is fed 12 V r.m.s. Two of its four diodes conduct at any instant, each dropping 0.7 V. Find the peak output voltage and the fraction of the peak lost in the diodes.
1.
Input peak: V₀ = 12√2 ≈ 17.0 V.
2.
Each half-cycle the current threads two conducting diodes: total drop = 2 × 0.7 = 1.4 V.
3.
Peak output ≈ 17.0 − 1.4 = 15.6 V.
4.
Fraction lost = 1.4 ÷ 17.0 ≈ 8% — the price of full-wave rectification, versus one drop but half the cycles for a single diode.
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Input peak: V₀ = 12√2 ≈ 17.0 V.
[Step 2] Each half-cycle the current threads two conducting diodes: total drop = 2 × 0.7 = 1.4 V.
[Step 3] Peak output ≈ 17.0 − 1.4 = 15.6 V.
[Step 4] Fraction lost = 1.4 ÷ 17.0 ≈ 8% — the price of full-wave rectification, versus one drop but half the cycles for a single diode.

## Slide 32
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
≈ 15.6 V peak; about 8% lost across the two conducting diodes
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 15.6 V peak; about 8% lost across the two conducting diodes

## Slide 33
ELECTROMAGNETISM
Where to go next
Plenary — What to take away, what to practise next
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-28/ac-rms-rectification/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-28/presentation/?lesson=ac
Chapter
All Electromagnetism lessons
https://giophysics.com/chapter-28/
PDF
Download the lesson PDF
https://giophysics.com/downloads/28-7-ac-rms-rectification.pdf
ELECTROMAGNETISM · A.C., R.M.S. & RECTIFICATION
GIOPHYSICS LESSON
Electromagnetism — A.C., R.M.S. & Rectification. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
33 / 33
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-28/presentation/?lesson=ac moves them.