## Slide 1
19 · Electromagnetism
Induction runs the grid
Generators & Transformers
Spin a coil in a field and induction hands you alternating voltage — a generator. Pass that AC through paired coils on an iron core and a transformer trades voltage for current across the grid.
POSITION
Lesson 4 of 7 in Electromagnetism
PLAN
16 slides in the 45-minute core run, about 43.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-28/generators-transformers/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Electromagnetism — Generators & Transformers. Lesson 4 of 7.
[Intro] Spin a coil in a field and induction hands you alternating voltage — a generator. Pass that AC through paired coils on an iron core and a transformer trades voltage for current across the grid.
[Source] https://giophysics.com/chapter-28/generators-transformers/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Faraday's law
https://giophysics.com/chapter-28/faradays-law/
Recall
Lenz's law
https://giophysics.com/chapter-28/lenzs-law/
Recall
Electric power
https://giophysics.com/chapter-22/electric-power/
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Faraday's law; Lenz's law; Electric power

## Slide 3
THINK FIRST
You wire a transformer straight to a car battery — 12 V of good d.c., hundreds of amps available. What comes out of the secondary?
Take answers before you click — the point is the commitment
It is a perfectly sound transformer; run it from the mains and it works. And the battery can deliver far more current than a mains socket will.
THE ANSWER
Nothing — except one brief flick as you touch the wire on, and another as you lift it off. A transformer lives on shared CHANGING flux: a steady current makes a steady flux, and a steady flux induces nothing at all. The only instants anything happens are the instants when the current is changing, which is the whole reason the world's grid runs on a.c.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] You wire a transformer straight to a car battery — 12 V of good d.c., hundreds of amps available. What comes out of the secondary? It is a perfectly sound transformer; run it from the mains and it works. And the battery can deliver far more current than a mains socket will.
[Answer] Nothing — except one brief flick as you touch the wire on, and another as you lift it off. A transformer lives on shared CHANGING flux: a steady current makes a steady flux, and a steady flux induces nothing at all. The only instants anything happens are the instants when the current is changing, which is the whole reason the world's grid runs on a.c.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A generator converts rotation into alternating e.m.f. by induction; a transformer uses shared changing flux to change an alternating voltage by its turns ratio.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A generator converts rotation into alternating e.m.f. by induction; a transformer uses shared changing flux to change an alternating voltage by its turns ratio.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
Power stations generate at ~25 kV, transformers step up to 400 kV for the journey, then step town by town back down to 230 V.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] Power stations generate at ~25 kV, transformers step up to 400 kV for the journey, then step town by town back down to 230 V.

## Slide 6
THE BIG IDEA
Induction runs the grid
Introduce the idea — The big idea and the definition
A rotating coil sweeps through changing flux, inducing e.m.f. = NBAω sin(ωt): alternating, peaking when the coil lies parallel to the field, spinning faster raises both frequency and peak. Transformers exploit the same induction: alternating flux in a shared core links primary to secondary, scaling voltage by the turns ratio.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A rotating coil sweeps through changing flux, inducing e.m.f. = NBAω sin(ωt): alternating, peaking when the coil lies parallel to the field, spinning faster raises both frequency and peak. Transformers exploit the same induction: alternating flux in a shared core links primary to secondary, scaling voltage by the turns ratio.

## Slide 7
THE PHYSICS · 1 OF 3
The AC cycle
Build the model — The formulae, one at a time, in plain English
E.m.f. peaks as the coil slices field lines fastest (coil parallel to field) and crosses zero face-on. Slip rings deliver the alternating output.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] E.m.f. peaks as the coil slices field lines fastest (coil parallel to field) and crosses zero face-on. Slip rings deliver the alternating output.

## Slide 8
THE PHYSICS · 2 OF 3
Why transform at all
Build the model — The formulae, one at a time, in plain English
Cable losses are I²R. Transmitting at high voltage and low current slashes the loss — the whole reason grids run at hundreds of kilovolts.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Cable losses are I²R. Transmitting at high voltage and low current slashes the loss — the whole reason grids run at hundreds of kilovolts.

## Slide 9
THE PHYSICS · 3 OF 3
Transformer needs AC
Build the model — The formulae, one at a time, in plain English
Only changing flux links the coils. Feed a transformer DC and the secondary sits at zero (after one startup blip) while the primary overheats.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Only changing flux links the coils. Feed a transformer DC and the secondary sits at zero (after one startup blip) while the primary overheats.

## Slide 10
FORMULA 1 OF 3
Generator e.m.f.
Build the model — The formulae, one at a time, in plain English
e.m.f. = NBAω sin(ωt)
Peak: NBAω
IN PLAIN ENGLISH
Turns, field, area, and spin rate multiply into the peak voltage; the sine comes from the rotation itself.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Generator e.m.f.: e.m.f. = NBAω sin(ωt)
[In plain English] Turns, field, area, and spin rate multiply into the peak voltage; the sine comes from the rotation itself.
[Note] Peak: NBAω

## Slide 11
FORMULA 2 OF 3
Transformer ratio
Build the model — The formulae, one at a time, in plain English
Vs/Vp = Ns/Np
Ideal transformer
IN PLAIN ENGLISH
Voltage scales exactly with the turns: twice the secondary turns, twice the output voltage.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Transformer ratio: Vs/Vp = Ns/Np
[In plain English] Voltage scales exactly with the turns: twice the secondary turns, twice the output voltage.
[Note] Ideal transformer

## Slide 12
FORMULA 3 OF 3
Ideal power balance
Build the model — The formulae, one at a time, in plain English
VpIp = VsIs
Step voltage up, current steps down
IN PLAIN ENGLISH
An ideal transformer passes power through unchanged — raising voltage must lower current in the same proportion.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Ideal power balance: VpIp = VsIs
[In plain English] An ideal transformer passes power through unchanged — raising voltage must lower current in the same proportion.
[Note] Step voltage up, current steps down

## Slide 13
THE PICTURE
The a.c. generator
Drawn for this lesson
A rectangular coil mounted on a vertical axle between a north pole block on the left and a south pole block on the right, with four field arrows crossing the gap between them and a curved arrow over the top showing the coil being spun. Below the coil two slip rings with brushes carry the output down to a pair of terminals with nothing connected across them.
The live version of this figure — click here
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A rectangular coil mounted on a vertical axle between a north pole block on the left and a south pole block on the right, with four field arrows crossing the gap between them and a curved arrow over the top showing the coil being spun. Below the coil two slip rings with brushes carry the output down to a pair of terminals with nothing connected across them.

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A transformer cannot boost power — stepping voltage up steps current down. And it does nothing at all with steady DC: no change, no induction.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A transformer cannot boost power — stepping voltage up steps current down. And it does nothing at all with steady DC: no change, no induction.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A transformer has 200 primary and 1000 secondary turns. What does 12 V AC on the primary give?
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A transformer has 200 primary and 1000 secondary turns. What does 12 V AC on the primary give?
[Answer] 60 V

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A transformer has 200 primary and 1000 secondary turns. What does 12 V AC on the primary give?
1.
Vs = Vp × Ns/Np = 12 × 5.
2.
Vs = 60 V — a step-up.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Vs = Vp × Ns/Np = 12 × 5.
[Step 2] Vs = 60 V — a step-up.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
60 V
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 60 V

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A generator coil (N = 150, A = 4.0 × 10⁻² m², B = 0.30 T) spins at 50 rev/s. Find the peak e.m.f.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A generator coil (N = 150, A = 4.0 × 10⁻² m², B = 0.30 T) spins at 50 rev/s. Find the peak e.m.f.
[Answer] Peak e.m.f. ≈ 570 V

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A generator coil (N = 150, A = 4.0 × 10⁻² m², B = 0.30 T) spins at 50 rev/s. Find the peak e.m.f.
1.
ω = 2π × 50 = 314 rad/s.
2.
Peak e.m.f. = NBAω = 150 × 0.30 × 4.0 × 10⁻² × 314.
3.
≈ 565 V.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] ω = 2π × 50 = 314 rad/s.
[Step 2] Peak e.m.f. = NBAω = 150 × 0.30 × 4.0 × 10⁻² × 314.
[Step 3] ≈ 565 V.

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
Peak e.m.f. ≈ 570 V
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Peak e.m.f. ≈ 570 V

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A generator coil (N = 150, A = 4.0 × 10⁻² m², B = 0.30 T) spins at 50 rev/s. Find the peak e.m.f.
2.
peak e.m.f. = NBAω
3.
ω = 50 rad/s
4.
peak = 150 × 0.30 × 4.0 × 10⁻² × 50
5.
peak = 90 V
LINE 3 IS WRONG
Revolutions per second are not radians per second. One revolution is 2π radians, so ω = 2πf = 314 rad/s, and leaving the 2π out makes the answer 6.3 times too small. It slips through because 50 appears in the question with a per-second on it and looks ready to use. The check is that ω belongs inside sin ωt, and a sine only accepts an angle — which means radians, every time.
IT SHOULD SAY
ω = 2πf = 2π × 50 = 314 rad/s, which gives peak = 150 × 0.30 × 4.0 × 10⁻² × 314 ≈ 570 V
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] Revolutions per second are not radians per second. One revolution is 2π radians, so ω = 2πf = 314 rad/s, and leaving the 2π out makes the answer 6.3 times too small. It slips through because 50 appears in the question with a per-second on it and looks ready to use. The check is that ω belongs inside sin ωt, and a sine only accepts an angle — which means radians, every time.
[It should say] ω = 2πf = 2π × 50 = 314 rad/s, which gives peak = 150 × 0.30 × 4.0 × 10⁻² × 314 ≈ 570 V

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The coil is spun steadily between the poles. At which point in each turn is the induced e.m.f. greatest?
A When the coil is square across the field, where the flux through it is greatest
B When the coil lies edge-on along the field, where the flux through it is zero
C At 45°, halfway between those two
A rectangular coil mounted on a vertical axle between a north pole block on the left and a south pole block on the right, with four field arrows crossing the gap between them and a curved arrow over the top showing the coil being spun. Below the coil two slip rings with brushes carry the output down to a pair of terminals with nothing connected across them.
The live version of this figure — click here
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The coil is spun steadily between the poles. At which point in each turn is the induced e.m.f. greatest?
[Options] A When the coil is square across the field, where the flux through it is greatest B When the coil lies edge-on along the field, where the flux through it is zero C At 45°, halfway between those two
[Figure] A rectangular coil mounted on a vertical axle between a north pole block on the left and a south pole block on the right, with four field arrows crossing the gap between them and a curved arrow over the top showing the coil being spun. Below the coil two slip rings with brushes carry the output down to a pair of terminals with nothing connected across them.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B When the coil lies edge-on along the field, where the flux through it is zero
WHY
The e.m.f. is the rate the flux changes, not the flux. Square across the field the flux is at a maximum — and a quantity sitting at a maximum is, for that instant, not changing at all, so the e.m.f. there is zero. Lying along the field the flux is zero and passing through zero at its very fastest, because the coil is sweeping its whole face through the lines. Φ = BA cos ωt gives ε = NBAω sin ωt: the two are a quarter of a cycle apart, so the peak of one falls exactly on the zero of the other.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — When the coil lies edge-on along the field, where the flux through it is zero. The e.m.f. is the rate the flux changes, not the flux. Square across the field the flux is at a maximum — and a quantity sitting at a maximum is, for that instant, not changing at all, so the e.m.f. there is zero. Lying along the field the flux is zero and passing through zero at its very fastest, because the coil is sweeping its whole face through the lines. Φ = BA cos ωt gives ε = NBAω sin ωt: the two are a quarter of a cycle apart, so the peak of one falls exactly on the zero of the other.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A transformer has 400 primary and 20 secondary turns, fed with 230 V AC. The output is…
A
11.5 V
B
4600 V
C
230 V
A transformer on a rectangular laminated iron core: a 400-turn primary wound on the left limb and fed from a 230 V a.c. supply, and a 20-turn secondary wound on the right limb whose two leads end at open terminals with nothing across them. No wire runs from one side to the other.
The live version of this figure — click here
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A transformer has 400 primary and 20 secondary turns, fed with 230 V AC. The output is…
[Figure] A transformer on a rectangular laminated iron core: a 400-turn primary wound on the left limb and fed from a 230 V a.c. supply, and a 20-turn secondary wound on the right limb whose two leads end at open terminals with nothing across them. No wire runs from one side to the other.
[Options] A 11.5 V B 4600 V C 230 V

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
A 11.5 V
HOW TO GET THERE
Vs = Vp × Ns/Np = 230 × 20/400 = 11.5 V — a step-down for a phone charger.
WHY THE OTHERS TEMPT
A Correct. Vs = Vp × Ns/Np = 230 × 20/400 = 11.5 V — the step-down inside a phone charger.
B 4600 V is 230 × 400/20, the turns ratio upside down. Settle the direction before touching the arithmetic: the primary has more turns than the secondary, so this is a step-DOWN and the answer has to come out smaller than 230 V.
C 230 V is the answer if the core simply carries the voltage across, which is what a 1:1 transformer would do. This one is 20:1. And nothing is connected through in any case — primary and secondary share the flux in the iron and not a single wire.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A transformer has 400 primary and 20 secondary turns, fed with 230 V AC. The output is…
[Option by option] A: Correct. Vs = Vp × Ns/Np = 230 × 20/400 = 11.5 V — the step-down inside a phone charger. B: 4600 V is 230 × 400/20, the turns ratio upside down. Settle the direction before touching the arithmetic: the primary has more turns than the secondary, so this is a step-DOWN and the answer has to come out smaller than 230 V. C: 230 V is the answer if the core simply carries the voltage across, which is what a 1:1 transformer would do. This one is 20:1. And nothing is connected through in any case — primary and secondary share the flux in the iron and not a single wire.
[Answer] A — 11.5 V
[Why] Vs = Vp × Ns/Np = 230 × 20/400 = 11.5 V — a step-down for a phone charger.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
An ideal transformer steps 230 V down to 11.5 V to run a 23 W device. Find the currents in both coils and the turns ratio.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] An ideal transformer steps 230 V down to 11.5 V to run a 23 W device. Find the currents in both coils and the turns ratio.
[Answer] 2.0 A and 0.10 A; ratio 20:1

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
An ideal transformer steps 230 V down to 11.5 V to run a 23 W device. Find the currents in both coils and the turns ratio.
1.
Secondary: Is = P/Vs = 23 ÷ 11.5 = 2.0 A.
2.
Primary: Ip = P/Vp = 23 ÷ 230 = 0.10 A.
3.
Np/Ns = Vp/Vs = 20 : 1 — and Is/Ip = 20 confirms the power balance.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Secondary: Is = P/Vs = 23 ÷ 11.5 = 2.0 A.
[Step 2] Primary: Ip = P/Vp = 23 ÷ 230 = 0.10 A.
[Step 3] Np/Ns = Vp/Vs = 20 : 1 — and Is/Ip = 20 confirms the power balance.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
2.0 A and 0.10 A; ratio 20:1
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 2.0 A and 0.10 A; ratio 20:1

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A generator's coil doubles its rotation speed. What happens to the peak e.m.f., the frequency, and the peak e.m.f. per unit frequency? Sketch the two waveforms' relationship.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A generator's coil doubles its rotation speed. What happens to the peak e.m.f., the frequency, and the peak e.m.f. per unit frequency? Sketch the two waveforms' relationship.
[Answer] Peak ×2 and frequency ×2, in fixed proportion — a taller, faster sine

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A generator's coil doubles its rotation speed. What happens to the peak e.m.f., the frequency, and the peak e.m.f. per unit frequency? Sketch the two waveforms' relationship.
1.
Peak = NBAω: doubling ω doubles the peak.
2.
Frequency = ω/2π also doubles — the wave is both taller and faster.
3.
Peak/frequency stays constant (2πNBA): amplitude and frequency are locked together, which is why over-revving a generator over-volts it.
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Peak = NBAω: doubling ω doubles the peak.
[Step 2] Frequency = ω/2π also doubles — the wave is both taller and faster.
[Step 3] Peak/frequency stays constant (2πNBA): amplitude and frequency are locked together, which is why over-revving a generator over-volts it.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
Peak ×2 and frequency ×2, in fixed proportion — a taller, faster sine
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Peak ×2 and frequency ×2, in fixed proportion — a taller, faster sine

## Slide 32
ELECTROMAGNETISM
Where to go next
Plenary — What to take away, what to practise next
Next
19.5 Induction Calculus
https://giophysics.com/chapter-28/induction-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-28/generators-transformers/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-28/presentation/?lesson=generators
Chapter
All Electromagnetism lessons
https://giophysics.com/chapter-28/
PDF
Download the lesson PDF
https://giophysics.com/downloads/28-4-generators-transformers.pdf
ELECTROMAGNETISM · GENERATORS & TRANSFORMERS
GIOPHYSICS LESSON
Electromagnetism — Generators & Transformers. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-28/presentation/?lesson=generators moves them.