## Slide 1
02 · Forces
Accumulate. Locate. Balance. Integrate. Check.
Equilibrium Calculus Integration
A distributed load is many tiny forces. Integration combines them into one resultant, locates where it acts, and builds the shear and bending-moment story along a beam.
POSITION
Lesson 11 of 11 in Forces
PLAN
16 slides in the 45-minute core run, about 45 minutes of it
LESSON PAGE
https://giophysics.com/chapter-3/equilibrium-calculus-integration/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 31
Notes: [Lesson] Forces — Equilibrium Calculus Integration. Lesson 11 of 11.
[Intro] A distributed load is many tiny forces. Integration combines them into one resultant, locates where it acts, and builds the shear and bending-moment story along a beam.
[Source] https://giophysics.com/chapter-3/equilibrium-calculus-integration/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
2.10 Equilibrium Advanced
https://giophysics.com/chapter-3/equilibrium-advanced/
Recall
2.8 Moments of Force
https://giophysics.com/chapter-3/moments-of-force/
Recall
2.7 Kinematics Calculus
https://giophysics.com/chapter-2/kinematics-calculus-integration-problems/
Recall
1.7 Calculus
https://giophysics.com/chapter-1/kinematics-calculus/
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 31
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: 2.10 Equilibrium Advanced; 2.8 Moments of Force; 2.7 Kinematics Calculus; 1.7 Calculus

## Slide 3
THINK FIRST
A shelf is loaded so the books thin out steadily from a full pile at one end to nothing at the other. Where does the whole load act?
Take answers before you click — the point is the commitment
You want to put one support under it, in the one place that would balance it. The obvious answer is the middle of the shelf.
THE ANSWER
Two thirds of the way along, measured from the empty end — the centroid of the triangle the load makes, not the centre of the span. The middle is right only when the load is uniform, and this one is not. The resultant of a distributed load has to reproduce both its total force and its total moment, and only the centroid does both.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 31
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A shelf is loaded so the books thin out steadily from a full pile at one end to nothing at the other. Where does the whole load act? You want to put one support under it, in the one place that would balance it. The obvious answer is the middle of the shelf.
[Answer] Two thirds of the way along, measured from the empty end — the centroid of the triangle the load makes, not the centre of the span. The middle is right only when the load is uniform, and this one is not. The resultant of a distributed load has to reproduce both its total force and its total moment, and only the centroid does both.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Equilibrium calculus replaces a distributed load with integrals that give its total force, position, shear, and bending moment.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Equilibrium calculus replaces a distributed load with integrals that give its total force, position, shear, and bending moment.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A triangular load on a beam has a resultant equal to the triangle’s area acting through the triangle’s centroid.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A triangular load on a beam has a resultant equal to the triangle’s area acting through the triangle’s centroid.

## Slide 6
THE BIG IDEA
Accumulate. Locate. Balance. Integrate. Check.
Introduce the idea — The big idea and the definition
Differentiation asks how fast a quantity changes at one position. Integration reverses that relationship and adds small contributions across an interval. Force is the negative slope of a potential-energy graph, and at an equilibrium point that slope is zero.
A definite integral is signed area: here its units are kN/m × m = kN, so the area represents a force. Load intensity integrates with sign into shear force, dV/dx = −w, and integrating again gives bending moment, dM/dx = V. The resultant that replaces a continuous load has the same total force and the same moment as the original distribution.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 31
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] Differentiation asks how fast a quantity changes at one position. Integration reverses that relationship and adds small contributions across an interval. Force is the negative slope of a potential-energy graph, and at an equilibrium point that slope is zero. A definite integral is signed area: here its units are kN/m × m = kN, so the area represents a force. Load intensity integrates with sign into shear force, dV/dx = −w, and integrating again gives bending moment, dM/dx = V. The resultant that replaces a continuous load has the same total force and the same moment as the original distribution.

## Slide 7
THE PHYSICS · 1 OF 4
Slopes describe local change; areas accumulate a whole effect.
Build the model — The formulae, one at a time, in plain English
Differentiation asks how fast a quantity changes at one position. Integration reverses that relationship and adds small contributions across an interval.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Differentiation asks how fast a quantity changes at one position. Integration reverses that relationship and adds small contributions across an interval.

## Slide 8
THE PHYSICS · 2 OF 4
Replace a continuous load without losing its force or moment.
Build the model — The formulae, one at a time, in plain English
Choose a load shape, then change the span and peak intensity. The resultant has the same total force and the same moment as the original distribution. A uniform distributed load has w(x) = w₀, the load intensity being the same at every point.
A triangular increasing load has w(x) = w₀x/L, growing linearly from zero at A to w₀ at B. A triangular decreasing load has w(x) = w₀(1 − x/L), falling linearly from w₀ at A to zero at B.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Choose a load shape, then change the span and peak intensity. The resultant has the same total force and the same moment as the original distribution. A uniform distributed load has w(x) = w₀, the load intensity being the same at every point. A triangular increasing load has w(x) = w₀x/L, growing linearly from zero at A to w₀ at B. A triangular decreasing load has w(x) = w₀(1 − x/L), falling linearly from w₀ at A to zero at B.

## Slide 9
THE PHYSICS · 3 OF 4
Read each graph as the accumulated area of the one before it.
Build the model — The formulae, one at a time, in plain English
The plotted values use exact antiderivatives for the selected load. The narrow bars are samples of those continuous functions, not a numerical approximation to the physics. Choose axes and signs, integrate the load to find W and x̄ = ∫xw dx/W, then solve the reactions with ΣF = 0 and ΣM = 0.
Integrate twice using dV/dx = −w and dM/dx = V, and apply the boundary conditions: for simple supports, M(0) = M(L) = 0. Check the endpoints — for this beam, V(L⁻) = −Rᵦ and the final reaction closes it.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The plotted values use exact antiderivatives for the selected load. The narrow bars are samples of those continuous functions, not a numerical approximation to the physics. Choose axes and signs, integrate the load to find W and x̄ = ∫xw dx/W, then solve the reactions with ΣF = 0 and ΣM = 0. Integrate twice using dV/dx = −w and dM/dx = V, and apply the boundary conditions: for simple supports, M(0) = M(L) = 0. Check the endpoints — for this beam, V(L⁻) = −Rᵦ and the final reaction closes it.

## Slide 10
THE PHYSICS · 4 OF 4
A zero net force can be stable, unstable, or neutral.
Build the model — The formulae, one at a time, in plain English
Equilibrium occurs where dU/dx = 0, and the shape around that point tells what happens after a small displacement. For U(x) = ½kx², x = 0 is a minimum of U and a small displacement produces a restoring force toward the center: stable equilibrium. For U(x) = U₀ − ½kx², x = 0 is a maximum of U and a small displacement produces a force farther away from the center: unstable equilibrium.
For U(x) = constant, every nearby position has the same potential energy, so a displacement produces no restoring force: neutral equilibrium. A minimum has U″ > 0, a maximum has U″ < 0, and a locally flat curve has U″ = 0.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Equilibrium occurs where dU/dx = 0, and the shape around that point tells what happens after a small displacement. For U(x) = ½kx², x = 0 is a minimum of U and a small displacement produces a restoring force toward the center: stable equilibrium. For U(x) = U₀ − ½kx², x = 0 is a maximum of U and a small displacement produces a force farther away from the center: unstable equilibrium. For U(x) = constant, every nearby position has the same potential energy, so a displacement produces no restoring force: neutral equilibrium. A minimum has U″ > 0, a maximum has U″ < 0, and a locally flat curve has U″ = 0.

## Slide 11
FORMULA 1 OF 5
Derivative
Build the model — The formulae, one at a time, in plain English
F = −dU/dx
At an equilibrium point, the slope is zero
IN PLAIN ENGLISH
Force is the negative slope of a potential-energy graph.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Derivative: F = −dU/dx
[In plain English] Force is the negative slope of a potential-energy graph.
[Note] At an equilibrium point, the slope is zero

## Slide 12
FORMULA 2 OF 5
Indefinite integral
Build the model — The formulae, one at a time, in plain English
V = ∫(−w) dx + C
A boundary condition fixes the constant
IN PLAIN ENGLISH
Integration reverses differentiation, just as one known point fixes an antiderivative.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Indefinite integral: V = ∫(−w) dx + C
[In plain English] Integration reverses differentiation, just as one known point fixes an antiderivative.
[Note] A boundary condition fixes the constant

## Slide 13
FORMULA 3 OF 5
Definite integral
Build the model — The formulae, one at a time, in plain English
W = ∫₀ᴸ w(x) dx
kN/m × m = kN, so the area represents a force
IN PLAIN ENGLISH
A definite integral is signed area.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Definite integral: W = ∫₀ᴸ w(x) dx
[In plain English] A definite integral is signed area.
[Note] kN/m × m = kN, so the area represents a force

## Slide 14
FORMULA 4 OF 5
Line of action
Build the model — The formulae, one at a time, in plain English
x̄ = ∫₀ᴸ xw(x) dx ÷ W
Rₐ = W(L − x̄)/L and Rᵦ = Wx̄/L
IN PLAIN ENGLISH
The resultant has the same total force and the same moment as the original distribution.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Line of action: x̄ = ∫₀ᴸ xw(x) dx ÷ W
[In plain English] The resultant has the same total force and the same moment as the original distribution.
[Note] Rₐ = W(L − x̄)/L and Rᵦ = Wx̄/L

## Slide 15
FORMULA 5 OF 5
Linked beam relationships
Build the model — The formulae, one at a time, in plain English
dV/dx = −w · dM/dx = V
Downward load intensity is shown as positive
IN PLAIN ENGLISH
Read each graph as the accumulated area of the one before it. M is greatest where V = 0.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Linked beam relationships: dV/dx = −w · dM/dx = V
[In plain English] Read each graph as the accumulated area of the one before it. M is greatest where V = 0.
[Note] Downward load intensity is shown as positive

## Slide 16
THE PICTURE
A load that is not uniform
Drawn for this lesson
A beam on two supports under a triangular load, the arrows onto it stubby at A and full depth at B where the intensity reaches 9 kN/m, the 6.0 m span dimensioned beneath, and no resultant drawn anywhere on the page.
The live version of this figure — click here
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A beam on two supports under a triangular load, the arrows onto it stubby at A and full depth at B where the intensity reaches 9 kN/m, the 6.0 m span dimensioned beneath, and no resultant drawn anywhere on the page.

## Slide 17
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
The resultant does not always act at the middle. It acts at the centroid of the load-intensity graph. A triangle is one-third of its base from the larger end.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 31
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] The resultant does not always act at the middle. It acts at the centroid of the load-intensity graph. A triangle is one-third of its base from the larger end.

## Slide 18
WORKED EXAMPLE 1 OF 3 · RESULTANT · REACTIONS · MAXIMUM MOMENT
The question
resultant · reactions · maximum moment
Worked examples — I do, we do — one step revealed at a time
Uniform load: 4 kN/m over a 6 m beam.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Uniform load: 4 kN/m over a 6 m beam.
[Answer] W = 24 kN; Rₐ = Rᵦ = 12 kN; Mmax = 18 kN·m at x = 3 m

## Slide 19
WORKED EXAMPLE 1 OF 3 · RESULTANT · REACTIONS · MAXIMUM MOMENT · THE WORKING
How to solve it
resultant · reactions · maximum moment
Worked examples — I do, we do — one step revealed at a time
Uniform load: 4 kN/m over a 6 m beam.
1.
1 · Accumulate the load. W = ∫₀⁶ 4 dx = 24 kN.
2.
2 · Locate it. The rectangle’s centroid is at x̄ = 3 m, so symmetry gives Rₐ = Rᵦ = 12 kN.
3.
3 · Build the functions. V(x) = 12 − 4x and M(x) = 12x − 2x².
4.
4 · Find the peak. V = 0 at x = 3 m, so Mmax = 18 kN·m.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] 1 · Accumulate the load. W = ∫₀⁶ 4 dx = 24 kN.
[Step 2] 2 · Locate it. The rectangle’s centroid is at x̄ = 3 m, so symmetry gives Rₐ = Rᵦ = 12 kN.
[Step 3] 3 · Build the functions. V(x) = 12 − 4x and M(x) = 12x − 2x².
[Step 4] 4 · Find the peak. V = 0 at x = 3 m, so Mmax = 18 kN·m.

## Slide 20
WORKED EXAMPLE 1 OF 3 · RESULTANT · REACTIONS · MAXIMUM MOMENT
Answer
resultant · reactions · maximum moment
Worked examples — I do, we do — one step revealed at a time
W = 24 kN; Rₐ = Rᵦ = 12 kN; Mmax = 18 kN·m at x = 3 m
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] W = 24 kN; Rₐ = Rᵦ = 12 kN; Mmax = 18 kN·m at x = 3 m

## Slide 21
WORKED EXAMPLE 2 OF 3 · FIRST MOMENT · UNEQUAL REACTIONS
The question
first moment · unequal reactions
Worked examples — I do, we do — one step revealed at a time
Triangular load: zero at A, 9 kN/m at B over 6 m.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Triangular load: zero at A, 9 kN/m at B over 6 m.
[Answer] W = 27 kN; Rₐ = 9 kN; Rᵦ = 18 kN

## Slide 22
WORKED EXAMPLE 2 OF 3 · FIRST MOMENT · UNEQUAL REACTIONS · THE WORKING
How to solve it
first moment · unequal reactions
Worked examples — I do, we do — one step revealed at a time
Triangular load: zero at A, 9 kN/m at B over 6 m.
1.
1 · Area. W = ½(6)(9) = 27 kN.
2.
2 · First moment. x̄ = 2L/3 = 4 m from the zero end.
3.
3 · Equilibrium. Rᵦ(6) = 27(4), so Rᵦ = 18 kN and Rₐ = 9 kN.
4.
4 · Check. The larger reaction is beside the larger part of the load.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] 1 · Area. W = ½(6)(9) = 27 kN.
[Step 2] 2 · First moment. x̄ = 2L/3 = 4 m from the zero end.
[Step 3] 3 · Equilibrium. Rᵦ(6) = 27(4), so Rᵦ = 18 kN and Rₐ = 9 kN.
[Step 4] 4 · Check. The larger reaction is beside the larger part of the load.

## Slide 23
WORKED EXAMPLE 2 OF 3 · FIRST MOMENT · UNEQUAL REACTIONS
Answer
first moment · unequal reactions
Worked examples — I do, we do — one step revealed at a time
W = 27 kN; Rₐ = 9 kN; Rᵦ = 18 kN
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] W = 27 kN; Rₐ = 9 kN; Rᵦ = 18 kN

## Slide 24
WORKED EXAMPLE 3 OF 3 · DERIVATIVE · STABILITY
The question
derivative · stability
Worked examples — I do, we do — one step revealed at a time
Energy bowl: U = ½kx² with k = 50 N/m.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Energy bowl: U = ½kx² with k = 50 N/m.
[Answer] x = 0 is a stable minimum

## Slide 25
WORKED EXAMPLE 3 OF 3 · DERIVATIVE · STABILITY · THE WORKING
How to solve it
derivative · stability
Worked examples — I do, we do — one step revealed at a time
Energy bowl: U = ½kx² with k = 50 N/m.
1.
1 · Differentiate. F = −dU/dx = −kx.
2.
2 · Find equilibrium. F = 0 at x = 0.
3.
3 · Classify. U″ = k = 50 N/m > 0, so x = 0 is a stable minimum.
4.
4 · Test a displacement. At x = 0.12 m, F = −6 N: the force points back toward zero.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] 1 · Differentiate. F = −dU/dx = −kx.
[Step 2] 2 · Find equilibrium. F = 0 at x = 0.
[Step 3] 3 · Classify. U″ = k = 50 N/m > 0, so x = 0 is a stable minimum.
[Step 4] 4 · Test a displacement. At x = 0.12 m, F = −6 N: the force points back toward zero.

## Slide 26
WORKED EXAMPLE 3 OF 3 · DERIVATIVE · STABILITY
Answer
derivative · stability
Worked examples — I do, we do — one step revealed at a time
x = 0 is a stable minimum
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] x = 0 is a stable minimum

## Slide 27
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A load rises linearly from zero at A to 9 kN/m at B on a 6.0 m simply supported beam. Find the reaction at B.
2.
Total load: W = ½ × 6.0 × 9 = 27 kN
3.
The resultant acts at the centre of the span, x̄ = 3.0 m
4.
Moments about A: RB × 6.0 = 27 × 3.0
5.
RB = 13.5 kN
LINE 3 IS WRONG
The area is right and its position is not. Line 1 has already treated the load as a triangle; line 2 then places it as though it were a rectangle. It is an easy slip because a symmetric load really does act at mid-span, and most of the loads anyone meets first are symmetric. The result should look wrong on inspection: it makes the two reactions equal on a beam that is loaded almost entirely at one end.
IT SHOULD SAY
The resultant acts at the centroid of the triangle, x̄ = 2L/3 = 4.0 m, so RB × 6.0 = 27 × 4.0 and RB = 18 kN
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The area is right and its position is not. Line 1 has already treated the load as a triangle; line 2 then places it as though it were a rectangle. It is an easy slip because a symmetric load really does act at mid-span, and most of the loads anyone meets first are symmetric. The result should look wrong on inspection: it makes the two reactions equal on a beam that is loaded almost entirely at one end.
[It should say] The resultant acts at the centroid of the triangle, x̄ = 2L/3 = 4.0 m, so RB × 6.0 = 27 × 4.0 and RB = 18 kN

## Slide 28
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
A load grows linearly from zero at A to 9 kN/m at B along a 6.0 m beam. Its 27 kN resultant acts where?
A 3.0 m from A — the middle of the span
B 4.0 m from A
C 2.0 m from A
A beam on two supports under a triangular load, the arrows onto it stubby at A and full depth at B where the intensity reaches 9 kN/m, the 6.0 m span dimensioned beneath, and no resultant drawn anywhere on the page.
The live version of this figure — click here
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] A load grows linearly from zero at A to 9 kN/m at B along a 6.0 m beam. Its 27 kN resultant acts where?
[Options] A 3.0 m from A — the middle of the span B 4.0 m from A C 2.0 m from A
[Figure] A beam on two supports under a triangular load, the arrows onto it stubby at A and full depth at B where the intensity reaches 9 kN/m, the 6.0 m span dimensioned beneath, and no resultant drawn anywhere on the page.

## Slide 29
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B 4.0 m from A
WHY
x̄ = ∫xw dx / W puts the resultant at the centroid of the load-intensity graph, and this graph is a triangle. A triangle's centroid sits one third of the base from its heavy end — 2.0 m back from B, which is 4.0 m from A. 3.0 m is the answer for a uniform load, and would leave the beam short at the heavily loaded end. 2.0 m is the right one-third, measured from the wrong end.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 31
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — 4.0 m from A. x̄ = ∫xw dx / W puts the resultant at the centroid of the load-intensity graph, and this graph is a triangle. A triangle's centroid sits one third of the base from its heavy end — 2.0 m back from B, which is 4.0 m from A. 3.0 m is the answer for a uniform load, and would leave the beam short at the heavily loaded end. 2.0 m is the right one-third, measured from the wrong end.

## Slide 30
EXTENSION
No harder example in this lesson
Worked examples — I do, we do — one step revealed at a time
This lesson sets no Hard or Challenging example. The extension for a class that has finished early is the next lesson, or the practice paper questions the figures came from.
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 31
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Extension] The lesson record carries no Hard or Challenging example.

## Slide 31
FORCES
Where to go next
Plenary — What to take away, what to practise next
Next
2.12 Forces Model for Gaming
https://giophysics.com/chapter-3/forces-model-for-gaming/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-3/equilibrium-calculus-integration/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-3/presentation/?lesson=calculus
Chapter
All Forces lessons
https://giophysics.com/chapter-3/
PDF
Download the lesson PDF
https://giophysics.com/downloads/3-11-equilibrium-calculus-integration.pdf
FORCES · EQUILIBRIUM CALCULUS INTEGRATION
GIOPHYSICS LESSON
Forces — Equilibrium Calculus Integration. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 31
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-3/presentation/?lesson=calculus moves them.