## Slide 1
20 · Electricity & Magnetism
Integrate the discharge
Electricity & Magnetism Calculus
A real battery’s current falls as it drains. Calculus handles it exactly: charge is the area under the I–t graph, energy is the integral of εI dt, and a wire crossing a non-uniform field sums its force strip by strip.
POSITION
Lesson 6 of 7 in Electricity & Magnetism
PLAN
15 slides in the 45-minute core run, about 43 minutes of it
LESSON PAGE
https://giophysics.com/chapter-39/em-calculus/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Electricity & Magnetism — Electricity & Magnetism Calculus. Lesson 6 of 7.
[Intro] A real battery’s current falls as it drains. Calculus handles it exactly: charge is the area under the I–t graph, energy is the integral of εI dt, and a wire crossing a non-uniform field sums its force strip by strip.
[Source] https://giophysics.com/chapter-39/em-calculus/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Electric cells
https://giophysics.com/chapter-39/electric-cells/
Recall
Circuit calculus
https://giophysics.com/chapter-23/circuit-calculus/
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Electric cells; Circuit calculus

## Slide 3
THINK FIRST
Your phone battery is rated 4000 mA·h. Is that an amount of energy?
Take answers before you click — the point is the commitment
Everyone treats it as the size of the tank: bigger number, longer between charges, and two phones with the same rating ought to hold the same amount.
THE ANSWER
No — it is an amount of charge. Ampere-hours are coulombs in disguise: 4000 mA·h is 14 400 C. To get joules you have to multiply by the voltage each coulomb carries, E = ∫εI dt, so two cells with identical A·h ratings hold quite different energies if their plateau voltages differ.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Your phone battery is rated 4000 mA·h. Is that an amount of energy? Everyone treats it as the size of the tank: bigger number, longer between charges, and two phones with the same rating ought to hold the same amount.
[Answer] No — it is an amount of charge. Ampere-hours are coulombs in disguise: 4000 mA·h is 14 400 C. To get joules you have to multiply by the voltage each coulomb carries, E = ∫εI dt, so two cells with identical A·h ratings hold quite different energies if their plateau voltages differ.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Electricity and magnetism calculus replaces the constant-value products It, εIt and BIL with integrals, so falling currents and varying fields can be handled exactly.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Electricity and magnetism calculus replaces the constant-value products It, εIt and BIL with integrals, so falling currents and varying fields can be handled exactly.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A cell whose current decays as I = I₀e^(−t/τ) delivers a total charge of exactly I₀τ — the entire area under its discharge curve.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A cell whose current decays as I = I₀e^(−t/τ) delivers a total charge of exactly I₀τ — the entire area under its discharge curve.

## Slide 6
THE BIG IDEA
Integrate the discharge
Introduce the idea — The big idea and the definition
When a quantity changes continuously, products become integrals. Q = ∫I dt is the charge delivered — the area under the current–time curve, which is exactly what a capacity rating in ampere-hours measures.
Each element of charge carries energy dW = ε dq, so the energy drawn from a cell is E = ∫εI dt. And a wire in a non-uniform field feels F = ∫BI dL — add up B along the length.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] When a quantity changes continuously, products become integrals. Q = ∫I dt is the charge delivered — the area under the current–time curve, which is exactly what a capacity rating in ampere-hours measures. Each element of charge carries energy dW = ε dq, so the energy drawn from a cell is E = ∫εI dt. And a wire in a non-uniform field feels F = ∫BI dL — add up B along the length.

## Slide 7
THE PHYSICS · 1 OF 3
Area under the curve
Build the model — The formulae, one at a time, in plain English
A capacity of 2 A·h is literally the area under the discharge current graph with time in hours. Any curve with the same area drains the same charge — fast and brief or slow and long.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A capacity of 2 A·h is literally the area under the discharge current graph with time in hours. Any curve with the same area drains the same charge — fast and brief or slow and long.

## Slide 8
THE PHYSICS · 2 OF 3
Energy, coulomb by coulomb
Build the model — The formulae, one at a time, in plain English
Each coulomb leaves the cell carrying ε joules, so while the plateau holds, E ≈ εQ. Once the terminal voltage sags, ε dq must be integrated properly — the last coulombs carry less.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Each coulomb leaves the cell carrying ε joules, so while the plateau holds, E ≈ εQ. Once the terminal voltage sags, ε dq must be integrated properly — the last coulombs carry less.

## Slide 9
THE PHYSICS · 3 OF 3
Slicing a wire
Build the model — The formulae, one at a time, in plain English
Near a magnet the field varies along a wire. Divide the wire into elements dL, give each its local B(x)I dx of force, and integrate. If B varies linearly, using its average value is an exact shortcut.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Near a magnet the field varies along a wire. Divide the wire into elements dL, give each its local B(x)I dx of force, and integrate. If B varies linearly, using its average value is an exact shortcut.

## Slide 10
FORMULA 1 OF 4
Charge from current
Build the model — The formulae, one at a time, in plain English
Q = ∫I dt
The area under the I–t graph
IN PLAIN ENGLISH
Slice time into moments, multiply each by its current, and add — with hours on the axis this area is the ampere-hour capacity.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Charge from current: Q = ∫I dt
[In plain English] Slice time into moments, multiply each by its current, and add — with hours on the axis this area is the ampere-hour capacity.
[Note] The area under the I–t graph

## Slide 11
FORMULA 2 OF 4
Energy from a cell
Build the model — The formulae, one at a time, in plain English
E = ∫εI dt, from dW = ε dq
While ε is steady, E = εQ
IN PLAIN ENGLISH
Every small charge dq leaving the cell carries ε dq of energy — integrate over the whole discharge to total it up.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Energy from a cell: E = ∫εI dt, from dW = ε dq
[In plain English] Every small charge dq leaving the cell carries ε dq of energy — integrate over the whole discharge to total it up.
[Note] While ε is steady, E = εQ

## Slide 12
FORMULA 3 OF 4
Exponential discharge
Build the model — The formulae, one at a time, in plain English
∫₀^∞ I₀e^(−t/τ) dt = I₀τ
τ is the time constant of the decay
IN PLAIN ENGLISH
The decaying exponential’s full area is just the starting current times the time constant — an infinite tail with a finite total.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Exponential discharge: ∫₀^∞ I₀e^(−t/τ) dt = I₀τ
[In plain English] The decaying exponential’s full area is just the starting current times the time constant — an infinite tail with a finite total.
[Note] τ is the time constant of the decay

## Slide 13
FORMULA 4 OF 4
Non-uniform field
Build the model — The formulae, one at a time, in plain English
F = ∫B(x)I dx
Reduces to BIL when B is constant
IN PLAIN ENGLISH
Cut the wire into slices dx, let each feel its local B, and add the pieces — for a linear field the average value gives the same answer.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Non-uniform field: F = ∫B(x)I dx
[In plain English] Cut the wire into slices dx, let each feel its local B, and add the pieces — for a linear field the average value gives the same answer.
[Note] Reduces to BIL when B is constant

## Slide 14
THE PICTURE
An infinite tail with a finite area
Drawn for this lesson
Current against time for a cell discharging as I = 3.0e^(−t/4.0) amperes: the curve falls steeply from 3.0 A at the origin and flattens towards the time axis without ever touching it, with a dashed vertical line at t = 4.0 h marking the time constant and the region beneath the curve left unshaded and unvalued.
The live version of this figure — click here
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] Current against time for a cell discharging as I = 3.0e^(−t/4.0) amperes: the curve falls steeply from 3.0 A at the origin and flattens towards the time axis without ever touching it, with a dashed vertical line at t = 4.0 h marking the time constant and the region beneath the curve left unshaded and unvalued.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
You cannot use E = εIt with the starting current once the current is falling — that overestimates the energy. The simple product only works while I is constant; otherwise the honest answer is the integral, the area under the εI curve.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] You cannot use E = εIt with the starting current once the current is falling — that overestimates the energy. The simple product only works while I is constant; otherwise the honest answer is the integral, the area under the εI curve.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A cell supplies a constant 2.0 A for 90 minutes. Find the charge delivered in ampere-hours and in coulombs.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A cell supplies a constant 2.0 A for 90 minutes. Find the charge delivered in ampere-hours and in coulombs.
[Answer] 3.0 A·h = 10 800 C

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A cell supplies a constant 2.0 A for 90 minutes. Find the charge delivered in ampere-hours and in coulombs.
1.
Constant current: Q = It = 2.0 × 1.5 = 3.0 A·h.
2.
In coulombs: 3.0 × 3600 = 10 800 C.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Constant current: Q = It = 2.0 × 1.5 = 3.0 A·h.
[Step 2] In coulombs: 3.0 × 3600 = 10 800 C.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
3.0 A·h = 10 800 C
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 3.0 A·h = 10 800 C

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A cell’s current falls as I(t) = 4.0 − 0.50t (amperes, t in hours) until it reaches zero at t = 8.0 h. Find the total charge delivered.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A cell’s current falls as I(t) = 4.0 − 0.50t (amperes, t in hours) until it reaches zero at t = 8.0 h. Find the total charge delivered.
[Answer] 16 A·h ≈ 5.8 × 10⁴ C

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A cell’s current falls as I(t) = 4.0 − 0.50t (amperes, t in hours) until it reaches zero at t = 8.0 h. Find the total charge delivered.
1.
Q = ∫₀⁸ (4.0 − 0.50t) dt = [4.0t − 0.25t²]₀⁸.
2.
Q = 32 − 0.25 × 64 = 32 − 16 = 16 A·h.
3.
In coulombs: 16 × 3600 ≈ 5.8 × 10⁴ C.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Q = ∫₀⁸ (4.0 − 0.50t) dt = [4.0t − 0.25t²]₀⁸.
[Step 2] Q = 32 − 0.25 × 64 = 32 − 16 = 16 A·h.
[Step 3] In coulombs: 16 × 3600 ≈ 5.8 × 10⁴ C.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
16 A·h ≈ 5.8 × 10⁴ C
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 16 A·h ≈ 5.8 × 10⁴ C

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
This cell's current decays as I = I₀e^(−t/τ) and never quite reaches zero. How much charge does it deliver altogether?
A Infinitely much — the current never stops, so the total never stops growing
B I₀τ, a perfectly finite amount
C I₀τ/2, since the average current is half the starting current
Current against time for a cell discharging as I = 3.0e^(−t/4.0) amperes: the curve falls steeply from 3.0 A at the origin and flattens towards the time axis without ever touching it, with a dashed vertical line at t = 4.0 h marking the time constant and the region beneath the curve left unshaded and unvalued.
The live version of this figure — click here
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] This cell's current decays as I = I₀e^(−t/τ) and never quite reaches zero. How much charge does it deliver altogether?
[Options] A Infinitely much — the current never stops, so the total never stops growing B I₀τ, a perfectly finite amount C I₀τ/2, since the average current is half the starting current
[Figure] Current against time for a cell discharging as I = 3.0e^(−t/4.0) amperes: the curve falls steeply from 3.0 A at the origin and flattens towards the time axis without ever touching it, with a dashed vertical line at t = 4.0 h marking the time constant and the region beneath the curve left unshaded and unvalued.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B I₀τ, a perfectly finite amount
WHY
The charge is the area under the curve, and an area can be finite even when the curve runs on for ever: each successive time constant contributes only about a third of the one before it, and that shrinking sum converges. ∫₀^∞ I₀e^(−t/τ) dt = I₀τ exactly — for I₀ = 3.0 A and τ = 4.0 h, 12 A·h. The last option is the triangle rule, which is right for a straight line falling to zero and wrong for a curve that never gets there.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — I₀τ, a perfectly finite amount. The charge is the area under the curve, and an area can be finite even when the curve runs on for ever: each successive time constant contributes only about a third of the one before it, and that shrinking sum converges. ∫₀^∞ I₀e^(−t/τ) dt = I₀τ exactly — for I₀ = 3.0 A and τ = 4.0 h, 12 A·h. The last option is the triangle rule, which is right for a straight line falling to zero and wrong for a curve that never gets there.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A cell’s current falls linearly from 4.0 A to zero over 2.0 h. How much charge does it deliver?
A
8.0 A·h
B
4.0 A·h
C
2.0 A·h
Current against time as a straight line falling from 4.0 A at t = 0 to zero at t = 2.0 h, with both endpoints marked as plotted points and the triangular region between the line and the time axis labelled only "area = ?".
The live version of this figure — click here
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A cell’s current falls linearly from 4.0 A to zero over 2.0 h. How much charge does it deliver?
[Figure] Current against time as a straight line falling from 4.0 A at t = 0 to zero at t = 2.0 h, with both endpoints marked as plotted points and the triangular region between the line and the time axis labelled only "area = ?".
[Options] A 8.0 A·h B 4.0 A·h C 2.0 A·h

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 4.0 A·h
HOW TO GET THERE
Charge is the area under the I–t graph: a triangle, ½ × 4.0 × 2.0 = 4.0 A·h.
WHY THE OTHERS TEMPT
A 8.0 A·h is 4.0 × 2.0 — the whole rectangle, as though the cell had held its opening 4.0 A for the entire two hours. The graph is a line sloping down to the axis, and half that rectangle is empty space above it.
B Correct. The charge is the area under the I–t graph: a triangle, ½ × 4.0 × 2.0 = 4.0 A·h.
C 2.0 A·h is the average current, 2.0 A, written down as if it were the answer — or ½ × 4.0 with the two hours never multiplied back in. The average is right; it still has to run for two hours, and 2.0 A × 2.0 h = 4.0 A·h.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A cell’s current falls linearly from 4.0 A to zero over 2.0 h. How much charge does it deliver?
[Option by option] A: 8.0 A·h is 4.0 × 2.0 — the whole rectangle, as though the cell had held its opening 4.0 A for the entire two hours. The graph is a line sloping down to the axis, and half that rectangle is empty space above it. B: Correct. The charge is the area under the I–t graph: a triangle, ½ × 4.0 × 2.0 = 4.0 A·h. C: 2.0 A·h is the average current, 2.0 A, written down as if it were the answer — or ½ × 4.0 with the two hours never multiplied back in. The average is right; it still has to run for two hours, and 2.0 A × 2.0 h = 4.0 A·h.
[Answer] B — 4.0 A·h
[Why] Charge is the area under the I–t graph: a triangle, ½ × 4.0 × 2.0 = 4.0 A·h.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A cell discharges with I = 3.0e^(−t/4.0) A (t in hours) while holding ε = 1.5 V. Find the total charge and the total energy delivered.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A cell discharges with I = 3.0e^(−t/4.0) A (t in hours) while holding ε = 1.5 V. Find the total charge and the total energy delivered.
[Answer] Q = 12 A·h; E ≈ 65 kJ

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A cell discharges with I = 3.0e^(−t/4.0) A (t in hours) while holding ε = 1.5 V. Find the total charge and the total energy delivered.
1.
Q = ∫₀^∞ I₀e^(−t/τ) dt = I₀τ = 3.0 × 4.0 = 12 A·h = 43 200 C.
2.
With ε steady: E = εQ = 1.5 × 43 200 = 64 800 J.
3.
E ≈ 65 kJ — computed from an infinite tail with a finite area.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Q = ∫₀^∞ I₀e^(−t/τ) dt = I₀τ = 3.0 × 4.0 = 12 A·h = 43 200 C.
[Step 2] With ε steady: E = εQ = 1.5 × 43 200 = 64 800 J.
[Step 3] E ≈ 65 kJ — computed from an infinite tail with a finite area.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
Q = 12 A·h; E ≈ 65 kJ
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Q = 12 A·h; E ≈ 65 kJ

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A 0.50 m wire carrying 3.0 A crosses a field that grows linearly from B = 0.20 T at one end to 0.40 T at the other: B(x) = 0.20(1 + 2x). Find the force by integration and check with the average field.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 0.50 m wire carrying 3.0 A crosses a field that grows linearly from B = 0.20 T at one end to 0.40 T at the other: B(x) = 0.20(1 + 2x). Find the force by integration and check with the average field.
[Answer] F = 0.45 N, both ways

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A 0.50 m wire carrying 3.0 A crosses a field that grows linearly from B = 0.20 T at one end to 0.40 T at the other: B(x) = 0.20(1 + 2x). Find the force by integration and check with the average field.
1.
F = I∫₀^0.5 B(x) dx = 3.0 × 0.20 ∫₀^0.5 (1 + 2x) dx.
2.
∫₀^0.5 (1 + 2x) dx = [x + x²]₀^0.5 = 0.50 + 0.25 = 0.75, so F = 0.60 × 0.75 = 0.45 N.
3.
Check: average B = (0.20 + 0.40)/2 = 0.30 T → F = 0.30 × 3.0 × 0.50 = 0.45 N ✓ — exact because B is linear.
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] F = I∫₀^0.5 B(x) dx = 3.0 × 0.20 ∫₀^0.5 (1 + 2x) dx.
[Step 2] ∫₀^0.5 (1 + 2x) dx = [x + x²]₀^0.5 = 0.50 + 0.25 = 0.75, so F = 0.60 × 0.75 = 0.45 N.
[Step 3] Check: average B = (0.20 + 0.40)/2 = 0.30 T → F = 0.30 × 3.0 × 0.50 = 0.45 N ✓ — exact because B is linear.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
F = 0.45 N, both ways
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] F = 0.45 N, both ways

## Slide 32
ELECTRICITY & MAGNETISM
Where to go next
Plenary — What to take away, what to practise next
Next
20.7 Electrical Safety
https://giophysics.com/chapter-39/electrical-safety/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-39/em-calculus/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-39/presentation/?lesson=calculus
Chapter
All Electricity & Magnetism lessons
https://giophysics.com/chapter-39/
PDF
Download the lesson PDF
https://giophysics.com/downloads/39-6-em-calculus.pdf
ELECTRICITY & MAGNETISM · ELECTRICITY & MAGNETISM CALCULUS
GIOPHYSICS LESSON
Electricity & Magnetism — Electricity & Magnetism Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-39/presentation/?lesson=calculus moves them.