## Slide 1
22 · Thermodynamics
Why every engine must waste heat
Heat Engines & the Second Law
An engine takes heat from something hot, turns part of it into work, and must dump the rest into something cold. The second law says the waste is not bad engineering — it is physics, and Carnot computed the ceiling.
POSITION
Lesson 2 of 6 in Thermodynamics
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-41/heat-engines-second-law/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Thermodynamics — Heat Engines & the Second Law. Lesson 2 of 6.
[Intro] An engine takes heat from something hot, turns part of it into work, and must dump the rest into something cold. The second law says the waste is not bad engineering — it is physics, and Carnot computed the ceiling.
[Source] https://giophysics.com/chapter-41/heat-engines-second-law/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
The first law
https://giophysics.com/chapter-41/first-law-gas-processes/
Recall
Power & efficiency
https://giophysics.com/chapter-5/power-efficiency/
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: The first law; Power & efficiency

## Slide 3
THINK FIRST
Build an engine with no friction at all, out of perfect materials, running between a flame and a river. What is its efficiency?
Take answers before you click — the point is the commitment
Nothing rubs, nothing leaks, nothing wears. The flame holds 800 K and the river holds 300 K, and every joule you spend on engineering is spent perfectly.
THE ANSWER
62.5% at the very best, and not a scrap more. η(max) = 1 − Tc/Th = 1 − 300/800, and the missing 37.5% has to be dumped into the river. The ceiling is set by the two temperatures alone — better bearings cannot move it, because the loss is not a mechanical one.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Build an engine with no friction at all, out of perfect materials, running between a flame and a river. What is its efficiency? Nothing rubs, nothing leaks, nothing wears. The flame holds 800 K and the river holds 300 K, and every joule you spend on engineering is spent perfectly.
[Answer] 62.5% at the very best, and not a scrap more. η(max) = 1 − Tc/Th = 1 − 300/800, and the missing 37.5% has to be dumped into the river. The ceiling is set by the two temperatures alone — better bearings cannot move it, because the loss is not a mechanical one.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A heat engine is a cyclic device that converts part of a heat flow into work; its efficiency η = W/Qh can never exceed 1 − Tc/Th.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A heat engine is a cyclic device that converts part of a heat flow into work; its efficiency η = W/Qh can never exceed 1 − Tc/Th.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A power-station turbine fed with steam at 800 K and cooled by a river at 300 K can never do better than 1 − 300/800 = 62.5% — and real ones manage about 40%.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A power-station turbine fed with steam at 800 K and cooled by a river at 300 K can never do better than 1 − 300/800 = 62.5% — and real ones manage about 40%.

## Slide 6
THE BIG IDEA
Why every engine must waste heat
Introduce the idea — The big idea and the definition
A heat engine runs in a cycle: heat Qh in from a hot reservoir, work W out, waste heat Qc into a cold reservoir, with Qh = W + Qc. Its efficiency is η = W/Qh. No engine between temperatures Th and Tc — however perfect — can beat the Carnot limit η(max) = 1 − Tc/Th, and no engine at all can reach 100%.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A heat engine runs in a cycle: heat Qh in from a hot reservoir, work W out, waste heat Qc into a cold reservoir, with Qh = W + Qc. Its efficiency is η = W/Qh. No engine between temperatures Th and Tc — however perfect — can beat the Carnot limit η(max) = 1 − Tc/Th, and no engine at all can reach 100%.

## Slide 7
THE PHYSICS · 1 OF 3
Why waste is unavoidable
Build the model — The formulae, one at a time, in plain English
After the hot gas expands and pushes the piston, the cycle must compress it back. Compressing it hot would cost all the work just gained — so the gas must first be cooled, and that shed heat is the unavoidable Qc.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] After the hot gas expands and pushes the piston, the cycle must compress it back. Compressing it hot would cost all the work just gained — so the gas must first be cooled, and that shed heat is the unavoidable Qc.

## Slide 8
THE PHYSICS · 2 OF 3
Two statements, one law
Build the model — The formulae, one at a time, in plain English
Clausius: heat never flows by itself from cold to hot. Kelvin: no cyclic engine can turn heat entirely into work. Each statement implies the other — break one and you could break both.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Clausius: heat never flows by itself from cold to hot. Kelvin: no cyclic engine can turn heat entirely into work. Each statement implies the other — break one and you could break both.

## Slide 9
THE PHYSICS · 3 OF 3
Nobody beats Carnot
Build the model — The formulae, one at a time, in plain English
Suppose an engine beat the Carnot value. Couple it to a Carnot refrigerator run off its output and the pair would move heat from cold to hot with nothing else happening — exactly what the second law forbids. So the ceiling stands.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Suppose an engine beat the Carnot value. Couple it to a Carnot refrigerator run off its output and the pair would move heat from cold to hot with nothing else happening — exactly what the second law forbids. So the ceiling stands.

## Slide 10
FORMULA 1 OF 4
Energy split
Build the model — The formulae, one at a time, in plain English
Qh = W + Qc
Every joule in becomes work or waste
IN PLAIN ENGLISH
The heat drawn from the flame has exactly two destinations: useful work, or waste heat rejected to the cold side. Nothing vanishes.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Energy split: Qh = W + Qc
[In plain English] The heat drawn from the flame has exactly two destinations: useful work, or waste heat rejected to the cold side. Nothing vanishes.
[Note] Every joule in becomes work or waste

## Slide 11
FORMULA 2 OF 4
Efficiency
Build the model — The formulae, one at a time, in plain English
η = W/Qh = 1 − Qc/Qh
The fraction of input heat delivered as work
IN PLAIN ENGLISH
Efficiency asks: of the heat you paid for, what fraction came out as work? The rest, Qc, went down the cooling tower.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Efficiency: η = W/Qh = 1 − Qc/Qh
[In plain English] Efficiency asks: of the heat you paid for, what fraction came out as work? The rest, Qc, went down the cooling tower.
[Note] The fraction of input heat delivered as work

## Slide 12
FORMULA 3 OF 4
Carnot ceiling
Build the model — The formulae, one at a time, in plain English
η(max) = 1 − Tc/Th
Temperatures in kelvin — always
IN PLAIN ENGLISH
The best possible engine between two temperatures is fixed by those temperatures alone. Hotter source or colder sink is the only way up.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Carnot ceiling: η(max) = 1 − Tc/Th
[In plain English] The best possible engine between two temperatures is fixed by those temperatures alone. Hotter source or colder sink is the only way up.
[Note] Temperatures in kelvin — always

## Slide 13
FORMULA 4 OF 4
Refrigerator
Build the model — The formulae, one at a time, in plain English
COP = Qc/W
An engine run backwards; Carnot best = Tc/(Th − Tc)
IN PLAIN ENGLISH
Push work in and heat flows uphill: a fridge pumps Qc out of the cold box per W of electricity. The closer the two temperatures, the cheaper the pumping.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Refrigerator: COP = Qc/W
[In plain English] Push work in and heat flows uphill: a fridge pumps Qc out of the cold box per W of electricity. The closer the two temperatures, the cheaper the pumping.
[Note] An engine run backwards; Carnot best = Tc/(Th − Tc)

## Slide 14
THE PICTURE
The cold reservoir is not optional
Drawn for this lesson
A heat engine drawn as a circle between two blocks: a hot reservoir at 800 K above it with an arrow labelled Q(h) coming down, an arrow labelled W leaving sideways as useful work, and an arrow labelled Q(c) running down into a cold reservoir at 300 K. None of the three is given a value.
The live version of this figure — click here
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A heat engine drawn as a circle between two blocks: a hot reservoir at 800 K above it with an arrow labelled Q(h) coming down, an arrow labelled W leaving sideways as useful work, and an arrow labelled Q(c) running down into a cold reservoir at 300 K. None of the three is given a value.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A 100% efficient engine is not waiting on better lubricants. Even a frictionless, perfectly built engine must reject heat, because only the reservoir temperatures set the ceiling: η(max) = 1 − Tc/Th reaches 1 only at Tc = 0 K, which is unreachable.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A 100% efficient engine is not waiting on better lubricants. Even a frictionless, perfectly built engine must reject heat, because only the reservoir temperatures set the ceiling: η(max) = 1 − Tc/Th reaches 1 only at Tc = 0 K, which is unreachable.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
Each cycle an engine absorbs 2000 J from its hot reservoir and exhausts 1500 J to the cold one. Find the work output and the efficiency.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Each cycle an engine absorbs 2000 J from its hot reservoir and exhausts 1500 J to the cold one. Find the work output and the efficiency.
[Answer] W = 500 J; η = 25%

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
Each cycle an engine absorbs 2000 J from its hot reservoir and exhausts 1500 J to the cold one. Find the work output and the efficiency.
1.
W = Qh − Qc = 2000 − 1500 = 500 J.
2.
η = W/Qh = 500/2000 = 0.25.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] W = Qh − Qc = 2000 − 1500 = 500 J.
[Step 2] η = W/Qh = 500/2000 = 0.25.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
W = 500 J; η = 25%
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] W = 500 J; η = 25%

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A salesman offers an engine running between 500 K and 300 K at '45% efficiency'. Should you buy it?
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A salesman offers an engine running between 500 K and 300 K at '45% efficiency'. Should you buy it?
[Answer] No — 45% > the 40% Carnot limit, so the claim is impossible

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A salesman offers an engine running between 500 K and 300 K at '45% efficiency'. Should you buy it?
1.
Carnot ceiling: η(max) = 1 − Tc/Th = 1 − 300/500 = 0.40.
2.
The claim of 0.45 exceeds the maximum any engine between these temperatures can reach.
3.
No engineering trick evades the second law — the claim is false.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Carnot ceiling: η(max) = 1 − Tc/Th = 1 − 300/500 = 0.40.
[Step 2] The claim of 0.45 exceeds the maximum any engine between these temperatures can reach.
[Step 3] No engineering trick evades the second law — the claim is false.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
No — 45% > the 40% Carnot limit, so the claim is impossible
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] No — 45% > the 40% Carnot limit, so the claim is impossible

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
This engine takes Q(h) from the 800 K reservoir. Could a perfect one send all of it out as work and none down to the cold reservoir?
A Yes, if it were frictionless and perfectly built
B No — at least three eighths of it must go down to the cold reservoir
C No, but only because real bearings and seals lose a little
A heat engine drawn as a circle between two blocks: a hot reservoir at 800 K above it with an arrow labelled Q(h) coming down, an arrow labelled W leaving sideways as useful work, and an arrow labelled Q(c) running down into a cold reservoir at 300 K. None of the three is given a value.
The live version of this figure — click here
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] This engine takes Q(h) from the 800 K reservoir. Could a perfect one send all of it out as work and none down to the cold reservoir?
[Options] A Yes, if it were frictionless and perfectly built B No — at least three eighths of it must go down to the cold reservoir C No, but only because real bearings and seals lose a little
[Figure] A heat engine drawn as a circle between two blocks: a hot reservoir at 800 K above it with an arrow labelled Q(h) coming down, an arrow labelled W leaving sideways as useful work, and an arrow labelled Q(c) running down into a cold reservoir at 300 K. None of the three is given a value.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B No — at least three eighths of it must go down to the cold reservoir
WHY
The reason is in the cycle, not in the workshop. An engine has to return to its starting state to run again, which means the gas that expanded has to be compressed back — and compressing it while it is still hot would cost every joule the expansion just gained. So it must be cooled first, and the heat shed in that cooling is Q(c). It cannot be made small by better engineering: 1 − 300/800 = 0.625 caps the work at 62.5%, leaving at least 37.5% for the river.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — No — at least three eighths of it must go down to the cold reservoir. The reason is in the cycle, not in the workshop. An engine has to return to its starting state to run again, which means the gas that expanded has to be compressed back — and compressing it while it is still hot would cost every joule the expansion just gained. So it must be cooled first, and the heat shed in that cooling is Q(c). It cannot be made small by better engineering: 1 − 300/800 = 0.625 caps the work at 62.5%, leaving at least 37.5% for the river.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
An engine takes in 800 J from the hot reservoir each cycle and delivers 200 J of work. How much heat does it reject, and what is its efficiency?
A
600 J rejected; η = 25%
B
200 J rejected; η = 75%
C
800 J rejected; η = 20%
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] An engine takes in 800 J from the hot reservoir each cycle and delivers 200 J of work. How much heat does it reject, and what is its efficiency?
[Options] A 600 J rejected; η = 25% B 200 J rejected; η = 75% C 800 J rejected; η = 20%

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
A 600 J rejected; η = 25%
HOW TO GET THERE
Qc = Qh − W = 800 − 200 = 600 J, and η = W/Qh = 200/800 = 25%.
WHY THE OTHERS TEMPT
A Correct. Q(c) = Q(h) − W = 800 − 200 = 600 J, and η = W/Q(h) = 200/800 = 25%.
B This has the two outputs swapped: 200 J is the work, not the waste. The efficiency gives it away — an engine rejecting only a quarter of its input would be running at 75%, far above the Carnot ceiling for any ordinary pair of reservoirs.
C 800 J is what went in, not what came out as waste; if all of it were rejected the engine would have done no work at all. And 200/800 is 25%, not 20% — 20% would need 1000 J of input.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] An engine takes in 800 J from the hot reservoir each cycle and delivers 200 J of work. How much heat does it reject, and what is its efficiency?
[Option by option] A: Correct. Q(c) = Q(h) − W = 800 − 200 = 600 J, and η = W/Q(h) = 200/800 = 25%. B: This has the two outputs swapped: 200 J is the work, not the waste. The efficiency gives it away — an engine rejecting only a quarter of its input would be running at 75%, far above the Carnot ceiling for any ordinary pair of reservoirs. C: 800 J is what went in, not what came out as waste; if all of it were rejected the engine would have done no work at all. And 200/800 is 25%, not 20% — 20% would need 1000 J of input.
[Answer] A — 600 J rejected; η = 25%
[Why] Qc = Qh − W = 800 − 200 = 600 J, and η = W/Qh = 200/800 = 25%.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A power station delivers 1000 MW of electrical power at 40% efficiency, with steam at 800 K and river cooling at 300 K. Find the heat input rate, the waste heat rate, and the Carnot ceiling.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A power station delivers 1000 MW of electrical power at 40% efficiency, with steam at 800 K and river cooling at 300 K. Find the heat input rate, the waste heat rate, and the Carnot ceiling.
[Answer] 2500 MW in; 1500 MW wasted; ceiling 62.5%

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A power station delivers 1000 MW of electrical power at 40% efficiency, with steam at 800 K and river cooling at 300 K. Find the heat input rate, the waste heat rate, and the Carnot ceiling.
1.
Heat input: Qh rate = 1000 ÷ 0.40 = 2500 MW.
2.
Waste: Qc rate = 2500 − 1000 = 1500 MW warms the river and the sky.
3.
Ceiling: η(max) = 1 − 300/800 = 0.625 — real turbines lose the rest to friction and finite-rate heat transfer.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Heat input: Qh rate = 1000 ÷ 0.40 = 2500 MW.
[Step 2] Waste: Qc rate = 2500 − 1000 = 1500 MW warms the river and the sky.
[Step 3] Ceiling: η(max) = 1 − 300/800 = 0.625 — real turbines lose the rest to friction and finite-rate heat transfer.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
2500 MW in; 1500 MW wasted; ceiling 62.5%
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 2500 MW in; 1500 MW wasted; ceiling 62.5%

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A kitchen fridge keeps its interior at 275 K in a 295 K room. Find the best possible coefficient of performance, the minimum work to pump out 2750 J, and where that energy ends up.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A kitchen fridge keeps its interior at 275 K in a 295 K room. Find the best possible coefficient of performance, the minimum work to pump out 2750 J, and where that energy ends up.
[Answer] COP(max) ≈ 14; W(min) = 200 J; 2950 J is dumped into the room

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A kitchen fridge keeps its interior at 275 K in a 295 K room. Find the best possible coefficient of performance, the minimum work to pump out 2750 J, and where that energy ends up.
1.
Carnot COP = Tc/(Th − Tc) = 275/20 = 13.75.
2.
Minimum work: W = Qc/COP = 2750 ÷ 13.75 = 200 J.
3.
The room receives Qh = Qc + W = 2750 + 200 = 2950 J — a fridge heats the kitchen. Real fridges manage a COP nearer 3.
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Carnot COP = Tc/(Th − Tc) = 275/20 = 13.75.
[Step 2] Minimum work: W = Qc/COP = 2750 ÷ 13.75 = 200 J.
[Step 3] The room receives Qh = Qc + W = 2750 + 200 = 2950 J — a fridge heats the kitchen. Real fridges manage a COP nearer 3.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
COP(max) ≈ 14; W(min) = 200 J; 2950 J is dumped into the room
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] COP(max) ≈ 14; W(min) = 200 J; 2950 J is dumped into the room

## Slide 32
THERMODYNAMICS
Where to go next
Plenary — What to take away, what to practise next
Next
22.3 Entropy
https://giophysics.com/chapter-41/entropy/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-41/heat-engines-second-law/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-41/presentation/?lesson=engines
Chapter
All Thermodynamics lessons
https://giophysics.com/chapter-41/
PDF
Download the lesson PDF
https://giophysics.com/downloads/41-2-heat-engines-second-law.pdf
THERMODYNAMICS · HEAT ENGINES & THE SECOND LAW
GIOPHYSICS LESSON
Thermodynamics — Heat Engines & the Second Law. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-41/presentation/?lesson=engines moves them.