## Slide 1
22 · Thermodynamics
Comparing the world's fuels honestly
Energy Sources
Coal, uranium, wind, water, sunlight — every power station is an energy-conversion chain, and every chain leaks. Specific energy, capacity factor, and the Sankey diagram are the tools for comparing them without slogans.
POSITION
Lesson 5 of 6 in Thermodynamics
PLAN
15 slides in the 45-minute core run, about 43 minutes of it
LESSON PAGE
https://giophysics.com/chapter-41/energy-sources/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 33
Notes: [Lesson] Thermodynamics — Energy Sources. Lesson 5 of 6.
[Intro] Coal, uranium, wind, water, sunlight — every power station is an energy-conversion chain, and every chain leaks. Specific energy, capacity factor, and the Sankey diagram are the tools for comparing them without slogans.
[Source] https://giophysics.com/chapter-41/energy-sources/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Heat engines
https://giophysics.com/chapter-41/heat-engines-second-law/
Recall
Gravitational PE
https://giophysics.com/chapter-6/gravitational-potential-energy/
Recall
Power & efficiency
https://giophysics.com/chapter-5/power-efficiency/
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Heat engines; Gravitational PE; Power & efficiency

## Slide 3
THINK FIRST
A coal station and a nuclear station each deliver 30 MW. One burns 320 tonnes of fuel a day. What does the other burn?
Take answers before you click — the point is the commitment
Same output, same 25% conversion efficiency, same turbine hall. 320 tonnes is about 213 railway wagons arriving every single day.
THE ANSWER
About 120 grams of uranium-235 — a lump the size of a golf ball. Coal stores 32.5 MJ per kilogram; fission of U-235 releases 9 × 10⁷ MJ per kilogram, roughly a million times more. That single ratio is why submarines went nuclear and why nobody has ever built a coal-fired one.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A coal station and a nuclear station each deliver 30 MW. One burns 320 tonnes of fuel a day. What does the other burn? Same output, same 25% conversion efficiency, same turbine hall. 320 tonnes is about 213 railway wagons arriving every single day.
[Answer] About 120 grams of uranium-235 — a lump the size of a golf ball. Coal stores 32.5 MJ per kilogram; fission of U-235 releases 9 × 10⁷ MJ per kilogram, roughly a million times more. That single ratio is why submarines went nuclear and why nobody has ever built a coal-fired one.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
An energy source is compared by how much energy each kilogram or cubic metre yields, how reliably it flows, and how much survives the conversion chain from fuel to electricity.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] An energy source is compared by how much energy each kilogram or cubic metre yields, how reliably it flows, and how much survives the conversion chain from fuel to electricity.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A 30 MW coal station at 25% efficiency burns 320 tonnes of coal a day; a uranium reactor with the same output burns about 115 grams of U-235.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A 30 MW coal station at 25% efficiency burns 320 tonnes of coal a day; a uranium reactor with the same output burns about 115 grams of U-235.

## Slide 6
THE BIG IDEA
Comparing the world's fuels honestly
Introduce the idea — The big idea and the definition
Fuels are compared by specific energy (J/kg) and energy density (J/m³): uranium beats coal by a factor of a million, wind and sunlight arrive dilute but free. Every conversion stage wastes energy — the second law guarantees it — and a Sankey diagram draws the flow with arrow widths proportional to power, waste peeling away at each stage.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] Fuels are compared by specific energy (J/kg) and energy density (J/m³): uranium beats coal by a factor of a million, wind and sunlight arrive dilute but free. Every conversion stage wastes energy — the second law guarantees it — and a Sankey diagram draws the flow with arrow widths proportional to power, waste peeling away at each stage.

## Slide 7
THE PHYSICS · 1 OF 5
Primary, secondary, renewable
Build the model — The formulae, one at a time, in plain English
Primary sources (coal, oil, gas, uranium, wind, water, sunlight) are used as found; electricity is a secondary form — versatile and transportable, but only as clean as whatever generated it. Renewables replenish on human timescales; fossil fuels are ancient sunlight, finite and CO₂-emitting when burned.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Primary sources (coal, oil, gas, uranium, wind, water, sunlight) are used as found; electricity is a secondary form — versatile and transportable, but only as clean as whatever generated it. Renewables replenish on human timescales; fossil fuels are ancient sunlight, finite and CO₂-emitting when burned.

## Slide 8
THE PHYSICS · 2 OF 5
One spine, many fuels
Build the model — The formulae, one at a time, in plain English
Coal, gas and nuclear stations share the same spine: heat → steam → turbine → generator. A reactor makes its heat from fission, kept steady by neutron-absorbing control rods and a moderator that slows neutrons enough to split U-235, with a heat exchanger passing the energy to clean steam.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Coal, gas and nuclear stations share the same spine: heat → steam → turbine → generator. A reactor makes its heat from fission, kept steady by neutron-absorbing control rods and a moderator that slows neutrons enough to split U-235, with a heat exchanger passing the energy to clean steam.

## Slide 9
THE PHYSICS · 3 OF 5
Reading a Sankey diagram
Build the model — The formulae, one at a time, in plain English
Draw the energy flow left to right with arrow width proportional to power; every conversion bends some width away as waste heat. A typical coal station's 100 units of chemical energy thin to about 40 units of electricity — the diagram makes the second law visible at a glance.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Draw the energy flow left to right with arrow width proportional to power; every conversion bends some width away as waste heat. A typical coal station's 100 units of chemical energy thin to about 40 units of electricity — the diagram makes the second law visible at a glance.

## Slide 10
THE PHYSICS · 4 OF 5
The resources by name
Build the model — The formulae, one at a time, in plain English
Fossil fuels — coal, oil and gas — burn a chemical store to raise steam that drives a turbine and generator: concentrated, available on demand, cheap to run, but finite, and every kilogram burned releases carbon dioxide. Biofuels, from wood, crops and waste, do the same but are renewable, and the carbon dioxide released was pulled from the air while the plant grew. Nuclear fuel releases about a million times the energy per kilogram of coal by fission of uranium-235 and emits no carbon dioxide while running, at the price of waste that stays radioactive for thousands of years.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Fossil fuels — coal, oil and gas — burn a chemical store to raise steam that drives a turbine and generator: concentrated, available on demand, cheap to run, but finite, and every kilogram burned releases carbon dioxide. Biofuels, from wood, crops and waste, do the same but are renewable, and the carbon dioxide released was pulled from the air while the plant grew. Nuclear fuel releases about a million times the energy per kilogram of coal by fission of uranium-235 and emits no carbon dioxide while running, at the price of waste that stays radioactive for thousands of years.

## Slide 11
THE PHYSICS · 5 OF 5
Getting electricity without a fuel
Build the model — The formulae, one at a time, in plain English
Hydroelectric, wind and tidal stations all turn a turbine directly: falling water, moving air, and the rise and fall of the tide. Geothermal uses heat from radioactive decay in the Earth's interior to raise steam. Solar cells convert light straight to electricity with no turbine at all, while a solar panel simply heats water.
All of these are renewable and emit nothing while running, but except for tidal and geothermal their output depends on the weather or the time of day, so a grid built on them needs storage or a dispatchable station held in reserve. Every one of them except geothermal and tidal traces back to the Sun — including the fossil fuels, which are ancient sunlight stored by plants.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Hydroelectric, wind and tidal stations all turn a turbine directly: falling water, moving air, and the rise and fall of the tide. Geothermal uses heat from radioactive decay in the Earth's interior to raise steam. Solar cells convert light straight to electricity with no turbine at all, while a solar panel simply heats water. All of these are renewable and emit nothing while running, but except for tidal and geothermal their output depends on the weather or the time of day, so a grid built on them needs storage or a dispatchable station held in reserve. Every one of them except geothermal and tidal traces back to the Sun — including the fossil fuels, which are ancient sunlight stored by plants.

## Slide 12
FORMULA 1 OF 3
Specific energy & energy density
Build the model — The formulae, one at a time, in plain English
E(sp) = E/m, E(d) = E/V
J/kg and J/m³; coal ≈ 32.5 MJ/kg, U-235 ≈ 9 × 10⁷ MJ/kg
IN PLAIN ENGLISH
How much energy a kilogram — or a cubic metre — of fuel can give. This single number explains why submarines went nuclear and why hydrogen blimps needed to be enormous.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Specific energy & energy density: E(sp) = E/m, E(d) = E/V
[In plain English] How much energy a kilogram — or a cubic metre — of fuel can give. This single number explains why submarines went nuclear and why hydrogen blimps needed to be enormous.
[Note] J/kg and J/m³; coal ≈ 32.5 MJ/kg, U-235 ≈ 9 × 10⁷ MJ/kg

## Slide 13
FORMULA 2 OF 3
Efficiency chain
Build the model — The formulae, one at a time, in plain English
η(overall) = η₁ × η₂ × η₃ …
efficiency = useful output ÷ input, stage by stage
IN PLAIN ENGLISH
Boiler, turbine, generator: each stage keeps only its fraction, and the fractions multiply. Three stages of 90% are already down to 73%.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Efficiency chain: η(overall) = η₁ × η₂ × η₃ …
[In plain English] Boiler, turbine, generator: each stage keeps only its fraction, and the fractions multiply. Three stages of 90% are already down to 73%.
[Note] efficiency = useful output ÷ input, stage by stage

## Slide 14
FORMULA 3 OF 3
Wind & water power
Build the model — The formulae, one at a time, in plain English
P(wind) = ½ρAv³, P(hydro) = (Δm/Δt)gh
A = πr² swept by blades; h = head of water
IN PLAIN ENGLISH
Wind power grows with the cube of wind speed — twice the wind is eight times the power, and a calm day is nothing. Hydro is just falling mass: flow rate times g times height.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Wind & water power: P(wind) = ½ρAv³, P(hydro) = (Δm/Δt)gh
[In plain English] Wind power grows with the cube of wind speed — twice the wind is eight times the power, and a calm day is nothing. Hydro is just falling mass: flow rate times g times height.
[Note] A = πr² swept by blades; h = head of water

## Slide 15
THE PICTURE
The second law, to scale
Drawn for this lesson
A Sankey diagram of a coal-fired power station drawn to scale: a band of 100 units of chemical energy entering on the left, waste branches peeling away downwards at the chimney, the condenser and the generator, and 40 units of electricity leaving on the right.
The live version of this figure — click here
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A Sankey diagram of a coal-fired power station drawn to scale: a band of 100 units of chemical energy entering on the left, waste branches peeling away downwards at the chimney, the condenser and the generator, and 40 units of electricity leaving on the right.

## Slide 16
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Renewable does not mean always-on or free of trade-offs. Wind power scales with v³, so output collapses in light air; capacity factors run 20–40% and storage or backup must fill the gaps. Conversely 'waste heat' is not destroyed energy — it is energy degraded to a temperature too close to the surroundings to be useful.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Renewable does not mean always-on or free of trade-offs. Wind power scales with v³, so output collapses in light air; capacity factors run 20–40% and storage or backup must fill the gaps. Conversely 'waste heat' is not destroyed energy — it is energy degraded to a temperature too close to the surroundings to be useful.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
Coal has a specific energy of 32.5 MJ/kg. How much energy is stored in 20 kg, and what mass gives 260 MJ?
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Coal has a specific energy of 32.5 MJ/kg. How much energy is stored in 20 kg, and what mass gives 260 MJ?
[Answer] 650 MJ; 8.0 kg

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
Coal has a specific energy of 32.5 MJ/kg. How much energy is stored in 20 kg, and what mass gives 260 MJ?
1.
E = 32.5 × 20 = 650 MJ.
2.
m = 260 ÷ 32.5 = 8.0 kg.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E = 32.5 × 20 = 650 MJ.
[Step 2] m = 260 ÷ 32.5 = 8.0 kg.

## Slide 19
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
650 MJ; 8.0 kg
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 650 MJ; 8.0 kg

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A city's coal plant must deliver 30.0 MW at 25% efficiency. Find the daily coal burn (32.5 MJ/kg), and the daily U-235 burn for a nuclear plant of the same output and efficiency (9.0 × 10⁷ MJ/kg).
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A city's coal plant must deliver 30.0 MW at 25% efficiency. Find the daily coal burn (32.5 MJ/kg), and the daily U-235 burn for a nuclear plant of the same output and efficiency (9.0 × 10⁷ MJ/kg).
[Answer] ≈ 320 000 kg of coal vs ≈ 0.12 kg of U-235 per day

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A city's coal plant must deliver 30.0 MW at 25% efficiency. Find the daily coal burn (32.5 MJ/kg), and the daily U-235 burn for a nuclear plant of the same output and efficiency (9.0 × 10⁷ MJ/kg).
1.
Input power = 30.0 ÷ 0.25 = 120 MW; daily input = 120 × 86 400 ≈ 1.04 × 10⁷ MJ.
2.
Coal: 1.04 × 10⁷ ÷ 32.5 ≈ 3.2 × 10⁵ kg — 320 tonnes, about 213 rail-car loads.
3.
U-235: 1.04 × 10⁷ ÷ 9.0 × 10⁷ ≈ 0.12 kg — a lump the size of a golf ball.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Input power = 30.0 ÷ 0.25 = 120 MW; daily input = 120 × 86 400 ≈ 1.04 × 10⁷ MJ.
[Step 2] Coal: 1.04 × 10⁷ ÷ 32.5 ≈ 3.2 × 10⁵ kg — 320 tonnes, about 213 rail-car loads.
[Step 3] U-235: 1.04 × 10⁷ ÷ 9.0 × 10⁷ ≈ 0.12 kg — a lump the size of a golf ball.

## Slide 22
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
≈ 320 000 kg of coal vs ≈ 0.12 kg of U-235 per day
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 320 000 kg of coal vs ≈ 0.12 kg of U-235 per day

## Slide 23
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The wind drops from 15 m/s to 7.5 m/s. The turbine's electrical output falls to…
A Half of what it was
B A quarter of what it was
C An eighth of what it was
A three-bladed wind turbine with the circle swept by its blades drawn faint and dashed, the blade radius dimensioned at 12 m, and three arrows of equal length on the left marking a 15 m/s wind. No power figure appears anywhere on the drawing.
The live version of this figure — click here
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The wind drops from 15 m/s to 7.5 m/s. The turbine's electrical output falls to…
[Options] A Half of what it was B A quarter of what it was C An eighth of what it was
[Figure] A three-bladed wind turbine with the circle swept by its blades drawn faint and dashed, the blade radius dimensioned at 12 m, and three arrows of equal length on the left marking a 15 m/s wind. No power figure appears anywhere on the drawing.

## Slide 24
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
C An eighth of what it was
WHY
P = ½ρAv³, and the cube is not a decoration — it is two separate halvings multiplied together. Each second, half as much air arrives through the same swept circle, and each kilogram of it carries a quarter of the kinetic energy, because energy goes as v². Half times a quarter is an eighth: this turbine's 410 kW becomes about 51 kW. It is also why a wind farm's capacity factor sits at 20–40% rather than near 100%.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] C — An eighth of what it was. P = ½ρAv³, and the cube is not a decoration — it is two separate halvings multiplied together. Each second, half as much air arrives through the same swept circle, and each kilogram of it carries a quarter of the kinetic energy, because energy goes as v². Half times a quarter is an eighth: this turbine's 410 kW becomes about 51 kW. It is also why a wind farm's capacity factor sits at 20–40% rather than near 100%.

## Slide 25
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A power station delivers 500 MW of electricity at an overall efficiency of 40%. At what rate does it consume fuel energy?
A
200 MW
B
1250 MW
C
900 MW
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A power station delivers 500 MW of electricity at an overall efficiency of 40%. At what rate does it consume fuel energy?
[Options] A 200 MW B 1250 MW C 900 MW

## Slide 26
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 1250 MW
HOW TO GET THERE
efficiency = output/input, so input = 500 ÷ 0.40 = 1250 MW — of which 750 MW leaves as waste heat.
WHY THE OTHERS TEMPT
A 200 MW is 500 × 0.40 — the efficiency multiplied in instead of divided out. The input must always be bigger than the output; an input smaller than the output would be an efficiency above 100%.
B Correct. Input = output ÷ efficiency = 500 ÷ 0.40 = 1250 MW, of which 750 MW leaves as waste heat.
C 900 MW is 500 + 400, adding a '400' read straight off the 40%. Efficiency is a ratio, not an amount — it has no megawatts of its own to contribute to a sum.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A power station delivers 500 MW of electricity at an overall efficiency of 40%. At what rate does it consume fuel energy?
[Option by option] A: 200 MW is 500 × 0.40 — the efficiency multiplied in instead of divided out. The input must always be bigger than the output; an input smaller than the output would be an efficiency above 100%. B: Correct. Input = output ÷ efficiency = 500 ÷ 0.40 = 1250 MW, of which 750 MW leaves as waste heat. C: 900 MW is 500 + 400, adding a '400' read straight off the 40%. Efficiency is a ratio, not an amount — it has no megawatts of its own to contribute to a sum.
[Answer] B — 1250 MW
[Why] efficiency = output/input, so input = 500 ÷ 0.40 = 1250 MW — of which 750 MW leaves as waste heat.
[Reveal] One click for the answer, then one for the reason.

## Slide 27
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A wind turbine has 12 m blades and faces a 15 m/s wind (ρ = 1.2 kg/m³). Find the wind power through its disc, the output at 45% efficiency, and the output if the wind halves.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A wind turbine has 12 m blades and faces a 15 m/s wind (ρ = 1.2 kg/m³). Find the wind power through its disc, the output at 45% efficiency, and the output if the wind halves.
[Answer] ≈ 916 kW in the wind; ≈ 410 kW out; ≈ 51 kW in half the wind

## Slide 28
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A wind turbine has 12 m blades and faces a 15 m/s wind (ρ = 1.2 kg/m³). Find the wind power through its disc, the output at 45% efficiency, and the output if the wind halves.
1.
A = πr² = π × 12² ≈ 452 m²; P = ½ρAv³ = 0.5 × 1.2 × 452 × 15³ ≈ 9.2 × 10⁵ W.
2.
Output = 0.45 × 916 kW ≈ 410 kW.
3.
P ∝ v³: halving v divides power by 8 — output falls to about 51 kW.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] A = πr² = π × 12² ≈ 452 m²; P = ½ρAv³ = 0.5 × 1.2 × 452 × 15³ ≈ 9.2 × 10⁵ W.
[Step 2] Output = 0.45 × 916 kW ≈ 410 kW.
[Step 3] P ∝ v³: halving v divides power by 8 — output falls to about 51 kW.

## Slide 29
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
≈ 916 kW in the wind; ≈ 410 kW out; ≈ 51 kW in half the wind
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 916 kW in the wind; ≈ 410 kW out; ≈ 51 kW in half the wind

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A pumped-storage reservoir holds 2.0 × 10⁶ m³ of water 350 m above its turbines. Find the stored energy, how long it can supply 500 MW, and the energy needed to refill it at 75% round-trip efficiency.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A pumped-storage reservoir holds 2.0 × 10⁶ m³ of water 350 m above its turbines. Find the stored energy, how long it can supply 500 MW, and the energy needed to refill it at 75% round-trip efficiency.
[Answer] ≈ 6.9 TJ stored; ≈ 3.8 h at 500 MW; ≈ 9.1 TJ to refill

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A pumped-storage reservoir holds 2.0 × 10⁶ m³ of water 350 m above its turbines. Find the stored energy, how long it can supply 500 MW, and the energy needed to refill it at 75% round-trip efficiency.
1.
m = ρV = 2.0 × 10⁹ kg; E = mgh = 2.0 × 10⁹ × 9.8 × 350 ≈ 6.9 × 10¹² J.
2.
t = E/P = 6.86 × 10¹² ÷ 5.0 × 10⁸ ≈ 13 700 s ≈ 3.8 h — enough to cover an evening demand peak.
3.
Refilling costs 6.86 × 10¹² ÷ 0.75 ≈ 9.1 × 10¹² J of off-peak electricity: the reservoir is a battery, not a source.
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] m = ρV = 2.0 × 10⁹ kg; E = mgh = 2.0 × 10⁹ × 9.8 × 350 ≈ 6.9 × 10¹² J.
[Step 2] t = E/P = 6.86 × 10¹² ÷ 5.0 × 10⁸ ≈ 13 700 s ≈ 3.8 h — enough to cover an evening demand peak.
[Step 3] Refilling costs 6.86 × 10¹² ÷ 0.75 ≈ 9.1 × 10¹² J of off-peak electricity: the reservoir is a battery, not a source.

## Slide 32
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
≈ 6.9 TJ stored; ≈ 3.8 h at 500 MW; ≈ 9.1 TJ to refill
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 6.9 TJ stored; ≈ 3.8 h at 500 MW; ≈ 9.1 TJ to refill

## Slide 33
THERMODYNAMICS
Where to go next
Plenary — What to take away, what to practise next
Next
22.6 Thermodynamic Calculus
https://giophysics.com/chapter-41/thermo-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-41/energy-sources/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-41/presentation/?lesson=sources
Chapter
All Thermodynamics lessons
https://giophysics.com/chapter-41/
PDF
Download the lesson PDF
https://giophysics.com/downloads/41-5-energy-sources.pdf
THERMODYNAMICS · ENERGY SOURCES
GIOPHYSICS LESSON
Thermodynamics — Energy Sources. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
33 / 33
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-41/presentation/?lesson=sources moves them.