## Slide 1
26 · Advanced Fission & Fusion
The reactor as a differential equation
Fission & Fusion Calculus
Every headline number in nuclear engineering — reactor period, doubling time, waste inventory, why stars burn slow — falls out of two small differential equations and one exponential inside a square root. This lesson solves them properly.
POSITION
Lesson 6 of 6 in Advanced Fission & Fusion
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-51/fission-fusion-calculus/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 34
Notes: [Lesson] Advanced Fission & Fusion — Fission & Fusion Calculus. Lesson 6 of 6.
[Intro] Every headline number in nuclear engineering — reactor period, doubling time, waste inventory, why stars burn slow — falls out of two small differential equations and one exponential inside a square root. This lesson solves them properly.
[Source] https://giophysics.com/chapter-51/fission-fusion-calculus/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Atomic calculus
https://giophysics.com/chapter-46/atomic-calculus/
Recall
Chain reactions & criticality
https://giophysics.com/chapter-51/chain-reactions/
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 34
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Atomic calculus; Chain reactions & criticality

## Slide 3
THINK FIRST
A neutron generation in a reactor lasts a tenth of a second, and the reactor's period is a hundred seconds. Are those two numbers the same kind of thing?
Take answers before you click — the point is the commitment
Operators watch the period, not the generation time, and the two differ by a factor of a thousand in an ordinary reactor at a slightly supercritical k.
THE ANSWER
No, and confusing them is what makes reactors sound uncontrollable. Each generation multiplies the population by k, and near criticality k − 1 is tiny, so it takes many generations to gain a factor of e. The period T = τ/(k − 1) is the clock a control room runs on.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 34
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A neutron generation in a reactor lasts a tenth of a second, and the reactor's period is a hundred seconds. Are those two numbers the same kind of thing? Operators watch the period, not the generation time, and the two differ by a factor of a thousand in an ordinary reactor at a slightly supercritical k.
[Answer] No, and confusing them is what makes reactors sound uncontrollable. Each generation multiplies the population by k, and near criticality k − 1 is tiny, so it takes many generations to gain a factor of e. The period T = τ/(k − 1) is the clock a control room runs on.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Reactor kinetics obeys dN/dt = (k − 1)N/τ, solved by N = N₀e^((k−1)t/τ) with reactor period T = τ/(k − 1); daughter nuclides obey dN₂/dt = λ₁N₁ − λ₂N₂ (rise, peak, fall); and fusion rates scale with the tunneling exponential e^(−b/√E), which makes burning ferociously temperature-sensitive.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 34
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Reactor kinetics obeys dN/dt = (k − 1)N/τ, solved by N = N₀e^((k−1)t/τ) with reactor period T = τ/(k − 1); daughter nuclides obey dN₂/dt = λ₁N₁ − λ₂N₂ (rise, peak, fall); and fusion rates scale with the tunneling exponential e^(−b/√E), which makes burning ferociously temperature-sensitive.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
With k = 1.001 and τ = 0.1 s, the period is T = 0.1/0.001 = 100 s: power multiplies by e every 100 seconds — the single number a reactor operator watches most closely.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 34
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] With k = 1.001 and τ = 0.1 s, the period is T = 0.1/0.001 = 100 s: power multiplies by e every 100 seconds — the single number a reactor operator watches most closely.

## Slide 6
THE BIG IDEA
The reactor as a differential equation
Introduce the idea — The big idea and the definition
A reactor's neutron population obeys point kinetics: each generation multiplies the population by k and takes time τ, so dN/dt = (k − 1)N/τ. This is the exponential-growth equation; separating variables gives N = N₀e^((k−1)t/τ). The time constant T = τ/(k − 1) is the reactor period (one e-fold), and the doubling time is T₂ = T ln 2.
Because power tracks N, integrating P(t) over a burn gives the total energy released: for exponential growth, E = P₀T(e^(t/T) − 1). Radioactive daughters add a second equation: a nuclide fed by its parent and drained by its own decay obeys dN₂/dt = λ₁N₁ − λ₂N₂ — its population rises from zero, peaks exactly when production equals loss (λ₁N₁ = λ₂N₂), then decays away; chains of these equations govern every waste inventory. Finally, fusion rates hide an exponential of their own: the tunneling probability through the Coulomb barrier scales as exp(−b/√E) (the Gamow factor), and multiplied by the Maxwell factor exp(−E/kT) it produces a sharply peaked window — the Gamow peak — whose height rises so steeply with temperature that a star's core is thermostatically self-regulating.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 34
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A reactor's neutron population obeys point kinetics: each generation multiplies the population by k and takes time τ, so dN/dt = (k − 1)N/τ. This is the exponential-growth equation; separating variables gives N = N₀e^((k−1)t/τ). The time constant T = τ/(k − 1) is the reactor period (one e-fold), and the doubling time is T₂ = T ln 2. Because power tracks N, integrating P(t) over a burn gives the total energy released: for exponential growth, E = P₀T(e^(t/T) − 1). Radioactive daughters add a second equation: a nuclide fed by its parent and drained by its own decay obeys dN₂/dt = λ₁N₁ − λ₂N₂ — its population rises from zero, peaks exactly when production equals loss (λ₁N₁ = λ₂N₂), then decays away; chains of these equations govern every waste inventory. Finally, fusion rates hide an exponential of their own: the tunneling probability through the Coulomb barrier scales as exp(−b/√E) (the Gamow factor), and multiplied by the Maxwell factor exp(−E/kT) it produces a sharply peaked window — the Gamow peak — whose height rises so steeply with temperature that a star's core is thermostatically self-regulating.

## Slide 7
THE PHYSICS · 1 OF 3
Solving point kinetics
Build the model — The formulae, one at a time, in plain English
Separate: dN/N = ((k − 1)/τ)dt. Integrate: ln N = ((k − 1)/τ)t + C, and N(0) = N₀ fixes C. Exponentiate: N = N₀e^((k−1)t/τ).
For k > 1 it grows with period T = τ/(k − 1); for k < 1 the same formula decays — the algebra does not care which side of critical you are on. Setting N = 2N₀ gives the doubling time T₂ = T ln 2, and every safety margin in a control room is a statement about keeping T long.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Separate: dN/N = ((k − 1)/τ)dt. Integrate: ln N = ((k − 1)/τ)t + C, and N(0) = N₀ fixes C. Exponentiate: N = N₀e^((k−1)t/τ). For k > 1 it grows with period T = τ/(k − 1); for k < 1 the same formula decays — the algebra does not care which side of critical you are on. Setting N = 2N₀ gives the doubling time T₂ = T ln 2, and every safety margin in a control room is a statement about keeping T long.

## Slide 8
THE PHYSICS · 2 OF 3
The rise and fall of a daughter
Build the model — The formulae, one at a time, in plain English
Start with pure parent: N₂(0) = 0, so initially dN₂/dt = λ₁N₁ > 0 and the daughter grows. As N₂ accumulates its own decay term catches up; the peak sits exactly where λ₁N₁ = λ₂N₂.
Afterwards the curve falls, governed by whichever half-life is longer. In the limit λ₁ ≪ λ₂ (long-lived parent, short-lived daughter) the system settles into secular equilibrium, N₂ ≈ (λ₁/λ₂)N₁ — the daughter's activity simply mirrors the parent's, which is how radium in rock keeps radon perpetually topped up.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Start with pure parent: N₂(0) = 0, so initially dN₂/dt = λ₁N₁ > 0 and the daughter grows. As N₂ accumulates its own decay term catches up; the peak sits exactly where λ₁N₁ = λ₂N₂. Afterwards the curve falls, governed by whichever half-life is longer. In the limit λ₁ ≪ λ₂ (long-lived parent, short-lived daughter) the system settles into secular equilibrium, N₂ ≈ (λ₁/λ₂)N₁ — the daughter's activity simply mirrors the parent's, which is how radium in rock keeps radon perpetually topped up.

## Slide 9
THE PHYSICS · 3 OF 3
Why stars have thermostats
Build the model — The formulae, one at a time, in plain English
The fusion rate integrates the Maxwell distribution (falling in E) against the tunneling factor (rising in E); the product is the Gamow peak, and its area is a steep function of temperature — for the Sun's p–p chain the burn rate scales roughly as T⁴, and for the CNO cycle as T¹⁷. Compress a star's core slightly: T rises, burning surges, pressure pushes back, the core re-expands and cools. The steep exponent is the negative feedback that lets a fusion reactor made of gravity idle stably for ten billion years.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The fusion rate integrates the Maxwell distribution (falling in E) against the tunneling factor (rising in E); the product is the Gamow peak, and its area is a steep function of temperature — for the Sun's p–p chain the burn rate scales roughly as T⁴, and for the CNO cycle as T¹⁷. Compress a star's core slightly: T rises, burning surges, pressure pushes back, the core re-expands and cools. The steep exponent is the negative feedback that lets a fusion reactor made of gravity idle stably for ten billion years.

## Slide 10
FORMULA 1 OF 4
Point kinetics
Build the model — The formulae, one at a time, in plain English
dN/dt = (k − 1)N/τ
Growth ∝ population — the exponential signature
IN PLAIN ENGLISH
In time dt the population completes dt/τ generations, each multiplying by k: the gain is (k − 1)N dt/τ. The same law as radioactive decay, with the sign set by whether k is above or below 1.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Point kinetics: dN/dt = (k − 1)N/τ
[In plain English] In time dt the population completes dt/τ generations, each multiplying by k: the gain is (k − 1)N dt/τ. The same law as radioactive decay, with the sign set by whether k is above or below 1.
[Note] Growth ∝ population — the exponential signature

## Slide 11
FORMULA 2 OF 4
The solution
Build the model — The formulae, one at a time, in plain English
N = N₀e^((k−1)t/τ) · T = τ/(k−1)
T is the reactor period; T₂ = T ln 2 doubles
IN PLAIN ENGLISH
Separate, integrate, exponentiate — identical steps to the decay law. The period T is where all the engineering lives: delayed neutrons make τ big, so T stays seconds-to-minutes even when k drifts.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] The solution: N = N₀e^((k−1)t/τ) · T = τ/(k−1)
[In plain English] Separate, integrate, exponentiate — identical steps to the decay law. The period T is where all the engineering lives: delayed neutrons make τ big, so T stays seconds-to-minutes even when k drifts.
[Note] T is the reactor period; T₂ = T ln 2 doubles

## Slide 12
FORMULA 3 OF 4
Daughter equation
Build the model — The formulae, one at a time, in plain English
dN₂/dt = λ₁N₁ − λ₂N₂
Fed by the parent, drained by its own decay
IN PLAIN ENGLISH
Production minus loss. The daughter rises while the feed wins, peaks at λ₁N₁ = λ₂N₂, then follows the slower of the two clocks down — the shape of every activity curve in a waste inventory.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Daughter equation: dN₂/dt = λ₁N₁ − λ₂N₂
[In plain English] Production minus loss. The daughter rises while the feed wins, peaks at λ₁N₁ = λ₂N₂, then follows the slower of the two clocks down — the shape of every activity curve in a waste inventory.
[Note] Fed by the parent, drained by its own decay

## Slide 13
FORMULA 4 OF 4
Gamow factor
Build the model — The formulae, one at a time, in plain English
P(tunnel) ∝ e^(−b/√E)
b grows with charge product and reduced mass
IN PLAIN ENGLISH
The barrier is wider for slower particles, and the exponent punishes that as 1/√E. Multiplied by the Maxwell factor e^(−E/kT), the fusion rate becomes a narrow peak that shifts and swells dramatically as T rises.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Gamow factor: P(tunnel) ∝ e^(−b/√E)
[In plain English] The barrier is wider for slower particles, and the exponent punishes that as 1/√E. Multiplied by the Maxwell factor e^(−E/kT), the fusion rate becomes a narrow peak that shifts and swells dramatically as T rises.
[Note] b grows with charge product and reduced mass

## Slide 14
PICTURE 1 OF 2
One equation, three regimes
Drawn for this lesson
Neutron population against time, with time counted in reactor periods rather than seconds. Three curves start together at N₀: a rising exponential labelled k > 1, a flat line labelled k = 1, and a decaying exponential labelled k < 1. Dashed construction lines mark the point one period along, where the growing curve has multiplied by e.
The live version of this figure — click here
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] Neutron population against time, with time counted in reactor periods rather than seconds. Three curves start together at N₀: a rising exponential labelled k > 1, a flat line labelled k = 1, and a decaying exponential labelled k < 1. Dashed construction lines mark the point one period along, where the growing curve has multiplied by e.

## Slide 15
PICTURE 2 OF 2
The narrow window stars burn in
Drawn for this lesson
Three curves against collision energy: the Maxwell factor falling steeply from the left, the tunnelling factor rising from almost nothing on the left to the right-hand edge, and their product — drawn scaled up, as it must be — rising and falling through a narrow peak where the two overlap, around a quarter of the way along the axis.
The live version of this figure — click here
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] Three curves against collision energy: the Maxwell factor falling steeply from the left, the tunnelling factor rising from almost nothing on the left to the right-hand edge, and their product — drawn scaled up, as it must be — rising and falling through a narrow peak where the two overlap, around a quarter of the way along the axis.

## Slide 16
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
The reactor period is not the generation time. Generations take τ ≈ 0.1 s, yet a reactor at k = 1.001 has a period of 100 s — a thousand generations per e-fold.
Growth per generation is only the factor k, and near criticality k − 1 is tiny, so the population inches up over many generations. Conflating τ with T makes reactors sound uncontrollable when the entire point of delayed neutrons is that T stays humanly long while τ alone would not be.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 34
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] The reactor period is not the generation time. Generations take τ ≈ 0.1 s, yet a reactor at k = 1.001 has a period of 100 s — a thousand generations per e-fold. Growth per generation is only the factor k, and near criticality k − 1 is tiny, so the population inches up over many generations. Conflating τ with T makes reactors sound uncontrollable when the entire point of delayed neutrons is that T stays humanly long while τ alone would not be.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A reactor runs at k = 1.002 with τ = 0.1 s. Find the reactor period and the power doubling time.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A reactor runs at k = 1.002 with τ = 0.1 s. Find the reactor period and the power doubling time.
[Answer] T = 50 s; doubling time ≈ 35 s

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A reactor runs at k = 1.002 with τ = 0.1 s. Find the reactor period and the power doubling time.
1.
T = τ/(k − 1) = 0.1 ÷ 0.002 = 50 s.
2.
T₂ = T ln 2 = 50 × 0.693 ≈ 35 s.
3.
Power multiplies by e every 50 s and doubles every 35 s — brisk, but well within what control rods handle.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] T = τ/(k − 1) = 0.1 ÷ 0.002 = 50 s.
[Step 2] T₂ = T ln 2 = 50 × 0.693 ≈ 35 s.
[Step 3] Power multiplies by e every 50 s and doubles every 35 s — brisk, but well within what control rods handle.

## Slide 19
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
T = 50 s; doubling time ≈ 35 s
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] T = 50 s; doubling time ≈ 35 s

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
Starting from dN/dt = (k − 1)N/τ, derive N(t) and the doubling-time formula.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Starting from dN/dt = (k − 1)N/τ, derive N(t) and the doubling-time formula.
[Answer] N = N₀e^((k−1)t/τ); T₂ = τ ln 2/(k − 1)

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
Starting from dN/dt = (k − 1)N/τ, derive N(t) and the doubling-time formula.
1.
Separate variables: dN/N = ((k − 1)/τ)dt. Integrate: ln N = ((k − 1)/τ)t + C.
2.
N(0) = N₀ gives C = ln N₀, so N = N₀e^((k−1)t/τ).
3.
Set N = 2N₀: e^((k−1)T₂/τ) = 2, so T₂ = τ ln 2/(k − 1). The same expression with N = N₀/2 gives the halving time when k < 1 — one formula for both sides of critical.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Separate variables: dN/N = ((k − 1)/τ)dt. Integrate: ln N = ((k − 1)/τ)t + C.
[Step 2] N(0) = N₀ gives C = ln N₀, so N = N₀e^((k−1)t/τ).
[Step 3] Set N = 2N₀: e^((k−1)T₂/τ) = 2, so T₂ = τ ln 2/(k − 1). The same expression with N = N₀/2 gives the halving time when k < 1 — one formula for both sides of critical.

## Slide 22
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
N = N₀e^((k−1)t/τ); T₂ = τ ln 2/(k − 1)
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] N = N₀e^((k−1)t/τ); T₂ = τ ln 2/(k − 1)

## Slide 23
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A reactor runs at k = 1.002 with τ = 0.1 s. Find the reactor period and the doubling time.
2.
T = τ/k = 0.1 ÷ 1.002.
3.
T = 0.0998 s.
4.
T₂ = T ln 2 = 0.0998 × 0.693 ≈ 0.069 s.
5.
So the power doubles about fourteen times a second.
LINE 2 IS WRONG
The period is τ/(k − 1), not τ/k. Writing k where k − 1 belongs is the single most common error in this topic, because near criticality k is so nearly 1 that dividing by it barely changes the number and the working looks tidy. The excess k − 1 is the whole physics: with k exactly 1 the period is infinite, which is what steady power means.
IT SHOULD SAY
T = τ/(k − 1) = 0.1 ÷ 0.002 = 50 s.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 2 is wrong] The period is τ/(k − 1), not τ/k. Writing k where k − 1 belongs is the single most common error in this topic, because near criticality k is so nearly 1 that dividing by it barely changes the number and the working looks tidy. The excess k − 1 is the whole physics: with k exactly 1 the period is infinite, which is what steady power means.
[It should say] T = τ/(k − 1) = 0.1 ÷ 0.002 = 50 s.

## Slide 24
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The reactor drawn has τ = 0.1 s and k = 1.001. How many neutron generations pass in the one e-fold marked on the graph?
A One — an e-fold is what a generation does
B About a thousand
C About a hundred thousand
Neutron population against time, with time counted in reactor periods rather than seconds. Three curves start together at N₀: a rising exponential labelled k > 1, a flat line labelled k = 1, and a decaying exponential labelled k < 1. Dashed construction lines mark the point one period along, where the growing curve has multiplied by e.
The live version of this figure — click here
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The reactor drawn has τ = 0.1 s and k = 1.001. How many neutron generations pass in the one e-fold marked on the graph?
[Options] A One — an e-fold is what a generation does B About a thousand C About a hundred thousand
[Figure] Neutron population against time, with time counted in reactor periods rather than seconds. Three curves start together at N₀: a rising exponential labelled k > 1, a flat line labelled k = 1, and a decaying exponential labelled k < 1. Dashed construction lines mark the point one period along, where the growing curve has multiplied by e.

## Slide 25
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B About a thousand
WHY
One period is T = τ/(k − 1) = 0.1/0.001 = 100 s, and each generation takes 0.1 s, so the marked interval holds 100 ÷ 0.1 = 1000 generations. Each of those multiplies the population by only 1.001; a thousand such nudges compound to a factor of e. That is why the curve leaves N₀ so gently.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 34
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — About a thousand. One period is T = τ/(k − 1) = 0.1/0.001 = 100 s, and each generation takes 0.1 s, so the marked interval holds 100 ÷ 0.1 = 1000 generations. Each of those multiplies the population by only 1.001; a thousand such nudges compound to a factor of e. That is why the curve leaves N₀ so gently.

## Slide 26
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
A reactor has k = 1.001 and effective generation time τ = 0.1 s. Its period T = τ/(k − 1) is…
A
10 s
B
100 s
C
1000 s
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 34
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A reactor has k = 1.001 and effective generation time τ = 0.1 s. Its period T = τ/(k − 1) is…
[Options] A 10 s B 100 s C 1000 s

## Slide 27
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B 100 s
HOW TO GET THERE
T = 0.1 ÷ 0.001 = 100 s: power multiplies by e every 100 seconds. Long τ (delayed neutrons) and small k − 1 (good control) both stretch the period.
WHY THE OTHERS TEMPT
A Tempting if τ and k − 1 get swapped in the fraction: 0.1 × 0.1, or 0.001 ÷ 0.0001, both land near 10 s. But check the size of the answer against the physics — a period of 10 s means power multiplying by e every ten seconds, which is a far brisker transient than a 0.1% excess in k should produce.
B Correct. T = τ/(k − 1) = 0.1 ÷ 0.001 = 100 s, so the power multiplies by e every hundred seconds. Both factors help the operator: the delayed neutrons make τ long, and good control keeps k − 1 small.
C Tempting because 1000 is the ratio between the prompt and effective generation times, and that factor of a thousand is everywhere in this topic. But it belongs to τ, not to T. Here τ is already the effective 0.1 s, so dividing by k − 1 = 0.001 gives 100 s; 1000 s would need k − 1 = 10⁻⁴.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 34
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] A reactor has k = 1.001 and effective generation time τ = 0.1 s. Its period T = τ/(k − 1) is…
[Option by option] A: Tempting if τ and k − 1 get swapped in the fraction: 0.1 × 0.1, or 0.001 ÷ 0.0001, both land near 10 s. But check the size of the answer against the physics — a period of 10 s means power multiplying by e every ten seconds, which is a far brisker transient than a 0.1% excess in k should produce. B: Correct. T = τ/(k − 1) = 0.1 ÷ 0.001 = 100 s, so the power multiplies by e every hundred seconds. Both factors help the operator: the delayed neutrons make τ long, and good control keeps k − 1 small. C: Tempting because 1000 is the ratio between the prompt and effective generation times, and that factor of a thousand is everywhere in this topic. But it belongs to τ, not to T. Here τ is already the effective 0.1 s, so dividing by k − 1 = 0.001 gives 100 s; 1000 s would need k − 1 = 10⁻⁴.
[Answer] B — 100 s
[Why] T = 0.1 ÷ 0.001 = 100 s: power multiplies by e every 100 seconds. Long τ (delayed neutrons) and small k − 1 (good control) both stretch the period.
[Reveal] One click for the answer, then one for the reason.

## Slide 28
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A daughter nuclide obeys dN₂/dt = λ₁N₁ − λ₂N₂ with N₂(0) = 0. Without solving fully, establish the shape of N₂(t): initial slope, the peak condition, and the long-time behaviour when λ₁ ≪ λ₂.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A daughter nuclide obeys dN₂/dt = λ₁N₁ − λ₂N₂ with N₂(0) = 0. Without solving fully, establish the shape of N₂(t): initial slope, the peak condition, and the long-time behaviour when λ₁ ≪ λ₂.
[Answer] Rises with slope λ₁N₁, peaks where λ₁N₁ = λ₂N₂, then tracks the slower clock — with N₂ ≈ (λ₁/λ₂)N₁ in secular equilibrium

## Slide 29
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A daughter nuclide obeys dN₂/dt = λ₁N₁ − λ₂N₂ with N₂(0) = 0. Without solving fully, establish the shape of N₂(t): initial slope, the peak condition, and the long-time behaviour when λ₁ ≪ λ₂.
1.
At t = 0: dN₂/dt = λ₁N₁(0) > 0 — the curve leaves the origin with slope equal to the parent's activity: growth is fastest at the start.
2.
Peak: dN₂/dt = 0 exactly when λ₂N₂ = λ₁N₁ — the daughter's activity momentarily equals the parent's; before this point production wins, after it decay wins.
3.
For λ₁ ≪ λ₂ the daughter reaches secular equilibrium, N₂ ≈ (λ₁/λ₂)N₁: it decays almost as fast as it is made, so its (small) population simply tracks the slowly fading parent — rise, brief peak, then a long descent on the parent's clock.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] At t = 0: dN₂/dt = λ₁N₁(0) > 0 — the curve leaves the origin with slope equal to the parent's activity: growth is fastest at the start.
[Step 2] Peak: dN₂/dt = 0 exactly when λ₂N₂ = λ₁N₁ — the daughter's activity momentarily equals the parent's; before this point production wins, after it decay wins.
[Step 3] For λ₁ ≪ λ₂ the daughter reaches secular equilibrium, N₂ ≈ (λ₁/λ₂)N₁: it decays almost as fast as it is made, so its (small) population simply tracks the slowly fading parent — rise, brief peak, then a long descent on the parent's clock.

## Slide 30
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
Rises with slope λ₁N₁, peaks where λ₁N₁ = λ₂N₂, then tracks the slower clock — with N₂ ≈ (λ₁/λ₂)N₁ in secular equilibrium
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Rises with slope λ₁N₁, peaks where λ₁N₁ = λ₂N₂, then tracks the slower clock — with N₂ ≈ (λ₁/λ₂)N₁ in secular equilibrium

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
(a) A reactor's power grows as P = P₀e^(t/T) with P₀ = 1.0 MW and T = 20 s. Integrate to find the energy released in the first 60 s. (b) Explain qualitatively why the Gamow exponent e^(−b/√E) makes stellar burn rates so temperature-sensitive.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] (a) A reactor's power grows as P = P₀e^(t/T) with P₀ = 1.0 MW and T = 20 s. Integrate to find the energy released in the first 60 s. (b) Explain qualitatively why the Gamow exponent e^(−b/√E) makes stellar burn rates so temperature-sensitive.
[Answer] ≈ 3.8 × 10⁸ J, mostly in the last e-fold; the doubled exponential sensitivity of the Gamow peak is why stars self-regulate

## Slide 32
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
(a) A reactor's power grows as P = P₀e^(t/T) with P₀ = 1.0 MW and T = 20 s. Integrate to find the energy released in the first 60 s. (b) Explain qualitatively why the Gamow exponent e^(−b/√E) makes stellar burn rates so temperature-sensitive.
1.
(a) E = ∫₀⁶⁰ P₀e^(t/T) dt = P₀T(e^(60/T) − 1) = 10⁶ × 20 × (e³ − 1).
2.
E = 2 × 10⁷ × 19.1 ≈ 3.8 × 10⁸ J — and notice most of it arrives in the final period: exponentials backload their totals.
3.
(b) The burn rate integrates e^(−E/kT) × e^(−b/√E), a product of one falling and one rising exponential that overlap only in a narrow window (the Gamow peak). Raise T slightly and the Maxwell factor lifts the whole window while the peak shifts to energies where tunneling is far likelier — two exponential boosts compounding, so a few percent in T can mean tens of percent in power. That steepness is the stellar thermostat: over-burn expands and cools the core, under-burn contracts and reheats it.
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] (a) E = ∫₀⁶⁰ P₀e^(t/T) dt = P₀T(e^(60/T) − 1) = 10⁶ × 20 × (e³ − 1).
[Step 2] E = 2 × 10⁷ × 19.1 ≈ 3.8 × 10⁸ J — and notice most of it arrives in the final period: exponentials backload their totals.
[Step 3] (b) The burn rate integrates e^(−E/kT) × e^(−b/√E), a product of one falling and one rising exponential that overlap only in a narrow window (the Gamow peak). Raise T slightly and the Maxwell factor lifts the whole window while the peak shifts to energies where tunneling is far likelier — two exponential boosts compounding, so a few percent in T can mean tens of percent in power. That steepness is the stellar thermostat: over-burn expands and cools the core, under-burn contracts and reheats it.

## Slide 33
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
≈ 3.8 × 10⁸ J, mostly in the last e-fold; the doubled exponential sensitivity of the Gamow peak is why stars self-regulate
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
33 / 34
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 3.8 × 10⁸ J, mostly in the last e-fold; the doubled exponential sensitivity of the Gamow peak is why stars self-regulate

## Slide 34
ADVANCED FISSION & FUSION
Where to go next
Plenary — What to take away, what to practise next
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-51/fission-fusion-calculus/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-51/presentation/?lesson=calculus
Chapter
All Advanced Fission & Fusion lessons
https://giophysics.com/chapter-51/
PDF
Download the lesson PDF
https://giophysics.com/downloads/51-6-fission-fusion-calculus.pdf
ADVANCED FISSION & FUSION · FISSION & FUSION CALCULUS
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fission & Fusion Calculus. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
34 / 34
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-51/presentation/?lesson=calculus moves them.