## Slide 1
26 · Advanced Fission & Fusion
Density × time × temperature
Fusion Technology
Hold a 150-million-kelvin plasma dense enough, long enough, and it will pay back more energy than you spent heating it. That single sentence — the Lawson criterion — has driven seventy years of engineering, two utterly different machine families, and some of the most careful honesty in physics.
POSITION
Lesson 4 of 6 in Advanced Fission & Fusion
PLAN
15 slides in the 45-minute core run, about 41.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-51/fusion-technology/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Advanced Fission & Fusion — Fusion Technology. Lesson 4 of 6.
[Intro] Hold a 150-million-kelvin plasma dense enough, long enough, and it will pay back more energy than you spent heating it. That single sentence — the Lawson criterion — has driven seventy years of engineering, two utterly different machine families, and some of the most careful honesty in physics.
[Source] https://giophysics.com/chapter-51/fusion-technology/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Fusion & the Coulomb barrier
https://giophysics.com/chapter-51/fusion-processes/
Recall
Nuclear reactions & binding energy
https://giophysics.com/chapter-46/nuclear-reactions/
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Fusion & the Coulomb barrier; Nuclear reactions & binding energy

## Slide 3
THINK FIRST
One machine holds a plasma a hundred thousand times thinner than air for several seconds; another crushes a peppercorn for a ten-billionth of a second. Both are chasing the same number — what number could the two possibly have in common?
Take answers before you click — the point is the commitment
Tokamaks and laser fusion have almost nothing in common as engineering, and their densities differ by eleven orders of magnitude, yet the two programmes report progress against the same criterion.
THE ANSWER
The Lawson triple product, nTτ. Only the product matters, so a modest density held for seconds and a fantastic density held for the flight time of its own explosion land in the same place — the choice between them is engineering, not physics.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] One machine holds a plasma a hundred thousand times thinner than air for several seconds; another crushes a peppercorn for a ten-billionth of a second. Both are chasing the same number — what number could the two possibly have in common? Tokamaks and laser fusion have almost nothing in common as engineering, and their densities differ by eleven orders of magnitude, yet the two programmes report progress against the same criterion.
[Answer] The Lawson triple product, nTτ. Only the product matters, so a modest density held for seconds and a fantastic density held for the flight time of its own explosion land in the same place — the choice between them is engineering, not physics.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
The Lawson criterion says a fusion plasma breaks even only if the product of its density, temperature, and energy confinement time is high enough (nTτ ≳ 3 × 10²¹ keV s m⁻³ for D–T); tokamaks pursue it with modest density held for seconds by magnetic fields, laser fusion with enormous density held for nanoseconds by inertia.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] The Lawson criterion says a fusion plasma breaks even only if the product of its density, temperature, and energy confinement time is high enough (nTτ ≳ 3 × 10²¹ keV s m⁻³ for D–T); tokamaks pursue it with modest density held for seconds by magnetic fields, laser fusion with enormous density held for nanoseconds by inertia.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A tokamak at n = 10²⁰ m⁻³ and T = 15 keV needs to keep its heat for about τ = 2 s to reach the threshold — which is why so much tokamak research is really research into plasma heat leaks.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A tokamak at n = 10²⁰ m⁻³ and T = 15 keV needs to keep its heat for about τ = 2 s to reach the threshold — which is why so much tokamak research is really research into plasma heat leaks.

## Slide 6
THE BIG IDEA
Density × time × temperature
Introduce the idea — The big idea and the definition
For a fusion plasma to break even, the fusion power born inside it must beat the rate it leaks heat. That condition compresses into the Lawson triple product: density × temperature × confinement time, nTτ ≳ 3 × 10²¹ keV s m⁻³ for D–T near its sweet spot of 10–20 keV. Two engineering families attack it from opposite ends.
Magnetic confinement (the tokamak) uses moderate density (~10²⁰ m⁻³) held for seconds: charged particles spiral along magnetic field lines, and a twisted combination of toroidal and poloidal fields keeps them from drifting into the wall. Inertial confinement (laser fusion) uses fantastic density — a frozen D–T pellet imploded by lasers to ~1000× solid density — held for only the ~10⁻¹⁰ s its own inertia provides. Progress is measured by Q, fusion power out over heating power in: JET reached Q = 0.67 in 1997; in December 2022 the NIF laser facility got 3.15 MJ out for 2.05 MJ delivered to the target (Q ≈ 1.5) — though the lasers drew ~300 MJ from the wall; ITER, under construction, is designed for Q ≥ 10, with full D–T operation now expected in the late 2030s.
Net electricity remains a hard engineering goal, not an accomplished fact.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] For a fusion plasma to break even, the fusion power born inside it must beat the rate it leaks heat. That condition compresses into the Lawson triple product: density × temperature × confinement time, nTτ ≳ 3 × 10²¹ keV s m⁻³ for D–T near its sweet spot of 10–20 keV. Two engineering families attack it from opposite ends. Magnetic confinement (the tokamak) uses moderate density (~10²⁰ m⁻³) held for seconds: charged particles spiral along magnetic field lines, and a twisted combination of toroidal and poloidal fields keeps them from drifting into the wall. Inertial confinement (laser fusion) uses fantastic density — a frozen D–T pellet imploded by lasers to ~1000× solid density — held for only the ~10⁻¹⁰ s its own inertia provides. Progress is measured by Q, fusion power out over heating power in: JET reached Q = 0.67 in 1997; in December 2022 the NIF laser facility got 3.15 MJ out for 2.05 MJ delivered to the target (Q ≈ 1.5) — though the lasers drew ~300 MJ from the wall; ITER, under construction, is designed for Q ≥ 10, with full D–T operation now expected in the late 2030s. Net electricity remains a hard engineering goal, not an accomplished fact.

## Slide 7
THE PHYSICS · 1 OF 3
The tokamak route
Build the model — The formulae, one at a time, in plain English
A doughnut of plasma carries a huge toroidal field from external coils plus a poloidal field from a current driven through the plasma itself; their sum is a helix that averages away particle drifts. Confinement time is the fight: turbulence leaks heat across the field, and performance improves steeply with machine size — the physics reason ITER is 30 m tall. Its design point: 500 MW of fusion from 50 MW of plasma heating, Q = 10, in pulses of about 400 s.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A doughnut of plasma carries a huge toroidal field from external coils plus a poloidal field from a current driven through the plasma itself; their sum is a helix that averages away particle drifts. Confinement time is the fight: turbulence leaks heat across the field, and performance improves steeply with machine size — the physics reason ITER is 30 m tall. Its design point: 500 MW of fusion from 50 MW of plasma heating, Q = 10, in pulses of about 400 s.

## Slide 8
THE PHYSICS · 2 OF 3
The laser route
Build the model — The formulae, one at a time, in plain English
NIF focuses 192 beams, 2 MJ in ~10 ns, onto a peppercorn-sized capsule. The surface explodes outward; the reaction drives the rest inward at ~350 km/s, compressing D–T to ~1000× solid density with a central hot spot that ignites and burns outward before the pellet flies apart. Confinement is nothing but inertia — τ ~ 10⁻¹⁰ s — but the density is so extreme the triple product reaches the same territory as a tokamak's.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] NIF focuses 192 beams, 2 MJ in ~10 ns, onto a peppercorn-sized capsule. The surface explodes outward; the reaction drives the rest inward at ~350 km/s, compressing D–T to ~1000× solid density with a central hot spot that ignites and burns outward before the pellet flies apart. Confinement is nothing but inertia — τ ~ 10⁻¹⁰ s — but the density is so extreme the triple product reaches the same territory as a tokamak's.

## Slide 9
THE PHYSICS · 3 OF 3
The honest scoreboard
Build the model — The formulae, one at a time, in plain English
JET (1997): 16 MW fusion, 24 MW heating — Q = 0.67, still the tokamak record. NIF (Dec 2022, repeated since): 3.15 MJ from 2.05 MJ on target — the first Q > 1 anywhere, but a 1-in-150 return on wall-plug energy, at a few shots per week.
ITER: designed for Q = 10; assembly is under way, with the full D–T campaign now expected in the late 2030s after schedule revisions. No fusion machine has yet sent a watt to the grid — the physics milestone is passed, the engineering ones are not.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] JET (1997): 16 MW fusion, 24 MW heating — Q = 0.67, still the tokamak record. NIF (Dec 2022, repeated since): 3.15 MJ from 2.05 MJ on target — the first Q > 1 anywhere, but a 1-in-150 return on wall-plug energy, at a few shots per week. ITER: designed for Q = 10; assembly is under way, with the full D–T campaign now expected in the late 2030s after schedule revisions. No fusion machine has yet sent a watt to the grid — the physics milestone is passed, the engineering ones are not.

## Slide 10
FORMULA 1 OF 3
Lawson triple product
Build the model — The formulae, one at a time, in plain English
nTτ ≳ 3 × 10²¹ keV s m⁻³
D–T, near the T ≈ 10–20 keV sweet spot
IN PLAIN ENGLISH
Density sets how often nuclei meet, temperature how likely a meeting fuses, confinement time how long the heat stays to keep it all going. Only their product matters — trade any one against the others.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Lawson triple product: nTτ ≳ 3 × 10²¹ keV s m⁻³
[In plain English] Density sets how often nuclei meet, temperature how likely a meeting fuses, confinement time how long the heat stays to keep it all going. Only their product matters — trade any one against the others.
[Note] D–T, near the T ≈ 10–20 keV sweet spot

## Slide 11
FORMULA 2 OF 3
Gain factor
Build the model — The formulae, one at a time, in plain English
Q = P(fusion) / P(heating)
Q = 1 breakeven · Q ≥ 5 burning · Q → ∞ ignition
IN PLAIN ENGLISH
Q is measured at the plasma, not the wall socket: lasers and magnets draw far more than reaches the fuel. A power plant needs plasma Q ≳ 10 and generous engineering margins on top.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Gain factor: Q = P(fusion) / P(heating)
[In plain English] Q is measured at the plasma, not the wall socket: lasers and magnets draw far more than reaches the fuel. A power plant needs plasma Q ≳ 10 and generous engineering margins on top.
[Note] Q = 1 breakeven · Q ≥ 5 burning · Q → ∞ ignition

## Slide 12
FORMULA 3 OF 3
Magnetic confinement
Build the model — The formulae, one at a time, in plain English
F = qvB → particles spiral along field lines
Toroidal + poloidal fields twist into a magnetic bottle
IN PLAIN ENGLISH
A charged particle circles a field line in a tight helix, so a strong field replaces a material wall. Bending the lines into a twisted torus stops the ends leaking — that twist is the tokamak's defining trick.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Magnetic confinement: F = qvB → particles spiral along field lines
[In plain English] A charged particle circles a field line in a tight helix, so a strong field replaces a material wall. Bending the lines into a twisted torus stops the ends leaking — that twist is the tokamak's defining trick.
[Note] Toroidal + poloidal fields twist into a magnetic bottle

## Slide 13
PICTURE 1 OF 2
The magnetic bottle
Drawn for this lesson
A vertical section through a tokamak, cutting the doughnut twice either side of its axis. Each limb of plasma is a circle inside a much larger coil circle; the toroidal field runs out of the page on the left limb and into it on the right, since it goes the long way round the ring, while a dashed loop with an arrow circles the left plasma to show the poloidal field the plasma current makes.
The live version of this figure — click here
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A vertical section through a tokamak, cutting the doughnut twice either side of its axis. Each limb of plasma is a circle inside a much larger coil circle; the toroidal field runs out of the page on the left limb and into it on the right, since it goes the long way round the ring, while a dashed loop with an arrow circles the left plasma to show the poloidal field the plasma current makes.

## Slide 14
PICTURE 2 OF 2
The other route, and its bill
Drawn for this lesson
A two-millimetre capsule with its frozen deuterium-tritium fuel shown dashed inside, struck symmetrically by eight converging laser beams. Beside it the energy chain is drawn as three stacked boxes joined by arrows: about 300 MJ drawn from the grid, 2.05 MJ delivered to the target, and the fusion energy returned left as a question mark.
The live version of this figure — click here
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A two-millimetre capsule with its frozen deuterium-tritium fuel shown dashed inside, struck symmetrically by eight converging laser beams. Beside it the energy chain is drawn as three stacked boxes joined by arrows: about 300 MJ drawn from the grid, 2.05 MJ delivered to the target, and the fusion energy returned left as a question mark.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Q > 1 does not mean net power. NIF's famous 2022 shot released 1.5× the laser energy that reached the target — but the lasers drew about 300 MJ from the grid to deliver those 2.05 MJ, so the facility as a whole consumed ~100× what the fusion returned.
Plasma gain, engineering gain, and commercial gain are three different hurdles, and only the first has been cleared. Precision about which Q is being claimed is what separates fusion news from fusion hype.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Q > 1 does not mean net power. NIF's famous 2022 shot released 1.5× the laser energy that reached the target — but the lasers drew about 300 MJ from the grid to deliver those 2.05 MJ, so the facility as a whole consumed ~100× what the fusion returned. Plasma gain, engineering gain, and commercial gain are three different hurdles, and only the first has been cleared. Precision about which Q is being claimed is what separates fusion news from fusion hype.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A tokamak plasma has n = 1.0 × 10²⁰ m⁻³, T = 15 keV, and confinement time τ = 2.0 s. Does it meet the Lawson threshold of 3 × 10²¹ keV s m⁻³?
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A tokamak plasma has n = 1.0 × 10²⁰ m⁻³, T = 15 keV, and confinement time τ = 2.0 s. Does it meet the Lawson threshold of 3 × 10²¹ keV s m⁻³?
[Answer] Yes — nTτ = 3 × 10²¹ keV s m⁻³, right at the threshold

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A tokamak plasma has n = 1.0 × 10²⁰ m⁻³, T = 15 keV, and confinement time τ = 2.0 s. Does it meet the Lawson threshold of 3 × 10²¹ keV s m⁻³?
1.
nTτ = 1.0 × 10²⁰ × 15 × 2.0.
2.
nTτ = 3.0 × 10²¹ keV s m⁻³.
3.
Exactly at threshold — this parameter set is essentially ITER's design territory.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] nTτ = 1.0 × 10²⁰ × 15 × 2.0.
[Step 2] nTτ = 3.0 × 10²¹ keV s m⁻³.
[Step 3] Exactly at threshold — this parameter set is essentially ITER's design territory.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
Yes — nTτ = 3 × 10²¹ keV s m⁻³, right at the threshold
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Yes — nTτ = 3 × 10²¹ keV s m⁻³, right at the threshold

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A deuteron with 10 keV of kinetic energy moves perpendicular to a 5.0 T field. Find its speed and the radius of its spiral (m = 3.34 × 10⁻²⁷ kg).
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A deuteron with 10 keV of kinetic energy moves perpendicular to a 5.0 T field. Find its speed and the radius of its spiral (m = 3.34 × 10⁻²⁷ kg).
[Answer] v ≈ 9.8 × 10⁵ m s⁻¹, spiral radius ≈ 4 mm

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A deuteron with 10 keV of kinetic energy moves perpendicular to a 5.0 T field. Find its speed and the radius of its spiral (m = 3.34 × 10⁻²⁷ kg).
1.
E = 10 × 10³ × 1.60 × 10⁻¹⁹ = 1.6 × 10⁻¹⁵ J; v = √(2E/m) = √(2 × 1.6 × 10⁻¹⁵ ÷ 3.34 × 10⁻²⁷) ≈ 9.8 × 10⁵ m s⁻¹.
2.
r = mv / qB = 3.34 × 10⁻²⁷ × 9.8 × 10⁵ ÷ (1.60 × 10⁻¹⁹ × 5.0).
3.
r ≈ 4.1 × 10⁻³ m — a 4 mm helix inside a 6-metre plasma. The field really is the bottle.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E = 10 × 10³ × 1.60 × 10⁻¹⁹ = 1.6 × 10⁻¹⁵ J; v = √(2E/m) = √(2 × 1.6 × 10⁻¹⁵ ÷ 3.34 × 10⁻²⁷) ≈ 9.8 × 10⁵ m s⁻¹.
[Step 2] r = mv / qB = 3.34 × 10⁻²⁷ × 9.8 × 10⁵ ÷ (1.60 × 10⁻¹⁹ × 5.0).
[Step 3] r ≈ 4.1 × 10⁻³ m — a 4 mm helix inside a 6-metre plasma. The field really is the bottle.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
v ≈ 9.8 × 10⁵ m s⁻¹, spiral radius ≈ 4 mm
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] v ≈ 9.8 × 10⁵ m s⁻¹, spiral radius ≈ 4 mm

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
In NIF's December 2022 shot the box marked with a question mark came out at 3.15 MJ. What had the facility achieved?
A Net energy: the plant produced more than it consumed, so fusion power is solved
B More fusion energy than the laser light that reached the target, while the building drew about a hundred times that from the grid
C Nothing meaningful — the lasers must simply have been over 100% efficient for one shot
A two-millimetre capsule with its frozen deuterium-tritium fuel shown dashed inside, struck symmetrically by eight converging laser beams. Beside it the energy chain is drawn as three stacked boxes joined by arrows: about 300 MJ drawn from the grid, 2.05 MJ delivered to the target, and the fusion energy returned left as a question mark.
The live version of this figure — click here
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] In NIF's December 2022 shot the box marked with a question mark came out at 3.15 MJ. What had the facility achieved?
[Options] A Net energy: the plant produced more than it consumed, so fusion power is solved B More fusion energy than the laser light that reached the target, while the building drew about a hundred times that from the grid C Nothing meaningful — the lasers must simply have been over 100% efficient for one shot
[Figure] A two-millimetre capsule with its frozen deuterium-tritium fuel shown dashed inside, struck symmetrically by eight converging laser beams. Beside it the energy chain is drawn as three stacked boxes joined by arrows: about 300 MJ drawn from the grid, 2.05 MJ delivered to the target, and the fusion energy returned left as a question mark.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B More fusion energy than the laser light that reached the target, while the building drew about a hundred times that from the grid
WHY
Read the chain from the top. The 3.15 MJ is measured against the middle box, the 2.05 MJ that actually landed on the capsule — a target gain of about 1.5, and a genuine first. Against the top box, the ~300 MJ the lasers drew from the grid, the same shot returns about one per cent. Three different Q values, and only the innermost one has been beaten.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — More fusion energy than the laser light that reached the target, while the building drew about a hundred times that from the grid. Read the chain from the top. The 3.15 MJ is measured against the middle box, the 2.05 MJ that actually landed on the capsule — a target gain of about 1.5, and a genuine first. Against the top box, the ~300 MJ the lasers drew from the grid, the same shot returns about one per cent. Three different Q values, and only the innermost one has been beaten.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
The Lawson criterion for net fusion energy is a condition on…
A
Temperature alone — hot enough and fusion pays
B
The product of density, temperature, and confinement time
C
The strength of the confining magnetic field
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] The Lawson criterion for net fusion energy is a condition on…
[Options] A Temperature alone — hot enough and fusion pays B The product of density, temperature, and confinement time C The strength of the confining magnetic field

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B The product of density, temperature, and confinement time
HOW TO GET THERE
Breakeven balances fusion power born in the plasma against heat leaking out, and that balance depends on n, T, and τ only through their product — which is why nanosecond laser fusion and multi-second tokamaks can chase the same number.
WHY THE OTHERS TEMPT
A Tempting because temperature is the number the news always quotes and 150 million kelvin sounds like the whole battle. But a hot, thin plasma that leaks its heat in milliseconds fuses almost nothing. Temperature only sets how likely a collision is to fuse; density sets how often collisions happen, and confinement time sets how long the heat stays to keep it going.
B Correct. Breakeven balances the fusion power born in the plasma against the heat leaking out of it, and that balance depends on n, T and τ only through their product — nTτ ≳ 3 × 10²¹ keV s m⁻³ for D–T. It is why nanosecond laser fusion and multi-second tokamaks can be scored on the same criterion.
C Tempting because the magnetic field is the tokamak's most visible feature and a stronger field really does help confinement. But it is a means, not the criterion: laser fusion meets the same Lawson condition with no confining field at all, using nothing but the inertia of an exploding pellet. The condition is on the plasma, not on the machine.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] The Lawson criterion for net fusion energy is a condition on…
[Option by option] A: Tempting because temperature is the number the news always quotes and 150 million kelvin sounds like the whole battle. But a hot, thin plasma that leaks its heat in milliseconds fuses almost nothing. Temperature only sets how likely a collision is to fuse; density sets how often collisions happen, and confinement time sets how long the heat stays to keep it going. B: Correct. Breakeven balances the fusion power born in the plasma against the heat leaking out of it, and that balance depends on n, T and τ only through their product — nTτ ≳ 3 × 10²¹ keV s m⁻³ for D–T. It is why nanosecond laser fusion and multi-second tokamaks can be scored on the same criterion. C: Tempting because the magnetic field is the tokamak's most visible feature and a stronger field really does help confinement. But it is a means, not the criterion: laser fusion meets the same Lawson condition with no confining field at all, using nothing but the inertia of an exploding pellet. The condition is on the plasma, not on the machine.
[Answer] B — The product of density, temperature, and confinement time
[Why] Breakeven balances fusion power born in the plasma against heat leaking out, and that balance depends on n, T, and τ only through their product — which is why nanosecond laser fusion and multi-second tokamaks can chase the same number.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
NIF's 2022 shot: 2.05 MJ delivered to the target, 3.15 MJ of fusion out, ~300 MJ drawn by the lasers. Compute the target gain and the wall-plug gain, and state what each means.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] NIF's 2022 shot: 2.05 MJ delivered to the target, 3.15 MJ of fusion out, ~300 MJ drawn by the lasers. Compute the target gain and the wall-plug gain, and state what each means.
[Answer] Q(target) ≈ 1.5; Q(wall-plug) ≈ 0.01 — a milestone, not yet a power source

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
NIF's 2022 shot: 2.05 MJ delivered to the target, 3.15 MJ of fusion out, ~300 MJ drawn by the lasers. Compute the target gain and the wall-plug gain, and state what each means.
1.
Target gain: Q = 3.15 ÷ 2.05 ≈ 1.5 — the plasma gave back more than the light that hit it: scientific breakeven, achieved for the first time anywhere.
2.
Wall-plug gain: 3.15 ÷ 300 ≈ 0.01 — the building consumed about 100 times more than the fusion returned.
3.
A power plant must also convert fusion heat to electricity (~40%) and fire many times per second, not per week. Between Q = 1.5 at the target and a viable plant sit factors of hundreds — real, but honestly stated, engineering distance.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Target gain: Q = 3.15 ÷ 2.05 ≈ 1.5 — the plasma gave back more than the light that hit it: scientific breakeven, achieved for the first time anywhere.
[Step 2] Wall-plug gain: 3.15 ÷ 300 ≈ 0.01 — the building consumed about 100 times more than the fusion returned.
[Step 3] A power plant must also convert fusion heat to electricity (~40%) and fire many times per second, not per week. Between Q = 1.5 at the target and a viable plant sit factors of hundreds — real, but honestly stated, engineering distance.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
Q(target) ≈ 1.5; Q(wall-plug) ≈ 0.01 — a milestone, not yet a power source
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Q(target) ≈ 1.5; Q(wall-plug) ≈ 0.01 — a milestone, not yet a power source

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
Magnetic fusion runs at n ≈ 10²⁰ m⁻³ for τ ≈ 3 s; inertial fusion at n ≈ 10³¹ m⁻³ for τ ≈ 3 × 10⁻¹⁰ s. Compare their nτ products and explain what this says about the Lawson criterion.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Magnetic fusion runs at n ≈ 10²⁰ m⁻³ for τ ≈ 3 s; inertial fusion at n ≈ 10³¹ m⁻³ for τ ≈ 3 × 10⁻¹⁰ s. Compare their nτ products and explain what this says about the Lawson criterion.
[Answer] Both land near nτ ~ 10²¹ s m⁻³ — the criterion cares only about the product, so both routes are legitimate

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
Magnetic fusion runs at n ≈ 10²⁰ m⁻³ for τ ≈ 3 s; inertial fusion at n ≈ 10³¹ m⁻³ for τ ≈ 3 × 10⁻¹⁰ s. Compare their nτ products and explain what this says about the Lawson criterion.
1.
Magnetic: nτ = 10²⁰ × 3 = 3 × 10²⁰ s m⁻³.
2.
Inertial: nτ = 10³¹ × 3 × 10⁻¹⁰ = 3 × 10²¹ s m⁻³ — the same order of magnitude, from parameters eleven orders of magnitude apart.
3.
Lawson constrains only the product: hold a modest plasma for seconds, or a fantastically compressed one for the flight time of its own explosion — physics accepts both. The choice between them is pure engineering: steady-state magnets and heat exhaust versus repetitive laser shots and target manufacture.
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Magnetic: nτ = 10²⁰ × 3 = 3 × 10²⁰ s m⁻³.
[Step 2] Inertial: nτ = 10³¹ × 3 × 10⁻¹⁰ = 3 × 10²¹ s m⁻³ — the same order of magnitude, from parameters eleven orders of magnitude apart.
[Step 3] Lawson constrains only the product: hold a modest plasma for seconds, or a fantastically compressed one for the flight time of its own explosion — physics accepts both. The choice between them is pure engineering: steady-state magnets and heat exhaust versus repetitive laser shots and target manufacture.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
Both land near nτ ~ 10²¹ s m⁻³ — the criterion cares only about the product, so both routes are legitimate
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Both land near nτ ~ 10²¹ s m⁻³ — the criterion cares only about the product, so both routes are legitimate

## Slide 32
ADVANCED FISSION & FUSION
Where to go next
Plenary — What to take away, what to practise next
Next
26.5 Radiation Safety & Nuclear Waste
https://giophysics.com/chapter-51/nuclear-safety/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-51/fusion-technology/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-51/presentation/?lesson=confinement
Chapter
All Advanced Fission & Fusion lessons
https://giophysics.com/chapter-51/
PDF
Download the lesson PDF
https://giophysics.com/downloads/51-4-fusion-technology.pdf
ADVANCED FISSION & FUSION · FUSION TECHNOLOGY
GIOPHYSICS LESSON
Advanced Fission & Fusion — Fusion Technology. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-51/presentation/?lesson=confinement moves them.