## Slide 1
26 · Advanced Fission & Fusion
Taming k with late neutrons
Inside a Fission Reactor
A pressurised-water reactor is a machine for holding k at exactly 1.000 while three gigawatts of heat pour out of a lattice of metal tubes. The startling part is why it is controllable at all: a rare handful of neutrons that arrive seconds late slow the whole clock down to human speed.
POSITION
Lesson 2 of 6 in Advanced Fission & Fusion
PLAN
15 slides in the 45-minute core run, about 41.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-51/fission-reactors/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 33
Notes: [Lesson] Advanced Fission & Fusion — Inside a Fission Reactor. Lesson 2 of 6.
[Intro] A pressurised-water reactor is a machine for holding k at exactly 1.000 while three gigawatts of heat pour out of a lattice of metal tubes. The startling part is why it is controllable at all: a rare handful of neutrons that arrive seconds late slow the whole clock down to human speed.
[Source] https://giophysics.com/chapter-51/fission-reactors/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Chain reactions & criticality
https://giophysics.com/chapter-51/chain-reactions/
Recall
Half-life & activity
https://giophysics.com/chapter-46/half-life/
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Chain reactions & criticality; Half-life & activity

## Slide 3
THINK FIRST
A neutron generation in a reactor lasts about a ten-thousandth of a second. So why does a reactor that drifts slightly above critical take a whole minute to double its power, rather than a fraction of a millisecond?
Take answers before you click — the point is the commitment
An operator nudges the control rods out a couple of centimetres and watches the power climb gently over minutes. If the chain really ran at generation speed, no human and no machine could follow it.
THE ANSWER
About one fission neutron in 150 is not emitted at fission at all: it comes seconds later from a decaying fragment. The average generation time is dragged up to about 0.1 s by those stragglers, and while k stays below roughly 1.0065 the chain cannot grow without waiting for them.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A neutron generation in a reactor lasts about a ten-thousandth of a second. So why does a reactor that drifts slightly above critical take a whole minute to double its power, rather than a fraction of a millisecond? An operator nudges the control rods out a couple of centimetres and watches the power climb gently over minutes. If the chain really ran at generation speed, no human and no machine could follow it.
[Answer] About one fission neutron in 150 is not emitted at fission at all: it comes seconds later from a decaying fragment. The average generation time is dragged up to about 0.1 s by those stragglers, and while k stays below roughly 1.0065 the chain cannot grow without waiting for them.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
A fission reactor holds a chain reaction at k = 1 using fuel rods (enriched uranium), a moderator (slows neutrons), control rods (absorb neutrons), and a coolant that carries the heat away — and it is controllable only because a small fraction of neutrons arrive seconds late.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] A fission reactor holds a chain reaction at k = 1 using fuel rods (enriched uranium), a moderator (slows neutrons), control rods (absorb neutrons), and a coolant that carries the heat away — and it is controllable only because a small fraction of neutrons arrive seconds late.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
Pushing the control rods in a few centimetres nudges k from 1.000 to 0.999; thanks to delayed neutrons the power then eases down over minutes — slow enough for operators, and automatic systems, to steer.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] Pushing the control rods in a few centimetres nudges k from 1.000 to 0.999; thanks to delayed neutrons the power then eases down over minutes — slow enough for operators, and automatic systems, to steer.

## Slide 6
THE BIG IDEA
Taming k with late neutrons
Introduce the idea — The big idea and the definition
A pressurised-water reactor (PWR) arranges its physics in layers. Fuel rods hold pellets of uranium dioxide, enriched from natural 0.7% ²³⁵U to 3–5%. Water between the rods is both moderator — slowing fission neutrons to thermal speeds — and coolant, carrying heat to a steam generator, with everything sealed inside a steel-and-concrete containment.
Control rods of neutron-absorbing boron or cadmium slide in and out to trim k: in to absorb more and lower k, out to raise it. Control is only possible because about 0.65% of fission neutrons are delayed — emitted seconds later by decaying fragments — which stretches the effective generation time from ~0.1 ms to ~0.1 s, turning power changes from explosive to leisurely. Water-moderated designs also self-stabilise: hotter water is less dense, moderates less, and k falls — negative temperature feedback.
The price of the whole enterprise is waste: intensely radioactive short-lived fission products, and long-lived actinides that stay hazardous for millennia.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A pressurised-water reactor (PWR) arranges its physics in layers. Fuel rods hold pellets of uranium dioxide, enriched from natural 0.7% ²³⁵U to 3–5%. Water between the rods is both moderator — slowing fission neutrons to thermal speeds — and coolant, carrying heat to a steam generator, with everything sealed inside a steel-and-concrete containment. Control rods of neutron-absorbing boron or cadmium slide in and out to trim k: in to absorb more and lower k, out to raise it. Control is only possible because about 0.65% of fission neutrons are delayed — emitted seconds later by decaying fragments — which stretches the effective generation time from ~0.1 ms to ~0.1 s, turning power changes from explosive to leisurely. Water-moderated designs also self-stabilise: hotter water is less dense, moderates less, and k falls — negative temperature feedback. The price of the whole enterprise is waste: intensely radioactive short-lived fission products, and long-lived actinides that stay hazardous for millennia.

## Slide 7
THE PHYSICS · 1 OF 3
A tour of the machine
Build the model — The formulae, one at a time, in plain English
Heat is born in the fuel pellets, conducted through the rod cladding into pressurised water at ~320 °C (kept liquid at 155 atmospheres), pumped to a steam generator that boils a separate water loop, and the steam spins the turbine. Three isolated water circuits keep radioactivity away from the turbine hall, and the containment building is designed to hold everything even if the pipework fails.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Heat is born in the fuel pellets, conducted through the rod cladding into pressurised water at ~320 °C (kept liquid at 155 atmospheres), pumped to a steam generator that boils a separate water loop, and the steam spins the turbine. Three isolated water circuits keep radioactivity away from the turbine hall, and the containment building is designed to hold everything even if the pipework fails.

## Slide 8
THE PHYSICS · 2 OF 3
Delayed neutrons: the whole secret of control
Build the model — The formulae, one at a time, in plain English
About 1 fission neutron in 150 is emitted not at fission but by a neutron-rich fragment decaying seconds later. As long as k stays below about 1.0065, the chain cannot be sustained by prompt neutrons alone — growth must wait for the delayed ones, and the reactor responds over seconds, not microseconds. Every control system in the plant lives inside that margin; exceeding it (prompt criticality) is the accident every design rules out.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] About 1 fission neutron in 150 is emitted not at fission but by a neutron-rich fragment decaying seconds later. As long as k stays below about 1.0065, the chain cannot be sustained by prompt neutrons alone — growth must wait for the delayed ones, and the reactor responds over seconds, not microseconds. Every control system in the plant lives inside that margin; exceeding it (prompt criticality) is the accident every design rules out.

## Slide 9
THE PHYSICS · 3 OF 3
Feedback and waste
Build the model — The formulae, one at a time, in plain English
In a PWR, rising temperature thins the moderator and Doppler-broadens ²³⁸U capture resonances, both of which push k down — the physics itself resists a power excursion. What the physics cannot remove is the waste: spent fuel is fiercely hot for decades (fission products like ⁹⁰Sr, ¹³⁷Cs), then quietly hazardous for millennia (actinides like ²³⁹Pu). Practice is cooling ponds first, dry casks next, deep geological disposal for the long tail — with low- and intermediate-level waste (filters, cladding, tools) handled separately.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] In a PWR, rising temperature thins the moderator and Doppler-broadens ²³⁸U capture resonances, both of which push k down — the physics itself resists a power excursion. What the physics cannot remove is the waste: spent fuel is fiercely hot for decades (fission products like ⁹⁰Sr, ¹³⁷Cs), then quietly hazardous for millennia (actinides like ²³⁹Pu). Practice is cooling ponds first, dry casks next, deep geological disposal for the long tail — with low- and intermediate-level waste (filters, cladding, tools) handled separately.

## Slide 10
FORMULA 1 OF 3
The k budget
Build the model — The formulae, one at a time, in plain English
k = 1.000 ← rods trim absorption
Fuel and geometry set k slightly above 1; rods absorb the excess
IN PLAIN ENGLISH
A reactor is built with a little spare reactivity, then deliberately poisoned back to exactly 1. Rods in: k dips, power falls. Rods out: k tips just past 1, power climbs, rods return to hold the new level.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] The k budget: k = 1.000 ← rods trim absorption
[In plain English] A reactor is built with a little spare reactivity, then deliberately poisoned back to exactly 1. Rods in: k dips, power falls. Rods out: k tips just past 1, power climbs, rods return to hold the new level.
[Note] Fuel and geometry set k slightly above 1; rods absorb the excess

## Slide 11
FORMULA 2 OF 3
Effective generation time
Build the model — The formulae, one at a time, in plain English
τ(eff) ≈ 0.1 s ≫ τ(prompt) ≈ 10⁻⁴ s
0.65% delayed neutrons dominate the average delay
IN PLAIN ENGLISH
Most neutrons appear within 10⁻⁴ s, but a rare few take seconds — and the average waits for the stragglers. The chain cannot outrun its slowest links while k stays below the prompt-only threshold.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Effective generation time: τ(eff) ≈ 0.1 s ≫ τ(prompt) ≈ 10⁻⁴ s
[In plain English] Most neutrons appear within 10⁻⁴ s, but a rare few take seconds — and the average waits for the stragglers. The chain cannot outrun its slowest links while k stays below the prompt-only threshold.
[Note] 0.65% delayed neutrons dominate the average delay

## Slide 12
FORMULA 3 OF 3
Doubling time
Build the model — The formulae, one at a time, in plain English
T₂ = τ ln 2 / (k − 1)
Small excess k and long τ → doubling in seconds to minutes
IN PLAIN ENGLISH
This is the exponential-growth clock. With k = 1.001 and τ(eff) = 0.1 s, power doubles in about 69 s — but with prompt neutrons alone it would double 1000 times faster, far beyond any control system.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Doubling time: T₂ = τ ln 2 / (k − 1)
[In plain English] This is the exponential-growth clock. With k = 1.001 and τ(eff) = 0.1 s, power doubles in about 69 s — but with prompt neutrons alone it would double 1000 times faster, far beyond any control system.
[Note] Small excess k and long τ → doubling in seconds to minutes

## Slide 13
PICTURE 1 OF 2
The machine, circuit by circuit
Drawn for this lesson
Inside a containment building sits the reactor vessel: five fuel rods hang the full depth of it with four control rods lowered between them from drives above. Pressurised water leaves the top of the vessel, runs to a steam generator also inside containment, and returns along a lower pipe; a separate steam line leaves the top of the steam generator for a turbine outside, and condensate returns from the condenser to the bottom of the generator.
The live version of this figure — click here
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] Inside a containment building sits the reactor vessel: five fuel rods hang the full depth of it with four control rods lowered between them from drives above. Pressurised water leaves the top of the vessel, runs to a steam generator also inside containment, and returns along a lower pipe; a separate steam line leaves the top of the steam generator for a turbine outside, and condensate returns from the condenser to the bottom of the generator.

## Slide 14
PICTURE 2 OF 2
Two fates for a neutron
Drawn for this lesson
A close-up of two fuel rods with water between them and a boron control rod lowered part-way in from the top. One neutron leaves the left rod horizontally and stops dead at the control rod, marked with a cross. A second leaves lower down and zig-zags between four collision points in the water before reaching the right-hand fuel rod.
The live version of this figure — click here
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A close-up of two fuel rods with water between them and a boron control rod lowered part-way in from the top. One neutron leaves the left rod horizontally and stops dead at the control rod, marked with a cross. A second leaves lower down and zig-zags between four collision points in the water before reaching the right-hand fuel rod.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Control rods do not slow neutrons down — that is the moderator's job. Rods absorb neutrons, removing them from the chain entirely; the moderator slows them so they fission more effectively.
Confusing the two reverses the logic of the machine: adding moderator generally raises k, adding absorber always lowers it. And a power reactor cannot detonate like a bomb — at 3–5% enrichment, the fast-neutron chain a weapon needs simply cannot form.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Control rods do not slow neutrons down — that is the moderator's job. Rods absorb neutrons, removing them from the chain entirely; the moderator slows them so they fission more effectively. Confusing the two reverses the logic of the machine: adding moderator generally raises k, adding absorber always lowers it. And a power reactor cannot detonate like a bomb — at 3–5% enrichment, the fast-neutron chain a weapon needs simply cannot form.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A reactor with effective generation time 0.1 s drifts to k = 1.001. Find the power doubling time.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A reactor with effective generation time 0.1 s drifts to k = 1.001. Find the power doubling time.
[Answer] ≈ 69 s — comfortably controllable

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A reactor with effective generation time 0.1 s drifts to k = 1.001. Find the power doubling time.
1.
T₂ = τ ln 2 / (k − 1) = 0.1 × 0.693 ÷ 0.001.
2.
T₂ ≈ 69 s.
3.
A power doubling every minute is easily caught by moving control rods a few centimetres.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] T₂ = τ ln 2 / (k − 1) = 0.1 × 0.693 ÷ 0.001.
[Step 2] T₂ ≈ 69 s.
[Step 3] A power doubling every minute is easily caught by moving control rods a few centimetres.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
≈ 69 s — comfortably controllable
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 69 s — comfortably controllable

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
Repeat with prompt neutrons only: τ = 1.0 × 10⁻⁴ s at the same k = 1.001. Why do delayed neutrons make reactors possible?
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Repeat with prompt neutrons only: τ = 1.0 × 10⁻⁴ s at the same k = 1.001. Why do delayed neutrons make reactors possible?
[Answer] 0.069 s doubling — uncontrollable; delayed neutrons slow the clock ×1000

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
Repeat with prompt neutrons only: τ = 1.0 × 10⁻⁴ s at the same k = 1.001. Why do delayed neutrons make reactors possible?
1.
T₂ = τ ln 2 / (k − 1) = 10⁻⁴ × 0.693 ÷ 0.001 = 0.069 s.
2.
Power would double 14 times a second — ×10⁴ every second. No mechanical system can chase that.
3.
The 0.65% of neutrons that arrive seconds late stretch the average generation time ~1000-fold. Provided k − 1 stays below that 0.65%, growth must wait for the stragglers, and the reactor answers in seconds.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] T₂ = τ ln 2 / (k − 1) = 10⁻⁴ × 0.693 ÷ 0.001 = 0.069 s.
[Step 2] Power would double 14 times a second — ×10⁴ every second. No mechanical system can chase that.
[Step 3] The 0.65% of neutrons that arrive seconds late stretch the average generation time ~1000-fold. Provided k − 1 stays below that 0.65%, growth must wait for the stragglers, and the reactor answers in seconds.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
0.069 s doubling — uncontrollable; delayed neutrons slow the clock ×1000
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 0.069 s doubling — uncontrollable; delayed neutrons slow the clock ×1000

## Slide 22
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A reactor with effective generation time τ = 0.1 s drifts to k = 1.001. Find the power doubling time.
2.
T₂ = τ ln 2 / (k − 1).
3.
T₂ = 0.1 × 0.693 ÷ 1.001.
4.
T₂ = 0.0692 s.
5.
So the power doubles about fourteen times a second.
LINE 3 IS WRONG
The denominator is k − 1 = 0.001, not k = 1.001. It is an easy substitution to fumble because k is so close to 1 that the two look almost identical on the page — but they differ by a factor of a thousand, which is exactly the factor between a controllable reactor and an excursion. Whenever k − 1 appears, work it out as a number before substituting.
IT SHOULD SAY
T₂ = 0.1 × 0.693 ÷ 0.001 ≈ 69 s.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The denominator is k − 1 = 0.001, not k = 1.001. It is an easy substitution to fumble because k is so close to 1 that the two look almost identical on the page — but they differ by a factor of a thousand, which is exactly the factor between a controllable reactor and an excursion. Whenever k − 1 appears, work it out as a number before substituting.
[It should say] T₂ = 0.1 × 0.693 ÷ 0.001 ≈ 69 s.

## Slide 23
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The control rod in the picture is pushed further down between the fuel rods. What happens to k?
A k falls — the boron absorbs neutrons that would otherwise have gone on to cause fission
B k rises — the rod slows the neutrons down, and slow neutrons fission ²³⁵U far more readily
C k is unchanged — the rods control the heat removed, not the neutron population
A close-up of two fuel rods with water between them and a boron control rod lowered part-way in from the top. One neutron leaves the left rod horizontally and stops dead at the control rod, marked with a cross. A second leaves lower down and zig-zags between four collision points in the water before reaching the right-hand fuel rod.
The live version of this figure — click here
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The control rod in the picture is pushed further down between the fuel rods. What happens to k?
[Options] A k falls — the boron absorbs neutrons that would otherwise have gone on to cause fission B k rises — the rod slows the neutrons down, and slow neutrons fission ²³⁵U far more readily C k is unchanged — the rods control the heat removed, not the neutron population
[Figure] A close-up of two fuel rods with water between them and a boron control rod lowered part-way in from the top. One neutron leaves the left rod horizontally and stops dead at the control rod, marked with a cross. A second leaves lower down and zig-zags between four collision points in the water before reaching the right-hand fuel rod.

## Slide 24
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
A k falls — the boron absorbs neutrons that would otherwise have gone on to cause fission
WHY
Follow the two neutrons in the picture. The one that meets the control rod ends at the cross: it is gone from the chain for good. Lower the rod and more neutrons meet that fate, so fewer survive to the next generation and k drops. Slowing neutrons down is what the water between the rods does, and it is a different job done by a different material.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] A — k falls — the boron absorbs neutrons that would otherwise have gone on to cause fission. Follow the two neutrons in the picture. The one that meets the control rod ends at the cross: it is gone from the chain for good. Lower the rod and more neutrons meet that fate, so fewer survive to the next generation and k drops. Slowing neutrons down is what the water between the rods does, and it is a different job done by a different material.

## Slide 25
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Control rods hold a reactor at steady power by…
A
Slowing fast neutrons down to thermal speeds
B
Absorbing neutrons, trimming k to exactly 1
C
Reflecting escaping neutrons back into the core
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Control rods hold a reactor at steady power by…
[Options] A Slowing fast neutrons down to thermal speeds B Absorbing neutrons, trimming k to exactly 1 C Reflecting escaping neutrons back into the core

## Slide 26
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B Absorbing neutrons, trimming k to exactly 1
HOW TO GET THERE
Rods are made of absorbers like boron and cadmium: they soak up the spare neutrons so that exactly one per fission survives to continue the chain. Slowing neutrons is the moderator's job.
WHY THE OTHERS TEMPT
A This is the moderator's job, not the rods'. It is a genuinely tempting swap because slowing neutrons and absorbing them both sound like 'controlling' them — but they push k in opposite directions. Add moderator and k generally rises; add absorber and k always falls. In a PWR the water between the rods does the slowing.
B Correct. Boron and cadmium are neutron absorbers: they remove neutrons from the chain entirely, so the operator can trim a core built with a little spare reactivity back to exactly one surviving neutron per fission. Rods in, k dips and power falls; rods out, k tips above 1 and power climbs.
C Reflectors are a real thing — a neutron reflector around a core does bounce escaping neutrons back and does raise k — which is what makes this tempting. But a reflector is a fixed part of the structure, not the movable rod. A rod that reflected neutrons back into the fuel would raise k when inserted, which is the opposite of what a control rod is for.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Control rods hold a reactor at steady power by…
[Option by option] A: This is the moderator's job, not the rods'. It is a genuinely tempting swap because slowing neutrons and absorbing them both sound like 'controlling' them — but they push k in opposite directions. Add moderator and k generally rises; add absorber and k always falls. In a PWR the water between the rods does the slowing. B: Correct. Boron and cadmium are neutron absorbers: they remove neutrons from the chain entirely, so the operator can trim a core built with a little spare reactivity back to exactly one surviving neutron per fission. Rods in, k dips and power falls; rods out, k tips above 1 and power climbs. C: Reflectors are a real thing — a neutron reflector around a core does bounce escaping neutrons back and does raise k — which is what makes this tempting. But a reflector is a fixed part of the structure, not the movable rod. A rod that reflected neutrons back into the fuel would raise k when inserted, which is the opposite of what a control rod is for.
[Answer] B — Absorbing neutrons, trimming k to exactly 1
[Why] Rods are made of absorbers like boron and cadmium: they soak up the spare neutrons so that exactly one per fission survives to continue the chain. Slowing neutrons is the moderator's job.
[Reveal] One click for the answer, then one for the reason.

## Slide 27
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A plant delivers 1.0 GW of electricity at 33% efficiency. Find the fission rate and the mass of ²³⁵U consumed per day (200 MeV = 3.2 × 10⁻¹¹ J per fission).
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A plant delivers 1.0 GW of electricity at 33% efficiency. Find the fission rate and the mass of ²³⁵U consumed per day (200 MeV = 3.2 × 10⁻¹¹ J per fission).
[Answer] ≈ 9.4 × 10¹⁹ fissions per second; ≈ 3.2 kg of ²³⁵U per day

## Slide 28
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A plant delivers 1.0 GW of electricity at 33% efficiency. Find the fission rate and the mass of ²³⁵U consumed per day (200 MeV = 3.2 × 10⁻¹¹ J per fission).
1.
Thermal power: 1.0 GW ÷ 0.33 = 3.0 GW = 3.0 × 10⁹ J s⁻¹.
2.
Fission rate: 3.0 × 10⁹ ÷ 3.2 × 10⁻¹¹ = 9.4 × 10¹⁹ fissions s⁻¹.
3.
Per day: 9.4 × 10¹⁹ × 86 400 = 8.1 × 10²⁴ fissions = 13.5 mol, so m = 13.5 × 235 g ≈ 3.2 kg per day — a lump the size of a plum, against ~9000 tonnes of coal for the same output.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Thermal power: 1.0 GW ÷ 0.33 = 3.0 GW = 3.0 × 10⁹ J s⁻¹.
[Step 2] Fission rate: 3.0 × 10⁹ ÷ 3.2 × 10⁻¹¹ = 9.4 × 10¹⁹ fissions s⁻¹.
[Step 3] Per day: 9.4 × 10¹⁹ × 86 400 = 8.1 × 10²⁴ fissions = 13.5 mol, so m = 13.5 × 235 g ≈ 3.2 kg per day — a lump the size of a plum, against ~9000 tonnes of coal for the same output.

## Slide 29
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
≈ 9.4 × 10¹⁹ fissions per second; ≈ 3.2 kg of ²³⁵U per day
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 9.4 × 10¹⁹ fissions per second; ≈ 3.2 kg of ²³⁵U per day

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
Explain negative temperature feedback in a PWR, and why the same argument warns against designs where boiling increases reactivity.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Explain negative temperature feedback in a PWR, and why the same argument warns against designs where boiling increases reactivity.
[Answer] Hotter → thinner moderator + broader ²³⁸U resonances → k falls; separate-moderator designs can invert the sign, with historic consequences

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
Explain negative temperature feedback in a PWR, and why the same argument warns against designs where boiling increases reactivity.
1.
Power rises → water heats and expands → fewer moderator molecules per unit volume → fewer neutrons reach thermal energies → fission rate falls. Simultaneously, hotter fuel Doppler-broadens the ²³⁸U capture resonances, absorbing more neutrons mid-slowdown. Both effects cut k as temperature climbs: the excursion throttles itself.
2.
The feedback loop is stabilising precisely because the moderator and coolant are the same water — losing coolant also means losing moderation, which kills the chain rather than feeding it.
3.
In designs where a separate moderator (e.g. graphite) survives while the water coolant boils away, the water's neutron absorption vanishes and k can rise as the core overheats — a positive void coefficient. That inverted feedback was a central ingredient of the 1986 Chernobyl accident, and modern designs are required to avoid it.
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Power rises → water heats and expands → fewer moderator molecules per unit volume → fewer neutrons reach thermal energies → fission rate falls. Simultaneously, hotter fuel Doppler-broadens the ²³⁸U capture resonances, absorbing more neutrons mid-slowdown. Both effects cut k as temperature climbs: the excursion throttles itself.
[Step 2] The feedback loop is stabilising precisely because the moderator and coolant are the same water — losing coolant also means losing moderation, which kills the chain rather than feeding it.
[Step 3] In designs where a separate moderator (e.g. graphite) survives while the water coolant boils away, the water's neutron absorption vanishes and k can rise as the core overheats — a positive void coefficient. That inverted feedback was a central ingredient of the 1986 Chernobyl accident, and modern designs are required to avoid it.

## Slide 32
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
Hotter → thinner moderator + broader ²³⁸U resonances → k falls; separate-moderator designs can invert the sign, with historic consequences
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Hotter → thinner moderator + broader ²³⁸U resonances → k falls; separate-moderator designs can invert the sign, with historic consequences

## Slide 33
ADVANCED FISSION & FUSION
Where to go next
Plenary — What to take away, what to practise next
Next
26.3 Fusion & the Coulomb Barrier
https://giophysics.com/chapter-51/fusion-processes/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-51/fission-reactors/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-51/presentation/?lesson=reactors
Chapter
All Advanced Fission & Fusion lessons
https://giophysics.com/chapter-51/
PDF
Download the lesson PDF
https://giophysics.com/downloads/51-2-fission-reactors.pdf
ADVANCED FISSION & FUSION · INSIDE A FISSION REACTOR
GIOPHYSICS LESSON
Advanced Fission & Fusion — Inside a Fission Reactor. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
33 / 33
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-51/presentation/?lesson=reactors moves them.