## Slide 1
26 · Advanced Fission & Fusion
Grays, sieverts, and honest trade-offs
Radiation Safety & Nuclear Waste
Radiation is invisible, but it is one of the most precisely measured hazards humans manage: we count individual decays, weight them by how much they hurt living tissue, and compare the answer to the two-and-a-half millisieverts nature gives everyone for free each year. The same arithmetic sorts nuclear waste into what is fierce and brief versus faint and nearly forever.
POSITION
Lesson 5 of 6 in Advanced Fission & Fusion
PLAN
16 slides in the 45-minute core run, about 44.5 minutes of it
LESSON PAGE
https://giophysics.com/chapter-51/nuclear-safety/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 33
Notes: [Lesson] Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Lesson 5 of 6.
[Intro] Radiation is invisible, but it is one of the most precisely measured hazards humans manage: we count individual decays, weight them by how much they hurt living tissue, and compare the answer to the two-and-a-half millisieverts nature gives everyone for free each year. The same arithmetic sorts nuclear waste into what is fierce and brief versus faint and nearly forever.
[Source] https://giophysics.com/chapter-51/nuclear-safety/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Radioactive decay
https://giophysics.com/chapter-46/radioactivity/
Recall
Half-life & activity
https://giophysics.com/chapter-46/half-life/
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Radioactive decay; Half-life & activity

## Slide 3
THINK FIRST
A technician spends an hour beside a gamma source and walks out. Is she now, in any sense, radioactive?
Take answers before you click — the point is the commitment
It is the question every news report about a radiation incident gets wrong, and the answer decides what you should actually do about it — shield, or wash.
THE ANSWER
No. Gamma rays deposit energy and are gone; nothing is left behind to emit anything. Radioactivity transfers only by contamination — radioactive atoms physically on or in the body — or, rarely, by neutron activation. Irradiation calls for shielding and distance; contamination calls for washing and containment.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 33
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A technician spends an hour beside a gamma source and walks out. Is she now, in any sense, radioactive? It is the question every news report about a radiation incident gets wrong, and the answer decides what you should actually do about it — shield, or wash.
[Answer] No. Gamma rays deposit energy and are gone; nothing is left behind to emit anything. Radioactivity transfers only by contamination — radioactive atoms physically on or in the body — or, rarely, by neutron activation. Irradiation calls for shielding and distance; contamination calls for washing and containment.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Absorbed dose (gray = J kg⁻¹) measures energy deposited in tissue; equivalent dose (sievert) weights it by radiation type (w(R) = 1 for gammas and betas, 20 for alphas); protection means minimising time, maximising distance, and adding shielding — always judged against a natural background of ~2.4 mSv per year.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Absorbed dose (gray = J kg⁻¹) measures energy deposited in tissue; equivalent dose (sievert) weights it by radiation type (w(R) = 1 for gammas and betas, 20 for alphas); protection means minimising time, maximising distance, and adding shielding — always judged against a natural background of ~2.4 mSv per year.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A chest X-ray delivers about 0.1 mSv — the same as two weeks of ordinary background, or one long-haul flight's worth of extra cosmic rays. A single abdominal CT scan is about 7 mSv: three years of background, spent in a minute, and usually well worth the diagnosis.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A chest X-ray delivers about 0.1 mSv — the same as two weeks of ordinary background, or one long-haul flight's worth of extra cosmic rays. A single abdominal CT scan is about 7 mSv: three years of background, spent in a minute, and usually well worth the diagnosis.

## Slide 6
THE BIG IDEA
Grays, sieverts, and honest trade-offs
Introduce the idea — The big idea and the definition
Absorbed dose D measures raw energy deposited per kilogram of tissue: 1 gray (Gy) = 1 J kg⁻¹. But equal energy does not mean equal harm — a slow, densely ionising alpha particle wrecks far more per joule than a gamma ray — so the equivalent dose H = w(R) × D, in sieverts (Sv), multiplies by a radiation weighting factor: 1 for photons and betas, up to 20 for alphas. Everyone receives background radiation — radon from the ground, cosmic rays, our own potassium-40, medical imaging — totalling roughly 2.4 mSv per year, the baseline any risk must be compared against.
Exposure control is summarised as ALARA (as low as reasonably achievable), enforced by three levers: less time, more distance (intensity falls as 1/r²), and shielding (each half-value thickness cuts intensity by 2). Waste management is a trade-off written in half-lives: short-lived nuclides are intensely active but soon gone, long-lived ones barely whisper but persist for millennia — activity per nucleus is inversely proportional to half-life. Fusion's safety case differs in kind: no chain reaction to run away, fuel measured in grams, and no actinide waste — only activated structural material and the tritium inventory.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 33
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] Absorbed dose D measures raw energy deposited per kilogram of tissue: 1 gray (Gy) = 1 J kg⁻¹. But equal energy does not mean equal harm — a slow, densely ionising alpha particle wrecks far more per joule than a gamma ray — so the equivalent dose H = w(R) × D, in sieverts (Sv), multiplies by a radiation weighting factor: 1 for photons and betas, up to 20 for alphas. Everyone receives background radiation — radon from the ground, cosmic rays, our own potassium-40, medical imaging — totalling roughly 2.4 mSv per year, the baseline any risk must be compared against. Exposure control is summarised as ALARA (as low as reasonably achievable), enforced by three levers: less time, more distance (intensity falls as 1/r²), and shielding (each half-value thickness cuts intensity by 2). Waste management is a trade-off written in half-lives: short-lived nuclides are intensely active but soon gone, long-lived ones barely whisper but persist for millennia — activity per nucleus is inversely proportional to half-life. Fusion's safety case differs in kind: no chain reaction to run away, fuel measured in grams, and no actinide waste — only activated structural material and the tritium inventory.

## Slide 7
THE PHYSICS · 1 OF 3
What background really is
Build the model — The formulae, one at a time, in plain English
The world average is ~2.4 mSv per year: roughly half radon seeping from rock into buildings, the rest cosmic rays (higher at altitude — aircrews log a few extra mSv yearly), gamma rays from soil, and the potassium-40 built into every body. Regional geology moves the number tenfold with no detectable difference in health outcomes, which is why regulators frame limits as additions to background: 1 mSv per year extra for the public, 20 mSv averaged for radiation workers.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The world average is ~2.4 mSv per year: roughly half radon seeping from rock into buildings, the rest cosmic rays (higher at altitude — aircrews log a few extra mSv yearly), gamma rays from soil, and the potassium-40 built into every body. Regional geology moves the number tenfold with no detectable difference in health outcomes, which is why regulators frame limits as additions to background: 1 mSv per year extra for the public, 20 mSv averaged for radiation workers.

## Slide 8
THE PHYSICS · 2 OF 3
The half-life trade-off in waste
Build the model — The formulae, one at a time, in plain English
Activity is A = λN, and λ = ln 2/T½: for a fixed number of nuclei, activity is inversely proportional to half-life. So iodine-131 (8 days) is ferociously radioactive but effectively gone in three months, strontium-90 and caesium-137 (~29–30 years) dominate spent fuel's heat for its first three centuries, and plutonium-239 (24 100 years) barely registers on a counter yet demands geological patience. Nothing is both intensely active and long-lived — the product of the two is bounded, and waste strategy is built on that fact: cool the hot decades in ponds and casks, isolate the long millennia in deep rock.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Activity is A = λN, and λ = ln 2/T½: for a fixed number of nuclei, activity is inversely proportional to half-life. So iodine-131 (8 days) is ferociously radioactive but effectively gone in three months, strontium-90 and caesium-137 (~29–30 years) dominate spent fuel's heat for its first three centuries, and plutonium-239 (24 100 years) barely registers on a counter yet demands geological patience. Nothing is both intensely active and long-lived — the product of the two is bounded, and waste strategy is built on that fact: cool the hot decades in ponds and casks, isolate the long millennia in deep rock.

## Slide 9
THE PHYSICS · 3 OF 3
Fission versus fusion, safely compared
Build the model — The formulae, one at a time, in plain English
A fission core contains months of fuel and a decay-heat inventory that must be cooled even after shutdown — the true lesson of Fukushima. A fusion plasma contains about a gram of fuel: any fault cools and stops it within seconds, and there is no chain reaction to run away. Fusion's residues are the activated steel of the vessel (radioactive for decades, not millennia) and the tritium inventory (12.3-year half-life, weak beta) — real hazards, but ones that decay on an engineering timescale rather than a geological one.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A fission core contains months of fuel and a decay-heat inventory that must be cooled even after shutdown — the true lesson of Fukushima. A fusion plasma contains about a gram of fuel: any fault cools and stops it within seconds, and there is no chain reaction to run away. Fusion's residues are the activated steel of the vessel (radioactive for decades, not millennia) and the tritium inventory (12.3-year half-life, weak beta) — real hazards, but ones that decay on an engineering timescale rather than a geological one.

## Slide 10
FORMULA 1 OF 3
Absorbed dose
Build the model — The formulae, one at a time, in plain English
D = E/m · 1 Gy = 1 J kg⁻¹
Pure physics: energy per kilogram of tissue
IN PLAIN ENGLISH
The gray counts joules only. Half a joule of anything in a kilogram of tissue is 0.5 Gy — the number a calorimeter would give, blind to biology.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Absorbed dose: D = E/m · 1 Gy = 1 J kg⁻¹
[In plain English] The gray counts joules only. Half a joule of anything in a kilogram of tissue is 0.5 Gy — the number a calorimeter would give, blind to biology.
[Note] Pure physics: energy per kilogram of tissue

## Slide 11
FORMULA 2 OF 3
Equivalent dose
Build the model — The formulae, one at a time, in plain English
H = w(R) × D · in sieverts
w(R): photons, betas 1 · protons 2 · alphas 20
IN PLAIN ENGLISH
The sievert folds in biology. An alpha dumps its energy along a track a few cells long — dense, unrepairable damage — so each of its grays counts twenty-fold. Same joules, very different consequences.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Equivalent dose: H = w(R) × D · in sieverts
[In plain English] The sievert folds in biology. An alpha dumps its energy along a track a few cells long — dense, unrepairable damage — so each of its grays counts twenty-fold. Same joules, very different consequences.
[Note] w(R): photons, betas 1 · protons 2 · alphas 20

## Slide 12
FORMULA 3 OF 3
Distance and shielding
Build the model — The formulae, one at a time, in plain English
I ∝ 1/r² · I = I₀(½)^(x/x½)
x½ = half-value thickness of the shield
IN PLAIN ENGLISH
Doubling your distance quarters the dose rate before any shield is raised; each half-value thickness of lead or concrete halves what remains. Time, distance, shielding — cheapest first.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Distance and shielding: I ∝ 1/r² · I = I₀(½)^(x/x½)
[In plain English] Doubling your distance quarters the dose rate before any shield is raised; each half-value thickness of lead or concrete halves what remains. Time, distance, shielding — cheapest first.
[Note] x½ = half-value thickness of the shield

## Slide 13
PICTURE 1 OF 2
Time, distance, shielding
Drawn for this lesson
A sealed gamma source stands in its lead pot on a bench, with three rays fanning out to a lead shield one half-value thickness deep. Beyond the shield two faint rays continue to the same worker drawn twice, once at distance r and once at 2r, with both distances dimensioned along the bottom; a clock on the wall stands for the third lever.
The live version of this figure — click here
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A sealed gamma source stands in its lead pot on a bench, with three rays fanning out to a lead shield one half-value thickness deep. Beyond the shield two faint rays continue to the same worker drawn twice, once at distance r and once at 2r, with both distances dimensioned along the bottom; a clock on the wall stands for the third lever.

## Slide 14
PICTURE 2 OF 2
The dose everyone already has
Drawn for this lesson
The annual background dose drawn as a bar 2.4 mSv long on a scale of millisieverts, divided into radon at about 1.2, gamma rays from the ground at 0.5, cosmic rays at 0.4, and food and potassium-40 in the body at 0.3. A short bar above it, a twelfth the length of the radon segment alone, marks a single chest X-ray at 0.1 mSv.
The live version of this figure — click here
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] The annual background dose drawn as a bar 2.4 mSv long on a scale of millisieverts, divided into radon at about 1.2, gamma rays from the ground at 0.5, cosmic rays at 0.4, and food and potassium-40 in the body at 0.3. A short bar above it, a twelfth the length of the radon segment alone, marks a single chest X-ray at 0.1 mSv.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Being irradiated does not make you radioactive. Alpha, beta, and gamma radiation deposit energy and are gone — a patient after radiotherapy, or a chest X-ray, emits nothing.
Radioactivity transfers only by contamination (radioactive atoms physically sticking to or entering the body) or, rarely, by neutron activation. Confusing irradiation with contamination is the commonest error in radiation reporting — and it inverts the correct protective response: shield against the first, wash and contain the second.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Being irradiated does not make you radioactive. Alpha, beta, and gamma radiation deposit energy and are gone — a patient after radiotherapy, or a chest X-ray, emits nothing. Radioactivity transfers only by contamination (radioactive atoms physically sticking to or entering the body) or, rarely, by neutron activation. Confusing irradiation with contamination is the commonest error in radiation reporting — and it inverts the correct protective response: shield against the first, wash and contain the second.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A 60 kg worker's tissue absorbs 0.18 J of energy from alpha radiation (w(R) = 20). Find the absorbed dose and the equivalent dose.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 60 kg worker's tissue absorbs 0.18 J of energy from alpha radiation (w(R) = 20). Find the absorbed dose and the equivalent dose.
[Answer] D = 3.0 mGy; H = 60 mSv

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A 60 kg worker's tissue absorbs 0.18 J of energy from alpha radiation (w(R) = 20). Find the absorbed dose and the equivalent dose.
1.
D = E/m = 0.18 ÷ 60 = 3.0 × 10⁻³ Gy = 3.0 mGy.
2.
H = w(R) × D = 20 × 3.0 = 60 mSv.
3.
Sixty millisieverts is three times the annual limit for radiation workers — the same 0.18 J of gamma rays would have been 3 mSv, twenty times less consequential.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] D = E/m = 0.18 ÷ 60 = 3.0 × 10⁻³ Gy = 3.0 mGy.
[Step 2] H = w(R) × D = 20 × 3.0 = 60 mSv.
[Step 3] Sixty millisieverts is three times the annual limit for radiation workers — the same 0.18 J of gamma rays would have been 3 mSv, twenty times less consequential.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
D = 3.0 mGy; H = 60 mSv
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] D = 3.0 mGy; H = 60 mSv

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A gamma source must have its dose rate cut by a factor of 8. The half-value thickness of lead for this energy is 12 mm. How much lead is needed?
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A gamma source must have its dose rate cut by a factor of 8. The half-value thickness of lead for this energy is 12 mm. How much lead is needed?
[Answer] 36 mm of lead

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A gamma source must have its dose rate cut by a factor of 8. The half-value thickness of lead for this energy is 12 mm. How much lead is needed?
1.
Each half-value thickness halves the intensity: 8 = 2³, so three thicknesses are needed.
2.
x = 3 × 12 = 36 mm.
3.
Check with I = I₀(½)^(x/x½): (½)^(36/12) = (½)³ = 1/8 ✓.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Each half-value thickness halves the intensity: 8 = 2³, so three thicknesses are needed.
[Step 2] x = 3 × 12 = 36 mm.
[Step 3] Check with I = I₀(½)^(x/x½): (½)^(36/12) = (½)³ = 1/8 ✓.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
36 mm of lead
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 36 mm of lead

## Slide 22
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A source gives 48 µSv/h at 1.0 m. A technician works for 30 minutes at 2.0 m. Find the dose.
2.
Inverse square: at 2.0 m the rate is 48 ÷ 2 = 24 µSv/h.
3.
Time = 30 minutes = 0.5 h.
4.
Dose = 24 × 0.5 = 12 µSv.
5.
About twice a day's worth of natural background.
LINE 2 IS WRONG
Intensity falls as 1/r², so doubling the distance divides the rate by 2² = 4, not by 2. Dividing by the distance ratio itself is the classic slip because the words 'twice as far' sit so naturally beside 'half as much' — and the answer that follows is wrong by a factor of two rather than an obvious mile, so nothing looks amiss.
IT SHOULD SAY
At 2.0 m the rate is 48 ÷ 2² = 12 µSv/h.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 2 is wrong] Intensity falls as 1/r², so doubling the distance divides the rate by 2² = 4, not by 2. Dividing by the distance ratio itself is the classic slip because the words 'twice as far' sit so naturally beside 'half as much' — and the answer that follows is wrong by a factor of two rather than an obvious mile, so nothing looks amiss.
[It should say] At 2.0 m the rate is 48 ÷ 2² = 12 µSv/h.

## Slide 23
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The sealed source is returned to its safe at the end of the day. Is the bench it stood on now radioactive?
A Yes — everything the beam fell on has been made radioactive by the exposure
B No — the gamma rays deposited their energy and were gone; only spilled radioactive material would leave anything behind
C Only the lead shield, because it absorbed the most radiation of anything in the room
A sealed gamma source stands in its lead pot on a bench, with three rays fanning out to a lead shield one half-value thickness deep. Beyond the shield two faint rays continue to the same worker drawn twice, once at distance r and once at 2r, with both distances dimensioned along the bottom; a clock on the wall stands for the third lever.
The live version of this figure — click here
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The sealed source is returned to its safe at the end of the day. Is the bench it stood on now radioactive?
[Options] A Yes — everything the beam fell on has been made radioactive by the exposure B No — the gamma rays deposited their energy and were gone; only spilled radioactive material would leave anything behind C Only the lead shield, because it absorbed the most radiation of anything in the room
[Figure] A sealed gamma source stands in its lead pot on a bench, with three rays fanning out to a lead shield one half-value thickness deep. Beyond the shield two faint rays continue to the same worker drawn twice, once at distance r and once at 2r, with both distances dimensioned along the bottom; a clock on the wall stands for the third lever.

## Slide 24
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B No — the gamma rays deposited their energy and were gone; only spilled radioactive material would leave anything behind
WHY
Look at what the picture actually shows: rays leaving a sealed source, being absorbed, and ending. Absorbing a gamma ray changes a tissue's or a bench's energy, not its nuclei. The source is sealed, so no radioactive atoms ever left the pot — and that is the difference between irradiation and contamination.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 33
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — No — the gamma rays deposited their energy and were gone; only spilled radioactive material would leave anything behind. Look at what the picture actually shows: rays leaving a sealed source, being absorbed, and ending. Absorbing a gamma ray changes a tissue's or a bench's energy, not its nuclei. The source is sealed, so no radioactive atoms ever left the pot — and that is the difference between irradiation and contamination.

## Slide 25
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Equivalent dose in sieverts differs from absorbed dose in grays because it…
A
Weights the energy by how damaging each radiation type is to tissue
B
Measures the total energy rather than the energy per kilogram
C
Subtracts the natural background before quoting the result
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Equivalent dose in sieverts differs from absorbed dose in grays because it…
[Options] A Weights the energy by how damaging each radiation type is to tissue B Measures the total energy rather than the energy per kilogram C Subtracts the natural background before quoting the result

## Slide 26
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
A Weights the energy by how damaging each radiation type is to tissue
HOW TO GET THERE
H = w(R) × D: same physics energy, multiplied by a factor for biological effectiveness — 1 for photons and betas, 20 for alphas. Sieverts are the unit risk limits are written in precisely because they carry that weighting.
WHY THE OTHERS TEMPT
A Correct. H = w(R) × D takes the same physical joules per kilogram and multiplies by a factor for biological effectiveness: 1 for photons and betas, up to 20 for alphas, which dump their energy densely along a track a few cells long. Dose limits are written in sieverts precisely because sieverts carry that weighting.
B Tempting because 'equivalent' sounds like a bigger, more total quantity than 'absorbed'. But both are per kilogram — the gray is defined as one joule per kilogram and the sievert inherits exactly that. The difference between them is a dimensionless weighting factor, not a change of what is divided by what.
C Tempting because doses genuinely are quoted as additions to background — the public limit of 1 mSv a year is an extra 1 mSv. But that subtraction is done when a limit is written, not by the unit. A sievert is a sievert whether it comes from a source or from radon, and the equivalent dose from a scan is quoted in full.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 33
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Equivalent dose in sieverts differs from absorbed dose in grays because it…
[Option by option] A: Correct. H = w(R) × D takes the same physical joules per kilogram and multiplies by a factor for biological effectiveness: 1 for photons and betas, up to 20 for alphas, which dump their energy densely along a track a few cells long. Dose limits are written in sieverts precisely because sieverts carry that weighting. B: Tempting because 'equivalent' sounds like a bigger, more total quantity than 'absorbed'. But both are per kilogram — the gray is defined as one joule per kilogram and the sievert inherits exactly that. The difference between them is a dimensionless weighting factor, not a change of what is divided by what. C: Tempting because doses genuinely are quoted as additions to background — the public limit of 1 mSv a year is an extra 1 mSv. But that subtraction is done when a limit is written, not by the unit. A sievert is a sievert whether it comes from a source or from radon, and the equivalent dose from a scan is quoted in full.
[Answer] A — Weights the energy by how damaging each radiation type is to tissue
[Why] H = w(R) × D: same physics energy, multiplied by a factor for biological effectiveness — 1 for photons and betas, 20 for alphas. Sieverts are the unit risk limits are written in precisely because they carry that weighting.
[Reveal] One click for the answer, then one for the reason.

## Slide 27
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A source gives 48 µSv/h at 1.0 m. A technician works for 30 minutes at 2.0 m. Find the dose received and compare it with daily background (2.4 mSv per year).
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A source gives 48 µSv/h at 1.0 m. A technician works for 30 minutes at 2.0 m. Find the dose received and compare it with daily background (2.4 mSv per year).
[Answer] 6 µSv — roughly one day of natural background

## Slide 28
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A source gives 48 µSv/h at 1.0 m. A technician works for 30 minutes at 2.0 m. Find the dose received and compare it with daily background (2.4 mSv per year).
1.
Inverse square: at 2.0 m the rate is 48 ÷ 2² = 12 µSv/h.
2.
Dose = 12 × 0.5 = 6 µSv.
3.
Daily background = 2400 µSv ÷ 365 ≈ 6.6 µSv — the job cost about one ordinary day of background. Halving the distance instead would have quadrupled it: distance is the cheapest shield.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Inverse square: at 2.0 m the rate is 48 ÷ 2² = 12 µSv/h.
[Step 2] Dose = 12 × 0.5 = 6 µSv.
[Step 3] Daily background = 2400 µSv ÷ 365 ≈ 6.6 µSv — the job cost about one ordinary day of background. Halving the distance instead would have quadrupled it: distance is the cheapest shield.

## Slide 29
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
6 µSv — roughly one day of natural background
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 6 µSv — roughly one day of natural background

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
Equal numbers of ⁹⁰Sr nuclei (T½ = 29 y) and ²³⁹Pu nuclei (T½ = 24 100 y) sit in a waste canister. Compare their activities now, and their populations after 300 years. What waste strategy do these numbers dictate?
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Equal numbers of ⁹⁰Sr nuclei (T½ = 29 y) and ²³⁹Pu nuclei (T½ = 24 100 y) sit in a waste canister. Compare their activities now, and their populations after 300 years. What waste strategy do these numbers dictate?
[Answer] Sr-90 is ~830× hotter now but 1300× depleted in 300 y; Pu-239 barely changes — hence casks for centuries, geology for millennia

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
Equal numbers of ⁹⁰Sr nuclei (T½ = 29 y) and ²³⁹Pu nuclei (T½ = 24 100 y) sit in a waste canister. Compare their activities now, and their populations after 300 years. What waste strategy do these numbers dictate?
1.
A = λN with λ = ln 2/T½, so for equal N: A(Sr)/A(Pu) = T½(Pu)/T½(Sr) = 24 100 ÷ 29 ≈ 830. The strontium is ~830 times more active — it dominates the canister's early heat and hazard.
2.
After 300 y ≈ 10.3 strontium half-lives: N(Sr) falls by 2^10.3 ≈ 1300×. For plutonium, 300/24 100 half-lives leaves e^(−λt) = (½)^0.0124 ≈ 0.991 — 99% remains.
3.
Hence the two-stage strategy: engineered cooling and monitoring for the fierce first centuries (ponds, dry casks), then deep geological isolation for the quiet, patient actinides. No single container problem — two different problems on two different clocks.
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] A = λN with λ = ln 2/T½, so for equal N: A(Sr)/A(Pu) = T½(Pu)/T½(Sr) = 24 100 ÷ 29 ≈ 830. The strontium is ~830 times more active — it dominates the canister's early heat and hazard.
[Step 2] After 300 y ≈ 10.3 strontium half-lives: N(Sr) falls by 2^10.3 ≈ 1300×. For plutonium, 300/24 100 half-lives leaves e^(−λt) = (½)^0.0124 ≈ 0.991 — 99% remains.
[Step 3] Hence the two-stage strategy: engineered cooling and monitoring for the fierce first centuries (ponds, dry casks), then deep geological isolation for the quiet, patient actinides. No single container problem — two different problems on two different clocks.

## Slide 32
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
Sr-90 is ~830× hotter now but 1300× depleted in 300 y; Pu-239 barely changes — hence casks for centuries, geology for millennia
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 33
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Sr-90 is ~830× hotter now but 1300× depleted in 300 y; Pu-239 barely changes — hence casks for centuries, geology for millennia

## Slide 33
ADVANCED FISSION & FUSION
Where to go next
Plenary — What to take away, what to practise next
Next
26.6 Fission & Fusion Calculus
https://giophysics.com/chapter-51/fission-fusion-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-51/nuclear-safety/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-51/presentation/?lesson=safety
Chapter
All Advanced Fission & Fusion lessons
https://giophysics.com/chapter-51/
PDF
Download the lesson PDF
https://giophysics.com/downloads/51-5-nuclear-safety.pdf
ADVANCED FISSION & FUSION · RADIATION SAFETY & NUCLEAR WASTE
GIOPHYSICS LESSON
Advanced Fission & Fusion — Radiation Safety & Nuclear Waste. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
33 / 33
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-51/presentation/?lesson=safety moves them.