## Slide 1
29 · Medical Physics
Solving for the interior
CT Scanning
A plain X-ray flattens you into one shadow — heart, spine, and sternum all printed on the same spot. CT asks a sharper question: what is the attenuation at every point inside? Spin the beam, measure thousands of shadows, and let a computer solve for the interior.
POSITION
Lesson 2 of 6 in Medical Physics
PLAN
16 slides in the 45-minute core run, about 45 minutes of it
LESSON PAGE
https://giophysics.com/chapter-57/ct-scanning/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Medical Physics — CT Scanning. Lesson 2 of 6.
[Intro] A plain X-ray flattens you into one shadow — heart, spine, and sternum all printed on the same spot. CT asks a sharper question: what is the attenuation at every point inside? Spin the beam, measure thousands of shadows, and let a computer solve for the interior.
[Source] https://giophysics.com/chapter-57/ct-scanning/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
X-ray imaging
https://giophysics.com/chapter-57/x-ray-imaging/
Recall
Electromagnetic waves
https://giophysics.com/chapter-24/electromagnetic-waves/
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: X-ray imaging; Electromagnetic waves

## Slide 3
THINK FIRST
A CT scanner and a chest X-ray use the same X-rays and much the same detectors. So how does the CT see a 1% difference between two soft tissues that the X-ray cannot see at all?
Take answers before you click — the point is the commitment
Both send a beam through the patient and measure what comes out the other side. The CT is not using a more powerful beam, and its detectors are not a hundred times better.
THE ANSWER
It is not the hardware — it is the arithmetic. On a plain film, a 1% difference in one centimetre of tissue is buried in the total of everything else along that line. The CT measures line totals from hundreds of directions and solves for each voxel separately, so the 1% is compared with its neighbours rather than with the whole chest.
A CT gantry seen end-on: the X-ray tube at the top, a curved bank of detector elements filling the arc below, the patient drawn as an ellipse at the centre, a fan of rays spreading from the tube through the patient to the detectors, and an arc arrow showing the whole assembly rotating about the patient.
The live version of this figure — click here
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A CT scanner and a chest X-ray use the same X-rays and much the same detectors. So how does the CT see a 1% difference between two soft tissues that the X-ray cannot see at all? Both send a beam through the patient and measure what comes out the other side. The CT is not using a more powerful beam, and its detectors are not a hundred times better.
[Answer] It is not the hardware — it is the arithmetic. On a plain film, a 1% difference in one centimetre of tissue is buried in the total of everything else along that line. The CT measures line totals from hundreds of directions and solves for each voxel separately, so the 1% is compared with its neighbours rather than with the whole chest.
[Figure] A CT gantry seen end-on: the X-ray tube at the top, a curved bank of detector elements filling the arc below, the patient drawn as an ellipse at the centre, a fan of rays spreading from the tube through the patient to the detectors, and an arc arrow showing the whole assembly rotating about the patient.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
CT scanning measures X-ray transmission along many directions through a thin slice, treats each reading as a sum of voxel attenuations along a line, and computes every voxel's μ by back-projection; stacked slices build a 3-D image.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] CT scanning measures X-ray transmission along many directions through a thin slice, treats each reading as a sum of voxel attenuations along a line, and computes every voxel's μ by back-projection; stacked slices build a 3-D image.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
A 2 × 2 slice probed by row, column and diagonal beams gives enough ray sums to solve all four voxels. A real scanner does the same bookkeeping for a 512 × 512 grid using around a thousand projection angles.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] A 2 × 2 slice probed by row, column and diagonal beams gives enough ray sums to solve all four voxels. A real scanner does the same bookkeeping for a 512 × 512 grid using around a thousand projection angles.

## Slide 6
THE BIG IDEA
Solving for the interior
Introduce the idea — The big idea and the definition
In a CT scanner an X-ray tube and an arc of detectors rotate around the patient, firing a fan beam through one thin slice from hundreds of angles. Each detector reading is a ray sum — the total attenuation accumulated along one line through the slice. A single projection cannot say where along the line the absorption happened, but many directions can: divide the slice into a grid of voxels and the ray sums become simultaneous equations for the voxel values.
The computer recovers them by back-projection — smear each ray sum back along its path, add the smears from every angle, then subtract the uniform background and rescale, and each voxel's attenuation emerges. Stacking the reconstructed slices while the couch glides through the gantry builds a full 3-D map of μ that can be re-sliced in any plane. The price is dose — a CT scan can equal a hundred or more chest X-rays — so CT is reserved for questions where the three-dimensional answer changes the treatment.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] In a CT scanner an X-ray tube and an arc of detectors rotate around the patient, firing a fan beam through one thin slice from hundreds of angles. Each detector reading is a ray sum — the total attenuation accumulated along one line through the slice. A single projection cannot say where along the line the absorption happened, but many directions can: divide the slice into a grid of voxels and the ray sums become simultaneous equations for the voxel values. The computer recovers them by back-projection — smear each ray sum back along its path, add the smears from every angle, then subtract the uniform background and rescale, and each voxel's attenuation emerges. Stacking the reconstructed slices while the couch glides through the gantry builds a full 3-D map of μ that can be re-sliced in any plane. The price is dose — a CT scan can equal a hundred or more chest X-rays — so CT is reserved for questions where the three-dimensional answer changes the treatment.

## Slide 7
THE PHYSICS · 1 OF 3
The hardware
Build the model — The formulae, one at a time, in plain English
The tube and a curved bank of detectors sit on a gantry spinning several times a second while the patient's couch moves steadily through it, tracing a helix. Each rotation collects hundreds of projections of one slice; the slice thickness (a millimetre or less) sets the resolution along the body's axis. Modern scanners image a chest in a single held breath.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The tube and a curved bank of detectors sit on a gantry spinning several times a second while the patient's couch moves steadily through it, tracing a helix. Each rotation collects hundreds of projections of one slice; the slice thickness (a millimetre or less) sets the resolution along the body's axis. Modern scanners image a chest in a single held breath.

## Slide 8
THE PHYSICS · 2 OF 3
Walking the 2 × 2 example
Build the model — The formulae, one at a time, in plain English
Take voxels A = 5, B = 2, C = 1, D = 4. The measured ray sums are rows 7 and 5, columns 6 and 6, and both diagonals: A + D = 9 and B + C = 3. Back-project onto A every ray that crosses it: (A+B) + (A+C) + (A+D) = 22.
But 22 = 2A + S, where S = 12 is the whole slice — every ray drags the rest of the slice in once. Subtract S and halve: (22 − 12)/2 = 5 = A. The same subtraction recovers B, C and D — at B, (A+B) + (B+D) + (B+C) = 7 + 6 + 3 = 16 and (16 − 12)/2 = 2.
Every voxel needs all three of its rays — row, column and diagonal — which is why a real scanner repeats exactly this logic a quarter of a million times per slice.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Take voxels A = 5, B = 2, C = 1, D = 4. The measured ray sums are rows 7 and 5, columns 6 and 6, and both diagonals: A + D = 9 and B + C = 3. Back-project onto A every ray that crosses it: (A+B) + (A+C) + (A+D) = 22. But 22 = 2A + S, where S = 12 is the whole slice — every ray drags the rest of the slice in once. Subtract S and halve: (22 − 12)/2 = 5 = A. The same subtraction recovers B, C and D — at B, (A+B) + (B+D) + (B+C) = 7 + 6 + 3 = 16 and (16 − 12)/2 = 2. Every voxel needs all three of its rays — row, column and diagonal — which is why a real scanner repeats exactly this logic a quarter of a million times per slice.

## Slide 9
THE PHYSICS · 3 OF 3
When the dose is worth it
Build the model — The formulae, one at a time, in plain English
CT distinguishes soft tissues whose μ differs by under 1%, locates anything in true 3-D for surgery or radiotherapy planning, and takes seconds — decisive for stroke and internal bleeding. But a body CT delivers several millisieverts against roughly 0.1 mSv for a chest X-ray, so the justification test is always the same: will seeing the interior in three dimensions change what happens to the patient?
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] CT distinguishes soft tissues whose μ differs by under 1%, locates anything in true 3-D for surgery or radiotherapy planning, and takes seconds — decisive for stroke and internal bleeding. But a body CT delivers several millisieverts against roughly 0.1 mSv for a chest X-ray, so the justification test is always the same: will seeing the interior in three dimensions change what happens to the patient?

## Slide 10
FORMULA 1 OF 3
Ray sum
Build the model — The formulae, one at a time, in plain English
P = μ₁x₁ + μ₂x₂ + …
one detector reading = attenuation totalled along a line
IN PLAIN ENGLISH
Exponentials multiply along a path, so their exponents add: taking a logarithm of the measured transmission turns each ray into a simple sum of the voxels it crossed.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Ray sum: P = μ₁x₁ + μ₂x₂ + …
[In plain English] Exponentials multiply along a path, so their exponents add: taking a logarithm of the measured transmission turns each ray into a simple sum of the voxels it crossed.
[Note] one detector reading = attenuation totalled along a line

## Slide 11
FORMULA 2 OF 3
Voxels
Build the model — The formulae, one at a time, in plain English
slice = grid of volume elements
512 × 512 voxels is routine — over 260 000 unknowns per slice
IN PLAIN ENGLISH
Each voxel is a little box of tissue with one unknown number μ. The scan must collect at least as many independent ray sums as there are voxels — which is why the tube goes right round.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Voxels: slice = grid of volume elements
[In plain English] Each voxel is a little box of tissue with one unknown number μ. The scan must collect at least as many independent ray sums as there are voxels — which is why the tube goes right round.
[Note] 512 × 512 voxels is routine — over 260 000 unknowns per slice

## Slide 12
FORMULA 3 OF 3
Back-projection
Build the model — The formulae, one at a time, in plain English
voxel ← Σ (ray sums through it)
then subtract the background and rescale
IN PLAIN ENGLISH
Adding every ray through a voxel counts that voxel once per ray but also drags in everything else once. Subtract the total of the slice and what is left is the voxel itself, amplified — divide down and the interior appears.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Back-projection: voxel ← Σ (ray sums through it)
[In plain English] Adding every ray through a voxel counts that voxel once per ray but also drags in everything else once. Subtract the total of the slice and what is left is the voxel itself, amplified — divide down and the interior appears.
[Note] then subtract the background and rescale

## Slide 13
THE PICTURE
Four voxels, six totals
Drawn for this lesson
A slice divided into a 2 × 2 grid of voxels labelled A, B, C and D, with arrows crossing it along both rows, along both columns and along the main diagonal, each arrow annotated outside the grid with the sum of the voxels it passes through and none of the voxel values given.
The live version of this figure — click here
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A slice divided into a 2 × 2 grid of voxels labelled A, B, C and D, with arrows crossing it along both rows, along both columns and along the main diagonal, each arrow annotated outside the grid with the sum of the voxels it passes through and none of the voxel values given.

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A CT slice is not a photograph taken from many angles. No single measurement sees any point inside the patient at all — every reading is a line total, blind to where along the line the attenuation happened. Position information exists only in the mathematics that intersects rays from different directions.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A CT slice is not a photograph taken from many angles. No single measurement sees any point inside the patient at all — every reading is a line total, blind to where along the line the attenuation happened. Position information exists only in the mathematics that intersects rays from different directions.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A 2 × 2 slice has voxel values A = 3, B = 1, C = 2, D = 6. Write down the six ray sums a scanner would measure (two rows, two columns, two diagonals).
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A 2 × 2 slice has voxel values A = 3, B = 1, C = 2, D = 6. Write down the six ray sums a scanner would measure (two rows, two columns, two diagonals).
[Answer] Rows 4, 8 · columns 5, 7 · diagonals 9, 3

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A 2 × 2 slice has voxel values A = 3, B = 1, C = 2, D = 6. Write down the six ray sums a scanner would measure (two rows, two columns, two diagonals).
1.
Rows: A + B = 4 and C + D = 8.
2.
Columns: A + C = 5 and B + D = 7.
3.
Diagonals: A + D = 9 and B + C = 3.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Rows: A + B = 4 and C + D = 8.
[Step 2] Columns: A + C = 5 and B + D = 7.
[Step 3] Diagonals: A + D = 9 and B + C = 3.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
Rows 4, 8 · columns 5, 7 · diagonals 9, 3
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Rows 4, 8 · columns 5, 7 · diagonals 9, 3

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
A scanner measures rows 9 and 7, columns 10 and 6, and diagonal A + D = 9. Reconstruct the four voxels.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A scanner measures rows 9 and 7, columns 10 and 6, and diagonal A + D = 9. Reconstruct the four voxels.
[Answer] A = 6, B = 3, C = 4, D = 3 — the diagonal ray supplied the missing information

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
A scanner measures rows 9 and 7, columns 10 and 6, and diagonal A + D = 9. Reconstruct the four voxels.
1.
Rows and columns alone are not enough: adding k to A and D while subtracting k from B and C leaves every row and column sum unchanged — a whole family of answers.
2.
The diagonal breaks the tie, because A + D + 2k changes with k. Write B = 9 − A, C = 10 − A, D = A − 3 (from C + D = 7).
3.
Then A + D = 2A − 3 = 9 gives A = 6, so B = 3, C = 4, D = 3. Check: rows 9, 7 ✓, columns 10, 6 ✓.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Rows and columns alone are not enough: adding k to A and D while subtracting k from B and C leaves every row and column sum unchanged — a whole family of answers.
[Step 2] The diagonal breaks the tie, because A + D + 2k changes with k. Write B = 9 − A, C = 10 − A, D = A − 3 (from C + D = 7).
[Step 3] Then A + D = 2A − 3 = 9 gives A = 6, so B = 3, C = 4, D = 3. Check: rows 9, 7 ✓, columns 10, 6 ✓.

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
A = 6, B = 3, C = 4, D = 3 — the diagonal ray supplied the missing information
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] A = 6, B = 3, C = 4, D = 3 — the diagonal ray supplied the missing information

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
A scanner measures rows 9 and 7 and columns 10 and 6, with the diagonal A + D = 9. Reconstruct the four voxels.
2.
A + B = 9, C + D = 7, A + C = 10, B + D = 6, A + D = 9
3.
Adding the two rows gives the slice total S = 16.
4.
Back-project onto A: (A + B) + (A + C) + (A + D) = 9 + 10 + 9 = 28
5.
That raw figure is 28, so A = 28 − S = 28 − 16 = 12
6.
Then B = 9 − 12 = −3, C = 10 − 12 = −2, D = 9 − 12 = −3.
LINE 5 IS WRONG
The back-projected total is not A + S but 2A + S: each of the three rays through A carries an A of its own, and the other three voxels between them make up one complete slice total. So 28 = 2A + 16, giving A = 6, and then B = 3, C = 4, D = 3. The line as written forgets that the voxel being solved for is counted three times, once by every ray, and the answer says so loudly — negative attenuation coefficients would mean tissue that adds intensity to a beam passing through it.
IT SHOULD SAY
That raw figure is 2A + S, so A = (28 − 16)/2 = 6
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 5 is wrong] The back-projected total is not A + S but 2A + S: each of the three rays through A carries an A of its own, and the other three voxels between them make up one complete slice total. So 28 = 2A + 16, giving A = 6, and then B = 3, C = 4, D = 3. The line as written forgets that the voxel being solved for is counted three times, once by every ray, and the answer says so loudly — negative attenuation coefficients would mean tissue that adds intensity to a beam passing through it.
[It should say] That raw figure is 2A + S, so A = (28 − 16)/2 = 6

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The scanner measures only the two row totals and the two column totals — four numbers for four unknown voxels. Can it solve the slice?
A Yes — four equations and four unknowns is exactly enough
B No — the four are not independent, because the rows and the columns both add up to the same grand total, so a diagonal ray is needed as well
C No — a 2 × 2 slice would need at least sixteen readings
A slice divided into a 2 × 2 grid of voxels labelled A, B, C and D, with arrows crossing it along both rows, along both columns and along the main diagonal, each arrow annotated outside the grid with the sum of the voxels it passes through and none of the voxel values given.
The live version of this figure — click here
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The scanner measures only the two row totals and the two column totals — four numbers for four unknown voxels. Can it solve the slice?
[Options] A Yes — four equations and four unknowns is exactly enough B No — the four are not independent, because the rows and the columns both add up to the same grand total, so a diagonal ray is needed as well C No — a 2 × 2 slice would need at least sixteen readings
[Figure] A slice divided into a 2 × 2 grid of voxels labelled A, B, C and D, with arrows crossing it along both rows, along both columns and along the main diagonal, each arrow annotated outside the grid with the sum of the voxels it passes through and none of the voxel values given.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B No — the four are not independent, because the rows and the columns both add up to the same grand total, so a diagonal ray is needed as well
WHY
Count what the four equations actually say. (A + B) + (C + D) is the total of the slice, and so is (A + C) + (B + D) — the same number twice, so the fourth equation carries no news the first three had not already given. Three independent equations cannot fix four unknowns, and the missing one has to cross the grid in a direction the rows and columns do not: A + D. That is the mathematical content of rotating the gantry, in the smallest case anyone can do by hand.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — No — the four are not independent, because the rows and the columns both add up to the same grand total, so a diagonal ray is needed as well. Count what the four equations actually say. (A + B) + (C + D) is the total of the slice, and so is (A + C) + (B + D) — the same number twice, so the fourth equation carries no news the first three had not already given. Three independent equations cannot fix four unknowns, and the missing one has to cross the grid in a direction the rows and columns do not: A + D. That is the mathematical content of rotating the gantry, in the smallest case anyone can do by hand.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Why must the X-ray tube and detectors rotate right around the patient?
A
To average out random detector noise
B
Because one direction only gives line totals — depth along the beam is invisible until rays from other angles cross it
C
To spread the dose over more skin
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Why must the X-ray tube and detectors rotate right around the patient?
[Options] A To average out random detector noise B Because one direction only gives line totals — depth along the beam is invisible until rays from other angles cross it C To spread the dose over more skin

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B Because one direction only gives line totals — depth along the beam is invisible until rays from other angles cross it
HOW TO GET THERE
A single projection collapses each line to one number. Only when rays from many angles intersect can the computer solve for where the attenuation actually sits — the crossing is the imaging.
WHY THE OTHERS TEMPT
A Rotation does help with noise, since every voxel ends up sampled by many rays and the errors partly average out. But that is a bonus rather than the reason: a perfectly noiseless single projection would still be unable to say where along each line the absorption happened.
B Correct. A single projection collapses each line to one number, and only when rays from many angles intersect can the computer solve for where the attenuation actually sits.
C Dose really is spread over the skin as the tube goes round, which is a genuine advantage of the geometry and is why this sounds plausible. It is not the purpose, though — a CT delivers several millisieverts against a chest film's fraction of one, so rotation buys information, and pays for it in dose rather than saving it.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Why must the X-ray tube and detectors rotate right around the patient?
[Option by option] A: Rotation does help with noise, since every voxel ends up sampled by many rays and the errors partly average out. But that is a bonus rather than the reason: a perfectly noiseless single projection would still be unable to say where along each line the absorption happened. B: Correct. A single projection collapses each line to one number, and only when rays from many angles intersect can the computer solve for where the attenuation actually sits. C: Dose really is spread over the skin as the tube goes round, which is a genuine advantage of the geometry and is why this sounds plausible. It is not the purpose, though — a CT delivers several millisieverts against a chest film's fraction of one, so rotation buys information, and pays for it in dose rather than saving it.
[Answer] B — Because one direction only gives line totals — depth along the beam is invisible until rays from other angles cross it
[Why] A single projection collapses each line to one number. Only when rays from many angles intersect can the computer solve for where the attenuation actually sits — the crossing is the imaging.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
Using the voxels A = 6, B = 3, C = 4, D = 3, carry out the back-projection: add onto each voxel every ray sum passing through it, then recover the true values.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Using the voxels A = 6, B = 3, C = 4, D = 3, carry out the back-projection: add onto each voxel every ray sum passing through it, then recover the true values.
[Answer] Raw 28, 22, 24, 22 → subtract S = 16, halve → A = 6, B = 3, C = 4, D = 3 ✓

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
Using the voxels A = 6, B = 3, C = 4, D = 3, carry out the back-projection: add onto each voxel every ray sum passing through it, then recover the true values.
1.
S = A + B + C + D = 16. Rays: rows 9, 7; columns 10, 6; diagonals A + D = 9, B + C = 7.
2.
Raw back-projection at A: (A+B) + (A+C) + (A+D) = 9 + 10 + 9 = 28. At B: 9 + 6 + 7 = 22. At C: 7 + 10 + 7 = 24. At D: 7 + 6 + 9 = 22.
3.
Each raw value equals 2 × voxel + S: (28 − 16)/2 = 6, (22 − 16)/2 = 3, (24 − 16)/2 = 4, (22 − 16)/2 = 3.
4.
The blurry raw image (every voxel contaminated by the whole slice) turns exact after one subtraction and one division — that is the essence of CT reconstruction.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] S = A + B + C + D = 16. Rays: rows 9, 7; columns 10, 6; diagonals A + D = 9, B + C = 7.
[Step 2] Raw back-projection at A: (A+B) + (A+C) + (A+D) = 9 + 10 + 9 = 28. At B: 9 + 6 + 7 = 22. At C: 7 + 10 + 7 = 24. At D: 7 + 6 + 9 = 22.
[Step 3] Each raw value equals 2 × voxel + S: (28 − 16)/2 = 6, (22 − 16)/2 = 3, (24 − 16)/2 = 4, (22 − 16)/2 = 3.
[Step 4] The blurry raw image (every voxel contaminated by the whole slice) turns exact after one subtraction and one division — that is the essence of CT reconstruction.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
Raw 28, 22, 24, 22 → subtract S = 16, halve → A = 6, B = 3, C = 4, D = 3 ✓
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Raw 28, 22, 24, 22 → subtract S = 16, halve → A = 6, B = 3, C = 4, D = 3 ✓

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
A slice is reconstructed on a 512 × 512 grid using a detector arc of 800 elements. Estimate the minimum number of projection angles needed, and explain why a CT head scan is justified for a suspected stroke but not for a routine headache.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A slice is reconstructed on a 512 × 512 grid using a detector arc of 800 elements. Estimate the minimum number of projection angles needed, and explain why a CT head scan is justified for a suspected stroke but not for a routine headache.
[Answer] ≥ ~330 angles (≈ 1000 in practice); dose is justified only when the 3-D answer changes the treatment

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
A slice is reconstructed on a 512 × 512 grid using a detector arc of 800 elements. Estimate the minimum number of projection angles needed, and explain why a CT head scan is justified for a suspected stroke but not for a routine headache.
1.
Unknowns: 512² ≈ 2.6 × 10⁵ voxel values. Each projection contributes at most 800 independent ray sums.
2.
Minimum angles ≈ 2.6 × 10⁵ ÷ 800 ≈ 330 — real scanners use about a thousand, because overlapping rays are not fully independent and noise demands redundancy.
3.
Stroke: the treatment (clot-busting drugs) is dangerous if the cause is a bleed, and only 3-D imaging distinguishes clot from bleed within the minutes available — the dose is decisively worth it.
4.
Routine headache: no finding is likely to change treatment, so several millisieverts buy nothing. Justification is a physics-informed medical judgement: dose spent must purchase information that alters action.
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Unknowns: 512² ≈ 2.6 × 10⁵ voxel values. Each projection contributes at most 800 independent ray sums.
[Step 2] Minimum angles ≈ 2.6 × 10⁵ ÷ 800 ≈ 330 — real scanners use about a thousand, because overlapping rays are not fully independent and noise demands redundancy.
[Step 3] Stroke: the treatment (clot-busting drugs) is dangerous if the cause is a bleed, and only 3-D imaging distinguishes clot from bleed within the minutes available — the dose is decisively worth it.
[Step 4] Routine headache: no finding is likely to change treatment, so several millisieverts buy nothing. Justification is a physics-informed medical judgement: dose spent must purchase information that alters action.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
≥ ~330 angles (≈ 1000 in practice); dose is justified only when the 3-D answer changes the treatment
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≥ ~330 angles (≈ 1000 in practice); dose is justified only when the 3-D answer changes the treatment

## Slide 32
MEDICAL PHYSICS
Where to go next
Plenary — What to take away, what to practise next
Next
29.3 Ultrasound Imaging
https://giophysics.com/chapter-57/ultrasound-imaging/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-57/ct-scanning/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-57/presentation/?lesson=ct
Chapter
All Medical Physics lessons
https://giophysics.com/chapter-57/
PDF
Download the lesson PDF
https://giophysics.com/downloads/57-2-ct-scanning.pdf
MEDICAL PHYSICS · CT SCANNING
GIOPHYSICS LESSON
Medical Physics — CT Scanning. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-57/presentation/?lesson=ct moves them.