## Slide 1
29 · Medical Physics
Magnetism, resonance, and radio
MRI
No X-rays, no radioactivity — MRI images you with magnetism and radio. Your body is mostly hydrogen, every hydrogen nucleus is a tiny spinning magnet, and if you make them all hum at their resonant radio frequency, the way each tissue's hum dies away tells you what that tissue is.
POSITION
Lesson 5 of 6 in Medical Physics
PLAN
15 slides in the 45-minute core run, about 43 minutes of it
LESSON PAGE
https://giophysics.com/chapter-57/mri-imaging/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Medical Physics — MRI. Lesson 5 of 6.
[Intro] No X-rays, no radioactivity — MRI images you with magnetism and radio. Your body is mostly hydrogen, every hydrogen nucleus is a tiny spinning magnet, and if you make them all hum at their resonant radio frequency, the way each tissue's hum dies away tells you what that tissue is.
[Source] https://giophysics.com/chapter-57/mri-imaging/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Magnets & magnetic fields
https://giophysics.com/chapter-27/magnets-magnetic-fields/
Recall
Describing waves
https://giophysics.com/chapter-24/describing-waves/
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Magnets & magnetic fields; Describing waves

## Slide 3
THINK FIRST
An MRI scan soaks you in radio waves for forty minutes, and the radiographer stays in the room without a lead apron. Is that carelessness?
Take answers before you click — the point is the commitment
For a chest X-ray lasting a few milliseconds, the same radiographer steps behind a screen. Forty minutes is roughly a million times longer.
THE ANSWER
No, because there is no dose to be careless about. Ionisation is a per-photon threshold, and a 64 MHz photon carries about 3 × 10⁻⁷ eV — some fifty million times short of the 13.6 eV that would break a hydrogen molecule apart. A million times more photons that each cannot ionise is still nothing. MRI's real hazards are mechanical: near a 1.5 T magnet a steel gas cylinder becomes a missile, and the field is never switched off.
Photon energy on a logarithmic scale from 10⁻⁸ to 10⁶ electronvolts with four markers on it: the 64 MHz radio photon of an MRI scanner near the far left, visible light at about 2 eV, the 13.6 eV needed to ionise hydrogen picked out as the threshold, and an 80 keV X-ray photon far to the right.
The live version of this figure — click here
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] An MRI scan soaks you in radio waves for forty minutes, and the radiographer stays in the room without a lead apron. Is that carelessness? For a chest X-ray lasting a few milliseconds, the same radiographer steps behind a screen. Forty minutes is roughly a million times longer.
[Answer] No, because there is no dose to be careless about. Ionisation is a per-photon threshold, and a 64 MHz photon carries about 3 × 10⁻⁷ eV — some fifty million times short of the 13.6 eV that would break a hydrogen molecule apart. A million times more photons that each cannot ionise is still nothing. MRI's real hazards are mechanical: near a 1.5 T magnet a steel gas cylinder becomes a missile, and the field is never switched off.
[Figure] Photon energy on a logarithmic scale from 10⁻⁸ to 10⁶ electronvolts with four markers on it: the 64 MHz radio photon of an MRI scanner near the far left, visible light at about 2 eV, the 13.6 eV needed to ionise hydrogen picked out as the threshold, and an 80 keV X-ray photon far to the right.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
MRI aligns hydrogen nuclei in a strong magnetic field, tips them with a radio pulse at the Larmor (resonance) frequency f₀ ≈ 42.6 MHz × B₀, and images the radio signal they re-emit as they relax; gradient fields make f₀ depend on position, and relaxation times supply the tissue contrast.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] MRI aligns hydrogen nuclei in a strong magnetic field, tips them with a radio pulse at the Larmor (resonance) frequency f₀ ≈ 42.6 MHz × B₀, and images the radio signal they re-emit as they relax; gradient fields make f₀ depend on position, and relaxation times supply the tissue contrast.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
At 1.5 T protons precess at about 64 MHz. Add a gradient of a few millitesla per metre and protons in the head hum at a slightly different pitch from protons in the neck — the scanner tunes in to one slice of pitch at a time.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] At 1.5 T protons precess at about 64 MHz. Add a gradient of a few millitesla per metre and protons in the head hum at a slightly different pitch from protons in the neck — the scanner tunes in to one slice of pitch at a time.

## Slide 6
THE BIG IDEA
Magnetism, resonance, and radio
Introduce the idea — The big idea and the definition
In the strong field B₀ of a superconducting magnet, the body's hydrogen nuclei — protons — behave as tiny magnets: slightly more settle aligned with the field than against it, giving each scrap of tissue a net magnetisation, and every proton precesses about the field direction like a leaning gyroscope at the Larmor frequency, about 42.6 MHz per tesla. A radio-frequency pulse applied at exactly that frequency — resonance — tips the magnetisation away from the field; off-frequency pulses do nothing. When the pulse stops, the protons relax back, re-emitting a radio signal, and the relaxation times differ from tissue to tissue — fat relaxes quickly, water slowly — which is where MRI's superb soft-tissue contrast comes from.
Position is encoded by gradient coils: making the field vary slightly across the body makes the Larmor frequency vary with position, so each frequency in the returned signal reports where it was born. The radio photons involved carry around 10⁻⁷ eV — tens of millions of times short of ionising anything — so MRI deposits no radiation dose. Its costs are different: the magnet is expensive and never off, a scan takes minutes of loud gradient-coil hammering, and ferromagnetic metal must never approach the room.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] In the strong field B₀ of a superconducting magnet, the body's hydrogen nuclei — protons — behave as tiny magnets: slightly more settle aligned with the field than against it, giving each scrap of tissue a net magnetisation, and every proton precesses about the field direction like a leaning gyroscope at the Larmor frequency, about 42.6 MHz per tesla. A radio-frequency pulse applied at exactly that frequency — resonance — tips the magnetisation away from the field; off-frequency pulses do nothing. When the pulse stops, the protons relax back, re-emitting a radio signal, and the relaxation times differ from tissue to tissue — fat relaxes quickly, water slowly — which is where MRI's superb soft-tissue contrast comes from. Position is encoded by gradient coils: making the field vary slightly across the body makes the Larmor frequency vary with position, so each frequency in the returned signal reports where it was born. The radio photons involved carry around 10⁻⁷ eV — tens of millions of times short of ionising anything — so MRI deposits no radiation dose. Its costs are different: the magnet is expensive and never off, a scan takes minutes of loud gradient-coil hammering, and ferromagnetic metal must never approach the room.

## Slide 7
THE PHYSICS · 1 OF 3
Spins in a field
Build the model — The formulae, one at a time, in plain English
A proton carries spin and charge, making it a microscopic magnet. In the scanner's field, alignment with B₀ is slightly lower in energy than against it, and the tiny population excess — a few protons per million — summed over the body's ~10²⁷ hydrogen nuclei gives a measurable net magnetisation. Each proton also precesses about the field direction, the way a tilted gyroscope wheels around the vertical, at the Larmor frequency set by the field strength.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A proton carries spin and charge, making it a microscopic magnet. In the scanner's field, alignment with B₀ is slightly lower in energy than against it, and the tiny population excess — a few protons per million — summed over the body's ~10²⁷ hydrogen nuclei gives a measurable net magnetisation. Each proton also precesses about the field direction, the way a tilted gyroscope wheels around the vertical, at the Larmor frequency set by the field strength.

## Slide 8
THE PHYSICS · 2 OF 3
Tip, release, listen
Build the model — The formulae, one at a time, in plain English
An RF pulse at the Larmor frequency tips the net magnetisation away from B₀; when it ends, the magnetisation spirals back, broadcasting a fading radio signal into the receiver coils. Two clocks govern the fade — the T₁ (spin–lattice) and T₂ (spin–spin) relaxation times — and they differ strongly between fat, muscle, white matter, grey matter, and fluid. By choosing pulse timing, the operator weights the image toward T₁ or T₂, dialling up whichever contrast the diagnosis needs — no other modality lets you re-mix tissue contrast in software.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] An RF pulse at the Larmor frequency tips the net magnetisation away from B₀; when it ends, the magnetisation spirals back, broadcasting a fading radio signal into the receiver coils. Two clocks govern the fade — the T₁ (spin–lattice) and T₂ (spin–spin) relaxation times — and they differ strongly between fat, muscle, white matter, grey matter, and fluid. By choosing pulse timing, the operator weights the image toward T₁ or T₂, dialling up whichever contrast the diagnosis needs — no other modality lets you re-mix tissue contrast in software.

## Slide 9
THE PHYSICS · 3 OF 3
Choosing the tool
Build the model — The formulae, one at a time, in plain English
X-ray: fast, cheap, sharp on bone; poor soft-tissue contrast; small dose. CT: full 3-D, seconds fast, excellent for bleeds and bone; the largest dose. Ultrasound: real-time, portable, dose-free; blocked by bone and gas, resolution limited.
MRI: the best soft-tissue contrast of all, any slice plane, no ionising radiation — but slow, loud, claustrophobic, costly, and forbidden to some implants and to loose ferromagnetic objects, because the field is enormous and permanently on. The clinic's daily art is matching the physics of each machine to the question being asked.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] X-ray: fast, cheap, sharp on bone; poor soft-tissue contrast; small dose. CT: full 3-D, seconds fast, excellent for bleeds and bone; the largest dose. Ultrasound: real-time, portable, dose-free; blocked by bone and gas, resolution limited. MRI: the best soft-tissue contrast of all, any slice plane, no ionising radiation — but slow, loud, claustrophobic, costly, and forbidden to some implants and to loose ferromagnetic objects, because the field is enormous and permanently on. The clinic's daily art is matching the physics of each machine to the question being asked.

## Slide 10
FORMULA 1 OF 4
Larmor frequency
Build the model — The formulae, one at a time, in plain English
f₀ ≈ 42.6 MHz × B₀ (in T)
1.5 T → 63.9 MHz · 3 T → 128 MHz
IN PLAIN ENGLISH
The precession rate is proportional to the field. This single proportionality is both the tuning dial (resonance) and, once the field is made position-dependent, the map grid.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Larmor frequency: f₀ ≈ 42.6 MHz × B₀ (in T)
[In plain English] The precession rate is proportional to the field. This single proportionality is both the tuning dial (resonance) and, once the field is made position-dependent, the map grid.
[Note] 1.5 T → 63.9 MHz · 3 T → 128 MHz

## Slide 11
FORMULA 2 OF 4
Resonance
Build the model — The formulae, one at a time, in plain English
RF pulse at f₀ tips the spins
off-frequency pulses are simply ignored
IN PLAIN ENGLISH
Energy transfers efficiently only at the natural frequency — the same physics as pushing a swing in time. Selectivity is the point: only protons whose local field matches the pulse respond.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Resonance: RF pulse at f₀ tips the spins
[In plain English] Energy transfers efficiently only at the natural frequency — the same physics as pushing a swing in time. Selectivity is the point: only protons whose local field matches the pulse respond.
[Note] off-frequency pulses are simply ignored

## Slide 12
FORMULA 3 OF 4
Photon energy
Build the model — The formulae, one at a time, in plain English
E = hf ≈ 3 × 10⁻⁷ eV at 64 MHz
ionisation needs ~10 eV — 10⁷ times more
IN PLAIN ENGLISH
A radio photon cannot break a molecule no matter how many arrive: ionisation is a per-photon threshold, and MRI sits about fifty million times below it. Hence no dose, ever.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Photon energy: E = hf ≈ 3 × 10⁻⁷ eV at 64 MHz
[In plain English] A radio photon cannot break a molecule no matter how many arrive: ionisation is a per-photon threshold, and MRI sits about fifty million times below it. Hence no dose, ever.
[Note] ionisation needs ~10 eV — 10⁷ times more

## Slide 13
FORMULA 4 OF 4
Slice selection
Build the model — The formulae, one at a time, in plain English
B(x) = B₀ + Gx ⇒ f(x) = 42.6 · B(x) MHz
frequency becomes a position coordinate
IN PLAIN ENGLISH
With a gradient switched on, each plane of the body owns a unique Larmor frequency. Transmit one narrow band and only one slice answers; read the returned frequencies and they spell out position.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Slice selection: B(x) = B₀ + Gx ⇒ f(x) = 42.6 · B(x) MHz
[In plain English] With a gradient switched on, each plane of the body owns a unique Larmor frequency. Transmit one narrow band and only one slice answers; read the returned frequencies and they spell out position.
[Note] frequency becomes a position coordinate

## Slide 14
THE PICTURE
Position, written as field
Drawn for this lesson
A patient lying in the bore between the two halves of a superconducting magnet with B₀ arrowed along the axis, one thin slice picked out by dashed lines, and below it a graph of magnetic field against position showing the straight line B = B₀ + Gx, with a band of field marked on the vertical axis mapping down to the slice thickness Δx.
The live version of this figure — click here
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A patient lying in the bore between the two halves of a superconducting magnet with B₀ arrowed along the axis, one thin slice picked out by dashed lines, and below it a graph of magnetic field against position showing the straight line B = B₀ + Gx, with a band of field marked on the vertical axis mapping down to the slice thickness Δx.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
MRI's radio waves are not a milder dose of the radiation in an X-ray. Dose is a per-photon affair, and a 64 MHz photon carries about 3 × 10⁻⁷ eV — roughly fifty million times too little to ionise a single molecule, no matter the exposure time. MRI's real hazards are mechanical and mundane: a steel cylinder near a 1.5 T magnet becomes a projectile, and the superconducting field never switches off.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] MRI's radio waves are not a milder dose of the radiation in an X-ray. Dose is a per-photon affair, and a 64 MHz photon carries about 3 × 10⁻⁷ eV — roughly fifty million times too little to ionise a single molecule, no matter the exposure time. MRI's real hazards are mechanical and mundane: a steel cylinder near a 1.5 T magnet becomes a projectile, and the superconducting field never switches off.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
Find the Larmor frequency of protons in a 3.0 T MRI scanner.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Find the Larmor frequency of protons in a 3.0 T MRI scanner.
[Answer] f₀ ≈ 128 MHz

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
Find the Larmor frequency of protons in a 3.0 T MRI scanner.
1.
f₀ = 42.6 MHz per tesla × B₀.
2.
f₀ = 42.6 × 3.0 = 128 MHz — in the FM-radio region of the spectrum.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] f₀ = 42.6 MHz per tesla × B₀.
[Step 2] f₀ = 42.6 × 3.0 = 128 MHz — in the FM-radio region of the spectrum.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
f₀ ≈ 128 MHz
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] f₀ ≈ 128 MHz

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
Find the energy of a 63.9 MHz RF photon in joules and electronvolts, and compare it with the ~13.6 eV needed to ionise hydrogen.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Find the energy of a 63.9 MHz RF photon in joules and electronvolts, and compare it with the ~13.6 eV needed to ionise hydrogen.
[Answer] ≈ 4.2 × 10⁻²⁶ J ≈ 2.6 × 10⁻⁷ eV — about 5 × 10⁷ times below the ionisation threshold

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
Find the energy of a 63.9 MHz RF photon in joules and electronvolts, and compare it with the ~13.6 eV needed to ionise hydrogen.
1.
E = hf = 6.63 × 10⁻³⁴ × 63.9 × 10⁶ = 4.2 × 10⁻²⁶ J.
2.
In eV: 4.2 × 10⁻²⁶ ÷ 1.60 × 10⁻¹⁹ = 2.6 × 10⁻⁷ eV.
3.
Ratio: 13.6 ÷ 2.6 × 10⁻⁷ ≈ 5 × 10⁷ — the MRI photon falls short of ionising by a factor of about fifty million. That is what 'no dose' means, photon by photon.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] E = hf = 6.63 × 10⁻³⁴ × 63.9 × 10⁶ = 4.2 × 10⁻²⁶ J.
[Step 2] In eV: 4.2 × 10⁻²⁶ ÷ 1.60 × 10⁻¹⁹ = 2.6 × 10⁻⁷ eV.
[Step 3] Ratio: 13.6 ÷ 2.6 × 10⁻⁷ ≈ 5 × 10⁷ — the MRI photon falls short of ionising by a factor of about fifty million. That is what 'no dose' means, photon by photon.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
≈ 4.2 × 10⁻²⁶ J ≈ 2.6 × 10⁻⁷ eV — about 5 × 10⁷ times below the ionisation threshold
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 4.2 × 10⁻²⁶ J ≈ 2.6 × 10⁻⁷ eV — about 5 × 10⁷ times below the ionisation threshold

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
A scan is extended from four minutes to forty. How much more ionising damage does the patient receive?
A Ten times as much — exposure accumulates with time, as it does for any radiation
B None either way, because a 64 MHz photon is seven decades below the threshold and more of them does not change that
C Ten times as much, but the total is still below the safe limit
Photon energy on a logarithmic scale from 10⁻⁸ to 10⁶ electronvolts with four markers on it: the 64 MHz radio photon of an MRI scanner near the far left, visible light at about 2 eV, the 13.6 eV needed to ionise hydrogen picked out as the threshold, and an 80 keV X-ray photon far to the right.
The live version of this figure — click here
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] A scan is extended from four minutes to forty. How much more ionising damage does the patient receive?
[Options] A Ten times as much — exposure accumulates with time, as it does for any radiation B None either way, because a 64 MHz photon is seven decades below the threshold and more of them does not change that C Ten times as much, but the total is still below the safe limit
[Figure] Photon energy on a logarithmic scale from 10⁻⁸ to 10⁶ electronvolts with four markers on it: the 64 MHz radio photon of an MRI scanner near the far left, visible light at about 2 eV, the 13.6 eV needed to ionise hydrogen picked out as the threshold, and an 80 keV X-ray photon far to the right.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B None either way, because a 64 MHz photon is seven decades below the threshold and more of them does not change that
WHY
Read the scale. Ionisation is not a matter of how much energy arrives in total; it is a matter of whether any single photon carries the 13.6 eV needed to knock an electron out, and the MRI marker sits seven decades to the left of that mark. No number of photons below a threshold add up to one above it, any more than a million pebbles thrown at a window will do what one brick does. That is also why the X-ray marker on the right belongs to a completely different conversation: at 80 keV, one photon does the damage.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — None either way, because a 64 MHz photon is seven decades below the threshold and more of them does not change that. Read the scale. Ionisation is not a matter of how much energy arrives in total; it is a matter of whether any single photon carries the 13.6 eV needed to knock an electron out, and the MRI marker sits seven decades to the left of that mark. No number of photons below a threshold add up to one above it, any more than a million pebbles thrown at a window will do what one brick does. That is also why the X-ray marker on the right belongs to a completely different conversation: at 80 keV, one photon does the damage.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
The gradient coils in an MRI scanner exist to…
A
Make the main field stronger everywhere
B
Make the Larmor frequency depend on position, so the signal can be located
C
Shield the room from outside radio interference
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] The gradient coils in an MRI scanner exist to…
[Options] A Make the main field stronger everywhere B Make the Larmor frequency depend on position, so the signal can be located C Shield the room from outside radio interference

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B Make the Larmor frequency depend on position, so the signal can be located
HOW TO GET THERE
A deliberate slight variation of B across the body makes each position precess at its own frequency. The received signal's frequencies then read out as coordinates — the gradient turns resonance into a map.
WHY THE OTHERS TEMPT
A Adding a gradient does change the field, but by design it changes it differently in different places — that variation IS the point, and it is deliberately small compared with B₀. Making the main field uniformly stronger is the job of the superconducting magnet, and it would locate nothing.
B Correct. A slight, deliberate variation of B across the body makes each position precess at its own frequency, so the frequencies in the received signal read out as coordinates.
C The room is shielded, and it has to be — a scanner listening for microvolts of radio signal is easily swamped by a passing taxi. But that shielding is the copper cage built into the walls, not the gradient coils, which sit inside the bore and are switched hundreds of times a second during a scan.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] The gradient coils in an MRI scanner exist to…
[Option by option] A: Adding a gradient does change the field, but by design it changes it differently in different places — that variation IS the point, and it is deliberately small compared with B₀. Making the main field uniformly stronger is the job of the superconducting magnet, and it would locate nothing. B: Correct. A slight, deliberate variation of B across the body makes each position precess at its own frequency, so the frequencies in the received signal read out as coordinates. C: The room is shielded, and it has to be — a scanner listening for microvolts of radio signal is easily swamped by a passing taxi. But that shielding is the copper cage built into the walls, not the gradient coils, which sit inside the bore and are switched hundreds of times a second during a scan.
[Answer] B — Make the Larmor frequency depend on position, so the signal can be located
[Why] A deliberate slight variation of B across the body makes each position precess at its own frequency. The received signal's frequencies then read out as coordinates — the gradient turns resonance into a map.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
A scanner applies a gradient of 10 mT m⁻¹ along the body and transmits an RF pulse with a bandwidth of 1.0 kHz. How thick is the slice of tissue that resonates?
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A scanner applies a gradient of 10 mT m⁻¹ along the body and transmits an RF pulse with a bandwidth of 1.0 kHz. How thick is the slice of tissue that resonates?
[Answer] ≈ 2.3 mm

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
A scanner applies a gradient of 10 mT m⁻¹ along the body and transmits an RF pulse with a bandwidth of 1.0 kHz. How thick is the slice of tissue that resonates?
1.
Frequency changes with position at 42.6 × 10⁶ Hz T⁻¹ × 0.010 T m⁻¹ = 4.26 × 10⁵ Hz m⁻¹.
2.
Only positions whose Larmor frequency falls inside the 1.0 kHz band respond.
3.
Slice thickness = 1000 ÷ 4.26 × 10⁵ = 2.3 × 10⁻³ m ≈ 2.3 mm — a sharper gradient or narrower band cuts a thinner slice.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Frequency changes with position at 42.6 × 10⁶ Hz T⁻¹ × 0.010 T m⁻¹ = 4.26 × 10⁵ Hz m⁻¹.
[Step 2] Only positions whose Larmor frequency falls inside the 1.0 kHz band respond.
[Step 3] Slice thickness = 1000 ÷ 4.26 × 10⁵ = 2.3 × 10⁻³ m ≈ 2.3 mm — a sharper gradient or narrower band cuts a thinner slice.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
≈ 2.3 mm
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 2.3 mm

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
Choose and justify the imaging modality: (a) suspected wrist fracture; (b) sudden one-sided weakness, possible stroke; (c) routine 20-week pregnancy check; (d) suspected knee ligament tear.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Choose and justify the imaging modality: (a) suspected wrist fracture; (b) sudden one-sided weakness, possible stroke; (c) routine 20-week pregnancy check; (d) suspected knee ligament tear.
[Answer] (a) X-ray · (b) CT, then MRI · (c) ultrasound · (d) MRI — each choice is the physics of contrast, speed, and dose

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
Choose and justify the imaging modality: (a) suspected wrist fracture; (b) sudden one-sided weakness, possible stroke; (c) routine 20-week pregnancy check; (d) suspected knee ligament tear.
1.
(a) X-ray: bone contrast is superb, the exam takes seconds, and the dose is tiny. Nothing else is as cheap or as available.
2.
(b) CT first: it is minutes-fast and cleanly separates a bleed from a clot — the treatments are opposite, and stroke care runs on the clock. MRI may follow for fine detail once the patient is stable.
3.
(c) Ultrasound: no ionising radiation for the fetus, real-time moving images, bedside equipment. The safety argument is decisive on its own.
4.
(d) MRI: ligaments are soft tissue invisible to X-rays and poorly seen on CT; MRI's soft-tissue contrast is unmatched, no dose is delivered, and the slowness of the scan does not matter for a stable knee.
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] (a) X-ray: bone contrast is superb, the exam takes seconds, and the dose is tiny. Nothing else is as cheap or as available.
[Step 2] (b) CT first: it is minutes-fast and cleanly separates a bleed from a clot — the treatments are opposite, and stroke care runs on the clock. MRI may follow for fine detail once the patient is stable.
[Step 3] (c) Ultrasound: no ionising radiation for the fetus, real-time moving images, bedside equipment. The safety argument is decisive on its own.
[Step 4] (d) MRI: ligaments are soft tissue invisible to X-rays and poorly seen on CT; MRI's soft-tissue contrast is unmatched, no dose is delivered, and the slowness of the scan does not matter for a stable knee.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
(a) X-ray · (b) CT, then MRI · (c) ultrasound · (d) MRI — each choice is the physics of contrast, speed, and dose
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] (a) X-ray · (b) CT, then MRI · (c) ultrasound · (d) MRI — each choice is the physics of contrast, speed, and dose

## Slide 32
MEDICAL PHYSICS
Where to go next
Plenary — What to take away, what to practise next
Next
29.6 Medical Physics Calculus
https://giophysics.com/chapter-57/medical-calculus/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-57/mri-imaging/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-57/presentation/?lesson=mri
Chapter
All Medical Physics lessons
https://giophysics.com/chapter-57/
PDF
Download the lesson PDF
https://giophysics.com/downloads/57-5-mri-imaging.pdf
MEDICAL PHYSICS · MRI
GIOPHYSICS LESSON
Medical Physics — MRI. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-57/presentation/?lesson=mri moves them.