## Slide 1
29 · Medical Physics
Imaging function, not form
Nuclear Medicine & PET
X-rays, CT and MRI draw anatomy — the shape of things. Nuclear medicine draws function: inject a radioactive tracer that rides the body's own chemistry, and the radiation it emits reports where that chemistry actually happens — a working map of thyroid, bone, heart, or tumour.
POSITION
Lesson 4 of 6 in Medical Physics
PLAN
15 slides in the 45-minute core run, about 41 minutes of it
LESSON PAGE
https://giophysics.com/chapter-57/nuclear-medicine/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Medical Physics — Nuclear Medicine & PET. Lesson 4 of 6.
[Intro] X-rays, CT and MRI draw anatomy — the shape of things. Nuclear medicine draws function: inject a radioactive tracer that rides the body's own chemistry, and the radiation it emits reports where that chemistry actually happens — a working map of thyroid, bone, heart, or tumour.
[Source] https://giophysics.com/chapter-57/nuclear-medicine/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Radioactive decay
https://giophysics.com/chapter-46/radioactivity/
Recall
Half-life & activity
https://giophysics.com/chapter-46/half-life/
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Radioactive decay; Half-life & activity

## Slide 3
THINK FIRST
A PET scanner is built to detect positrons. It has never detected one, and never will. What is it actually detecting?
Take answers before you click — the point is the commitment
The tracer is a β⁺ emitter — that is the whole reason it was chosen — and the ring of detectors is only a few tens of centimetres from where the positrons are being made.
THE ANSWER
Pairs of gamma photons. A positron in tissue survives a millimetre or two before it meets an electron and both are annihilated, and what leaves the body is two 511 keV photons flying back to back. The scanner never sees the particle it was built around — and that one or two millimetres of positron travel, not any detector, is what limits how sharp a PET image can ever be.
A magnified few millimetres of tissue with a 1 mm scale bar: the tracer molecule marked at the point where a positron is emitted, a short wandering track from there to the point where it meets an electron, and the two annihilation photons leaving that second point in opposite directions.
The live version of this figure — click here
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] A PET scanner is built to detect positrons. It has never detected one, and never will. What is it actually detecting? The tracer is a β⁺ emitter — that is the whole reason it was chosen — and the ring of detectors is only a few tens of centimetres from where the positrons are being made.
[Answer] Pairs of gamma photons. A positron in tissue survives a millimetre or two before it meets an electron and both are annihilated, and what leaves the body is two 511 keV photons flying back to back. The scanner never sees the particle it was built around — and that one or two millimetres of positron travel, not any detector, is what limits how sharp a PET image can ever be.
[Figure] A magnified few millimetres of tissue with a 1 mm scale bar: the tracer molecule marked at the point where a positron is emitted, a short wandering track from there to the point where it meets an electron, and the two annihilation photons leaving that second point in opposite directions.

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Nuclear medicine images function by detecting radiation from a tracer that follows the body's chemistry. PET uses a β⁺ tracer: each annihilation emits two 511 keV photons back-to-back, and detecting the pair in coincidence defines a line of response through the source.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Nuclear medicine images function by detecting radiation from a tracer that follows the body's chemistry. PET uses a β⁺ tracer: each annihilation emits two 511 keV photons back-to-back, and detecting the pair in coincidence defines a line of response through the source.

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
An FDG-PET scan lights up wherever cells burn unusual amounts of glucose — a tumour betrays itself by its metabolism long before it changes shape on a CT.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] An FDG-PET scan lights up wherever cells burn unusual amounts of glucose — a tumour betrays itself by its metabolism long before it changes shape on a CT.

## Slide 6
THE BIG IDEA
Imaging function, not form
Introduce the idea — The big idea and the definition
A tracer is a radioactive nuclide attached to a molecule the body routes for its own reasons: iodine to the thyroid, phosphates to growing bone, glucose to hungry cells. The workhorse is technetium-99m — a 6-hour half-life (long enough to image, short enough to clear), a pure gamma emitter (no alpha or beta particles to dose tissue while never leaving the body), and a 140 keV photon energy that escapes the patient yet is easily stopped by a detector. A gamma camera images it: a lead collimator passes only photons travelling parallel to its holes, a scintillator crystal converts each accepted photon into a flash of light, and an array of photomultiplier tubes locates each flash.
PET goes further: a β⁺ emitter such as fluorine-18, packaged as fluorodeoxyglucose (FDG), is injected; each emitted positron annihilates with an electron within a millimetre or two, producing two 511 keV photons flying in opposite directions — momentum conservation demands it. A ring of detectors registers the pair in coincidence, defining a line of response through the source, and millions of intersecting lines map metabolic activity: tumours announce themselves by their appetite for glucose.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A tracer is a radioactive nuclide attached to a molecule the body routes for its own reasons: iodine to the thyroid, phosphates to growing bone, glucose to hungry cells. The workhorse is technetium-99m — a 6-hour half-life (long enough to image, short enough to clear), a pure gamma emitter (no alpha or beta particles to dose tissue while never leaving the body), and a 140 keV photon energy that escapes the patient yet is easily stopped by a detector. A gamma camera images it: a lead collimator passes only photons travelling parallel to its holes, a scintillator crystal converts each accepted photon into a flash of light, and an array of photomultiplier tubes locates each flash. PET goes further: a β⁺ emitter such as fluorine-18, packaged as fluorodeoxyglucose (FDG), is injected; each emitted positron annihilates with an electron within a millimetre or two, producing two 511 keV photons flying in opposite directions — momentum conservation demands it. A ring of detectors registers the pair in coincidence, defining a line of response through the source, and millions of intersecting lines map metabolic activity: tumours announce themselves by their appetite for glucose.

## Slide 7
THE PHYSICS · 1 OF 3
What makes a good tracer
Build the model — The formulae, one at a time, in plain English
Half-life comparable to the study: hours, not seconds (gone before imaging) or years (a permanent dose). Emission: gamma only, because alphas and betas deposit all their energy in the patient and none in the detector — pure dose, no image.
Energy: high enough to escape the body, low enough to interact in the camera; 100–200 keV is the sweet spot. Chemistry: the nuclide must bolt onto a molecule the body actively routes, because the biology is the lens.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Half-life comparable to the study: hours, not seconds (gone before imaging) or years (a permanent dose). Emission: gamma only, because alphas and betas deposit all their energy in the patient and none in the detector — pure dose, no image. Energy: high enough to escape the body, low enough to interact in the camera; 100–200 keV is the sweet spot. Chemistry: the nuclide must bolt onto a molecule the body actively routes, because the biology is the lens.

## Slide 8
THE PHYSICS · 2 OF 3
Inside the gamma camera
Build the model — The formulae, one at a time, in plain English
Gamma rays cannot be focused, so the camera selects instead: a lead collimator — a slab drilled with thousands of parallel holes — absorbs every photon except those travelling along the hole axis, projecting the tracer distribution onto the crystal. The sodium-iodide scintillator converts each photon to a flash of visible light; the photomultiplier array behind it locates the flash by comparing signal strengths, and each located flash becomes one dot in the functional image.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] Gamma rays cannot be focused, so the camera selects instead: a lead collimator — a slab drilled with thousands of parallel holes — absorbs every photon except those travelling along the hole axis, projecting the tracer distribution onto the crystal. The sodium-iodide scintillator converts each photon to a flash of visible light; the photomultiplier array behind it locates the flash by comparing signal strengths, and each located flash becomes one dot in the functional image.

## Slide 9
THE PHYSICS · 3 OF 3
PET and coincidence
Build the model — The formulae, one at a time, in plain English
The PET ring accepts an event only when two opposite detectors fire within a few nanoseconds of each other — a coincidence. No collimator is needed: the geometry of annihilation is the collimator, which is why PET harvests far more of its photons than a gamma camera can. Each coincidence adds one line of response; the reconstruction is CT's mathematics run on lines of glow instead of lines of shadow, and a combined PET-CT machine overlays function on anatomy in a single session.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] The PET ring accepts an event only when two opposite detectors fire within a few nanoseconds of each other — a coincidence. No collimator is needed: the geometry of annihilation is the collimator, which is why PET harvests far more of its photons than a gamma camera can. Each coincidence adds one line of response; the reconstruction is CT's mathematics run on lines of glow instead of lines of shadow, and a combined PET-CT machine overlays function on anatomy in a single session.

## Slide 10
FORMULA 1 OF 4
Annihilation
Build the model — The formulae, one at a time, in plain English
e⁺ + e⁻ → 2γ
each photon carries E = mₑc² = 511 keV
IN PLAIN ENGLISH
The positron and electron vanish and their whole rest mass becomes light. Two photons, not one: a single photon could carry the energy but never balance the momentum.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Annihilation: e⁺ + e⁻ → 2γ
[In plain English] The positron and electron vanish and their whole rest mass becomes light. Two photons, not one: a single photon could carry the energy but never balance the momentum.
[Note] each photon carries E = mₑc² = 511 keV

## Slide 11
FORMULA 2 OF 4
Back-to-back geometry
Build the model — The formulae, one at a time, in plain English
total p ≈ 0 ⇒ photons opposite
the pair leaves within a fraction of a degree of 180°
IN PLAIN ENGLISH
The annihilating pair is essentially at rest, so the two photons must carry equal and opposite momentum. That guaranteed geometry is what turns two detector clicks into a line through the patient.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Back-to-back geometry: total p ≈ 0 ⇒ photons opposite
[In plain English] The annihilating pair is essentially at rest, so the two photons must carry equal and opposite momentum. That guaranteed geometry is what turns two detector clicks into a line through the patient.
[Note] the pair leaves within a fraction of a degree of 180°

## Slide 12
FORMULA 3 OF 4
The ideal tracer
Build the model — The formulae, one at a time, in plain English
Tc-99m · T½ = 6.0 h · 140 keV γ only
milked on-site from a molybdenum-99 generator
IN PLAIN ENGLISH
Six hours matches the length of a working day of imaging; gamma-only means minimal absorbed dose; 140 keV escapes the body but stops in the camera. Every clause is a design decision.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] The ideal tracer: Tc-99m · T½ = 6.0 h · 140 keV γ only
[In plain English] Six hours matches the length of a working day of imaging; gamma-only means minimal absorbed dose; 140 keV escapes the body but stops in the camera. Every clause is a design decision.
[Note] milked on-site from a molybdenum-99 generator

## Slide 13
FORMULA 4 OF 4
Line of response
Build the model — The formulae, one at a time, in plain English
offset from midpoint = cΔt/2
time-of-flight PET reads the arrival difference
IN PLAIN ENGLISH
If one photon arrives Δt earlier, the annihilation happened cΔt/2 nearer that detector. Even a few hundred picoseconds of timing narrows down where on the line the source sits.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Line of response: offset from midpoint = cΔt/2
[In plain English] If one photon arrives Δt earlier, the annihilation happened cΔt/2 nearer that detector. Even a few hundred picoseconds of timing narrows down where on the line the source sits.
[Note] time-of-flight PET reads the arrival difference

## Slide 14
THE PICTURE
A coincidence defines a line
Drawn for this lesson
A PET ring of detector elements around a patient in cross-section, with an annihilation happening off-centre and two 511 keV photons leaving it back to back to opposite detectors; the line of response is drawn between those two detectors and its midpoint marked, with the offset between midpoint and annihilation dimensioned but not valued.
The live version of this figure — click here
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Figure] A PET ring of detector elements around a patient in cross-section, with an annihilation happening off-centre and two 511 keV photons leaving it back to back to opposite detectors; the line of response is drawn between those two detectors and its midpoint marked, with the offset between midpoint and annihilation dimensioned but not valued.

## Slide 15
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
A PET camera never detects the positron. The β⁺ travels at most a millimetre or two in tissue before annihilating — what leaves the body is the pair of 511 keV gamma photons. That millimetre of positron range, not the detector hardware, sets the ultimate resolution limit of PET.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] A PET camera never detects the positron. The β⁺ travels at most a millimetre or two in tissue before annihilating — what leaves the body is the pair of 511 keV gamma photons. That millimetre of positron range, not the detector hardware, sets the ultimate resolution limit of PET.

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
A Tc-99m dose (T½ = 6.0 h) is prepared at 8 a.m. What fraction of its activity remains at 8 a.m. the next day?
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] A Tc-99m dose (T½ = 6.0 h) is prepared at 8 a.m. What fraction of its activity remains at 8 a.m. the next day?
[Answer] 1/16 ≈ 6% remains

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
A Tc-99m dose (T½ = 6.0 h) is prepared at 8 a.m. What fraction of its activity remains at 8 a.m. the next day?
1.
24 hours ÷ 6.0 hours = 4 half-lives.
2.
Fraction = (½)⁴ = 1/16 ≈ 6.3%.
3.
By the next morning the patient's dose has essentially administered itself away — exactly the design.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] 24 hours ÷ 6.0 hours = 4 half-lives.
[Step 2] Fraction = (½)⁴ = 1/16 ≈ 6.3%.
[Step 3] By the next morning the patient's dose has essentially administered itself away — exactly the design.

## Slide 18
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
1/16 ≈ 6% remains
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 1/16 ≈ 6% remains

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
Show that each annihilation photon carries about 511 keV. (mₑ = 9.11 × 10⁻³¹ kg)
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Show that each annihilation photon carries about 511 keV. (mₑ = 9.11 × 10⁻³¹ kg)
[Answer] E = mₑc² ≈ 8.2 × 10⁻¹⁴ J = 511 keV per photon

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
Show that each annihilation photon carries about 511 keV. (mₑ = 9.11 × 10⁻³¹ kg)
1.
Each photon carries one electron rest mass of energy: E = mₑc² = 9.11 × 10⁻³¹ × (3.00 × 10⁸)².
2.
E = 8.20 × 10⁻¹⁴ J.
3.
In electronvolts: 8.20 × 10⁻¹⁴ ÷ 1.60 × 10⁻¹⁹ = 5.1 × 10⁵ eV = 511 keV. Every PET scanner on Earth is tuned to this one number.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Each photon carries one electron rest mass of energy: E = mₑc² = 9.11 × 10⁻³¹ × (3.00 × 10⁸)².
[Step 2] E = 8.20 × 10⁻¹⁴ J.
[Step 3] In electronvolts: 8.20 × 10⁻¹⁴ ÷ 1.60 × 10⁻¹⁹ = 5.1 × 10⁵ eV = 511 keV. Every PET scanner on Earth is tuned to this one number.

## Slide 21
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
E = mₑc² ≈ 8.2 × 10⁻¹⁴ J = 511 keV per photon
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] E = mₑc² ≈ 8.2 × 10⁻¹⁴ J = 511 keV per photon

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
The line of response passes exactly through which point in this picture?
A The tracer molecule — that is the thing the scan is trying to find
B The annihilation point, a millimetre or two away from the molecule
C Neither; the line is only as good as the width of a detector element
A magnified few millimetres of tissue with a 1 mm scale bar: the tracer molecule marked at the point where a positron is emitted, a short wandering track from there to the point where it meets an electron, and the two annihilation photons leaving that second point in opposite directions.
The live version of this figure — click here
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] The line of response passes exactly through which point in this picture?
[Options] A The tracer molecule — that is the thing the scan is trying to find B The annihilation point, a millimetre or two away from the molecule C Neither; the line is only as good as the width of a detector element
[Figure] A magnified few millimetres of tissue with a 1 mm scale bar: the tracer molecule marked at the point where a positron is emitted, a short wandering track from there to the point where it meets an electron, and the two annihilation photons leaving that second point in opposite directions.

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
B The annihilation point, a millimetre or two away from the molecule
WHY
The two photons are created at the annihilation, so the line joining the detectors they reach passes through the annihilation and nothing else. Between the molecule and that point sits the positron's short wandering track, and the scanner has no way of knowing which direction it went. Everything downstream of that gap — better crystals, faster timing, a bigger ring — sharpens the line but cannot recover the millimetre already lost. It is why PET resolution has a floor set by physics rather than by engineering.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] B — The annihilation point, a millimetre or two away from the molecule. The two photons are created at the annihilation, so the line joining the detectors they reach passes through the annihilation and nothing else. Between the molecule and that point sits the positron's short wandering track, and the scanner has no way of knowing which direction it went. Everything downstream of that gap — better crystals, faster timing, a bigger ring — sharpens the line but cannot recover the millimetre already lost. It is why PET resolution has a floor set by physics rather than by engineering.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Why must the two annihilation photons fly in almost exactly opposite directions?
A
Charge conservation — the charges must separate
B
Momentum conservation — the e⁺e⁻ pair is essentially at rest, so the photon momenta must cancel
C
The magnetic field of the scanner steers them apart
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Why must the two annihilation photons fly in almost exactly opposite directions?
[Options] A Charge conservation — the charges must separate B Momentum conservation — the e⁺e⁻ pair is essentially at rest, so the photon momenta must cancel C The magnetic field of the scanner steers them apart

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B Momentum conservation — the e⁺e⁻ pair is essentially at rest, so the photon momenta must cancel
HOW TO GET THERE
Before annihilation the total momentum is nearly zero, so afterwards the two photons must carry equal and opposite momenta: back-to-back at 511 keV each. PET's whole geometry rests on this conservation law.
WHY THE OTHERS TEMPT
A Charge is conserved, and it does so trivially here: an electron and a positron start with a total of zero and finish as two photons carrying none. Nothing needs to separate, and conservation of charge places no constraint on which way the photons go.
B Correct. The pair is essentially at rest, so the total momentum before is nearly zero and the two photons must carry equal and opposite momenta — back to back, at 511 keV each.
C A PET scanner has no magnetic field: that is MRI. And a magnetic field could not do this anyway, since photons are uncharged and go straight regardless. The whole design depends on the photons already being opposite when they are born.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Why must the two annihilation photons fly in almost exactly opposite directions?
[Option by option] A: Charge is conserved, and it does so trivially here: an electron and a positron start with a total of zero and finish as two photons carrying none. Nothing needs to separate, and conservation of charge places no constraint on which way the photons go. B: Correct. The pair is essentially at rest, so the total momentum before is nearly zero and the two photons must carry equal and opposite momenta — back to back, at 511 keV each. C: A PET scanner has no magnetic field: that is MRI. And a magnetic field could not do this anyway, since photons are uncharged and go straight regardless. The whole design depends on the photons already being opposite when they are born.
[Answer] B — Momentum conservation — the e⁺e⁻ pair is essentially at rest, so the photon momenta must cancel
[Why] Before annihilation the total momentum is nearly zero, so afterwards the two photons must carry equal and opposite momenta: back-to-back at 511 keV each. PET's whole geometry rests on this conservation law.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
In a PET scanner, one photon of a coincident pair arrives 600 ps before its partner. How far from the midpoint of the line of response did the annihilation occur, and on which side?
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] In a PET scanner, one photon of a coincident pair arrives 600 ps before its partner. How far from the midpoint of the line of response did the annihilation occur, and on which side?
[Answer] 9.0 cm from the midpoint, on the side of the earlier detector

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
In a PET scanner, one photon of a coincident pair arrives 600 ps before its partner. How far from the midpoint of the line of response did the annihilation occur, and on which side?
1.
The annihilation is nearer the detector that fired first: the early photon travelled less distance.
2.
Offset = cΔt/2 = 3.00 × 10⁸ × 600 × 10⁻¹² ÷ 2.
3.
Offset = 0.090 m = 9.0 cm toward the early detector. Timing at hundreds of picoseconds localises the source along the line — this is time-of-flight PET.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] The annihilation is nearer the detector that fired first: the early photon travelled less distance.
[Step 2] Offset = cΔt/2 = 3.00 × 10⁸ × 600 × 10⁻¹² ÷ 2.
[Step 3] Offset = 0.090 m = 9.0 cm toward the early detector. Timing at hundreds of picoseconds localises the source along the line — this is time-of-flight PET.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
9.0 cm from the midpoint, on the side of the earlier detector
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 9.0 cm from the midpoint, on the side of the earlier detector

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
F-18 has T½ = 110 min. A hospital 3.0 hours from the cyclotron needs 300 MBq at injection time. What activity must be produced, and why does Tc-99m avoid this problem entirely?
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] F-18 has T½ = 110 min. A hospital 3.0 hours from the cyclotron needs 300 MBq at injection time. What activity must be produced, and why does Tc-99m avoid this problem entirely?
[Answer] ≈ 930 MBq at production; Tc-99m is generated on-site from long-lived Mo-99

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
F-18 has T½ = 110 min. A hospital 3.0 hours from the cyclotron needs 300 MBq at injection time. What activity must be produced, and why does Tc-99m avoid this problem entirely?
1.
Transit = 180 min = 180/110 = 1.64 half-lives.
2.
Required at production: A₀ = 300 × 2^1.64 = 300 × 3.11 ≈ 930 MBq — the cyclotron must make three times the dose that arrives.
3.
Tc-99m is not shipped at all: its parent Mo-99 (T½ = 66 h) travels well, and the hospital milks fresh Tc-99m from the generator each morning as the parent decays into it.
4.
Every tracer's logistics are its decay law: short half-lives buy low patient dose at the price of a race against the exponential.
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Transit = 180 min = 180/110 = 1.64 half-lives.
[Step 2] Required at production: A₀ = 300 × 2^1.64 = 300 × 3.11 ≈ 930 MBq — the cyclotron must make three times the dose that arrives.
[Step 3] Tc-99m is not shipped at all: its parent Mo-99 (T½ = 66 h) travels well, and the hospital milks fresh Tc-99m from the generator each morning as the parent decays into it.
[Step 4] Every tracer's logistics are its decay law: short half-lives buy low patient dose at the price of a race against the exponential.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
≈ 930 MBq at production; Tc-99m is generated on-site from long-lived Mo-99
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] ≈ 930 MBq at production; Tc-99m is generated on-site from long-lived Mo-99

## Slide 32
MEDICAL PHYSICS
Where to go next
Plenary — What to take away, what to practise next
Next
29.5 MRI
https://giophysics.com/chapter-57/mri-imaging/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-57/nuclear-medicine/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-57/presentation/?lesson=nuclear
Chapter
All Medical Physics lessons
https://giophysics.com/chapter-57/
PDF
Download the lesson PDF
https://giophysics.com/downloads/57-4-nuclear-medicine.pdf
MEDICAL PHYSICS · NUCLEAR MEDICINE & PET
GIOPHYSICS LESSON
Medical Physics — Nuclear Medicine & PET. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-57/presentation/?lesson=nuclear moves them.