## Slide 1
29 · Medical Physics
Sonar for people
Ultrasound Imaging
Press a buzzing crystal against the skin and listen. Every boundary inside the body — fat to muscle, muscle to bone — throws back a faint echo, and each echo's delay is a tape measure: d = vt/2. No ionising radiation, no dose. Just sonar, miniaturised and pointed inward.
POSITION
Lesson 3 of 6 in Medical Physics
PLAN
15 slides in the 45-minute core run, about 43 minutes of it
LESSON PAGE
https://giophysics.com/chapter-57/ultrasound-imaging/
Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
1 / 32
Notes: [Lesson] Medical Physics — Ultrasound Imaging. Lesson 3 of 6.
[Intro] Press a buzzing crystal against the skin and listen. Every boundary inside the body — fat to muscle, muscle to bone — throws back a faint echo, and each echo's delay is a tape measure: d = vt/2. No ionising radiation, no dose. Just sonar, miniaturised and pointed inward.
[Source] https://giophysics.com/chapter-57/ultrasound-imaging/
[Disclaimer] Built by GioPhysics from the lesson's own page. Every word on these slides is the lesson's; nothing here is re-authored. Teaching material, not an awarding body's document.

## Slide 2
WHAT THIS NEEDS
What you already know
Starter — Recall what this lesson stands on
Recall
Describing waves
https://giophysics.com/chapter-24/describing-waves/
Recall
Sound & the Doppler effect
https://giophysics.com/chapter-24/sound-doppler/
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
2 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Starter] Recall: Describing waves; Sound & the Doppler effect

## Slide 3
THINK FIRST
Ultrasound gel is cold, sticky and universally disliked. What happens to the picture if the sonographer skips it?
Take answers before you click — the point is the commitment
The probe still presses firmly against the skin. The gap left between them is thinner than a hair, and it contains nothing but air.
THE ANSWER
There is no picture. About 99.9% of the intensity reflects straight back off that film of air before the pulse ever enters the body — the impedance of air is 430 against tissue's 1.63 × 10⁶, and α = (Z₂ − Z₁)²/(Z₂ + Z₁)² is merciless about a mismatch that large. The gel is not a lubricant; it is an impedance match, and its job is to make the boundary disappear.
Two panels of the same probe pressed against skin: in the first a thin film of air of impedance 430 lies between them, in the second a layer of coupling gel of impedance 1.65 × 10⁶, and in both the pulse is drawn arriving at the boundary with the reflected fraction marked only as α = ?
The live version of this figure — click here
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
3 / 32
Notes: [Phase] Starter: Recall what this lesson stands on (minutes 0–5 of 45)
[Hook] Ultrasound gel is cold, sticky and universally disliked. What happens to the picture if the sonographer skips it? The probe still presses firmly against the skin. The gap left between them is thinner than a hair, and it contains nothing but air.
[Answer] There is no picture. About 99.9% of the intensity reflects straight back off that film of air before the pulse ever enters the body — the impedance of air is 430 against tissue's 1.63 × 10⁶, and α = (Z₂ − Z₁)²/(Z₂ + Z₁)² is merciless about a mismatch that large. The gel is not a lubricant; it is an impedance match, and its job is to make the boundary disappear.
[Figure] Two panels of the same probe pressed against skin: in the first a thin film of air of impedance 430 lies between them, in the second a layer of coupling gel of impedance 1.65 × 10⁶, and in both the pulse is drawn arriving at the boundary with the reflected fraction marked only as α = ?

## Slide 4
EXPLAINED SIMPLY
In one sentence
Introduce the idea — The big idea and the definition
Ultrasound imaging fires megahertz sound pulses from a piezoelectric transducer and times the echoes reflected wherever the acoustic impedance Z = ρc changes; depth d = vt/2, and the reflected intensity fraction is α = (Z₂ − Z₁)²/(Z₂ + Z₁)².
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
4 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Definition] Ultrasound imaging fires megahertz sound pulses from a piezoelectric transducer and times the echoes reflected wherever the acoustic impedance Z = ρc changes; depth d = vt/2, and the reflected intensity fraction is α = (Z₂ − Z₁)²/(Z₂ + Z₁)².

## Slide 5
EXPLAINED SIMPLY
What that looks like
Introduce the idea — The big idea and the definition
FOR EXAMPLE
An echo returning 91 µs after the pulse in soft tissue (v = 1540 m s⁻¹) marks a boundary at d = 1540 × 91 × 10⁻⁶ ÷ 2 ≈ 7.0 cm.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
5 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Worked illustration] An echo returning 91 µs after the pulse in soft tissue (v = 1540 m s⁻¹) marks a boundary at d = 1540 × 91 × 10⁻⁶ ÷ 2 ≈ 7.0 cm.

## Slide 6
THE BIG IDEA
Sonar for people
Introduce the idea — The big idea and the definition
A piezoelectric transducer is loudspeaker and microphone in one: an alternating p.d. makes the crystal vibrate at megahertz frequency, firing a microseconds-long ultrasound pulse into the body, and each returning echo squeezes the same crystal to regenerate a voltage. Echoes are born wherever the acoustic impedance Z = ρc changes: the fraction of intensity reflected at a boundary is α = (Z₂ − Z₁)²/(Z₂ + Z₁)². Neighbouring soft tissues are closely matched, reflecting a percent or less, so most of the pulse survives to probe deeper boundaries; a tissue–air boundary reflects about 99.9%, which is why coupling gel must exclude every air film between probe and skin.
Depth comes from timing — d = vt/2, the factor two paying for the round trip. An A-scan plots echo amplitude against time along one line; a B-scan sweeps many lines into a 2-D grey-scale image. Higher frequency means shorter wavelength and finer detail, but attenuation grows with frequency, so resolution is always bought with depth.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
6 / 32
Notes: [Phase] Introduce the idea: The big idea and the definition (minutes 5–13 of 45)
[Big idea] A piezoelectric transducer is loudspeaker and microphone in one: an alternating p.d. makes the crystal vibrate at megahertz frequency, firing a microseconds-long ultrasound pulse into the body, and each returning echo squeezes the same crystal to regenerate a voltage. Echoes are born wherever the acoustic impedance Z = ρc changes: the fraction of intensity reflected at a boundary is α = (Z₂ − Z₁)²/(Z₂ + Z₁)². Neighbouring soft tissues are closely matched, reflecting a percent or less, so most of the pulse survives to probe deeper boundaries; a tissue–air boundary reflects about 99.9%, which is why coupling gel must exclude every air film between probe and skin. Depth comes from timing — d = vt/2, the factor two paying for the round trip. An A-scan plots echo amplitude against time along one line; a B-scan sweeps many lines into a 2-D grey-scale image. Higher frequency means shorter wavelength and finer detail, but attenuation grows with frequency, so resolution is always bought with depth.

## Slide 7
THE PHYSICS · 1 OF 3
The piezoelectric pulse-echo cycle
Build the model — The formulae, one at a time, in plain English
A quartz or PZT crystal changes thickness when a p.d. is applied and generates a p.d. when compressed — the piezoelectric effect runs both ways. The transducer transmits for about a microsecond, then listens for a millisecond, and a damping block glued behind the crystal kills the ringing quickly: a short, crisp pulse is what makes each echo's arrival time — and hence each depth — sharply defined.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
7 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] A quartz or PZT crystal changes thickness when a p.d. is applied and generates a p.d. when compressed — the piezoelectric effect runs both ways. The transducer transmits for about a microsecond, then listens for a millisecond, and a damping block glued behind the crystal kills the ringing quickly: a short, crisp pulse is what makes each echo's arrival time — and hence each depth — sharply defined.

## Slide 8
THE PHYSICS · 2 OF 3
Why the gel
Build the model — The formulae, one at a time, in plain English
With air between probe and skin, Z values of about 430 and 1.6 × 10⁶ kg m⁻² s⁻¹ meet, and α = (Z₂ − Z₁)²/(Z₂ + Z₁)² evaluates to roughly 0.999: the pulse bounces off the patient. Coupling gel has an impedance close to skin's, so the boundary nearly vanishes and the sound gets in — and, just as importantly, back out to the crystal.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
8 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] With air between probe and skin, Z values of about 430 and 1.6 × 10⁶ kg m⁻² s⁻¹ meet, and α = (Z₂ − Z₁)²/(Z₂ + Z₁)² evaluates to roughly 0.999: the pulse bounces off the patient. Coupling gel has an impedance close to skin's, so the boundary nearly vanishes and the sound gets in — and, just as importantly, back out to the crystal.

## Slide 9
THE PHYSICS · 3 OF 3
A-scan, B-scan, and safety
Build the model — The formulae, one at a time, in plain English
An A-scan is the raw physics: amplitude spikes on a time axis, ideal for one clean distance such as the eye's length before lens surgery. A B-scan converts each echo to a bright dot and sweeps the beam through a plane, painting the familiar grey-scale image in real time. Because ultrasound deposits no ionising energy, it is the default for obstetrics — and the machine rolls to the bedside, costing a hundredth of an MRI suite.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
9 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Section] An A-scan is the raw physics: amplitude spikes on a time axis, ideal for one clean distance such as the eye's length before lens surgery. A B-scan converts each echo to a bright dot and sweeps the beam through a plane, painting the familiar grey-scale image in real time. Because ultrasound deposits no ionising energy, it is the default for obstetrics — and the machine rolls to the bedside, costing a hundredth of an MRI suite.

## Slide 10
FORMULA 1 OF 4
Acoustic impedance
Build the model — The formulae, one at a time, in plain English
Z = ρc
units kg m⁻² s⁻¹ · soft tissues ≈ 1.4–1.7 × 10⁶
IN PLAIN ENGLISH
Impedance measures how hard a medium is to shake: density times sound speed. Echoes care only about the mismatch between the two sides of a boundary, not the values themselves.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
10 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Acoustic impedance: Z = ρc
[In plain English] Impedance measures how hard a medium is to shake: density times sound speed. Echoes care only about the mismatch between the two sides of a boundary, not the values themselves.
[Note] units kg m⁻² s⁻¹ · soft tissues ≈ 1.4–1.7 × 10⁶

## Slide 11
FORMULA 2 OF 4
Reflection coefficient
Build the model — The formulae, one at a time, in plain English
α = (Z₂ − Z₁)² / (Z₂ + Z₁)²
fraction of the intensity reflected at the boundary
IN PLAIN ENGLISH
Matched impedances (Z₂ ≈ Z₁) reflect almost nothing; wildly mismatched ones (tissue–air, tissue–bone) reflect almost everything. The squares make α blind to which side the pulse came from.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
11 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Reflection coefficient: α = (Z₂ − Z₁)² / (Z₂ + Z₁)²
[In plain English] Matched impedances (Z₂ ≈ Z₁) reflect almost nothing; wildly mismatched ones (tissue–air, tissue–bone) reflect almost everything. The squares make α blind to which side the pulse came from.
[Note] fraction of the intensity reflected at the boundary

## Slide 12
FORMULA 3 OF 4
Pulse-echo depth
Build the model — The formulae, one at a time, in plain English
d = vt/2
the factor 2 pays for the round trip
IN PLAIN ENGLISH
The clock starts at transmission and stops at the echo, but the pulse covered the distance twice. Every depth the scanner reports is really a time measurement wearing units of length.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
12 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Pulse-echo depth: d = vt/2
[In plain English] The clock starts at transmission and stops at the echo, but the pulse covered the distance twice. Every depth the scanner reports is really a time measurement wearing units of length.
[Note] the factor 2 pays for the round trip

## Slide 13
FORMULA 4 OF 4
Resolution vs reach
Build the model — The formulae, one at a time, in plain English
λ = v/f
5 MHz in tissue → λ ≈ 0.3 mm
IN PLAIN ENGLISH
Detail smaller than a wavelength is invisible, so high frequency sees finer structure — but attenuation grows with frequency, so the sharpest probes are also the shallowest.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
13 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Formula] Resolution vs reach: λ = v/f
[In plain English] Detail smaller than a wavelength is invisible, so high frequency sees finer structure — but attenuation grows with frequency, so the sharpest probes are also the shallowest.
[Note] 5 MHz in tissue → λ ≈ 0.3 mm

## Slide 14
WATCH OUT
The common trap
Check and misconception — The quick check and the trap
Coupling gel is not a lubricant. Without it, a hair's breadth of air sits between probe and skin, and the tissue–air impedance mismatch reflects about 99.9% of the intensity before the pulse even enters the body. The gel's job is acoustic impedance matching — it makes the probe-to-skin boundary almost disappear.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
14 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Misconception] Coupling gel is not a lubricant. Without it, a hair's breadth of air sits between probe and skin, and the tissue–air impedance mismatch reflects about 99.9% of the intensity before the pulse even enters the body. The gel's job is acoustic impedance matching — it makes the probe-to-skin boundary almost disappear.

## Slide 15
WORKED EXAMPLE 1 OF 2 · EASY
The question
Easy
Worked examples — I do, we do — one step revealed at a time
Muscle has density 1075 kg m⁻³ and sound speed 1590 m s⁻¹. Find its acoustic impedance.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
15 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Muscle has density 1075 kg m⁻³ and sound speed 1590 m s⁻¹. Find its acoustic impedance.
[Answer] Z ≈ 1.71 × 10⁶ kg m⁻² s⁻¹

## Slide 16
WORKED EXAMPLE 1 OF 2 · EASY · THE WORKING
How to solve it
Easy
Worked examples — I do, we do — one step revealed at a time
Muscle has density 1075 kg m⁻³ and sound speed 1590 m s⁻¹. Find its acoustic impedance.
1.
Z = ρc = 1075 × 1590.
2.
Z = 1.71 × 10⁶ kg m⁻² s⁻¹ — comfortably inside the narrow soft-tissue band.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
16 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Z = ρc = 1075 × 1590.
[Step 2] Z = 1.71 × 10⁶ kg m⁻² s⁻¹ — comfortably inside the narrow soft-tissue band.

## Slide 17
WORKED EXAMPLE 1 OF 2 · EASY
Answer
Easy
Worked examples — I do, we do — one step revealed at a time
Z ≈ 1.71 × 10⁶ kg m⁻² s⁻¹
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
17 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] Z ≈ 1.71 × 10⁶ kg m⁻² s⁻¹

## Slide 18
WORKED EXAMPLE 2 OF 2 · MEDIUM
The question
Medium
Worked examples — I do, we do — one step revealed at a time
Find the fraction of ultrasound intensity reflected at a fat–muscle boundary. Z(fat) = 1.38 × 10⁶, Z(muscle) = 1.71 × 10⁶ kg m⁻² s⁻¹.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
18 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Find the fraction of ultrasound intensity reflected at a fat–muscle boundary. Z(fat) = 1.38 × 10⁶, Z(muscle) = 1.71 × 10⁶ kg m⁻² s⁻¹.
[Answer] α ≈ 0.011 — about 1.1% reflected, 99% transmitted

## Slide 19
WORKED EXAMPLE 2 OF 2 · MEDIUM · THE WORKING
How to solve it
Medium
Worked examples — I do, we do — one step revealed at a time
Find the fraction of ultrasound intensity reflected at a fat–muscle boundary. Z(fat) = 1.38 × 10⁶, Z(muscle) = 1.71 × 10⁶ kg m⁻² s⁻¹.
1.
α = (Z₂ − Z₁)²/(Z₂ + Z₁)² = (0.33 × 10⁶)² ÷ (3.09 × 10⁶)².
2.
α = (0.1068)² = 0.0114.
3.
About 1.1% reflects — a readable echo — while 98.9% carries on to interrogate deeper boundaries. Weak reflections are a feature, not a flaw.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
19 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] α = (Z₂ − Z₁)²/(Z₂ + Z₁)² = (0.33 × 10⁶)² ÷ (3.09 × 10⁶)².
[Step 2] α = (0.1068)² = 0.0114.
[Step 3] About 1.1% reflects — a readable echo — while 98.9% carries on to interrogate deeper boundaries. Weak reflections are a feature, not a flaw.

## Slide 20
WORKED EXAMPLE 2 OF 2 · MEDIUM
Answer
Medium
Worked examples — I do, we do — one step revealed at a time
α ≈ 0.011 — about 1.1% reflected, 99% transmitted
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
20 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] α ≈ 0.011 — about 1.1% reflected, 99% transmitted

## Slide 21
SPOT THE MISTAKE
One line here is wrong
The whole working is up — find the bad line before you click
1.
In soft tissue (v = 1540 m/s) an A-scan shows an echo 52 μs after the pulse. Find the depth of the boundary.
2.
The pulse travels at 1540 m/s for 52 μs.
3.
d = vt = 1540 × 52 × 10⁻⁶
4.
d = 0.080 m = 8.0 cm
5.
So the boundary is 8.0 cm below the skin.
LINE 3 IS WRONG
The factor of two is missing: 52 μs is the round trip, out to the boundary and back, so the depth is half of what the pulse travelled. d = vt/2 = 4.0 cm. It is the single most common slip in pulse-echo work because the formula looks like ordinary speed × time, and 8.0 cm is a perfectly believable depth — nothing about the answer complains. The only defence is to say out loud what the clock was timing.
IT SHOULD SAY
d = vt/2 = 1540 × 52 × 10⁻⁶ / 2
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
21 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Spot the mistake] The working is complete and one line of it is wrong. Let the room hunt: one click names the line, a second shows it done correctly.
[Line 3 is wrong] The factor of two is missing: 52 μs is the round trip, out to the boundary and back, so the depth is half of what the pulse travelled. d = vt/2 = 4.0 cm. It is the single most common slip in pulse-echo work because the formula looks like ordinary speed × time, and 8.0 cm is a perfectly believable depth — nothing about the answer complains. The only defence is to say out loud what the clock was timing.
[It should say] d = vt/2 = 1540 × 52 × 10⁻⁶ / 2

## Slide 22
PREDICT · TAKE THE VOTE
Commit before you are told
Hands up for each option, then click
In panel 1 there is a hair's breadth of air between probe and skin. What fraction of the pulse gets into the patient?
A About 99% — the layer is far too thin to matter
B About half — some in, some back
C About 0.1% — almost all of it comes straight back off the air
Two panels of the same probe pressed against skin: in the first a thin film of air of impedance 430 lies between them, in the second a layer of coupling gel of impedance 1.65 × 10⁶, and in both the pulse is drawn arriving at the boundary with the reflected fraction marked only as α = ?
The live version of this figure — click here
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
22 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Predict] In panel 1 there is a hair's breadth of air between probe and skin. What fraction of the pulse gets into the patient?
[Options] A About 99% — the layer is far too thin to matter B About half — some in, some back C About 0.1% — almost all of it comes straight back off the air
[Figure] Two panels of the same probe pressed against skin: in the first a thin film of air of impedance 430 lies between them, in the second a layer of coupling gel of impedance 1.65 × 10⁶, and in both the pulse is drawn arriving at the boundary with the reflected fraction marked only as α = ?

## Slide 23
PREDICT · THE OUTCOME
What actually happens
Ask the room who changed their mind, and why
C About 0.1% — almost all of it comes straight back off the air
WHY
Thickness has nothing to do with it. What is reflected at a boundary is set by the mismatch in acoustic impedance across it, and 430 against 1.63 × 10⁶ is about as mismatched as two materials get: α = (Z₂ − Z₁)²/(Z₂ + Z₁)² works out at roughly 0.999. A film of air one micron thick reflects as thoroughly as a metre of it. Panel 2 is the fix — gel at 1.65 × 10⁶ against skin at 1.63 × 10⁶ gives a mismatch so small that the pulse crosses almost untouched.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
23 / 32
Notes: [Phase] Build the model: The formulae, one at a time, in plain English (minutes 13–22 of 45)
[Answer] C — About 0.1% — almost all of it comes straight back off the air. Thickness has nothing to do with it. What is reflected at a boundary is set by the mismatch in acoustic impedance across it, and 430 against 1.63 × 10⁶ is about as mismatched as two materials get: α = (Z₂ − Z₁)²/(Z₂ + Z₁)² works out at roughly 0.999. A film of air one micron thick reflects as thoroughly as a metre of it. Panel 2 is the fix — gel at 1.65 × 10⁶ against skin at 1.63 × 10⁶ gives a mismatch so small that the pulse crosses almost untouched.

## Slide 24
QUICK CHECK
Decide before the answer goes up
Check and misconception — The quick check and the trap
Two tissues have nearly equal acoustic impedances. The boundary between them…
A
Reflects almost all of the ultrasound intensity
B
Reflects almost none of it — α is tiny when Z₂ ≈ Z₁
C
Cannot transmit ultrasound at all
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
24 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Two tissues have nearly equal acoustic impedances. The boundary between them…
[Options] A Reflects almost all of the ultrasound intensity B Reflects almost none of it — α is tiny when Z₂ ≈ Z₁ C Cannot transmit ultrasound at all

## Slide 25
QUICK CHECK · THE ANSWER
The answer, and why
Check and misconception — The quick check and the trap
B Reflects almost none of it — α is tiny when Z₂ ≈ Z₁
HOW TO GET THERE
α = (Z₂ − Z₁)²/(Z₂ + Z₁)² → 0 as the impedances approach each other. Faint boundaries are the price of deep imaging — and the reason soft-tissue echoes are gentle rather than blinding.
WHY THE OTHERS TEMPT
A This is the answer for the tissue–air boundary of panel 1, where the mismatch is enormous — and it is the reason the gel exists. Two soft tissues are the opposite case: their Z values are within a few per cent of each other, and the formula is a difference squared over a sum squared, so near-equality drives α toward zero.
B Correct. α = (Z₂ − Z₁)²/(Z₂ + Z₁)² → 0 as the impedances approach each other. Faint boundaries are the price of being able to image deep at all.
C Almost nothing is reflected, which means almost everything is transmitted — the two are the same statement. A boundary that reflects weakly is the most transparent kind there is, which is exactly why a pulse can reach an organ 15 cm down and still have something left to come back with.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
25 / 32
Notes: [Phase] Check and misconception: The quick check and the trap (minutes 35–41 of 45)
[Question] Two tissues have nearly equal acoustic impedances. The boundary between them…
[Option by option] A: This is the answer for the tissue–air boundary of panel 1, where the mismatch is enormous — and it is the reason the gel exists. Two soft tissues are the opposite case: their Z values are within a few per cent of each other, and the formula is a difference squared over a sum squared, so near-equality drives α toward zero. B: Correct. α = (Z₂ − Z₁)²/(Z₂ + Z₁)² → 0 as the impedances approach each other. Faint boundaries are the price of being able to image deep at all. C: Almost nothing is reflected, which means almost everything is transmitted — the two are the same statement. A boundary that reflects weakly is the most transparent kind there is, which is exactly why a pulse can reach an organ 15 cm down and still have something left to come back with.
[Answer] B — Reflects almost none of it — α is tiny when Z₂ ≈ Z₁
[Why] α = (Z₂ − Z₁)²/(Z₂ + Z₁)² → 0 as the impedances approach each other. Faint boundaries are the price of deep imaging — and the reason soft-tissue echoes are gentle rather than blinding.
[Reveal] One click for the answer, then one for the reason.

## Slide 26
EXTENSION 1 OF 2 · HARD
The question
Hard
Worked examples — I do, we do — one step revealed at a time
In soft tissue (v = 1540 m s⁻¹) an A-scan shows echoes at 52 µs and 91 µs after the pulse. Find the depth of each boundary and the thickness of the organ between them.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
26 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] In soft tissue (v = 1540 m s⁻¹) an A-scan shows echoes at 52 µs and 91 µs after the pulse. Find the depth of each boundary and the thickness of the organ between them.
[Answer] 4.0 cm and 7.0 cm deep; the organ is 3.0 cm thick

## Slide 27
EXTENSION 1 OF 2 · HARD · THE WORKING
How to solve it
Hard
Worked examples — I do, we do — one step revealed at a time
In soft tissue (v = 1540 m s⁻¹) an A-scan shows echoes at 52 µs and 91 µs after the pulse. Find the depth of each boundary and the thickness of the organ between them.
1.
d₁ = vt/2 = 1540 × 52 × 10⁻⁶ ÷ 2 = 0.040 m.
2.
d₂ = 1540 × 91 × 10⁻⁶ ÷ 2 = 0.070 m.
3.
Thickness = d₂ − d₁ = 3.0 cm — the two faces of one organ, measured without a single incision.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
27 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] d₁ = vt/2 = 1540 × 52 × 10⁻⁶ ÷ 2 = 0.040 m.
[Step 2] d₂ = 1540 × 91 × 10⁻⁶ ÷ 2 = 0.070 m.
[Step 3] Thickness = d₂ − d₁ = 3.0 cm — the two faces of one organ, measured without a single incision.

## Slide 28
EXTENSION 1 OF 2 · HARD
Answer
Hard
Worked examples — I do, we do — one step revealed at a time
4.0 cm and 7.0 cm deep; the organ is 3.0 cm thick
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
28 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] 4.0 cm and 7.0 cm deep; the organ is 3.0 cm thick

## Slide 29
EXTENSION 2 OF 2 · CHALLENGING
The question
Challenging
Worked examples — I do, we do — one step revealed at a time
Z(soft tissue) = 1.63 × 10⁶, Z(air) = 430 kg m⁻² s⁻¹. Show why an air gap ruins a scan, and then explain the choice of 3.5 MHz for an abdominal probe versus 10 MHz for the eye.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
29 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Question] Z(soft tissue) = 1.63 × 10⁶, Z(air) = 430 kg m⁻² s⁻¹. Show why an air gap ruins a scan, and then explain the choice of 3.5 MHz for an abdominal probe versus 10 MHz for the eye.
[Answer] α ≈ 0.999 for tissue–air (hence gel); high f for shallow detail, low f for deep organs

## Slide 30
EXTENSION 2 OF 2 · CHALLENGING · THE WORKING
How to solve it
Challenging
Worked examples — I do, we do — one step revealed at a time
Z(soft tissue) = 1.63 × 10⁶, Z(air) = 430 kg m⁻² s⁻¹. Show why an air gap ruins a scan, and then explain the choice of 3.5 MHz for an abdominal probe versus 10 MHz for the eye.
1.
Air gap: α = (1.6296 × 10⁶ ÷ 1.6304 × 10⁶)² ≈ 0.9990 — 99.9% of the intensity reflects at entry, and the 0.1% that gets in loses 99.9% again on the way out. Effectively nothing returns: hence gel.
2.
Wavelengths: at 3.5 MHz, λ = 1540 ÷ 3.5 × 10⁶ ≈ 0.44 mm; at 10 MHz, λ ≈ 0.15 mm — three times the detail.
3.
But attenuation in tissue grows roughly in proportion to frequency, so the 10 MHz pulse dies within a few centimetres. The eye is 2.4 cm deep: perfect. A kidney at 10 cm needs the longer reach of 3.5 MHz and accepts the coarser resolution.
4.
Every probe is this same bargain: frequency buys resolution and spends penetration.
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
30 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Reveal] One click per step. The class works each line before the next appears.
[Step 1] Air gap: α = (1.6296 × 10⁶ ÷ 1.6304 × 10⁶)² ≈ 0.9990 — 99.9% of the intensity reflects at entry, and the 0.1% that gets in loses 99.9% again on the way out. Effectively nothing returns: hence gel.
[Step 2] Wavelengths: at 3.5 MHz, λ = 1540 ÷ 3.5 × 10⁶ ≈ 0.44 mm; at 10 MHz, λ ≈ 0.15 mm — three times the detail.
[Step 3] But attenuation in tissue grows roughly in proportion to frequency, so the 10 MHz pulse dies within a few centimetres. The eye is 2.4 cm deep: perfect. A kidney at 10 cm needs the longer reach of 3.5 MHz and accepts the coarser resolution.
[Step 4] Every probe is this same bargain: frequency buys resolution and spends penetration.

## Slide 31
EXTENSION 2 OF 2 · CHALLENGING
Answer
Challenging
Worked examples — I do, we do — one step revealed at a time
α ≈ 0.999 for tissue–air (hence gel); high f for shallow detail, low f for deep organs
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
31 / 32
Notes: [Phase] Worked examples: I do, we do — one step revealed at a time (minutes 22–35 of 45)
[Answer] α ≈ 0.999 for tissue–air (hence gel); high f for shallow detail, low f for deep organs

## Slide 32
MEDICAL PHYSICS
Where to go next
Plenary — What to take away, what to practise next
Next
29.4 Nuclear Medicine & PET
https://giophysics.com/chapter-57/nuclear-medicine/
Lesson
This lesson on giophysics.com
https://giophysics.com/chapter-57/ultrasound-imaging/
Live
The live, interactive version of these slides
https://giophysics.com/chapter-57/presentation/?lesson=ultrasound
Chapter
All Medical Physics lessons
https://giophysics.com/chapter-57/
PDF
Download the lesson PDF
https://giophysics.com/downloads/57-3-ultrasound-imaging.pdf
MEDICAL PHYSICS · ULTRASOUND IMAGING
GIOPHYSICS LESSON
Medical Physics — Ultrasound Imaging. Built by GioPhysics from the lesson's own copy; nothing on these slides is re-authored.
32 / 32
Notes: [Phase] Plenary: What to take away, what to practise next (minutes 41–45 of 45)
[Interactive] The graphs and the circuit topology on these slides are frozen. The live version at https://giophysics.com/chapter-57/presentation/?lesson=ultrasound moves them.